## Slide 1: CSE 311 Foundations of Computing I
Spring 2013, Lecture 3
Propositional Logic, Boolean Logic/Boolean Algebra

## Slide 2: Administrative
Course web: http://www.cs.washington.edu/311
  Homework, Lecture slides, Office Hours ...
Homework:
  Due Wednesday at the start of class

## Slide 3: Announcements
Reading assignments
  Propositional Logic
    1.1 -1.3 7th Edition
    1.1 -1.2 6th Edition
  Boolean Algebra
    12.1 – 12.3 7th Edition
    11.1 – 11.3 6th Edition

## Slide 4: So far
Propositional/Boolean logic
  Basic logical connectives
    If pigs can whistle, then horses can fly
  Basic circuits
  Tautologies, equivalences (in progress)

## Slide 5: Combinational Logic Circuits
OR
AND
AND
Design a 3 input circuit to compute the majority of 3. Output 1 if at least two
inputs are 1, output 0 otherwise
What about a majority of 5 circuit?

## Slide 6: Other gates (more later)
NAND
NOR
XOR X Y
XNOR X ↔ Y, X = Y
X
Y
Z
X Y Z 0 0 1 0 1 1 1 0 1
1 1 0
X Y Z 0 0 1 0 1 0 1 0 0
1 1 0
Z
X
Y
X
Y
Z
X Y Z 0 0 1 0 1 0 1 0 0
1 1 1
X Y Z 0 0 0 0 1 1 1 0 1
1 1 0
Z
X
Y

## Slide 7: Logical equivalence
Terminology: A compound proposition is a
  Tautology if it is always true
  Contradiction if it is always false
  Contingency if it can be either true or false
p   p
p  p
(p  q)  p
(p  q)  (p   q)  ( p  q)  ( p   q)
Review

## Slide 8: Logical Equivalence
p and q are logically equivalent iff p  q is a tautology
  i.e. p and q have the same truth table
The notation p  q denotes p and q are logically equivalent
Example: p    p
p |  p |   p | p   p
Review

## Slide 9: De Morgan’s Laws
 (p  q)   p   q
 (p  q)   p   q
What are the negations of:
  The Yankees and the Phillies will play in the World Series
  It will rain today or it will snow on New Year’s Day
Review

## Slide 10: De Morgan’s Laws
p | q |  p |  q |  p  q | p  q | (p  q) | (p  q) ( p  q)
T | T |  |  |  |  |  | 
T | F |  |  |  |  |  | 
F | T |  |  |  |  |  | 
F | F |  |  |  |  |  | 
Example:  (p  q)  ( p   q)
Review

## Slide 11: Law of Implication
p | q | p  q |  p |  p  q | (p  q)  ( p  q)
Example: (p  q)  ( p  q)

## Slide 12: Understanding connectives
Reflect basic rules of reasoning and logic
Allow manipulation of logical formulas
  Simplification
  Testing for equivalence
Applications
  Query optimization
  Search optimization and caching
  Artificial Intelligence
  Program verification

## Slide 13: Properties of logical connectives
Identity
Domination
Idempotent
Commutative
Associative
Distributive
Absorption
Negation
DeMorgan’s Laws
Double Negation
p  T  p
p  F  F
p  p  p
p  q  q  p
(p  q)  r  p  (q  r)
p  (q  r)  (p q)  (p  r)
p  (p  q)  p
p   p  F
Textbook, 1.3 7th Edition/1.2 6th Edition, Table 6

## Slide 14: Equivalences relating to implication
p  q   p  q
p  q   q   p
p  q   p  q
p  q   (p   q)
p  q  (p q)  (q  p)
p  q   p   q
p  q  (p  q)  ( p   q)
 (p  q)  p   q

## Slide 15: Logical Proofs
To show P is equivalent to Q
  Apply a series of logical equivalences to subexpressions to convert P to Q
To show P is a tautology
  Apply a series of logical equivalences to subexpressions to convert P to T

## Slide 16: Show (p  q)  (p  q) is a tautology

## Slide 17: Show (p  q)  r and r  (q  p) are not equivalent
All false works

## Slide 18: Boolean Logic
Applications of Propositional Logic for Circuits

## Slide 19: Boolean logic
Combinational logic
  outputt = F(inputt)
Sequential logic
  outputt = F(outputt-1, inputt)
    output dependent on history
    concept of a time step (clock)
An algebraic structure consists of
  a set of elements B = {0, 1}
  binary operations { + , • } (OR, AND)
  and a unary operation { ’ } (NOT )

## Slide 20: A quick combinational logic example
Calendar subsystem: number of days in a month (to control watch display)
  used in controlling the display of a wrist-watch LCD screen
  inputs: month, leap year flag
  outputs: number of days

## Slide 21: Implementation in software
integer number_of_days ( month, leap_year_flag) {
  switch (month) {
    case 1: return (31);
    case 2: if (leap_year_flag == 1) then return (29) else return (28);
    case 3: return (31);
    ...
    case 12: return (31);
    default: return (0);
  }
}

## Slide 22: Implementation as a combinational digital system
Encoding:
  how many bits for each input/output?
  binary number for month
  four wires for 28, 29, 30, and 31
leap
month
d28
d29
d30
d31
month leap d28 d29 d30 d31 0000 – – – – – 0001 – 0 0 0 1 0010 0 1 0 0 0 0010 1 0 1 0 0 0011 – 0 0 0 1 0100 – 0 0 1 0 0101 – 0 0 0 1 0110 – 0 0 1 0 0111 – 0 0 0 1 1000 – 0 0 0 1 1001 – 0 0 1 0 1010 – 0 0 0 1 1011 – 0 0 1 0 1100 – 0 0 0 1 1101 – – – – – 1110 – – – – – 1111 – – – – –

## Slide 23: Combinational example (cont.)
Truth-table to logic to switches to gates
  d28 = “1 when month=0010 and leap=0”
  d28 = m8'•m4'•m2•m1'•leap'
  d31 = “1 when month=0001 or month=0011 or ... month=1100”
  d31 = (m8'•m4'•m2'•m1) + (m8'•m4'•m2•m1) + ... (m8•m4•m2'•m1')
  d31 = can we simplify more?
month leap d28 d29 d30 d31 0000 – – – – – 0001 – 0 0 0 1 0010 0 1 0 0 0 0010 1 0 1 0 0 0011 – 0 0 0 1 0100 – 0 0 1 0 ... 1100 – 0 0 0 1 1101 – – – – – 111– – – – – –

## Slide 24: Combinational example (cont.)
d28 = m8'•m4'•m2•m1'•leap’
d29 = m8'•m4'•m2•m1'•leap
d30 = (m8'•m4•m2'•m1') + (m8'•m4•m2•m1') + (m8•m4'•m2'•m1) + (m8•m4'•m2•m1) = (m8'•m4•m1') + (m8•m4'•m1)
d31 = (m8'•m4'•m2'•m1) + (m8'•m4'•m2•m1) + (m8'•m4•m2'•m1) + (m8'•m4•m2•m1) + (m8•m4'•m2'•m1') + (m8•m4'•m2•m1') + (m8•m4•m2'•m1')

## Slide 25: Combinational logic
Switches
Basic logic and truth tables
Logic functions
Boolean algebra
Proofs by re-writing and by truth table

## Slide 26: Switches: basic element of physical implementations
Implementing a simple circuit (arrow shows action if wire changes to “1”):
close switch (if A is “1” or asserted) and turn on light bulb (Z)
A
Z
open switch (if A is “0” or unasserted) and turn off light bulb (Z)
Z  A
A
Z

## Slide 27: Switches (cont.)
Compose switches into more complex ones (Boolean functions):
AND
OR
Z  A and B
Z  A or B
A
B
A
B

## Slide 28: Transistor networks
Modern digital systems are designed in CMOS technology
  MOS stands for Metal-Oxide on Semiconductor
  C is for complementary because there are both normally-open and normally-closed switches
MOS transistors act as voltage-controlled switches
  similar, though easier to work with than relays.

## Slide 29: Multi-input logic gates
CMOS logic gates are inverting
  Easy to implement NAND, NOR, NOT while AND, OR, and Buffer are harder
X Y Z 0 0 1 0 1 1 1 0 1
1 1 0
Z
X
1.8V
0V
Y
1.8V
X
Y
X
Z
1.8V
0V
Y
1.8V
X
Y
X
Y
Z
Claude Shannon – 1938

## Slide 30: Possible logic functions of two variables
There are 16 possible functions of 2 input variables:
  in general, there are 2**(2**n) functions of n inputs
        X Y 16 possible functions (F0–F15) 0 0 0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1 0 1 0 0 0 0 1 1 1 1 0 0 0 0 1 1 1 1
        1 0 0 0 1 1 0 0 1 1 0 0 1 1 0 0 1 1
        1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
0
X and Y
X
Y
X or Y
not Y
not X
1
X
Y
F
X xor Y
X nor Y not (X or Y)
X = Y
X nand Y not (X and Y)

## Slide 31: Boolean algebra
An algebraic structure consisting of
  a set of elements B
  binary operations { + , • }
  and a unary operation { ’ }
  such that the following axioms hold:
1. the set B contains at least two elements: a, b 2. closure: a + b is in B a • b is in B 3. commutativity: a + b = b + a a • b = b • a 4. associativity: a + (b + c) = (a + b) + c a • (b • c) = (a • b) • c 5. identity: a + 0 = a a • 1 = a 6. distributivity: a + (b • c) = (a + b) • (a + c) a • (b + c) = (a • b) + (a • c) 7. complementarity: a + a’ = 1 a • a’ = 0
George Boole – 1854

## Slide 32: Logic functions and Boolean algebra
Any logic function that can be expressed as a truth table can be written as an expression in Boolean algebra using the operators: ’, +, and •
X, Y are Boolean algebra variables
X Y X • Y 0 0 0 0 1 0 1 0 0
1 1 1
X Y X’ Y’ X • Y X’ • Y’ ( X • Y ) + ( X’ • Y’ ) 0 0 1 1 0 1 1 0 1 1 0 0 0 0 1 0 0 1 0 0 0
1 1 0 0 1 0 1
( X • Y ) + ( X’ • Y’ )  X = Y
X Y X’ X’ • Y 0 0 1 0 0 1 1 1 1 0 0 0
1 1 0 0
Boolean expression that is true when the variables X and Y have the same value
and false, otherwise

## Slide 33: Axioms and theorems of Boolean algebra
identity 1. X + 0 = X 1D. X • 1 = X
null 2. X + 1 = 1 2D. X • 0 = 0
idempotency: 3. X + X = X 3D. X • X = X
involution: 4. (X’)’ = X
complementarity: 5. X + X’ = 1 5D. X • X’ = 0
commutatively: 6. X + Y = Y + X 6D. X • Y = Y • X
associativity: 7. (X + Y) + Z = X + (Y + Z) 7D. (X • Y) • Z = X • (Y • Z)
distributivity: 8. X • (Y + Z) = (X • Y) + (X • Z) 8D. X + (Y • Z) = (X + Y) • (X + Z)

## Slide 34: Axioms and theorems of Boolean algebra (cont.)
uniting: 9. X • Y + X • Y’ = X 9D. (X + Y) • (X + Y’) = X
absorption: 10. X + X • Y = X 10D. X • (X + Y) = X 11. (X + Y’) • Y = X • Y 11D. (X • Y’) + Y = X + Y
factoring: 12. (X + Y) • (X’ + Z) = 12D. X • Y + X’ • Z = X • Z + X’ • Y (X + Z) • (X’ + Y)
consensus: 13. (X • Y) + (Y • Z) + (X’ • Z) = 13D. (X + Y) • (Y + Z) • (X’ + Z) = X • Y + X’ • Z (X + Y) • (X’ + Z)
de Morgan’s: 14. (X + Y + ...)’ = X’ • Y’ • ... 14D. (X • Y • ...)’ = X’ + Y’ + ...

## Slide 35: Proving theorems (rewriting)
Using the laws of Boolean algebra:
  e.g., prove the theorem: X • Y + X • Y’ = X e.g., prove the theorem: X + X • Y = X
distributivity (8)
complementarity (5)
identity (1D)
identity (1D)
distributivity (8)
identity (2)
identity (1D)
X • Y + X • Y’ = X • (Y + Y’)
= X • (1)
= X
X + X • Y = X • 1 + X • Y
= X • (1 + Y)
= X • (1)
= X

## Slide 36: Proving theorems (truth table)
Using complete truth table:
  e.g., de Morgan’s:
(X + Y)’ = X’ • Y’ NOR is equivalent to AND with inputs complemented
(X • Y)’ = X’ + Y’ NAND is equivalent to OR with inputs complemented
X Y X’ Y’ (X + Y)’ X’ • Y’ 0 0 1 1 0 1 1 0
1 0 0 1
1 1 0 0
X Y X’ Y’ (X • Y)’ X’ + Y’ 0 0 1 1
0 1 1 0 1 0 0 1
1 1 0 0