## Slide 1: CSE 311 Foundations of Computing I
Lecture 4, Boolean Algebra and Circuits
Spring 2013

## Slide 2: Administrative
Course web: http://www.cs.washington.edu/311
  Homework, Lecture slides, Office Hours, ...
  Worksheets from Section, too
Homework:
  Due Wednesday at the start of class

## Slide 3: Announcements
Reading assignments
  Boolean Algebra
    12.1 – 12.3 7th Edition
    11.1 – 11.3 6th Edition
  For next time: Predicates and Quantifiers
    1.4 7th Edition
    1.3 6th Edition

## Slide 4: Highlights from last lecture Calendar: Number of Days in a Month
Encoding:
  how many bits for each input/output?
  binary number for month
  four wires for 28, 29, 30, and 31
leap
month
d28
d29
d30
d31
month leap d28 d29 d30 d31 0000 – – – – – 0001 – 0 0 0 1 0010 0 1 0 0 0 0010 1 0 1 0 0 0011 – 0 0 0 1 0100 – 0 0 1 0 0101 – 0 0 0 1 0110 – 0 0 1 0 0111 – 0 0 0 1 1000 – 0 0 0 1 1001 – 0 0 1 0 1010 – 0 0 0 1 1011 – 0 0 1 0 1100 – 0 0 0 1 1101 – – – – – 1110 – – – – – 1111 – – – – –

## Slide 5: Highlights from last lecture Calendar: Number of Days in a Month
d28 = m8'•m4'•m2•m1'•leap’
d29 = m8'•m4'•m2•m1'•leap
d30 = (m8'•m4•m2'•m1') + (m8'•m4•m2•m1') + (m8•m4'•m2'•m1) + (m8•m4'•m2•m1) = (m8'•m4•m1') + (m8•m4'•m1)
d31 = (m8'•m4'•m2'•m1) + (m8'•m4'•m2•m1) + (m8'•m4•m2'•m1) + (m8'•m4•m2•m1) + (m8•m4'•m2'•m1') + (m8•m4'•m2•m1') + (m8•m4•m2'•m1')

## Slide 6: Highlights from last lecture
Boolean algebra to circuit design
Boolean algebra
  a set of elements B = {0, 1}
  binary operations { + , • }
  and a unary operation { ’ }
  such that the following axioms hold:
1. the set B contains at least two elements: a, b 2. closure: a + b is in B a • b is in B 3. commutativity: a + b = b + a a • b = b • a 4. associativity: a + (b + c) = (a + b) + c a • (b • c) = (a • b) • c 5. identity: a + 0 = a a • 1 = a 6. distributivity: a + (b • c) = (a + b) • (a + c) a • (b + c) = (a • b) + (a • c) 7. complementarity: a + a’ = 1 a • a’ = 0
George Boole – 1854

## Slide 7: Axioms and theorems of Boolean algebra
identity 1. X + 0 = X 1D. X • 1 = X
null 2. X + 1 = 1 2D. X • 0 = 0
idempotency: 3. X + X = X 3D. X • X = X
involution: 4. (X’)’ = X
complementarity: 5. X + X’ = 1 5D. X • X’ = 0
commutatively: 6. X + Y = Y + X 6D. X • Y = Y • X
associativity: 7. (X + Y) + Z = X + (Y + Z) 7D. (X • Y) • Z = X • (Y • Z)
distributivity: 8. X • (Y + Z) = (X • Y) + (X • Z) 8D. X + (Y • Z) = (X + Y) • (X + Z)

## Slide 8: Axioms and theorems of Boolean algebra (cont.)
uniting: 9. X • Y + X • Y’ = X 9D. (X + Y) • (X + Y’) = X
absorption: 10. X + X • Y = X 10D. X • (X + Y) = X 11. (X + Y’) • Y = X • Y 11D. (X • Y’) + Y = X + Y
factoring: 12. (X + Y) • (X’ + Z) = 12D. X • Y + X’ • Z = X • Z + X’ • Y (X + Z) • (X’ + Y)
consensus: 13. (X • Y) + (Y • Z) + (X’ • Z) = 13D. (X + Y) • (Y + Z) • (X’ + Z) = X • Y + X’ • Z (X + Y) • (X’ + Z)
de Morgan’s: 14. (X + Y + ...)’ = X’ • Y’ • ... 14D. (X • Y • ...)’ = X’ + Y’ + ...

## Slide 9: Proving theorems (rewriting)
Using the laws of Boolean algebra:
  e.g., prove the theorem: X • Y + X • Y’ = X e.g., prove the theorem: X + X • Y = X
distributivity (8)
complementarity (5)
identity (1D)
identity (1D)
distributivity (8)
uniting (2)
identity (1D)
X • Y + X • Y’ = X • (Y + Y’)
= X • (1)
= X
X + X • Y = X • 1 + X • Y
= X • (1 + Y)
= X • (1)
= X

## Slide 10: Proving theorems (truth table)
Using complete truth table:
  e.g., de Morgan’s:
(X + Y)’ = X’ • Y’ NOR is equivalent to AND with inputs complemented
(X • Y)’ = X’ + Y’ NAND is equivalent to OR with inputs complemented
X Y X’ Y’ (X + Y)’ X’ • Y’ 0 0 1 1 0 1 1 0
1 0 0 1
1 1 0 0
X Y X’ Y’ (X • Y)’ X’ + Y’ 0 0 1 1
0 1 1 0 1 0 0 1
1 1 0 0

## Slide 11: A simple example: 1-bit binary adder
Inputs: A, B, Carry-in
Outputs: Sum, Carry-out
A
B
Cin
Cout
S
A B Cin Cout S
0 0 0 0 0 1
0 1 0
0 1 1
1 0 0 1 0 1
1 1 0
1 1 1
0
1
1
0
1
0
0
1
0
0
0
1
0
1
1
1
Cout = A’ B Cin + A B’ Cin + A B Cin’ + A B Cin
S = A’ B’ Cin + A’ B Cin’ + A B’ Cin’ + A B Cin
A A A A A
B B B B B
S S S S S
Cin
Cout

## Slide 12: Cout = A’ B Cin + A B’ Cin + A B Cin’ + A B Cin

## Slide 13: Apply the theorems to simplify expressions
The theorems of Boolean algebra can simplify expressions
  e.g., full adder’s carry-out function
Cout = A’ B Cin + A B’ Cin + A B Cin’ + A B Cin
= A’ B Cin + A B’ Cin + A B Cin’ + A B Cin + A B Cin
= A’ B Cin + A B Cin + A B’ Cin + A B Cin’ + A B Cin
= (A’ + A) B Cin + A B’ Cin + A B Cin’ + A B Cin
= (1) B Cin + A B’ Cin + A B Cin’ + A B Cin
= B Cin + A B’ Cin + A B Cin’ + A B Cin + A B Cin
= B Cin + A B’ Cin + A B Cin + A B Cin’ + A B Cin
= B Cin + A (B’ + B) Cin + A B Cin’ + A B Cin
= B Cin + A (1) Cin + A B Cin’ + A B Cin
= B Cin + A Cin + A B (Cin’ + Cin)
= B Cin + A Cin + A B (1)
= B Cin + A Cin + A B
adding extra terms creates new factoring opportunities

## Slide 14: S = A’ B’ Cin + A’ B Cin’ + A B’ Cin’ + A B Cin

## Slide 15: A simple example: 1-bit binary adder
Inputs: A, B, Carry-in
Outputs: Sum, Carry-out
Cout = B Cin + A Cin + A B
S = A xor (B xor Cin)
A A A A A
B B B B B
S S S S S
Cin
Cout
A
B
Cin
Cout
S
A B Cin Cout S
0 0 0 0 0 1
0 1 0
0 1 1
1 0 0 1 0 1
1 1 0
1 1 1
0
1
1
0
1
0
0
1
0
0
0
1
0
1
1
1

## Slide 16: Recall Gates
NOT
X’ X X
AND
X • Y XY X  Y
OR
X + Y X  Y
X Y Z 0 0 0 0 1 0 1 0 0
1 1 1
X Y 0 1 1 0
X Y Z 0 0 0 0 1 1 1 0 1
1 1 1
X
Y
X
Y
Z
X
Y
Z

## Slide 17: Recall gates (cont)
NAND
NOR
XOR X Y
XNOR X ↔ Y, X = Y
X
Y
Z
X Y Z 0 0 1 0 1 1 1 0 1
1 1 0
X Y Z 0 0 1 0 1 0 1 0 0
1 1 0
Z
X
Y
X
Y
Z
X Y Z 0 0 1 0 1 0 1 0 0
1 1 1
X Y Z 0 0 0 0 1 1 1 0 1
1 1 0
Z
X
Y

## Slide 18: A 2-bit ripple-carry adder
A1
B1
Cout
Cin
Sum1
A
Sum
Cout
Cin
B
1-Bit Adder
A2
B2
Sum2
Cout
Cin
0

## Slide 19: Mapping truth tables to logic gates
Given a truth table:
  Write the Boolean expression
  Minimize the Boolean expression
  Draw as gates
  Map to available gates
A B C F
0 0 0 0
0 0 1 0
0 1 0 1
0 1 1 1
1 0 0 0
1 0 1 1
1 1 0 0
1 1 1 1
F = A’BC’+A’BC+AB’C+ABC
= A’B(C’+C)+AC(B’+B)
= A’B+AC
1
2
3
4

## Slide 20: Canonical forms
Truth table is the unique signature of a Boolean function
The same truth table can have many gate realizations
  we’ve seen this already
  depends on how good we are at Boolean simplification
Canonical forms
  standard forms for a Boolean expression
  we all come up with the same expression

## Slide 21: Sum-of-products canonical form
Also known as Disjunctive Normal Form (DNF)
Also known as minterm expansion
A B C F F’ 0 0 0 0 1
0 0 1 1 0
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 0
F =
F’ = A’B’C’ + A’BC’ + AB’C’
F = 001 011 101 110 111
+ A’BC
+ AB’C
+ ABC’
+ ABC
A’B’C

## Slide 22: Sum-of-products canonical form (cont)
Product term (or minterm)
  ANDed product of literals – input combination for which output is true
  each variable appears exactly once, true or inverted (but not both)
short-hand notation for minterms of 3 variables
A B C minterms 0 0 0 A’B’C’ m0
0 0 1 A’B’C m1
0 1 0 A’BC’ m2
0 1 1 A’BC m3
1 0 0 AB’C’ m4
1 0 1 AB’C m5
1 1 0 ABC’ m6
1 1 1 ABC m7
F in canonical form: F(A, B, C) = m(1,3,5,6,7) = m1 + m3 + m5 + m6 + m7
= A’B’C + A’BC + AB’C + ABC’ + ABC
canonical form  minimal form F(A, B, C) = A’B’C + A’BC + AB’C + ABC + ABC’
      = (A’B’ + A’B + AB’ + AB)C + ABC’
      = ((A’ + A)(B’ + B))C + ABC’ = C + ABC’ = ABC’ + C
= AB + C

## Slide 23: Product-of-sums canonical form
Also known as Conjunctive Normal Form (CNF)
Also known as maxterm expansion
A B C F F’ 0 0 0 0 1
0 0 1 1 0
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 0
F = 000 010 100 F =
F’ = (A + B + C’) (A + B’ + C’) (A’ + B + C’) (A’ + B’ + C) (A’ + B’ + C’)
(A + B + C)
(A + B’ + C)
(A’ + B + C)

## Slide 24: Product-of-sums canonical form (cont)
Sum term (or maxterm)
  ORed sum of literals – input combination for which output is false
  each variable appears exactly once, true or inverted (but not both)
A B C maxterms 0 0 0 A+B+C M0
0 0 1 A+B+C’ M1
0 1 0 A+B’+C M2
0 1 1 A+B’+C’ M3
1 0 0 A’+B+C M4
1 0 1 A’+B+C’ M5
1 1 0 A’+B’+C M6
1 1 1 A’+B’+C’ M7
short-hand notation for maxterms of 3 variables
F in canonical form: F(A, B, C) = M(0,2,4) = M0 • M2 • M4
= (A + B + C) (A + B’ + C) (A’ + B + C)
canonical form  minimal form F(A, B, C) = (A + B + C) (A + B’ + C) (A’ + B + C)
      = (A + B + C) (A + B’ + C)
      (A + B + C) (A’ + B + C)
      = (A + C) (B + C)