## Slide 2: 1-bit Binary Adder
Inputs: A, B, Carry-in
Outputs: Sum, Carry-out
A
B
Cin
Cout
S
0 0 0 0 0 1
0 1 0
0 1 1
1 0 0 1 0 1
1 1 0
1 1 1
A B Cin Cout S
0
1
1
0
1
0
0
1
0
0
0
1
0
1
1
1
Cout = A’ B Cin + A B’ Cin + A B Cin’ + A B Cin
S = A’ B’ Cin + A’ B Cin’ + A B’ Cin’ + A B Cin
A A A A A
B B B B B
S S S S S
Cin
Cout

## Slide 3: Apply Theorems to Simplify Expressions
The theorems of Boolean algebra can simplify expressions
  e.g., full adder’s carry-out function
Cout = A’ B Cin + A B’ Cin + A B Cin’ + A B Cin
= A’ B Cin + A B’ Cin + A B Cin’ + A B Cin + A B Cin
= A’ B Cin + A B Cin + A B’ Cin + A B Cin’ + A B Cin
= (A’ + A) B Cin + A B’ Cin + A B Cin’ + A B Cin
= (1) B Cin + A B’ Cin + A B Cin’ + A B Cin
= B Cin + A B’ Cin + A B Cin’ + A B Cin + A B Cin
= B Cin + A B’ Cin + A B Cin + A B Cin’ + A B Cin
= B Cin + A (B’ + B) Cin + A B Cin’ + A B Cin
= B Cin + A (1) Cin + A B Cin’ + A B Cin
= B Cin + A Cin + A B (Cin’ + Cin)
= B Cin + A Cin + A B (1)
= B Cin + A Cin + A B
adding extra terms creates new factoring opportunities

## Slide 4: Gates Again!
X Y Z 0 0 0 0 1 0 1 0 0
1 1 1
X Y 0 1 1 0
X Y Z 0 0 0 0 1 1 1 0 1
1 1 1
X
Y
X
Y
Z
X
Y
Z

## Slide 5: More Gates!
X
Y
Z
X Y Z 0 0 1 0 1 1 1 0 1
1 1 0
X Y Z 0 0 1 0 1 0 1 0 0
1 1 0
Z
X
Y
X
Y
Z
X Y Z 0 0 1 0 1 0 1 0 0
1 1 1
X Y Z 0 0 0 0 1 1 1 0 1
1 1 0
Z
X
Y

## Slide 6: A 2-bit Ripple-Carry Adder
A
Sum
Cout
Cin
B
1-Bit Adder
A0
B0
Cout
Cin
Sum0
0
A1
B1
Sum1
Cout
Cin
A2
B2
Sum2
Cout
Cin

## Slide 7: Mapping Truth Tables to Logic Gates
Given a truth table:
  Write the Boolean expression
  Minimize the Boolean expression
  Draw as gates
  Map to available gates
A B C F
0 0 0 0
0 0 1 0
0 1 0 1
0 1 1 1
1 0 0 0
1 0 1 1
1 1 0 0
1 1 1 1
F = A’BC’+A’BC+AB’C+ABC
= A’B(C’+C)+AC(B’+B)
= A’B+AC
1
2
3
4

## Slide 8: CSE 311: Foundations of Computing
Fall 2014
Lecture 5: Canonical Forms, Predicate Logic

## Slide 9: Canonical Forms
Truth table is the unique signature of a Boolean function
The same truth table can have many gate realizations
  we’ve seen this already
  depends on how good we are at Boolean simplification
Canonical forms
  standard forms for a Boolean expression
  we all come up with the same expression

## Slide 10: Sum-of-Products Canonical Form
also known as Disjunctive Normal Form (DNF)
also known as minterm expansion
A B C F F’ 0 0 0 0 1
0 0 1 1 0
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 0
F =
F = 001 011 101 110 111
+ A’BC
+ AB’C
+ ABC’
+ ABC
A’B’C
Notes: F’ = A’B’C’ + A’BC’ + AB’C’

## Slide 11: Sum-of-Products Canonical Form
Product term (or minterm)
  ANDed product of literals – input combination for which output is true
  each variable appears exactly once, true or inverted (but not both)
A B C minterms 0 0 0 A’B’C’
0 0 1 A’B’C
0 1 0 A’BC’
0 1 1 A’BC
1 0 0 AB’C’
1 0 1 AB’C
1 1 0 ABC’
1 1 1 ABC
F in canonical form: F(A, B, C) = A’B’C + A’BC + AB’C + ABC’ + ABC
canonical form  minimal form F(A, B, C) = A’B’C + A’BC + AB’C + ABC + ABC’
      = (A’B’ + A’B + AB’ + AB)C + ABC’
      = ((A’ + A)(B’ + B))C + ABC’ = C + ABC’ = ABC’ + C
= AB + C

## Slide 12: Product-of-Sums Canonical Form
Also known as Conjunctive Normal Form (CNF)
Also known as maxterm expansion
A B C F F’ 0 0 0 0 1
0 0 1 1 0
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 0
F = 000 010 100 F =
(A + B + C)
(A + B’ + C)
(A’ + B + C)
Notes: F’ = (A + B + C’) (A + B’ + C’) (A’ + B + C’) (A’ + B’ + C) (A’ + B’ + C’)

## Slide 13: s-o-p, p-o-s, and de Morgan’s theorem
Complement of function in sum-of-products form:
  F’ = A’B’C’ + A’BC’ + AB’C’
Complement again and apply de Morgan’s and get the product-of-sums form:
  (F’)’ = (A’B’C’ + A’BC’ + AB’C’)’
  F = (A + B + C) (A + B’ + C) (A’ + B + C)

## Slide 14: Product-of-Sums Canonical Form
Sum term (or maxterm)
  ORed sum of literals – input combination for which output is false
  each variable appears exactly once, true or inverted (but not both)
A B C maxterms 0 0 0 A+B+C
0 0 1 A+B+C’
0 1 0 A+B’+C
0 1 1 A+B’+C’
1 0 0 A’+B+C
1 0 1 A’+B+C’
1 1 0 A’+B’+C
1 1 1 A’+B’+C’
F in canonical form: F(A, B, C) = (A + B + C) (A + B’ + C) (A’ + B + C)
canonical form  minimal form F(A, B, C) = (A + B + C) (A + B’ + C) (A’ + B + C)
      = (A + B + C) (A + B’ + C)
      (A + B + C) (A’ + B + C)
      = (A + C) (B + C)

## Slide 15: Predicate Logic
Propositional Logic
  If the tortoise walks at a rate of one node per step, and the hare walks at a rate of two nodes per step, ...
Predicate Logic
  If the tortoise is on node x, and the hare is on node 2x, then …
Prime(65353)

## Slide 16: Predicate Logic
Propositional Logic
  Allows us to analyze complex propositions in terms of their simpler constituent parts joined by connectives
Predicate Logic
  Lets us analyze them at a deeper level…
Prime(65353)

## Slide 17: Predicate Logic
Predicate or Propositional Function
  A function that returns a truth value, e.g.,
    “x is a cat”
    “x is prime”
    “student x has taken course y”
    “x > y”
    “x + y = z” or Sum(x, y, z)
    “5 < x”
Predicates will have variables or constants as arguments.
Prime(65353)

## Slide 18: Domain of Discourse
We must specify a “domain of discourse”, which is the possible things we’re talking about.
“x is a cat”
(e.g., mammals)
“x is prime”
(e.g., numbers)
student x has taken course y”
(e.g., students and courses)
Relate  and  to  and 

## Slide 19: Quantifiers
x P(x)
  P(x) is true for every x in the domain
  read as “for all x, P of x”
x P(x)
There is an x in the domain for which P(x) is true
  read as “there exists x, P of x”
Relate  and  to  and 

## Slide 20: Statements with Quantifiers
x Even(x)
x Odd(x)
x (Even(x)  Odd(x))
x (Even(x)  Odd(x))
x Greater(x+1, x)
x (Even(x)  Prime(x))
Even(x)
Odd(x)
Prime(x)
Greater(x,y)
(or “x>y”)
Equal(x,y)
(or “x=y”)
Sum(x,y,z)
Domain:
Positive Integers

## Slide 21: Statements with Quantifiers
x y Greater (y, x)
x y Greater (x, y)
x y (Greater(y, x)  Prime(y))
x (Prime(x)  (Equal(x, 2)  Odd(x))
x y (Sum(x, 2, y)  Prime(x)  Prime(y))
Even(x)
Odd(x)
Prime(x)
Greater(x,y)
(or “x>y”)
Equal(x,y)
(or “x=y”)
Sum(x,y,z)
Domain:
Positive Integers

## Slide 22: English to Predicate Logic
Cat(x)
Red(x)
LikesTofu(x)
“Red cats like tofu”
“Some red cats don’t like tofu”

## Slide 23: Negations of Quantifiers
not every positive integer is prime
some positive integer is not prime
prime numbers do not exist
every positive integer is not prime

## Slide 24: Negations of Quantifiers
x PurpleFruit(x)
  “All fruits are purple”
x PurpleFruit(x)
  “Not all fruits are purple”
How about x PurpleFruit(x)?
  “There is a purple fruit”
  If it’s the negation, all situations should be covered by a statement and its negation
  Consider the domain {Orange}: Neither statement is true!
How about x PurpleFruit(x)?
  “There is a fruit that isn’t purple”
Domain:
Fruit
PurpleFruit(x)

## Slide 25: De Morgan’s Laws for Quantifiers
x P(x)  x P(x)
x P(x)  x P(x)

## Slide 26: de morgan’s laws for quantifiers
  x  y ( x ≥ y)
 x  y ( x ≥ y)
 x  y  ( x ≥ y)
 x  y (y > x)
“There is no largest integer”
“For every integer there is a larger integer”
x P(x)  x  P(x)
 x P(x)  x  P(x)

## Slide 27: scope of quantifiers
    example: Notlargest(x)   y Greater (y, x)   z Greater (z, x)
    truth value:
    doesn’t depend on y or z “bound variables”
    does depend on x “free variable”
    quantifiers only act on free variables of the formula they quantify
   x ( y (P(x,y)   x Q(y, x)))

## Slide 28: Scope of Quantifiers
x (P(x)  Q(x)) vs. x P(x)  x Q(x)