## Slide 1: A few announcements
Course web page – check often
  cse.uw.edu/351
  Schedule, policies, labs, homeworks, and everything else
  Videos: watch them for review! Quizzes at the end.
Course discussion board
Course mailing list – check your @uw.edu
  Low traffic – mostly announcements; you are already subscribed
Office hours, appointments, drop-ins
  We spread our office hours throughout the week
Staff e-mail: cse351-tas@cse.uw.edu
  For things that are not appropriate for the discussion board
Anonymous feedback
Late policy: 3 late day as you wish, 10% per day after that

## Slide 2: Hardware: Logical View
CPU
Memory
Disks
Net
USB
Etc.
Bus
Notes: Big pipe between CPU and memory, since…
Disks bigger storage, slower, farther away
Network, etc.

## Slide 3: Hardware: Physical View
CPU
USB…
Bus connections
I/O
controller
Storage connections
Memory

## Slide 4: Hardware: 351 View (version 0)
CPU executes instructions; memory stores data
To execute an instruction, the CPU must:
  fetch an instruction;
  fetch the data used by the instruction; and, finally,
  execute the instruction on the data…
  which may result in writing data back to memory.
Memory
CPU
?
data
instructions
Notes: The CPU and Memory are what this course focuses on.

## Slide 5: Hardware: 351 View (version 1)
The CPU holds instructions temporarily in the instruction cache
The CPU holds data temporarily in a fixed number of registers
Instruction and operand fetching is HW-controlled
Data movement is programmer-controlled
We’ll learn about the instructions the CPU executes – take 352 to find out how it actually executes them
Memory
data
instructions
CPU
take 352…
registers
i-cache
this week…
Notes: The CPU and Memory are what this course focuses on.

## Slide 6: Hardware: 351 View (version 1)
The CPU holds instructions temporarily in the instruction cache.
The CPU holds data temporarily in a fixed number of registers.
Instruction fetching is HW-controlled.
Data movement is programmer-controlled.
Memory
data
instructions
CPU
take 352…
registers
i-cache
this week…
How are data and instructions represented?
How does a program find its data in memory?
Notes: The CPU and Memory are what this course focuses on.

## Slide 7: Roadmap
car *c = malloc(sizeof(car));
c->miles = 100;
c->gals = 17;
float mpg = get_mpg(c);
free(c);
Car c = new Car();
c.setMiles(100);
c.setGals(17);
float mpg = c.getMPG();
get_mpg:
pushq %rbp
movq %rsp, %rbp
...
popq %rbp
ret
Java:
C:
Assembly language:
Machine code:
0111010000011000
100011010000010000000010
1000100111000010
110000011111101000011111
Computer system:
OS:
Memory & data
Integers & floats
Machine code & C
x86 assembly
Procedures & stacks
Arrays & structs
Memory & caches
Processes
Virtual memory
Memory allocation
Java vs. C

## Slide 8: Memory, Data, and Addressing
Representing information as bits and bytes
Organizing and addressing data in memory
Manipulating data in memory using C
Boolean algebra and bit-level manipulations

## Slide 9
Memory
data
instructions
CPU
take 352…
registers
i-cache
this week…
How are data and instructions represented?

## Slide 10: Binary Representations
Base 2 number representation
  A base 2 digit (0 or 1) is called a bit.
  Represent 35110 as 00000001010111112 or 1010111112
Electronic implementation
  Easy to store with bi-stable elements
  Reliably transmitted on noisy and inaccurate wires
0.0V
0.5V
2.8V
3.3V
0
1
0
Notes: Speed of transition from low to high and back limits the speed over our computers.
Stay away from middle voltages.

## Slide 11: Describing Byte Values
Binary 000000002 -- 111111112
  Byte = 8 bits (binary digits)
Decimal 010 -- 25510
Hexadecimal 0016 -- FF16
  Byte = 2 hexadecimal (or “hex” or base 16) digits
  Base 16 number representation
  Use characters ‘0’ to ‘9’ and ‘A’ to ‘F’
  Write FA1D37B16 in the C language
    as 0xFA1D37B or 0xfa1d37b
More on specific data types later…
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111
Hex
Decimal
Binary

## Slide 12
Memory
data
instructions
CPU
take 352…
registers
i-cache
this week…
How does a program find its data in memory?

## Slide 13: Byte-Oriented Memory Organization
Conceptually, memory is a single, large array of bytes, each with an unique address (index)
The value of each byte in memory can be read and written
Programs refer to bytes in memory by their addresses
  Domain of possible addresses = address space
But not all values (e.g., 351) fit in a single byte…
  Store addresses to “remember” where other data is in memory
  How much memory can we address with 1-byte (8-bit) addresses?
Many operations actually use multi-byte values
• • •
00•••0
FF•••F
Notes: Run-time system: program loader, standard C libraries, operating system – parts of the program that are needed but not built in by the compiler itself.

## Slide 14: Machine Words
Word size = address size = register size
Word size bounds the size of the address space and memory
  word size = w bits => 2w addresses
  Until recently, most machines used 32-bit (4-byte) words
    Potential address space: 232 addresses 232 bytes  4 x 109 bytes = 4 billion bytes = 4GB
    Became too small for memory-intensive applications
  Current x86 systems use 64-bit (8-byte) words
    Potential address space: 264 addresses 264 bytes  1.8 x 1019 bytes = 18 billion billion bytes = 18 EB (exabytes)
Notes:     You could count the world population with 33 fingers.
    [x86-64 currently supports up to 48-bit physical addresses: 256 TB (terabytes)]

## Slide 15: Word-Oriented Memory Organization
Addresses specify locations of bytes in memory
  Address of word = address of first byte in word
  Addresses of successive words differ by word size (in bytes): e.g., 4 (32-bit) or 8 (64-bit)
  Address of word 0, 1, .. 10?
0000
0001
0002
0003
0004
0005
0006
0007
0008
0009
0010
0011
32-bit
Words
Bytes
Addr.
0012
0013
0014
0015
64-bit
Words
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
(note: decimal
addresses)

## Slide 16: Word-Oriented Memory Organization
Addresses still specify locations of bytes in memory
  Address of word = address of first byte in word
  Addresses of successive words differ by word size (in bytes): e.g., 4 (32-bit) or 8 (64-bit)
  Address of word 0, 1, .. 10?
  Alignment
0000
0001
0002
0003
0005
0006
0007
0008
0009
0010
0011
32-bit
Words
Bytes
Addr.
0012
0013
0014
0015
64-bit
Words
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
0000
0004
0008
0012
0000
0008
0004
(note: decimal
addresses)

## Slide 17: Memory Alignment
Data of size n only stored at addresses a where a mod n = 0
  Convention or rule, depending on platform
  n is usually a power of 2
A 32-bit (4-byte) word-aligned view of memory:
  Each row is a word composed of 4 bytes
  Cells in a row are the word’s bytes
  More about alignment later in the course
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
…
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
(note hex
addresses)

## Slide 18: Addresses and Pointers
An address is a location in memory
A pointer is a data object that holds an address
The value 351 is stored at address 0x04
  35110 = 15F16 = 0x00 00 01 5F
5F
01
00
00
0x00
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
0x04
Notes: Interpretation

## Slide 19: Addresses and Pointers
An address is a location in memory
A pointer is a data object that holds an address
The value 351 is stored at address 0x04
  35110 = 15F16 = 0x00 00 01 5F
A pointer stored at address 0x1C points to address 0x04
Pointer to a pointer?
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
04
00
00
00
5F
01
00
00
Notes: Interpretation

## Slide 20: Addresses and Pointers
An address is a location in memory
A pointer is a data object that holds an address
The value 351 is stored at address 0x04
  35110 = 15F16 = 0x00 00 01 5F
A pointer stored at address 0x1C points to address 0x04
A pointer to a pointer is stored at address 0x24
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
04
00
00
00
1C
00
00
00
5F
01
00
00
Notes: Interpretation

## Slide 21: Addresses and Pointers
An address is a location in memory
A pointer is a data object that holds an address.
The value 351 is stored at address 0x04
  35110 = 15F16 = 0x00 00 01 5F
A pointer stored at address 0x1C points to address 0x04
A pointer to a pointer is stored at address 0x24
The value 12 is stored at address 0x14
  Is it a pointer? Hmmm
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
04
00
00
00
1C
00
00
00
5F
01
00
00
0C
00
00
00
Notes: Interpretation

## Slide 22: Data Representations
Sizes of data types (in bytes)
  Java Data Type C Data Type Typical 32-bit x86-64
    boolean bool 1 1
    byte char 1 1
    char 2 2
    short short int 2 2
    int int 4 4
    float float 4 4
    long int 4 8
    double double 8 8
    long long long 8 8
    long double 8 16
    (reference) pointer * 4 8
address size = word size
Notes: This mapping is mostly an arbitrary historical artifact except for address sizes.

## Slide 23: Byte Ordering
How should bytes within a word be ordered in memory?
Example: Store the 4-byte word 0xa1 b2 c3 d4
  In what order will the bytes be stored?
Conventions!
  Big-endian, Little-endian
  Based on Gulliver’s Travels: tribes cut eggs on different sides (big, little)

## Slide 24: Byte Ordering
Big-Endian (PowerPC, SPARC, The Internet)
  Least significant byte has highest address
Little-Endian (x86)
  Least significant byte has lowest address
Example
  Variable has 4-byte representation 0xa1b2c3d4
  Address of variable is 0x100
0x100
0x101
0x102
0x103
01
23
45
67
0x100
0x101
0x102
0x103
67
45
23
01
Big Endian
Little Endian
a1
b2
c3
d4
d4
c3
b2
a1

## Slide 25: Byte Ordering Examples
Decimal: 12345
Binary: 0011 0000 0011 1001
Hex: 3 0 3 9
39
30
00
00
IA32, x86-64 (little endian)
00
00
00
00
39
30
00
00
x86-64
39
30
00
00
IA32
30
39
00
00
SPARC (big endian)
30
39
00
00
32-bit
SPARC
30
39
00
00
64-bit
SPARC
00
00
00
00
int x = 12345;
// or x = 0x3039;
long int y = 12345;
// or y = 0x3039;
(A long int is the size of a word)
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07

## Slide 26: Reading Byte-Reversed Listings
Disassembly
  Take binary machine code and generate an assembly code version
  Does the reverse of the assembler
Example instruction in memory
  add value 0x12ab to register ‘ebx’ (a special location in CPU’s memory)
Address Instruction Code Assembly Rendition
8048366: 81 c3 ab 12 00 00 add $0x12ab,%ebx

## Slide 27: Reading Byte-Reversed Listings
Disassembly
  Take binary machine code and generate an assembly code version
  Does the reverse of the assembler
Example instruction in memory
  add value 0x12ab to register ‘ebx’ (a special location in CPU’s memory)
Address Instruction Code Assembly Rendition
8048366: 81 c3 ab 12 00 00 add $0x12ab,%ebx
Deciphering numbers
  Value: 0x12ab
  Pad to 32 bits: 0x000012ab
  Split into bytes: 00 00 12 ab
  Reverse (little-endian): ab 12 00 00

## Slide 28: Addresses and Pointers in C
& = ‘address of’
* = ‘value at address’ or ‘dereference’
int* ptr;
int x = 5;
int y = 2;
ptr = &x;
y = 1 + *ptr;
Declares a variable, ptr, that is a pointer to (i.e., holds the address of) an int in memory
Declares two variables, x and y, that hold ints, and sets them to 5 and 2, respectively
Sets ptr to the address of x.
Now, “ptr points to x”
Sets y to “1 plus the value stored at the address held by ptr,
because ptr points to x, this is equivalent to y=1+x;
“Dereference ptr”
What is *(&y) ?

## Slide 29: Today (Jan 9)
C assignments
C arrays
C strings
Bit manipulations
Announcements:
  Lab 1 out today

## Slide 30: Assignment in C
A variable is represented by a memory location
Initially, it may hold any value
int x, y;
  x is at location 0x04, y is at 0x18
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
F3
29
01
00
00
00
00
01
x
y
00
32
00
A7
EE
EE
EE
EE
FE
CA
CE
FA
00
00
00
26
00
10
00
00
96
F4
00
FF
00
00
00
00
34
17
42
00
& = ‘address of’
* = ‘value at address’ or ‘dereference’
0x00
0x01
0x02
0x03
* is also used with variable declarations

## Slide 31: Assignment in C
A variable is represented by a memory location
Initially, it may hold any value
int x, y;
  x is at location 0x04, y is at 0x18
x
y
F3
29
01
00
00
00
00
01
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
& = ‘address of’
* = ‘value at address’ or ‘dereference’
0x00
0x01
0x02
0x03

## Slide 32: Assignment in C
Left-hand-side = right-hand-side;
  LHS must evaluate to a memory location
  RHS must evaluate to a value (could be an address!)
  Store RHS value at LHS location
int x, y;
x = 0;
00
00
00
00
00
00
00
01
x
y
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
& = ‘address of’
* = ‘value at address’ or ‘dereference’
0x00
0x01
0x02
0x03

## Slide 33: Assignment in C
Left-hand-side = right-hand-side;
  LHS must evaluate to a memory location
  RHS must evaluate to a value (could be an address!)
  Store RHS value at LHS location
int x, y;
x = 0;
y = 0x3CD02700;
00
00
00
00
3C
D0
27
00
x
y
little endian!
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
& = ‘address of’
* = ‘value at address’ or ‘dereference’
0x00
0x01
0x02
0x03

## Slide 34: Assignment in C
Left-hand-side = right-hand-side;
  LHS must evaluate to a memory location
  RHS must evaluate to a value (could be an address!)
  Store RHS value at LHS location
int x, y;
x = 0;
y = 0x3CD02700;
x = y + 3;
  Get value at y, add 3, put it in x
3C
D0
27
03
3C
D0
27
00
x
y
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
& = ‘address of’
* = ‘value at address’ or ‘dereference’
0x00
0x01
0x02
0x03

## Slide 35: Assignment in C
Left-hand-side = right-hand-side;
  LHS must evaluate to a memory location
  RHS must evaluate to a value (could be an address!)
  Store RHS value at LHS location
int x, y;
x = 0;
y = 0x3CD02700;
x = y + 3;
  Get value at y, add 3, put it in x
int* z
3C
D0
27
03
3C
D0
27
00
x
y
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
z
& = ‘address of’
* = ‘value at address’ or ‘dereference’
0x00
0x01
0x02
0x03

## Slide 36: Assignment in C
Left-hand-side = right-hand-side;
  LHS must evaluate to a memory location
  RHS must evaluate to a value (could be an address!)
  Store RHS value at LHS location
int x, y;
x = 0;
y = 0x3CD02700;
x = y + 3;
  Get value at y, add 3, put it in x
int* z = &y + 3;
  Get address of y, add ???, put it in z
3C
D0
27
03
3C
D0
27
00
x
y
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
z
& = ‘address of’
* = ‘value at address’ or ‘dereference’
0x00
0x01
0x02
0x03

## Slide 37: Assignment in C
Left-hand-side = right-hand-side;
  LHS must evaluate to a memory location
  RHS must evaluate to a value (could be an address!)
  Store RHS value at LHS location
int x, y;
x = 0;
y = 0x3CD02700;
x = y + 3;
  Get value at y, add 3, put it in x
int* z = &y + 3;
  Get address of y, add 12, put it in z
3C
D0
27
03
3C
D0
27
00
x
y
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
z
00
00
00
24
Pointer arithmetic is scaled by size of target type
Pointer arithmetic can be dangerous
& = ‘address of’
* = ‘value at address’ or ‘dereference’
0x00
0x01
0x02
0x03
0x18 = 24 (decimal) + 12 36 = 0x24
Notes: y is an int.
This means “the address 3 ints beyond &y in the address space”
Since an int is 4 bytes

## Slide 38: Assignment in C
Left-hand-side = right-hand-side;
  LHS must evaluate to a memory location
  RHS must evaluate to a value (could be an address!)
  Store RHS value at LHS location
int x, y;
x = 0;
y = 0x3CD02700;
x = y + 3;
  Get value at y, add 3, put it in x
int* z = &y + 3;
  Get address of y, add 12, put it in z
*z = y;
  What does this do?
3C
D0
27
03
3C
D0
27
00
x
y
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
z
00
00
00
24
& = ‘address of’
* = ‘value at address’ or ‘dereference’
0x00
0x01
0x02
0x03

## Slide 39: Assignment in C
Left-hand-side = right-hand-side;
  LHS must evaluate to a memory location
  RHS must evaluate to a value (could be an address!)
  Store RHS value at LHS location
int x, y;
x = 0;
y = 0x3CD02700;
x = y + 3;
  Get value at y, add 3, put it in x
int* z = &y + 3;
  Get address of y, add 12, put it in z
*z = y;
  Get value of y, put it at the address stored in z
3C
D0
27
03
3C
D0
27
00
x
y
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
z
00
00
00
24
3C
D0
27
00
The target of a pointer is also a memory location
& = ‘address of’
* = ‘value at address’ or ‘dereference’
0x00
0x01
0x02
0x03

## Slide 40: Arrays in C
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
Declaration:
int a[6];
a is a name for the array’s address
Arrays are adjacent locations in memory storing the same type of data object
element type
name
number of elements
0x00
0x01
0x02
0x03

## Slide 41: Arrays in C
00
00
01
5F
00
00
01
5F
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
Declaration:
a[0]
a[1]
a[5]
…
a[0] = 0x015f;
a[5] = a[0];
Indexing:
int a[6];
The address of a[i] is the address of a[0] plus i times the element size in bytes
a is a name for the array’s address
Arrays are adjacent locations in memory storing the same type of data object
0x00
0x01
0x02
0x03

## Slide 42: Arrays in C
00
00
01
5F
00
00
01
5F
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
Declaration:
a[0]
a[1]
a[5]
…
a[0] = 0x015f;
a[5] = a[0];
Indexing:
a[6] = 0xBAD;
a[-1] = 0xBAD;
No bounds
check:
00
00
0B
AD
00
00
0B
AD
int a[6];
The address of a[i] is the address of a[0] plus i times the element size in bytes
a is a name for the array’s address
Arrays are adjacent locations in memory storing the same type of data object
0x00
0x01
0x02
0x03

## Slide 43: Arrays in C
00
00
01
5F
00
00
01
5F
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
00
00
00
04
Declaration:
p
a[0]
a[1]
a[5]
…
a[0] = 0x015f;
a[5] = a[0];
Indexing:
Pointers:
{
equivalent
a[6] = 0xBAD;
a[-1] = 0xBAD;
No bounds
check:
00
00
0B
AD
00
00
0B
AD
int* p;
p = a;
p = &a[0];
int a[6];
The address of a[i] is the address of a[0] plus i times the element size in bytes
a is a name for the array’s address
Arrays are adjacent locations in memory storing the same type of data object
0x00
0x01
0x02
0x03

## Slide 44: Arrays in C
00
00
01
5F
00
00
01
5F
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
00
00
00
04
Declaration:
p
a[0]
a[1]
a[5]
…
a[0] = 0x015f;
a[5] = a[0];
Indexing:
Pointers:
{
equivalent
a[6] = 0xBAD;
a[-1] = 0xBAD;
No bounds
check:
00
00
0B
AD
00
00
0B
AD
int* p;
p = a;
p = &a[0];
*p = 0xA;
int a[6];
The address of a[i] is the address of a[0] plus i times the element size in bytes
a is a name for the array’s address
Arrays are adjacent locations in memory storing the same type of data object
0x00
0x01
0x02
0x03

## Slide 45: Arrays in C
00
00
00
0A
00
00
01
5F
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
00
00
00
04
Declaration:
p
a[0]
a[1]
a[5]
…
a[0] = 0x015f;
a[5] = a[0];
Indexing:
Pointers:
{
equivalent
a[6] = 0xBAD;
a[-1] = 0xBAD;
No bounds
check:
00
00
0B
AD
00
00
0B
AD
int* p;
p = a;
p = &a[0];
*p = 0xA;
int a[6];
The address of a[i] is the address of a[0] plus i times the element size in bytes
a is a name for the array’s address
Arrays are adjacent locations in memory storing the same type of data object
0x00
0x01
0x02
0x03

## Slide 46: Arrays in C
00
00
00
0A
00
00
01
5F
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
00
00
00
04
Declaration:
p
a[0]
a[1]
a[5]
…
a[0] = 0x015f;
a[5] = a[0];
Indexing:
Pointers:
{
equivalent
a[6] = 0xBAD;
a[-1] = 0xBAD;
No bounds
check:
00
00
0B
AD
00
00
0B
AD
00
00
00
0B
int* p;
p = a;
p = &a[0];
*p = 0xA;
p[1] = 0xB;
int a[6];
The address of a[i] is the address of a[0] plus i times the element size in bytes
a is a name for the array’s address
Arrays are adjacent locations in memory storing the same type of data object
0x00
0x01
0x02
0x03

## Slide 47: Arrays in C
array indexing = address arithmetic
Both are scaled by the size of the type
00
00
00
0A
00
00
01
5F
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
00
00
00
04
Declaration:
p
a[0]
a[1]
a[5]
…
a[0] = 0x015f;
a[5] = a[0];
Indexing:
Pointers:
{
equivalent
a[6] = 0xBAD;
a[-1] = 0xBAD;
No bounds
check:
00
00
0B
AD
00
00
0B
AD
00
00
00
0B
int* p;
p = a;
p = &a[0];
*p = 0xA;
p[1] = 0xB;
int a[6];
The address of a[i] is the address of a[0] plus i times the element size in bytes
a is a name for the array’s address
Arrays are adjacent locations in memory storing the same type of data object
0x00
0x01
0x02
0x03

## Slide 48: Arrays in C
array indexing = address arithmetic
Both are scaled by the size of the type
00
00
00
0A
00
00
01
5F
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
00
00
00
04
Declaration:
p
a[0]
a[1]
a[5]
…
a[0] = 0x015f;
a[5] = a[0];
Indexing:
Pointers:
{
equivalent
a[6] = 0xBAD;
a[-1] = 0xBAD;
No bounds
check:
00
00
0B
AD
00
00
0B
AD
00
00
00
0B
int* p;
p = a;
p = &a[0];
*p = 0xA;
{
equivalent
p[1] = 0xB;
*(p + 1) = 0xB;
int a[6];
The address of a[i] is the address of a[0] plus i times the element size in bytes
a is a name for the array’s address
Arrays are adjacent locations in memory storing the same type of data object
0x00
0x01
0x02
0x03

## Slide 49: Arrays in C
array indexing = address arithmetic
Both are scaled by the size of the type
00
00
00
0A
00
00
01
5F
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
00
00
00
04
Declaration:
p
a[0]
a[1]
a[5]
…
a[0] = 0x015f;
a[5] = a[0];
Indexing:
Pointers:
{
equivalent
a[6] = 0xBAD;
a[-1] = 0xBAD;
No bounds
check:
00
00
0B
AD
00
00
0B
AD
00
00
00
0B
int* p;
p = a;
p = &a[0];
*p = 0xA;
{
equivalent
p[1] = 0xB;
*(p + 1) = 0xB;
p = p + 2;
int a[6];
The address of a[i] is the address of a[0] plus i times the element size in bytes
a is a name for the array’s address
Arrays are adjacent locations in memory storing the same type of data object
0x00
0x01
0x02
0x03

## Slide 50: Arrays in C
array indexing = address arithmetic
Both are scaled by the size of the type
00
00
00
0A
00
00
01
5F
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
00
00
00
0C
Declaration:
p
a[0]
a[1]
a[5]
…
a[0] = 0x015f;
a[5] = a[0];
Indexing:
Pointers:
{
equivalent
a[6] = 0xBAD;
a[-1] = 0xBAD;
No bounds
check:
00
00
0B
AD
00
00
0B
AD
00
00
00
0B
int* p;
p = a;
p = &a[0];
*p = 0xA;
{
equivalent
p[1] = 0xB;
*(p + 1) = 0xB;
p = p + 2;
int a[6];
The address of a[i] is the address of a[0] plus i times the element size in bytes
a is a name for the array’s address
Arrays are adjacent locations in memory storing the same type of data object
0x00
0x01
0x02
0x03

## Slide 51: Arrays in C
array indexing = address arithmetic
Both are scaled by the size of the type
00
00
00
0A
00
00
01
5F
0x00
0x04
0x08
0x0C
0x10
0x14
0x18
0x1C
0x20
0x24
00
00
00
0C
Declaration:
p
a[0]
a[1]
a[5]
…
a[0] = 0x015f;
a[5] = a[0];
Indexing:
Pointers:
{
equivalent
a[6] = 0xBAD;
a[-1] = 0xBAD;
No bounds
check:
00
00
0B
AD
00
00
0B
AD
00
00
00
0B
int* p;
p = a;
p = &a[0];
*p = 0xA;
{
equivalent
p[1] = 0xB;
*(p + 1) = 0xB;
p = p + 2;
int a[6];
*p = a[1] + 1;
00
00
00
0C
The address of a[i] is the address of a[0] plus i times the element size in bytes
a is a name for the array’s address
Arrays are adjacent locations in memory storing the same type of data object
0x00
0x01
0x02
0x03

## Slide 52: Representing strings?

## Slide 53: Representing strings
A C-style string is represented by an array of bytes (char)
  Elements are one-byte ASCII codes for each character
  ASCII = American Standard Code for Information Interchange
32 | space |  | 48 | 0 |  | 64 | @ |  | 80 | P |  | 96 | ` |  | 112 | p
33 | ! |  | 49 | 1 |  | 65 | A |  | 81 | Q |  | 97 | a |  | 113 | q
34 | ” |  | 50 | 2 |  | 66 | B |  | 82 | R |  | 98 | b |  | 114 | r
35 | # |  | 51 | 3 |  | 67 | C |  | 83 | S |  | 99 | c |  | 115 | s
36 | $ |  | 52 | 4 |  | 68 | D |  | 84 | T |  | 100 | d |  | 116 | t
37 | % |  | 53 | 5 |  | 69 | E |  | 85 | U |  | 101 | e |  | 117 | u
38 | & |  | 54 | 6 |  | 70 | F |  | 86 | V |  | 102 | f |  | 118 | v
39 | ’ |  | 55 | 7 |  | 71 | G |  | 87 | W |  | 103 | g |  | 119 | w
40 | ( |  | 56 | 8 |  | 72 | H |  | 88 | X |  | 104 | h |  | 120 | x
41 | ) |  | 57 | 9 |  | 73 | I |  | 89 | Y |  | 105 | I |  | 121 | y
42 | * |  | 58 | : |  | 74 | J |  | 90 | Z |  | 106 | j |  | 122 | z
43 | + |  | 59 | ; |  | 75 | K |  | 91 | [ |  | 107 | k |  | 123 | {
44 | , |  | 60 | < |  | 76 | L |  | 92 | \ |  | 108 | l |  | 124 | ¦
45 | - |  | 61 | = |  | 77 | M |  | 93 | ] |  | 109 | m |  | 125 | }
46 | . |  | 62 | > |  | 78 | N |  | 94 | ^ |  | 110 | n |  | 126 | ~
47 | / |  | 63 | ? |  | 79 | O |  | 95 | _ |  | 111 | o |  | 127 | del

## Slide 54: Null-terminated Strings
72 | 97 | 114 | 114 | 121 | 32 | 80 | 111 | 116 | 116 | 101 | 114 | 0
H | a | r | r | y |  | P | o | t | t | e | r | \0
For example, “Harry Potter” can be stored as a 13-byte array
Why do we put a 0, or null zero, at the end of the string?
  Note the special symbol: string[12] = '\0';
How do we compute the string length?

## Slide 55: Endianness and Strings
char s[6] = "12345";
Byte ordering (endianness) is not an issue for 1-byte values
  The whole array does not constitute a single value
  Individual elements are values; chars are single bytes
Unicode characters – up to 4 bytes/character
  ASCII codes still work (just add leading zeros)
  Unicode can support the many characters in all languages in the world
  Java and C have libraries for Unicode (Java commonly uses 2 bytes/char)
33
34
31
32
35
00
33
34
31
32
35
00
C (char = 1 byte)
0x00
0x01
0x02
0x03
0x04
0x05
0x00
0x01
0x02
0x03
0x04
0x05
Note: 0x31 = 49 decimal = ASCII ‘1’
‘1’
‘2’
‘3’
‘4’
‘5’
‘\0’
IA32, x86-64 (little endian)
SPARC (big endian)

## Slide 56: Examining Data Representations
Code to print byte representation of data
  Any data type can be treated as a byte array by casting it to char
  C has unchecked casts. << DANGER >>
void show_bytes(char* start, int len) {
int i;
for (i = 0; i < len; i++)
printf("%p\t0x%.2x\n", start+i, *(start+i));
printf("\n");
}
printf directives:
%p Print pointer
\t Tab
%x Print value as hex
\n New line
void show_int (int x) {
show_bytes( (char *) &x, sizeof(int));
}
Notes: %p: prefix “0x” automatically printed

## Slide 57: show_bytes Execution Example
int a = 12345; // represented as 0x00003039
printf("int a = 12345;\n");
show_int(a); // show_bytes((char *) &a, sizeof(int));
Result:
int a = 12345;
0x11ffffcb8 0x39
0x11ffffcb9 0x30
0x11ffffcba 0x00
0x11ffffcbb 0x00

## Slide 58: Boolean Algebra
Developed by George Boole in 19th Century
  Algebraic representation of logic
    Encode “True” as 1 and “False” as 0
  AND: A&B = 1 when both A is 1 and B is 1
  OR: A|B = 1 when either A is 1 or B is 1
  XOR: A^B = 1 when either A is 1 or B is 1, but not both
  NOT: ~A = 1 when A is 0 and vice-versa
  DeMorgan’s Law: ~(A | B) = ~A & ~B ~(A & B) = ~A | ~B

## Slide 59: Boolean Algebra
Developed by George Boole in 19th Century
  Algebraic representation of logic
    Encode “True” as 1 and “False” as 0
  AND: A&B = 1 when both A is 1 and B is 1
  OR: A|B = 1 when either A is 1 or B is 1
  XOR: A^B = 1 when either A is 1 or B is 1, but not both
  NOT: ~A = 1 when A is 0 and vice-versa
  DeMorgan’s Law: ~(A | B) = ~A & ~B ~(A & B) = ~A | ~B

## Slide 60: General Boolean Algebras
Operate on bit vectors
  Operations applied bitwise
All of the properties of Boolean algebra apply
How does this relate to set operations?
01101001
& 01010101
01000001
01101001
| 01010101
01111101
01101001
^ 01010101
00111100
~ 01010101
10101010
01010101
^ 01010101
00000000

## Slide 61: Representing & Manipulating Sets
Representation
  A w-bit vector represents subsets of {0, …, w–1}
  aj = 1 iff j  A
    01101001 { 0, 3, 5, 6 }
    76543210
    01010101 { 0, 2, 4, 6 }
    76543210
Operations
  & Intersection 01000001 { 0, 6 }
  | Union 01111101 { 0, 2, 3, 4, 5, 6 }
  ^ Symmetric difference 00111100 { 2, 3, 4, 5 }
  ~ Complement 10101010 { 1, 3, 5, 7 }

## Slide 62: Bit-Level Operations in C
& | ^ ~
  Apply to any “integral” data type
    long, int, short, char, unsigned
  View arguments as bit vectors
Examples (char data type)
  ~0x41 --> 0xBE
    ~010000012 --> 101111102
  ~0x00 --> 0xFF
    ~000000002 --> 111111112
  0x69 & 0x55 --> 0x41
    011010012 & 010101012 --> 010000012
  0x69 | 0x55 --> 0x7D
    011010012 | 010101012 --> 011111012
Some bit-twiddling puzzles in Lab 1

## Slide 63: Contrast: Logic Operations in C
Contrast to logical operators
  && || !
    0 is “False”
    Anything nonzero is “True”
    Always return 0 or 1
    Early termination a.k.a. short-circuit evaluation
Examples (char data type)
  !0x41 --> 0x00
  !0x00 --> 0x01
  !!0x41 --> 0x01
  0x69 && 0x55 --> 0x01
  0x69 || 0x55 --> 0x01
  p && *p++ (avoids null pointer access, null pointer = 0x00000000 )