## Slide 1: Lecture 19
Logistics
  HW5 is due today (full credit today, 20% off Monday 10:29am, Solutions up Monday 10:30am)
  HW6 is due Wednesday (no late HW accepted, solutions posted immediately)
  Midterm next Friday --- covers materials up to HW6 and Monday lecture)
Last lecture
  Finite State Machines (FSM)
Today
  Timing issues
    Timing terminology and issues and solutions (e.g. clock skew)
    Asynchronous inputs and issues and solutions (e.g. debouncing)
19

## Slide 2: The “WHY” slide
Timing issues
  For sequential logic, “timing” is critical because for the same inputs, the output could be different at different times (like T-flip flops). In order to achieve desired outputs, timing has to be taken into consideration.
  Transistors, chips, and even wires have their own delays. Because of this, nothing could ever be perfectly synchronized. It is important to understand how fast a clock can tick based on these delays and what the common issues are in making computers to run fast and accurately.
  There are synchronous and asynchronous inputs. For example, typing on the keyboard, you are putting in asynchronous inputs to the computer. Asynchronous inputs can change the outputs immediately regardless of the clock state, and it is important to know how to handle that.
19

## Slide 3: Latches versus flip-flops
behavior is the same unless input
changes while the clock is high
For most applications, it is not good to see
Input changes instantaneously at the output
CLK
D
Qff
Qlatch
D
Q
Q
CLK
D
Q
Q
CLK
19

## Slide 4: The master-slave D
D
Q
CLK
Input
Master D latch
D
Q
Output
Slave D latch
master-slave D flip-flop
Because of the timing issue, it was good to use two latches as master-slave configuration or use one flip-flop.
19

## Slide 5: Timing terminology and constraints
  Setup time tsu: Amount of time the input must be stable before the clock transitions high (or low for negative-edge triggered FF)
  Hold time th: Amount of time the input must be stable after the clock transitions high (or low for negative-edge triggered FF)
  Clock width tw : Clock width that must be met
  Propagation delays tplh and tphl: Propagation delay (high to low, low to high) (longer than hold time)
th
tw
tplh
tphl
tsu
D
CLK
Q
th
tsu
D
Q
Q
CLK
15
19

## Slide 6: Cascading flip-flops
Flip-flop propagation delays exceed hold times
  Second stage commits its input before Q0 changes
In
Q0
Q1
Clk
tsu
tphl
th
tsu
th
tplh
IN
CLK
Q0
Q1
D
Q
D
Q
>
>
15
19

## Slide 7: Side note: Clock skew
Goal: Clock all flip-flops at the same time
  Difficult to achieve in high-speed systems
    Clock delays (wire, buffers) are comparable to logic delays
  Problem is called clock skew
  Avoiding clock skew: design identical delays
Original state: IN = 0, Q0 = 1, Q1 = 1
Next state: Q0 = 0, Q1 = 0 (should be Q1 = 1)
CLK0 clocks first flipflop
CLK1 clocks second flipflop
CLK1 should align with
CLK0, but is delayed
due to clock skew
IN
Q0
Q1
CLK0
CLK1
15
19

## Slide 8: System considerations
Use edge-triggered flip-flops wherever possible
  Avoid latches
  Most common: Master-slave D
Basic rules for correct timing
  Clock flip-flops synchronously (all at the same time)
    No flip-flop changes state more than once per clock cycle
    FF propagation delay > hold time
  Avoid mixing positive-edge triggered and negative-edge triggered flip-flops in the same circuit
19

## Slide 9: Asynchronous versus synchronous
Asynchronous
  State changes occur when state inputs change
  Feedback elements may be wires or delays
Synchronous
  State changes occur synchronously
  Feedback elements are clocked
Clock
Combinational Logic
Combinational Logic
Synchronous
Asynchronous
16
19

## Slide 10: Asynchronous inputs
Clocked circuits are synchronous
  Circuit changes state only at clock edges
  Signals (voltages) settle in-between clock edges
Unclocked circuits or signals are asynchronous
  No master clock
  Real-world inputs (e.g. a keypress) are asynchronous
Synchronous circuits have asynchronous inputs
  Reset signal, memory wait, user input, etc.
  Inputs “bounce”
  Inputs can change at any time
    We must synchronize the input to our clock
    Inputs will violate flip-flop setup/hold times
19

## Slide 11: Debouncing
Switch inputs bounce
  i. e. don’t make clean transitions
Can use RS latch for debouncing
  Eliminates dynamic hazards
  “Cleans-up” inputs
R
S
Q
Q'
3.3V
3.3V
0V
3.3V
0V
1
0
1
0
15
19

## Slide 12: Synchronizer failure
Occurs when FF input changes near clock edge
  Input is neither 1 or 0 when clock goes high
  Output may be neither 0 or 1
    May stay undefined for a long time
  Undefined state is called metastability
logic 0
logic 1
D
CLK
Q
19

## Slide 13: Minimizing synchronizer failures
Failure probability can never be zero
  Cascade two (or more) flip-flops
    Effectively synchronizes twice
    Both would have to fail for system to fail
D
D
Q
asynchronous
input
synchronized
input
Clk
Q
15
19

## Slide 14: Handling asynchronous inputs
Never fan-out asynchronous inputs
  Synchronize at circuit boundary
  Fan-out synchronized signal
D
Q
D
Q
Q0
Clock
Clock
Q1
Async
Input
D
Q
D
Q
Q0
Clock
Clock
Q1
Async
Input
D
Q
Synchronizer
19

## Slide 15: Summary: Timing issues with asynchronous inputs
For sequential logic circuits, timing issues have to be considered.
Inputs are often asynchronous and can cause problems.
Different amount of delay at different part of the circuit can cause problems also.
Solutions:
  Cascade flip flops in series
  Incorporate RS latch for debouncing
  Design to keep timing alignment in mind (length of cable, etc)
15
19