## Slide 1: CSE373: Data Structures & Algorithms Lecture 26: Memory Hierarchy and Locality
1
Kevin Quinn, Fall 2015

## Slide 2: Why do we need to know about the memory Hierarchy?
One of the assumptions that Big-Oh makes is that all operations take the same amount of time
  This is not quite correct.

## Slide 3: Example
8
16
0
1
2
…
1000
1001
…
1999
…
3000
3001
…
5000
5001
…
7000
7001
x
y
z[0]
z[1]
…
z[999]
…
top
…
val
next
…
val
next
address 5000
address 7000
7
24
null
0
0
0
int x = 8;
int y = 2 * x;
int[] z = new int[1000]
int val = z[0] + z[1] + z[999];
ListNode top = new ListNode(7);
top.next = new ListNode(24);
ListNode temp = top.next;

## Slide 4: Definitions
Cycle (for our purposes): the time is takes to execute a single simple instruction (for example, add 2 registers together)
Memory Latency: The time it takes to access memory

## Slide 6: Moral of the story
It is much faster to do:
  5 million arithmetic ops than 1 disk access
  25000 L2 cache accesses than 1 disk access
  400 main memory accesses then 1 disk access
Why though?
  Physical realities (speed of light, closeness to CPU)
  Cost (price per byte of different technologies)
  Disks get much bigger but not much faster
    Spinning at 7200 RPM account for much of the slowness, spinning hard disks are unlikely to get much faster.
    What about SSDs?
  Speedup at higher levels (i.e. a faster processor) makes lower level accesses relatively slower. Yikes.

## Slide 9: What can we do to optimize?
Hardware automatically moves data into caches from main memory
  Replacing items already there
  Algorithms are much faster if data fits in the cache
Disk accesses are abstracted away by the operating system
Code “just runs” but sometimes it’s worth designing algorithms/data structures with knowledge of the memory hierarchy

## Slide 10: Locality
Temporal Locality (locality in time)
  If an item (a location in memory) is referenced, that same location will tend to be referenced again soon
Spatial Locality (locality in space)
  If an item is referenced, items whose addresses are close by will tend to be referenced soon as well

## Slide 11: How does data move up the hierarchy?
Moving data up the hierarchy is slow because of latency (distance to travel)
  Since we are making a trip anyway, might as well carpool!
    Get a block of data in the same time it takes to get a byte
  Send nearby memory
    Because its cheap and easy
    And spatial locality says it will be asked for soon!
Once we move something to the cache, keep it around for a while, no rush to get rid of it! (Temporal Locality)

## Slide 12: Cache Facts
Each level is a sub-set of the level below
Definitions
  Cache hit: address requested already in the cache
  Cache miss: address request NOT in the cache
  Block of page size: the number of contiguous bytes moved from disk to memory
  Cache line size: the number of contiguous bytes moved from memory to the cache

## Slide 13: Examples
x = a + 6; miss
y = a + 5; hit Temporal
z = 8 * a; hit Locality
x = a[0]; miss
y = a[1] + 5; hit Spatial
z = 8 * a[2]; hit Locality

## Slide 14: Locality in Data Structure
Which has the least potential for better spatial locality, arrays or linked lists?

## Slide 15: Where is the locality?
for (int i = 1; i < 100; i++) {
a = a * 7;
b = b + x[i];
c = y[5] + d;
}
= Spatial Locality on locations in array x
= Temporal Locality