## Slide 1: CSE 451: Operating Systems Winter 2022 Module 15 I/O System and Secondary Storage
Gary Kimura
Notes: 1x day
1

## Slide 2: What’s Ahead
High level view of the I/O System
We will concentrate on two major I/O components
Secondary Storage
  Disk Drives and SSD
File System
  Objectives
  Programming Interface
  On-Disk Structure (Storage layout)

## Slide 3: But first the I/O System Hardware Environment
Major components of a computer system: CPU, memories (primary/secondary), I/O system
I/O devices:
  Block devices – store information in fixed-sized blocks; typical sizes: 128-4096 bytes
  Character devices – delivers/accepts stream of characters (bytes)
Device controllers:
  Connects physical device to system bus (Minicomputers, PCs)
  Mainframes use a more complex model: Multiple buses and specialized I/O computers (I/O channels)
Communication:
  Memory-mapped I/O, controller registers
  Direct Memory Access - DMA

## Slide 4: I/O Hardware - Single Bus
CPU
Memory
Video Controller
Keyboard Controller
Mouse Controller
Disk Controller
System bus
Monitor
Keyboard
Mouse
Disk drive

## Slide 5: I/O Hardware - Multiple Buses
Video controller
Network controller
IDE disk controller
USB interface
keyboard
mouse
CPU
PCI bridge/ memory controller
Memory
Cache
SCSI controller
SCSI disk
SCSI disk
SCSI disk
PCI bus
USB bus
SCSI bus
Memory bus

## Slide 6: Diversity among I/O Devices
The I/O System has to consider device characteristics:
Data rate:
  may vary by several orders of magnitude
Complexity of control:
  exclusive vs. shared devices
Unit of transfer:
  stream of bytes vs. block-I/O
Data representations:
  character encoding, error codes, parity conventions
Error conditions:
  consequences, range of responses
Applications:
  impact on resource scheduling, buffering schemes

## Slide 7: The I/O System’s role
The I/O System is essentially the glue that holds this all together. By providing
A programming interface for applications to use (hopefully not too big, also not too cumbersome). Some functions are straightforward, like open, close, read, and write. And some are device specific like ioctl’s.
A way for the myriad of hardware devices to attach to the system through device drivers.
In the Windows, its I/O System, File Systems, and Device Drivers are the largest pieces of code in the OS.

## Slide 8: Organization of the I/O Function
Programmed I/O with polling:
  The processor issues an I/O command on behalf of a process
  The process busy waits for completion of the operation before proceeding
Interrupt-driven I/O:
  The processor issues an I/O command and continues to execute
  The I/O module interrupts the processor when it has finished I/O
  The initiator process may be suspended pending the interrupt
Direct memory access (DMA):
  A DMA module controls exchange of data between I/O module and main memory
  The processor requests transfer of a block of data from DMA and is interrupted only after the entire block has been transferred

## Slide 9: I/O System and Secondary Storage
That was our quick overview of the I/O System.
  There is a lot more to discuss if time permits. Such as following a full I/O request from the time the User issues the request, until it causes some action at the hardware level, and then the return trip back to the User.
But now onto Secondary Storage

## Slide 10: Secondary storage
Secondary storage typically:
  is anything that is outside of “primary memory”
  does not permit direct execution of instructions or data retrieval via machine load/store instructions
Characteristics:
  it’s large: 500-2000GB
  it’s cheap: $0.05-$0.10/GB for hard drives from Dell (at 2TB size)
  it’s persistent: data survives power loss
  it’s slow: milliseconds to access
    why is this slow??
  it does fail, if rarely
    big failures (drive dies; MTBF ~3 years)
      if you have 100K drives and MTBF is 3 years, that’s 1 “big failure” every 15 minutes!
    little failures (read/write errors, one byte in 1013)

## Slide 11: Another trip down memory lane …
IBM 2314
About the size of
6 refrigerators
8 x 29MB (M!)
Required similar-sized air condx!
.01% (not 1% – .01%!) the capacity of this $100 4”x6”x1” item

## Slide 12: Disk trends
Disk capacity, 1975-1989
  doubled every 3+ years
  25% improvement each year
  factor of 10 every decade
  Still exponential, but far less rapid than processor performance
Disk capacity, 1990-recently
  doubling every 12 months
  100% improvement each year
  factor of 1000 every decade
  Capacity growth 10x as fast as processor performance!

## Slide 13
Only a few years ago, we purchased disks by the megabyte (and it hurt!)
Today, 1 GB (a billion bytes) costs $1 $0.50 $0.10-$0.05 from Dell (except you have to buy in increments of 40 80 250 2000 GB)
  => 1 TB costs $1K $500 $100, 1 PB costs $1M $500K $100K
Technology is amazing
  Flying a 747 6” above the ground
  Reading/writing a strip of postage stamps
But …
  Jets do crash …

## Slide 14: Memory hierarchy
Each level acts as a cache of lower levels
CPU registers
L1 cache
L2 cache
Primary Memory
Secondary Storage
Tertiary Storage
100 bytes
32KB
256KB
1GB
1TB
1PB
10 ms
1s-1hr
< 1 ns
1 ns
4 ns
60 ns

## Slide 15: Memory hierarchy: distance analogy
CPU registers
L1 cache
L2 cache
Primary Memory
Secondary Storage
Tertiary Storage
1 minute
10 minutes
1.5 hours
2 years
2,000 years
Pluto
Andromeda
“My head”
“This room”
“This building”
Olympia
seconds

## Slide 16
© 2004 Jim Gray, Microsoft Corporation

## Slide 17: Disks and the OS
Disks are messy, messy devices
  errors, bad blocks, missed seeks, etc.
Job of OS is to hide this mess from higher-level software (disk hardware increasingly helps with this)
  low-level device drivers (initiate a disk read, etc.)
  higher-level abstractions (files, databases, etc.)
  (note that modern disk drives do some of this masking for the OS)
OS may provide different levels of disk access to different clients
  physical disk block (surface, cylinder, sector)
  disk logical block (disk block #)
  file logical (filename, block or record or byte #)

## Slide 18: Physical disk structure
Disk components
  platters
  surfaces
  tracks
  sectors
  cylinders
  arm
  heads
platter
surface
track
sector
cylinder
arm
head

## Slide 19: Interacting with disks
In the old days…
  OS would have to specify cylinder #, sector #, surface #, transfer size
    i.e., OS needs to know all of the disk parameters
Modern disks are even more complicated
  not all sectors are the same size, sectors are remapped, …
  disk provides a higher-level interface, e.g., SCSI
    exports data as a logical array of blocks [0 … N]
    maps logical blocks to cylinder/surface/sector
    OS only needs to name logical block #, disk maps this to cylinder/surface/sector
    on-board cache
    as a result, physical parameters are hidden from OS
      both good and bad

## Slide 20: Disks and the File System
There is a lot more to say about disks and their peculiar characteristics, but some of it is antiquated because of Solid State Drives (SSD). Hopefully, we will find time to talk about this later.
From a simple File System perspective. Secondary storage (disk and SSD) are logical blocks that it can read and write.
And the File System is our next topic.