## Slide 1: Edge Detection
CSE 455
Linda Shapiro

## Slide 2: Edge
Attneave's Cat (1954)

## Slide 3
Edges are caused by a variety of factors.
depth discontinuity
surface color discontinuity
illumination discontinuity
surface normal discontinuity
Origin of edges

## Slide 4: Characterizing edges
An edge is a place of rapid change in the image intensity function
image
intensity function (along horizontal scanline)
first derivative
edges correspond to extrema of derivative

## Slide 5
The gradient of an image:
The gradient points in the direction of most rapid change in intensity
Image gradient

## Slide 6: The discrete gradient
How can we differentiate a digital image F[x,y]?
  Option 1: reconstruct a continuous image, then take gradient
  Option 2: take discrete derivative (“finite difference”)

## Slide 7
The gradient direction is given by:
  How does this relate to the direction of the edge?
The edge strength is given by the gradient magnitude
Simple image gradient
How would you implement this as a filter?
perpendicular
or various
simplifications
0 -1 1

## Slide 8
Sobel operator
-1 | 0 | 1
-2 | 0 | 2
-1 | 0 | 1
-1 | -2 | -1
0 | 0 | 0
1 | 2 | 1
Magnitude:
Orientation:
In practice, it is common to use:
What’s the C/C++ function?
Use atan2
Who was Sobel?

## Slide 9
Sobel operator
Original
Orientation
Magnitude

## Slide 10: Effects of noise
Consider a single row or column of the image
  Plotting intensity as a function of position gives a signal
Where is the edge?

## Slide 11: Effects of noise
Difference filters respond strongly to noise
  Image noise results in pixels that look very different from their neighbors
  Generally, the larger the noise the stronger the response
What can we do about it?
Source: D. Forsyth

## Slide 12: Solution: smooth first
Where is the edge?
Look for peaks in

## Slide 13: Derivative theorem of convolution
Differentiation is convolution, and convolution is associative:
This saves us one operation:
f
Source: S. Seitz
How can we find (local) maxima of a function?
We don’t
do that.

## Slide 14: Remember: Derivative of Gaussian filter
x-direction
y-direction

## Slide 15: Laplacian of Gaussian
Consider
Laplacian of Gaussian
operator
Where is the edge?
Zero-crossings of bottom graph

## Slide 16: 2D edge detection filters
is the Laplacian operator:
Laplacian of Gaussian
Gaussian
derivative of Gaussian
Notes: How many 2nd derivative filters are there? There are four 2nd partial derivative filters.
In practice, it’s handy to define a single 2nd derivative filter—the Laplacian

## Slide 17: Edge detection by subtraction
original

## Slide 18: Edge detection by subtraction
smoothed (5x5 Gaussian)

## Slide 19: Edge detection by subtraction
smoothed – original
(scaled by 4, offset +128)

## Slide 20: Using the LoG Function (Laplacian of Gaussian)
The LoG function will be
  Zero far away from the edge
  Positive on one side
  Negative on the other side
  Zero just at the edge
It has simple digital mask implementation(s)
So it can be used as an edge operator
BUT, THERE’S SOMETHING BETTER

## Slide 21: Canny edge detector
This is probably the most widely used edge detector in computer vision
J. Canny, A Computational Approach To Edge Detection, IEEE Trans. Pattern Analysis and Machine Intelligence, 8:679-714, 1986.
Source: L. Fei-Fei

## Slide 22: The Canny edge detector
original image (Lena)
Note:
I hate the
Lena images.

## Slide 23: The Canny edge detector
norm of the gradient

## Slide 24: The Canny edge detector
thresholding

## Slide 25: Get Orientation at Each Pixel
theta = atan2(-gy, gx)
Notes: -gy because y=2 is below y=1, and we typically want 90 degrees to point up

## Slide 26: The Canny edge detector

## Slide 27: The Canny edge detector
thinning
(non-maximum suppression)

## Slide 28: Non-maximum suppression
Check if pixel is local maximum along gradient direction
Picture from Prem K Kalra

## Slide 29: Compute Gradients (DoG)
X-Derivative of Gaussian
Y-Derivative of Gaussian
Gradient Magnitude

## Slide 30: Canny Edges

## Slide 31: Canny on Kidney

## Slide 32: Canny Characteristics
The Canny operator gives single-pixel-wide images with good continuation between adjacent pixels
It is the most widely used edge operator today; no one has done better since it came out in the late 80s. Many implementations are available.
It is very sensitive to its parameters, which need to be adjusted for different application domains.

## Slide 33: Effect of  (Gaussian kernel spread/size)
Canny with
Canny with
original
The choice of depends on desired behavior
  large detects large scale edges
  small detects fine features

## Slide 34: An edge is not a line...
How can we detect lines ?

## Slide 35: Finding lines in an image
Option 1:
  Search for the line at every possible position/orientation
  What is the cost of this operation?
Option 2:
  Use a voting scheme: Hough transform

## Slide 36: Finding lines in an image
Connection between image (x,y) and Hough (m,b) spaces
  A line in the image corresponds to a point in Hough space
  To go from image space to Hough space:
    given a set of points (x,y), find all (m,b) such that y = mx + b
x
y
m
b
m0
b0
image space
Hough space

## Slide 37: Hough transform algorithm
Typically use a different parameterization
  d is the perpendicular distance from the line to the origin
   is the angle of this perpendicular with the horizontal.

## Slide 38: Hough transform algorithm
Basic Hough transform algorithm
  Initialize H[d, ]=0
  for each edge point I[x,y] in the image
    for  = 0 to 180
      H[d, ] += 1
  Find the value(s) of (d, ) where H[d, ] is maximum
  The detected line in the image is given by
What’s the running time (measured in # votes)?
How big is the array H?
Do we need to try all θ?
d

Array H

## Slide 39: Example
0 0 0 100 100
0 0 0 100 100
0 0 0 100 100
100 100 100 100 100
100 100 100 100 100
- - 0 0 -
- - 0 0 -
90 90 40 20 -
90 90 90 40 -
- - - - -
- - 3 3 -
- - 3 3 -
3 3 3 3 -
3 3 3 3 -
- - - - -
360
.
6
3
0
- - - - - - -
- - - - - - -
- - - - - - -
4 - 1 - 2 - 5
- - - - - - -
0 10 20 30 40 …90
360
.
6
3
0
- - - - - - -
- - - - - - -
- - - - - - -
* - * - * - *
- - - - - - -
(1,3)(1,4)(2,3)(2,4)
(3,1)
(3,2)
(4,1)
(4,2)
(4,3)
gray-tone image
DQ
THETAQ
Accumulator H
PTLIST
distance
angle

## Slide 40
Chalmers University
of Technology

## Slide 41
Chalmers University
of Technology

## Slide 42: How do you extract the line segments from the accumulators?
pick the bin of H with highest value V
while V > value_threshold {
order the corresponding pointlist from PTLIST
merge in high gradient neighbors within 10 degrees
create line segment from final point list
zero out that bin of H
pick the bin of H with highest value V }

## Slide 43: Line segments from Hough Transform

## Slide 44: Extensions
Extension 1: Use the image gradient
  same
  for each edge point I[x,y] in the image
    compute unique (d, ) based on image gradient at (x,y)
      H[d, ] += 1
  same
  same
What’s the running time measured in votes?
Extension 2
  give more votes for stronger edges
Extension 3
  change the sampling of (d, ) to give more/less resolution
Extension 4
  The same procedure can be used with circles, squares, or any other shape, How?
Extension 5; the Burns procedure. Uses only angle, two different quantifications, and connected components with votes for larger one.
Notes: Ask: what are the axes for a circle Hough space? What does a point in the image map to in the Hough space?

## Slide 45: A Nice Hough Variant The Burns Line Finder
1. Compute gradient magnitude and direction at each pixel.
2. For high gradient magnitude points, assign direction labels
to two symbolic images for two different quantizations.
3. Find connected components of each symbolic image.
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
Each pixel belongs to 2 components, one for each symbolic image.
Each pixel votes for its longer component.
Each component receives a count of pixels who voted for it.
The components that receive majority support are selected.
-22.5
+22.5
0
45

## Slide 46: Example
Quantization 1 Quantization 2
Quantization 1 leads to 2 yellow components and 2 green.
Quantization 2 leads to 1 BIG red component.
All the pixels on the line vote for their Quantization 2
component. It becomes the basis for the line.
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
-22.5
+22.5
0

## Slide 47: Burns Example 1

## Slide 48: Burns Example 2

## Slide 49: Hough Transform for Finding Circles
Equations:
r = r0 + d sin 
c = c0 - d cos 
r, c, d are parameters
Main idea: The gradient vector at an edge pixel points
to the center of the circle.
*(r,c)
d

## Slide 50: Why it works
Filled Circle:
Outer points of circle have gradient
direction pointing to center.
Circular Ring:
Outer points gradient towards center.
Inner points gradient away from center.
The points in the away direction don’t
accumulate in one bin!

## Slide 51: Procedure to Accumulate Circles
Set accumulator array A to all zero.
Set point list array PTLIST to all NIL.
For each pixel (R,C) in the image {
For each possible value of D {
- compute gradient magnitude GMAG
- if GMAG > gradient_threshold {
. Compute THETA(R,C,D)
. R0 := R - D*sin(THETA)
. C0 := C + D*cos(THETA)
. increment A(R0,C0,D)
. update PTLIST(R0,C0,D) }}

## Slide 53: Finding lung nodules (Kimme & Ballard)

## Slide 54: Finale
Edge operators are based on estimating derivatives.
While first derivatives show approximately where the edges are, zero crossings of second derivatives were shown to be better.
Ignoring that entirely, Canny developed his own edge detector that everyone uses now.
After finding good edges, we have to group them into lines, circles, curves, etc. to use further.
The Hough transform for circles works well, but for lines the performance can be poor. The Burns operator or some tracking operators (old ORT pkg) work better.