## Slide 1
Manipulating and Understanding Images via Edges, Features and Alignment
Harpreet S Sawhney
Microsoft / Vision & Mixed Reality
May 7th and 12th , 2020

## Slide 2: (Dynamic) Images Afford Two Types of Inferences
Inferences on scene content without object identity
Frame-to-frame motions
Foreground/background and independent object motions
3D structure / 2-2.5D layers
…
Inferences on scene content involving object identity
  Object/event recognition
  Object/scene classification
  Object/scene fingerprinting
  Extended space-time tracking
  …

## Slide 3: A Bit of Historical Perspective : My Work
Analysis / Manipulation of scene content without object / scene identity
  Pixels In  Pixels Out
  Stabilization, Mosaicking, 3D Structure,…
Inferences on scene content involving scene /object / event identity
  Pixels In  Decisions / Labels Out
  Model-based object/event recognition
  Object/scene classification
  Object/scene fingerprinting
  Extended space-time tracking
  Multi-modal Video Analysis
Dynamic Images Afford Two Types of Inferences

## Slide 4: (Dynamic) Images Afford Two Types of Inferences
Inferences on scene content without object identity
  Frame-to-frame motions
  Foreground/background and independent object motions
  3D structure / 2-2.5D layers
  …
Inferences on scene content involving object identity
  Model-based object/event recognition
  Object/scene classification
  Object/scene fingerprinting
  Extended space-time tracking
  …

## Slide 5: Plan of Two Lectures : May 7th (and 12th )
Why and How of Edges in Images
Why Image / Video Alignment and Matching
A Swift Primer on Sum of Squares Optimization and Fitting
Short Range Matching with Patches
Image Transformations and Robust Fitting with RANSAC

## Slide 6: Plan of Two Lectures : May 12th
Long Range Matching
  Quasi-Invariant Feature Detectors and Descriptors: SIFT, HOG
Location and Image based Object Instance Retrieval
Learned Features through Metric Learning with CNNs
Long Range Matching and Localization : Contrast between Hand-crafted and Learned Features
Take Home Lessons

## Slide 7: What do edges tell us about the Physical World?

## Slide 8
Figure-Ground
3D Perception

## Slide 9: Why do we care about edges?
Extract information, recognize objects
Recover geometry and viewpoint
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)

## Slide 10
Notes: We perceive boundaries rather than edges. Edges are historically computational entities that are correlated with various types of boundaries.

## Slide 11: Edges have Physical / Geometric causes
Orientation Discontinuity

## Slide 12: Edges have Physical / Geometric causes
Surface Albedo Changes

## Slide 13: Edges have Physical / Geometric causes
Texture Change

## Slide 14: Edges have Physical / Geometric causes
Shadow Edge

## Slide 15: Edges have Physical / Geometric causes
Color Change

## Slide 16: Edges have Physical / Geometric causes
Noisy Edge

## Slide 18: Origin of Edges
Edges are caused by a variety of factors
depth discontinuity
surface color discontinuity
illumination discontinuity
surface normal discontinuity
Source: Steve Seitz

## Slide 19
Subjective Contours: 3D Perception / Perceptual Organization

## Slide 20
Complex Subjective “Contours”
High-Level meets Low-Level ?

## Slide 21: Early Work In Computer Vision: Interpretation of Line Drawings as 3D

## Slide 22: Machine Perception of 3D Solids

## Slide 23
“+” label represents a convex edge
“-” label represents a concave edge
or a represents an occluding convex edge
or a represents a limb

## Slide 24
We evolved to infer the World as 3D because you do not want to mistake a tiger in the bushes as a painting on the Wall!
Perceptual Organization makes sense the World as Figure-Ground / 3D Percepts
Perceptual Organization
Perceptual Organization (Lance’s view)
Perceptual organization is the process of deriving the topological component of a representation of visible and partially occluded surfaces.
The topological component is represented using labeled knot diagrams.
Labeled knot diagrams can be derived from images through a process of figural completion.

## Slide 25: Edges correspond to changes in image intensities
On a discrete pixel grid as above:

## Slide 26: Computing Edges via Derivatives on a Pixel Grid: 1D Case for Simplicity
x
0
2
1
-2
-1
-1
1
-1
1
0
Two Approximations:

## Slide 27: Computing Edges via Derivatives on a Pixel Grid: 1D Case for Simplicity
To compute derivatives of f(x) at x=0, let us use Taylor series expansion
First Approximation:
Second Approximation:
Good exercise to derive the second derivative approximation:
x
0
2
1
-2
-1
-1
1
-1
1
0
Two Approximations:

## Slide 28: Closeup of edges
via DerekHoiem

## Slide 29: Closeup of edges
via DerekHoiem

## Slide 30: Closeup of edges
via DerekHoiem

## Slide 31: Closeup of edges
via DerekHoiem

## Slide 32: Characterizing edges
An edge is a place of rapid change in the image intensity function
image
intensity function (along horizontal scanline)
first derivative
edges correspond to extrema of derivative
via DerekHoiem

## Slide 33: Intensity profile
Intensity
Gradient
via DerekHoiem

## Slide 34: With a little Gaussian noise
Gradient
via DerekHoiem

## Slide 35: Effects of noise
Consider a single row or column of the image
Plotting intensity as a function of position gives a signal
Where is the edge?
Source: S. Seitz
Notes: How to fix?

## Slide 36: Differentiating noisy signals : Frequencey Domain Intuition

## Slide 37: Solution: Smooth First
To find edges, look for peaks in
f
g
f * g
Source: S. Seitz

## Slide 38: Derivative theorem of convolution
Differentiation is convolution, and convolution is associative:
This saves us one operation:
Source: S. Seitz
f

## Slide 39
via DerekHoiem

## Slide 40
Derivative of Gaussian is a Matched Filter for a Step / Smooth Edge (Max response)
Laplacian is also a Matched Filter at appropriate scales for a bar detector (1D) and Blob detector (2D)
This property is effectively exploited by SIFT Detector
More on that later.
SMOOTHING
EXTREMA
ZERO-CROSSING
via DerekHoiem

## Slide 41: Sobel filter! Smooth & derivative
via JoeRedmon
Notes: Instead of using a fixed Gaussian kernel, compute the kernel as a function of sigma.

## Slide 42: 2D Gaussian is Separable…
Given an arbitrary sigma, 95% of the AUC for Gaussian is between -2*sigma and 2*sigma
99.7% of the AUC is between -3*sigma to 3*sigma
Choose one of these for your implementation
Separable kernels (M x M ) reduce the complexity of smoothing for an N x N image to O(N2M) instead of O(N2 M2 )
Separable kernel
• Factors into product of two 1D Gaussians
• Discrete example:
http://onlinestatbook.com/2/calculators/normal_dist.html

## Slide 43: Edges in 2D Domains : Images I(x, y)
Edges have an Orientation and a Magnitude
via SteveSeitz

## Slide 48: Seeing with Receptive Fields: From John Frisby
via JohnFrisby “Seeing”

## Slide 49: Seeing with Receptive Fields: From John Frisby
via JohnFrisby “Seeing”
Notes: Although individual cells are tuned to discrete orientations at 10 deg spacing the joint signature can distinguish between 90 and 92 degs.

## Slide 50: Edges Occur at Different Scales

## Slide 51: Edges Occur at Different Scales
This will be discussed in more details in
Wide Baseline Features and Matching (SIFT).

## Slide 52: Role of Edges ?
From the time when Edge Detection was considered essential to understanding and manipulating images:
To Modern Learning to Segment, Detect Boundaries, Objects and much more…
Object-Contextual Representations for Semantic Segmentation
Yuhui Yuan, Xilin Chen, Jingdong Wang
https://arxiv.org/abs/1909.11065v2

## Slide 53: Image Matching & Alignment

## Slide 54: Why Align Images?
Match to create Panoramas for Single Center of Projection Images

## Slide 55
Mercator projection of spherical mosaic

## Slide 56: Why Align Images?
Match to create Planar Mosaics

## Slide 57: Why Align Images?
“Build Rome in a Day”

## Slide 58: Why Align Images?
Image / Location / Object Retrieval from a Large Database
via DavidNister

## Slide 59: Matching & Alignment
Matching:
Find locations / spatial coordinates in images that correspond to the same location / direction in the World
via Feature Detectors and Feature Descriptors
Alignment:
  Use the matching locations to find Transformations for Camera Estimation and Warping
via Linear and Non-linear Optimization

## Slide 60: A Swift Primer on Optimization Methods for Linear and Non-Linear (Sum of Squares) Cost Functions

## Slide 61
If f(p) is quadratic:
Gradient:
Steepest Descent: But how much do we move along g?
=0
Rate of convergence governed by:
p0

## Slide 62: Observations
Gradient Descent “looks” at the cost function VERY LOCALLY.
r = 1 => Single step convergence
r >> 1 => Very slow convergence
Line search does not let the descent overshoot.
  Too expensive in Backprop for CNNs because of millions of parameters
  So learning rate used as a hyperparameter that is “globally” set and varied a bit
CAN WE DO BETTER?

## Slide 63: Quadratic Cost Functions
Model the 2nd order variation (CURVATURE) in addition to the Gradient
Convex second order cost functions have a unique global minimum
f(p) is convex quadratic: H is Positive Definite (Concave Upwards)
is a Global minimum : f(p) >= f()
By modeling the globally convex function we obtain minimum solution in a single step!

## Slide 64: Optimization of General Cost Functions
We can model local quadratic behavior and apply descent type methods to general cost functions
Only local minima can be found
For local descent to happen the function needs to be PD (positive definite)
Let us see why

## Slide 65: Optimization of General Cost Functions
At any point use quadratic approximation to define a descent direction:
For generality define a descent direction as:
=> For this to do descent > 0 (Positive Definite)
guarantees PD but is gradient descent that converges linearly.
has quadratic convergence but not guaranteed to be PD.

## Slide 66: Optimization of General Cost Functions
guarantees PD but is gradient descent that converges linearly.
has quadratic convergence but not guaranteed to be PD.
By melding both aspects:
>> 1 is Steepest Descent. = 0 is Second Order method such as Newton’s method.
Special case for Sum of Squares problems (like in Vision) called Levenberg-Marquardt method.
If descent possible use current otherwise scale up .
Close to the solution decrease towards zero to approximate second order descent.

## Slide 67: Special Common Case : Sum of Squares Cost Functions
is a vector of measurements corrupted by noise. X is the unknown.
Assuming independence of measurements , the negative log likelihoods of the measurements given X is:
=
To find the optimal X we take the derivative w.r.t. X and set it to zero:
= 0
Solvable in Closed form. For large systems iterative methods are used.

## Slide 68: Special Case : Least squares line fitting
Data: (x1, y1), …, (xn, yn)
Line equation: yi = m xi + b
Find (m, b) to minimize
(xi, yi)
y=mx+b
Modified from S. Lazebnik
Notes: X is assumed noise free. Y is the measurement.

## Slide 69: Special Case : Least squares line fitting
Data: (x1, y1), …, (xn, yn)
Line equation: yi = m xi + b
Find (m, b) to minimize
(xi, yi)
y=mx+b
Modified from S. Lazebnik
Caveat:
Errors are in y’s and not in x’s.
Say x is time for example.

## Slide 70: Line Fitting with Realistic Error Model
Typically errors are in all the measured quantities: x and y here
A proper error measure to optimize is normal distance of measured points to a best fit line
Line:
2 =
where is the centroid of all the points
Non-trivial solution is the Null space vector of
Eigenvector with the smaller (~ 0) eigenvalue
d
S

## Slide 71: Total least squares
Find (a, b, c) to minimize the sum of squared perpendicular distances
(xi, yi)
ax+by+c=0
Unit normal: N=(a, b)
Solution is eigenvector corresponding to smallest eigenvalue of ATA
See details on Raleigh Quotient: http://en.wikipedia.org/wiki/Rayleigh_quotient
Slide modified from S. Lazebnik
To be Modified

## Slide 72: Special Common Case : Sum of Squares Cost Functions
is a vector of measurements corrupted by noise. X is the unknown.
Assuming independence of measurements , the negative log likelihoods of the measurements given X is:
=
To find the optimal X we take the derivative w.r.t. X and set it to zero:
= 0
Solvable in Closed form. For large systems iterative methods are used.

## Slide 73: Panorama Homework
Finding keypoints in an image
  // Calculate corners and descriptors
  vector<Descriptor> ad = harris_corner_detector(a, sigma, thresh, window, nms, corner_method);
  vector<Descriptor> bd = harris_corner_detector(b, sigma, thresh, window, nms, corner_method);
Describing those key points,
Matching them to those points in another image,
  vector<Match> m = match_descriptors(ad, bd);
Computing the transform from one image to the other, and
  // Run RANSAC to find the homography
  Matrix Hba = RANSAC(m, inlier_thresh, iters, cutoff);
Stitching them
  return combine_images(a, b, Hba, acoeff);

## Slide 74: Panorama Homework (Details)
Harris corner detection
  Calculate image derivatives Ix and Iy.
  Calculate measures IxIx, IyIy, and IxIy.
  Calculate structure matrix components as weighted sum of nearby measures.
  Calculate Harris "cornerness" as estimate of 2nd eigenvalue: det(S)/tr(S)
  Alternatively (Optionally) find the exact 2nd eigenvalue
  Run non-max suppression on response map
  Compute the structure matrix
    Fill in `Image structure_matrix(const Image& im2, float sigma)` in `harris_image.cpp`.
    This will perform the first 3 steps of the algorithm: calculating derivatives, the corresponding measures,
    and the weighted sum of nearby derivative information.
    This weighted sum can be easily computed with a Gaussian blur.
    For gradients use the Sobel filters (slightly smoothed versions of the regular -101 filter).
    It is true that we don't have to do that but please for this exercise do it, so it can match the output provided.

## Slide 75: Why is Fitting and Features Important for Image Matching?
Find 2D / 3D Transformations
Create Panoramas
Fit to what : Coordinates defined by Features
Features have two Components:
Feature Detector
Feature Descriptor

## Slide 76: Two Types of Matching Problems
SHORT BASELINE
Limited change in viewpoint & illumination
Typically Videos / Image Sequences
Very similar looking images
WIDE BASELINE
Larger changes in viewpoint & illumination
Jumble of frames
“Distant” in time:
  Retrieve Locations, Objects, “THINGS”, Images, …
Video Example

## Slide 77: Two Types of Matching Problems
SHORT BASELINE
Limited change in viewpoint & illumination
Typically Videos / Image Sequences
Very similar looking images
WIDE BASELINE
Larger changes in viewpoint & illumination
Jumble of frames
“Distant” in time:
  Retrieve Locations, Objects, “THINGS”, Images, …
Video Example

## Slide 78: Features
Detector / Keypoints: Discrete “distinctive” locations in the image.
Descriptors: Raw / Filtered Representations of Patches around the Keypoints
Intensity
Patch
Filtered
Patch
Quasi-invariant Feature
SIFT
Learned
Detectors
&
Descriptors

## Slide 79: Where would you define good features?
via JoeRedmon

## Slide 80: How can we find unique patches?
Sky: bad
  Very little variation
  Could match any other sky
via JoeRedmon

## Slide 81: How can we find unique patches?
Sky: bad
  Very little variation
  Could match any other sky
Edge: ok
  Variation in one direction
  Could match other patches along same edge

## Slide 82: How can we find unique patches?
Sky: bad
  Very little variation
  Could match any other sky
Edge: ok
  Variation in one direction
  Could match other patches along same edge
Corners: good!
  Only one alignment matches
via JoeRedmon

## Slide 83: Making Panoramas
Say we are stitching a panorama
Want patches in image to match to other image
Hopefully only match one spot
via JoeRedmon

## Slide 84: How close are two patches?
Sum squared difference
Images I, J
Σx,y (I(x,y) - J(x,y))2
via JoeRedmon

## Slide 85: How can we find unique patches?
Want a patch that is unique in the image
Can calculate distance between patch and every other patch, lot of computation
Instead, we could think about auto-correlation:
  How well does image match shifted version of itself?
ΣdΣx,y (I(x,y) - I(x+dx,y+dy))2
Measure of self-difference (how am I not myself?)
via JoeRedmon

## Slide 86: Self-difference
Sky: low everywhere
via JoeRedmon

## Slide 87: Self-difference
Edge: low along edge
via JoeRedmon

## Slide 88: Self-difference
Corner: mostly high
via JoeRedmon

## Slide 89: Self-difference
Sky: low everywhere
Edge: low along edge
Corner: mostly high
via JoeRedmon

## Slide 90: Characterize Self-Difference to Compute Keypoints
Compute an Auto-SSD or Auto-Correlation Surface locally at each point
Measures the sum-of-square differences as a function of
With first order approximation of image patch locally, we get:
Best Practice: Compute Smoothed Gradients with derivatives of Gaussian
Eigen-structure of A captures the notion of flat or peaky self-similarity:
λ1 and λ2 are eigenvalues
  λ1 and λ2 both small: no gradient (flat
  λ1 >> λ2: gradient in one direction (edge)
  λ1 and λ2 similar: multiple gradient directions, corner
Structure Matrix

## Slide 91: Harris Detector [Harris88]
“Second moment matrix” / Structure Matrix
Intuition: Search for local neighborhoods where the image content has two main directions (eigenvectors).
Weighted Summation can be implemented as
Gaussian Smoothing of Squared Gradient Images
via DerekHoeim

## Slide 92: Harris Detector [Harris88]
Second moment matrix
1. Image derivatives
2. Square of derivatives
3. Gaussian filter g(sI)
Ix
Iy
Ix2
Iy2
IxIy
g(Ix2)
g(Iy2)
g(IxIy)
4. Cornerness function – both eigenvalues are strong
har
5. Non-maxima suppression
(optionally, blur first)
via DerekHoeim

## Slide 93: Harris Detector: Mathematics
(k :empirical constant, k = 0.04-0.06)
Nice brief derivation on wikipedia
Want large eigenvalues, and small ratio
We know
Leads to
-

## Slide 94: Explanation of Harris Criterion
From Grauman and Leibe
via DerekHoeim

## Slide 95: Non-Maximal Suppression (NMS)
Harris corner responses beyond a certain threshold typically create bunched up corner pixels
Too much data to handle
Suppress responses other than MAX within an NxN neighborhood everywhere. And choose top K responses.
Alternatively use Adaptive NMS.
  For each response compute the min distance to a local MAX response
  Choose the Top K points with the largest radii
via MIT

## Slide 96: Harris Detector – Responses [Harris88]
Effect: A very precise corner detector.
via DerekHoeim

## Slide 97: Harris Detector - Responses [Harris88]
via DerekHoeim

## Slide 98
via JoeRedmon

## Slide 99
via JoeRedmon

## Slide 100: Ok, we found corners, now what?
Need to match image patches to each other
Need to figure out transform between images
via JoeRedmon

## Slide 101: Ok, we found corners, now what?
Need to match image patches to each other
  What is a patch? How do we look for matches? Pixels?
Need to figure out transform between images
  How can we transform images?
  How do we solve for this transformation given matches?
via JoeRedmon

## Slide 102: Matching patches: descriptors!
We want a way to represent an image patch
Can be very simple, just pixels!
Finding matching patch is easy, distance metric:
  Σx,y (I(x,y) - J(x,y))2
  What problems are there with just using pixels?
via JoeRedmon

## Slide 103: Matching patches: descriptors!
We want a way to represent an image patch
Can be very simple, just pixels!
Finding matching patch is easy, distance metric:
  Σx,y (I(x,y) - J(x,y))2
  What problems are there with just using pixels?
via JoeRedmon

## Slide 104: Short Baseline: Matching patches (descriptors!)
We want a way to represent an image patch
Can be very simple, just pixels!
Finding matching patch is easy, L2 distance metric:
  Σx,y (I(x,y) - J(x,y))2
  What problems are there with just using pixels?
Descriptors can be more complex
  Gradient information
  How much context?
  Edges, etc. we’ll talk more about descriptors later!
via JoeRedmon

## Slide 105: Match Measures for matching Descriptors / Patches
L2 Norm
Sensitive to outliers
Sensitive to brightness / contrast changes
L1 Norm
Less Sensitive to outliers
Sensitive to brightness / contrast changes
Inverse Normalized Correlation
Sensitive to outliers
Invariant to Local offset and scale changes in intensity/color

## Slide 106: Match Measures for matching Descriptors / Patches
L2 Norm
Sensitive to outliers
Sensitive to brightness / contrast changes
L1 Norm
Less Sensitive to outliers
Sensitive to brightness / contrast changes
Inverse Normalized Correlation
Sensitive to outliers
Invariant to Local offset and scale changes in intensity/color

## Slide 107: Matching patches: descriptors!
Already have our patches that are likely “unique”-ish
Loop over good patches in one image
  Find best match in other image
Find mutually best matches:
A = BestMatch(B) & B = BestMatch(A)
via JoeRedmon

## Slide 108: MOSAICS IN ART …combine individual chips to create a big picture...
Part of the Byzantine mosaic floor that has been preserved in the
Church of Multiplication in Tabkha (near the Sea of Galilee).
www.rtlsoft.com/mmmosaic

## Slide 109: Image Transformations : Induced by Camera Motion
3D Rotations : Pan / Tilt
Image Displacment is Independent of Depth

## Slide 110: Image Transformations : Induced by Camera Motion
3D Rotations : Pan / Tilt

## Slide 111: Image Transformations : Induced by Camera Motion
3D Rotations : Pan / Tilt

## Slide 112: Basic Concept : Planar Mosaic Construction
Align Pairwise: 1:2, 2:3, 3:4, ...
Select a Reference Frame
Align all Images to the Reference Frame
Combine into a Single Mosaic
1
2
3
4
Virtual Camera (Pan)
Image Surface - Plane
Projection - Perspective

## Slide 113: Image Transformation : Rotations What is the mapping from image rays to the mosaic coordinates ?
Images
COP
Rotations/Homographies
Plane Projective Transformations

## Slide 114: Image Transformations : Induced by Camera Motion
3D Translations : Image Displacement is a function of Depth (3D Parallax)
x
x
x
x

## Slide 115: Image Transformations : Induced by Camera Motion
3D Translations : Image Displacement is a function of Depth (3D Parallax)
x
x
x
x

## Slide 116: Image Transformation : Translations

## Slide 117: Image Transformation : Special Cases
Planar Scene (e.g. A Whiteboard)
Plane Equation:
3D Camera Motion:
Imaging a Plane Under Motion leads to:
Scene at a Distance (e.g. Rainier)
 Image Displacement due to T is 0
Same as the case of Rotational Motion
Image Displacements well approximated by:

## Slide 118: Closer Look at Homography
are called Homogeneous coordinates.
a 3x3 matrix relates view rays in images.
View rays are represented as homogeneous coordinates. upto an arbitrary constant .
Observed 2D image coordinates are related via:
Transformation is upto an arbitrary scale

## Slide 119: Approximations of Homography
via JoeRedmon

## Slide 120: Approximations of Homography
Translation: Preserves Orientations, Angles, Lengths, Areas
Euclidean: Preserves Angles, Lengths, Areas
Similarity: s * Preserves Angles
Affine: Preserves Parallelism
Homography: : Preserves Cross-Ratios

## Slide 121: Fitting Transformations to Noisy Matches
Already have our patches that are likely “unique”-ish
Loop over good patches in one image
  Find best match in other image
Find mutually best matches:
A = BestMatch(B) & B = BestMatch(A)
via JoeRedmon

## Slide 122
such that:
Model parameters
RANSAC
Fischler & Bolles in ‘81.
(RANdom SAmple Consensus) :
Learning technique to estimate
parameters of a model by random
sampling of observed data
Source: Savarese
Notes: Let me give you an intuition of what is going on. Suppose we have the standard line fitting problem in presence of outliers.
We can formulate this problem as follows: want to find the best partition of points in inlier set and outlier set such that…
The objective consists of adjusting the parameters of a model function so as to best fit a data set.
"best" is defined by a function f that needs to be minimized.
Such that the best parameter of fitting the line give rise to a residual error lower that delta
as when the sum, S, of squared residuals

## Slide 123
RANSAC
Algorithm:
Sample (randomly) the number of points required to fit the model
Solve for model parameters using samples
Score by the fraction of inliers within a preset threshold of the model
Repeat 1-3 until the best model is found with high confidence
Fischler & Bolles in ‘81.
(RANdom SAmple Consensus) :
Notes: Let me give you an intuition of what is going on. Suppose we have the standard line fitting problem in presence of outliers.
We can formulate this problem as follows: want to find the best partition of points in inlier set and outlier set such that…
The objective consists of adjusting the parameters of a model function so as to best fit a data set.
"best" is defined by a function f that needs to be minimized.
Such that the best parameter of fitting the line give rise to a residual error lower that delta
as when the sum, S, of squared residuals

## Slide 124
RANSAC
Algorithm:
Sample (randomly) the number of points required to fit the model (#=2)
Solve for model parameters using samples
Score by the fraction of inliers within a preset threshold of the model
Repeat 1-3 until the best model is found with high confidence
Illustration by Savarese
Line fitting example
Notes: Let me give you an intuition of what is going on. Suppose we have the standard line fitting problem in presence of outliers.
We can formulate this problem as follows: want to find the best partition of points in inlier set and outlier set such that…
The objective consists of adjusting the parameters of a model function so as to best fit a data set.
"best" is defined by a function f that needs to be minimized.
Such that the best parameter of fitting the line give rise to a residual error lower that delta
as when the sum, S, of squared residuals

## Slide 125
RANSAC
Algorithm:
Sample (randomly) the number of points required to fit the model (#=2)
Solve for model parameters using samples
Score by the fraction of inliers within a preset threshold of the model
Repeat 1-3 until the best model is found with high confidence
Line fitting example
Notes: Let me give you an intuition of what is going on. Suppose we have the standard line fitting problem in presence of outliers.
We can formulate this problem as follows: want to find the best partition of points in inlier set and outlier set such that…
The objective consists of adjusting the parameters of a model function so as to best fit a data set.
"best" is defined by a function f that needs to be minimized.
Such that the best parameter of fitting the line give rise to a residual error lower that delta
as when the sum, S, of squared residuals

## Slide 126
RANSAC
Algorithm:
Sample (randomly) the number of points required to fit the model (#=2)
Solve for model parameters using samples
Score by the fraction of inliers within a preset threshold of the model
Repeat 1-3 until the best model is found with high confidence
Line fitting example
Notes: Let me give you an intuition of what is going on. Suppose we have the standard line fitting problem in presence of outliers.
We can formulate this problem as follows: want to find the best partition of points in inlier set and outlier set such that…
The objective consists of adjusting the parameters of a model function so as to best fit a data set.
"best" is defined by a function f that needs to be minimized.
Such that the best parameter of fitting the line give rise to a residual error lower that delta
as when the sum, S, of squared residuals

## Slide 127
RANSAC
Algorithm:
Sample (randomly) the number of points required to fit the model (#=2)
Solve for model parameters using samples
Score by the fraction of inliers within a preset threshold of the model
Repeat 1-3 until the best model is found with high confidence
Notes: Let me give you an intuition of what is going on. Suppose we have the standard line fitting problem in presence of outliers.
We can formulate this problem as follows: want to find the best partition of points in inlier set and outlier set such that…
The objective consists of adjusting the parameters of a model function so as to best fit a data set.
"best" is defined by a function f that needs to be minimized.
Such that the best parameter of fitting the line give rise to a residual error lower that delta
as when the sum, S, of squared residuals

## Slide 128: How to choose parameters?
Number of samples N
  Choose N so that, with probability p, at least one random sample is free from outliers (e.g. p=0.99) (outlier ratio: e )
Number of sampled points s
  Minimum number needed to fit the model
Distance threshold 
  Choose  so that a good point with noise is likely (e.g., prob=0.95) within threshold
  Zero-mean Gaussian noise with std. dev. σ: t2=3.84σ2
 | proportion of outliers e |  |  |  |  |  | 
s | 5% | 10% | 20% | 25% | 30% | 40% | 50%
2 | 2 | 3 | 5 | 6 | 7 | 11 | 17
3 | 3 | 4 | 7 | 9 | 11 | 19 | 35
4 | 3 | 5 | 9 | 13 | 17 | 34 | 72
5 | 4 | 6 | 12 | 17 | 26 | 57 | 146
6 | 4 | 7 | 16 | 24 | 37 | 97 | 293
7 | 4 | 8 | 20 | 33 | 54 | 163 | 588
8 | 5 | 9 | 26 | 44 | 78 | 272 | 1177
modified from M. Pollefeys

## Slide 129: RANSAC
Good
Robust to outliers
Applicable for larger number of objective function parameters than Hough transform
Optimization parameters are easier to choose than Hough transform
Bad
Computational time grows quickly with fraction of outliers and number of parameters
Not as good for getting multiple fits (though one solution is to remove inliers after each fit and repeat)
Common applications
Computing a homography (e.g., image stitching)
Estimating fundamental matrix (relating two views)

## Slide 130: Solving for Homography with Correspondences: Linear Least Squares
Given corresponding matches in two images , find the best fit H
Convert the rational equations above into linear algebraic form:
For each correspondence:
Image Displacement

## Slide 131: Solving for Homography with Correspondences: Linear Least Squares
Given corresponding matches in two images , find the best fit H
Convert the rational equations above into linear algebraic form:
For each correspondence:
Image Displacement

## Slide 132: Solving for Homography with Correspondences: Linear Least Squares

Setting dervivative w.r.t. h to zero gives us:
 
Sub-optimal since Algebraic error does not account for measurement errors in keypoints and matches
Can normalize the error with Jacobian (see Book)

## Slide 133: Optimal Solution for Homography : Non-Linear Least Squares with Levenberg-Marquardt
(Non-linear in h)
: Computed at a current estimate h
Setting derivative w.r.t. to zero gives us:
Gradient Descent = 0 Gauss-Newton
Far from the local optimal solution, keep high so that descent is guaranteed.
Closer to the minimum = 0 to get faster convergence

## Slide 134: In practice:
via JoeRedmon

## Slide 135: In practice:
via JoeRedmon

## Slide 136: In practice:
via JoeRedmon

## Slide 137
via JoeRedmon

## Slide 138: In practice:
via JoeRedmon

## Slide 139: In practice:
via JoeRedmon

## Slide 140: What’s happening?
via JoeRedmon

## Slide 141: Very bad for big panoramas!
via JoeRedmon

## Slide 142: Fails :-(
via JoeRedmon

## Slide 143: How do we fix it? Cylinders!
via JoeRedmon

## Slide 144: Cylindrical Projection
Mapping planar image to Cylindrical Coordinates
via CMU

## Slide 145: Cylindrical Re-Projection
Developing / Reprojecting a Cylinder onto a plane to create a Planar Viewable Panorama
Try different focal lengths or use the focal length of the camera
via CMU

## Slide 146: Cylindrical Reprojection: Dependence on f
Fill the panorama image to the max or use f
via CMU

## Slide 147
UNBLENDED MOSAIC

## Slide 148: Image Merging withLaplacian Pyramids
Image 1
Image 2
1
2
Combined Seamless Image

## Slide 149
VORONOI TESSELATIONS W/ L1 NORM

## Slide 150
BLENDED MOSAIC

## Slide 151
UNBLENDED MOSAIC

## Slide 152: How does iPhone panoramic stitching work?
Capture images at 30 fps
Stitch the central 1/8 of a selection of images
  Select which images to stitch using the accelerometer and frame-to-frame matching
  Faster and avoids radial distortion that often occurs towards corners of images
Alignment
  Initially, perform cross-correlation of small patches aided by accelerometer to find good regions for matching
  Register by matching points (KLT tracking or RANSAC with FAST (similar to SIFT) points) or correlational matching
Blending
  Linear (or similar) blending, using a face detector to avoid blurring face regions and choose good face shots (not blinking, etc)
http://www.patentlyapple.com/patently-apple/2012/11/apples-cool-iphone-5-panorama-app-revealed-in-5-patents.html
via DerekHoeim

## Slide 153
1D vs. 2D SCANNING
1D : The topology of frames is a ribbon or a string.
Frames overlap only with their temporal neighbors.
2D : The topology of frames is a 2D graph
Frames overlap with neighbors on many
sides
(A 300x332 mosaic captured by mosaicing a 1D sequence of 6 frames)

## Slide 154
1D vs. 2D SCANNING
The 1D scan scaled by 2 to 600x692
A 2D scanned mosaic of size 600x692

## Slide 155
FRAME-TO-MOSAIC VS. LOCAL-TO-GLOBAL ALIGNMENT
Uses limited 2D spatial context
Causal commitment to parameters
cannot be corrected
Demands large overlap between
frames
Uses all the available frame-to-frame
constraints
Global solution is optimal subject to
local frame-to-frame constraints
Works even with small overlap between
frames

## Slide 156
LOCAL TO GLOBAL MOSAIC ALGORITHM
Topology
Determination
Temporal
Coarse
Registration
Local
Coarse&Fine
Registration
Global
Consistency
Color
Matching/
Blending
Mosaic
Representation
Images
or
Video
Panoramic Visualization
Virtual Reality
Other Applications

## Slide 157
SPECIFIC EXAMPLES : 2. SPHERICAL MOSAICS
Frame to mosaic transformation model:
Local Registration
  Coarse 2D translation & fine 2D projective alignment
Parameter Initialization
  Compute F and R’s from the 2D projective matrices
Topology :
  Initial graph topology computed with the 2D R & T estimates on a plane
  Subsequently the topology defined on a sphere
  Iterative refinement using arcs based on alignment with F and R’s
Global Alignment

## Slide 158
SPHERICAL MOSAICS
Video
Captures almost the complete sphere
with 380 frames

## Slide 159
SPHERICAL TOPOLOGY EVOLUTION

## Slide 160
SPHERICAL MOSAIC
Sarnoff Library

## Slide 161
Mercator projection of spherical mosaic

## Slide 162: MultiView Panoramas
0o
180o
360o
Regular Panorama
Left-Eye
Panorama
Right-Eye
Panorama

## Slide 163: Stereo Panorama from Video
Stereo viewing with Red/Blue Glasses

## Slide 164: Viewing Panoramic Stereo Printed Cylindrical Surfaces
Print panorama on a cylinder
No computation needed!!!

## Slide 165: DYNAMIC MOSAICS
Video Stream with
deleted moving object
Original Video
Dynamic Mosaic Video

## Slide 166: SYNOPISIS MOSAICS