## Slide 1: Morphometric Analysis of Biomedical Images
Sara Rolfe
10/9/17

## Slide 2: Morphometric Analysis of Biomedical Images
Object surface contours
Framework to quantify, compare, and visualize image differences
Validation
on multiple datasets
Compact representation
of feature differences
Image difference features
Framework for Morphometric Shape Analysis

## Slide 3: Quantification and Description of Morphological Differences
Two developmental stages of a chick embryo
Left and right mouse hemi-mandibles
Trend towards increased use of biomedical imaging in craniofacial medicine
Increased need for tools enabling assessment of biomedical images.
  Identify optimal treatment strategies
  Quantify genetic and epigenetic impact on phenotypes.
Notes: craniofacial developmental abnormalities to understand gene-environment interactions that contribute to disease susceptibility and severity.
I developed new computational tools for biomedical image analysis to assist in identifying these causative factors.

## Slide 4: Challenges in Quantifying 3D Shape Change
Traditional methods rely on landmark points
  Tedious and subject to variability
  Require locations where landmarks can be reliably placed
  Spatially sparse
Embryonic growth
Alternative analysis technique is needed
Notes: To correlate growth abnormalities observed back to genetic and environmental factors, it is crucial to have detailed information about the shape changes, both normal and abnormal, during development.
Typical morphometric analysis relies on the precise identification of landmarks on images of the specimens which are easily repeatable. Landmarks typically placed at the junctures between identifiable structures. The embryos have few of these landmarks.
Due to these constraints and the progress that is being made in the quality and availability of high resolution 3D scan data, alternative techniques are needed that are capable of more descriptive analysis of shape change.

## Slide 5: High Resolution 3D Scan Data
Chick embryo
2D image slices

## Slide 6: Problematic Scan Data
High quality image
Low quality image
Notes: These images show one axial slice from two different scans, one high and one low quality. Your eye can probably follow a smooth contour around the edge of the chick embryo, distinguishing background from the foreground. However, this is not a simple task to automate.

## Slide 7: Problematic Scan Data
High quality image
Low quality image
Notes: These images show one axial slice from two different scans, one high and one low quality. Your eye can probably follow a smooth contour around the edge of the chick embryo, distinguishing background from the foreground. However, this is not a simple task to automate.

## Slide 8: Problematic Scan Data
High quality image
Low quality image
Notes: These images show one axial slice from two different CT scans, one high and one low quality. Your eye can probably follow a smooth contour around the edge of the chick embryo, distinguishing background from the foreground. However, this is not a simple task to automate.

## Slide 9: Problematic Scan Data
High quality image
Low quality image
Notes: These images show one axial slice from two different CT scans, one high and one low quality. Your eye can probably follow a smooth contour around the edge of the chick embryo, distinguishing background from the foreground. However, this is not a simple task to automate.

## Slide 10: Preprocessing: 3D Surface Generation
Surface contour of embryo head
3D scan of embryo head
Surface Extraction
Notes: Here you can see the three dimensional surface that is generated from the contours. In the following slides, the chick embryo images will be shown as 3D contours, such as the image on the right
Point out anatomical structure

## Slide 11: Geodesic Active Contours
Snakes: Active contour models, Kass, M. and Witkin, A. and Terzopoulos, D.
Method for detecting image boundaries
Start with contour approximating image boundary
Initial contour evolved over time according to “forces” calculated from image

## Slide 12: Steps for Geodesic Active Contour Algorithm
Model the shape with an estimated surface
Define energy function for surface as:
  E = Internal energy (curvature) + external energy (image edges)
Derive curve to minimize energy
Propagate curve using level set to attain minimum energy

## Slide 13: Geodesic Active Contour Implementation
Input Image
Image Level Set
Image Surface Estimate
Active Contour Filter
Output Surface

## Slide 14: Geodesic Active Contour Implementation
Confidence Connected Filter
Fast Marching Filter
Input Image
Otsu Threshold Noise Filter
Image Level Set
Gradient Magnitude Filter
Sigmoid Filter
Smoothing Filter
Edge Image
Active Contour Filter
Output Surface
Notes: Otsu threshold noise filter classifies foreground and background in the image and sets background to predefined level to reduce low level noise.
Confidence connected image filter then segments image into foreground and background using the mean and st dev
Fast marching filter creates a level set based on distance from the edges in the segmented image
Sigmoid filter remaps the values from the gradient magnitude filter to intensify differences between high and low gradient values.

## Slide 15: 2D Example

## Slide 16: 3D Surface Generation
Notes: Here you can see the three dimensional surface that is generated from the contours. In the following slides, the chick embryo images will be shown as 3D contours, such as the image on the right
Point out anatomical structure

## Slide 17: Deformable Registration
Dense field of vectors describes transformation at each point
Essentially provides continuous landmark data
Overlay of two objects
Deformation Vectors
Notes: Difference between two images can be expressed as a vector field transforming one image to the other

## Slide 18: Reducing Data Dimensionality
High resolution images can have over a million surface points
Need to reduce this number to track meaningful differences
Displaying 500,000 vectors

## Slide 19: Overview of Base Methodology
Low-level feature extraction
Mid-level feature extraction
Image 2
Image 1
Group similar features
Compact
Feature Description
Deformable Registration
Notes: Overview of the pipeline we have developed, will walk briefly through each step.

## Slide 20: Overview of Base Methodology
Surface normal angle
Reference vector angle
  Magnitude: Vector length
  Normal angle: Cosine distance from normal angle
  Reference vector angle: Cosine distance from reference vector
Low-Level Features
Low-level feature extraction
Mid-level feature extraction
Image 2
Image 1
Group similar features
ROIs
Deformable Registration
Notes: In this slide I’ve zoomed in on the low-level feature extraction.

## Slide 21: Spatiograms for Identifying Regions
Chart: Histogram of Feature Values
| Bin 1 | Bin 2 | Bin 3 | Bin 4 | Bin 5
Series 1 | 0.03 | 0.1 | 0.5 | 0.27 | 0.1
Heat Map of Feature Values
Bins contain Gaussian distributions describing spatial position of values
…
Bin spatial distributions
Notes: To generate a spatiogram from a feature difference image like the one seen here, the values are first partitioned into histogram bins, as is typically done in a histogram.
However, the spatial position of the points in each bin is recorded.
The spatial distribution of the points in each bin is later modeled using a mixture of Gaussian distributions.
Each bin is then characterized by the number of values in the bin, a number of Gaussian distributions, and the mean and variance of each Gaussian in the bin.

## Slide 22: Calculating the Spatiogram Distance Metric
Based on the Bhattacharya coefficient: measures overlap between statistical samples
Spatiograms represented as histograms with an added dimension
B = number of bins,
= value of bin b
= spatial weighting term expressing similarity of distributions
Notes: The Bhattacharya coefficient is modified to include a spatial weighting term to address the similarity of the Gaussian distributions in corresponding bins.

## Slide 23: Chick Embryo Developmental Sequence
Developmental Growth Sequence
  16 specimens
  5 developmental stages
HH 19.5
HH 24
HH 24.5
HH 25
HH 26
Notes: The first data set we used to validate our methods is a set of 16 normal chick embryos from 5 developmental stage groups.
This slide shows an example from each age group.
Some changes are obvious, others are subtle.
There is also variation within groups that complicates the dataset.

## Slide 24: Application to Developmental Sequence
Notes: These retrieval experiments help validate the methods that we’re using
They could be used to help determine the developmental stage group of an individual specimen.
But the goal is to use them to examine differences that are not previously known, such as differences due to genetic manipulation or variance within groups.
This slide shows the feature heat maps from a template image that is warped to a developmental sequence of images.
Progressive changes can be seen in the sequence, indicating that this can be used to explore variation both within and across developmental stage groups.

## Slide 25: Retrieval of Similar Growth Trajectories
Query feature heat maps
Heat maps of top 3 ranked results
Magnitude
Normal Angle
Notes: To verify our methods, we used the fact that the comparison between two given stages should be most similar to other comparison between those same two stages.
We did similarity retrieval by using the features from one image comparison as a query, and ranking the similarity of other image comparisons in the database
Most similar image comparisons should be returned.
In the example in this slide, the three image comparisons returned are visually similar to the query, and do each represent comparisons between the same two stages as the query.

## Slide 26: Similarity Scores: Growth Trajectory
Average Score: 0.049
Close to the ideal score of 0
 | HH 24 | HH 24.5 | HH 25 | HH 26
HH 19.5 | 0.087 | 0.018 | 0.156 | 0.020
HH 24 | X | 0.017 | 0.021 | 0.045
HH 24.5 | 0.044 | X | 0.008 | 0.069
HH 25 | 0.007 | 0.100 | X | 0.072
HH 26 | 0.030 | 0.067 | 0.045 | X
Developmental Stage
Template
Notes: The average retrieval scores for the transitions between each developmental stage group were very low, indicating successful retrievals
As a rule of thumb scores of 0.1 and under are considered very good.

## Slide 27: Morphological Shape Change: Characterizing Asymmetry
(ii) (iv)
(iii) (v)
(i)
Normal Reference Image
Angle Heat Map
Zoom of Facial Region
Normal Image
Cleft Image

## Slide 28: Assessing Mouse Mandible Symmetry
Low-level feature extraction
Mid-level feature extraction
Image 2
Image 1
Group similar features
ROIs
Deformable Registration
Asymmetry Score
Notes: Overview of the pipeline we have developed, will walk briefly through each step.

## Slide 29: Assessing Mouse Mandible Symmetry
Tool for characterizing and quantifying the asymmetry in bilaterally paired structures.
Applied it to the two sides of the mandible of the mouse.
Asymmetry scores compared to human expert
our
score = height
blue = normal
orange = abnormal
Correlation Coefficient = .92
Rolfe, S. M., Camci, E. D., Mercan, E., Shapiro, L. G., & Cox, T. C. "A New Tool for Quantifying and Characterizing Asymmetry in Bilaterally Paired Structures.“ IEEE EMBS ‘13 Jul 2013.

## Slide 30: Retrieval of Specimen with Similar Morphological Shape Differences
(ii) (iv)
(iii) (v)
(i)
Normal Reference Image
Angle Heat Map
Zoom of Facial Region
Normal Image
Cleft Image
(i) Query Image (ii) First Result (iii) Second Result
Magnitude Heat Map
Left/Right Overlay
Correlation between distance from most asymmetric and expert asymmetry ranking = 0.91
Magnitude Sample Query
Rolfe, S. M., Camci, E. D., Mercan, E., Shapiro, L. G., & Cox, T. C. "A New Tool for Quantifying and Characterizing Asymmetry in Bilaterally Paired Structures.“ IEEE EMBS ‘13 Jul 2013.

## Slide 31: Morphological Shape Change: Additional Applications
Magnitude Heat Maps – Mouse Skull
Wild Type to Wild Type
Wild Type to Mutant
Notes: In the examples that we ran here we were able to differentiate between comparisons of two wild types and mutants to wild types.
Indicating that this framework could provide shape information for these applications.

## Slide 32: Questions?
Object surface contours
Framework to quantify, compare, and visualize image differences
Validation
on multiple datasets
Compact representation
of feature differences
Image difference features
Framework for Morphometric Shape Analysis