## Slide 2: Direct Neural Sensory Feedback and Control of a Prosthetic Arm

## Slide 3: Introduction
Modern artificial limbs by amputees may be enhanced with appropriate, graded, distally referred sensations
  Touch
  Joint movement

## Slide 4: Problem
Different sensory feedback systems tried do no provide discrete and natural sensations.
 Users have to translated unrelated motion into intended one.

## Slide 5: Possible Solutions to Explore
Provide direct neural interface with nerve fibers
  In peripheral nerve stumps
  Allows feedback provided through sensory pathways associated with missing parts of arm
  Allows control signals derived from neural activity generated by amputee

## Slide 6: Study Purposes
Demonstrate sensory feedback about
  Joint position
  Grip force
  From artificial arm
  Through stimulation of peripheral nerves

## Slide 7: Methods
Sensory input
Motor output

## Slide 8: Methods
Electrodes
  LIFEs
    Another to saddle connector, adhered to skin surrounding percutaneous electrodes exited arm
    Connector used to interface outside circuitry:
      Recording hardware
      Stimulation hardware

## Slide 9: Methods
Subject training
  With
    One or more electrodes providing sensory input
    Output from motor control channels fed to loudspeaker
  Instructed to attempt a missing limb movement while listening to nerve activity over loudspeaker
    Ex. finger flexion
  Recorded signals fed to DAC to computer to quantify neural activity associated with movement

## Slide 10: Methods

## Slide 11: Methods
Subject training (cont.)
  Subject asked to control cursor position on computer screen by modulating motor activity
    Cursor position linearly related to level of motor activity
      Minimal output: left end of screen
      Maximal output: right end of screen
    Goal: place cursor and make it stay within random stationary target for specified period of time
    Subject scored on percentage of time of success in a block of trials
    Task difficulty increased with improved performance
      Target size change
      Time constraint change

## Slide 12: Methods
Nerve-arm interface
  Force sensor in thumb of hand
  Position sensor in elbow of prosthesis
    Both to provide sensory feedback
    Input mapped logarithmically to stimulus frequency to selected stimulating electrode
      Tactile sensation for force
      Proprioception for position
  Actuators in elbow & hand controlled by nueronal firing rate recorded from motor control electrode

## Slide 13: Methods
Sensory Input
  3 subjects
    For each, one tactile & proprioceptive electrode selected for testing
  Prior to testing
    3 & then 5 different force/position matches with visual feedback
  Testings:

## Slide 14: Methods
Sensory input (cont.)
    Force applied to sensor on thumb
      Subject asked to rate force using open numerical scale without visual feedback
    Elbow of artificial arm moved to different positions
      Subject asked to match perceived angle of elbow flexion/extension without visual feedback

## Slide 15: Methods
Motor output
  3 subjects
    Eah with one of vailable motor channel electrodes
    2 for grip force
    1 for elbow control
  Prior to testing
    Subject given time to train for given movement
  Testings:

## Slide 16: Methods
  Grip force control:
    Subject asked to match 3 levels of force (typically 22, 44, & 67 N) and,
      Within 5 s for each target value
    After succeeding more than 70 % of target values, 5 levels (ranging from 13 to 67 N)
      Within 5 s for each target value
    Match random target value (ranging from 22 to 67 N)
  Elbow position control:
    Similar with grip force control training paradigm

## Slide 17: Results
Sensory input
  All 3 subjects could judge changes in indentation or force applied to thumb sensor
    Slops of linear regression lines significantly different from 0 (at the end of testing)
    Regression slope of only 1 subject significantly increased
    Significant decrease in variance of residuals around regression lines in 2 subjects

## Slide 18: Results

## Slide 19: Results
  Subjects could judge static position of elbow join in artificial arm
    Linear regression P-value < 0.001 at the end of testing
    General increase in slops of regression lines with time statistically significant in 2 subjects
    Statistically significant decline in variance around regression line in only 1 subject

## Slide 20: Results

## Slide 21: Results
Motor output
  Grip force control
    Linear regression P-value >> 0.05
    Significant nonzero slope
    Significant decline in variance around regression in time in both subjects
    No significant change in slopes of regression lines

## Slide 22: Results

## Slide 23: Results
  Elbow control
    Linear regression P-value >> 0.5
    significant nonzero slope
    Significant increase in slopes of regression line
    Significant decline in variance of residuals around regression line in time

## Slide 24: Results

## Slide 25: Conclusions
Appropriate, graded, distally referred sensations can be used to provide feedback information about grip force & limb position
Control of trip force & limb position can be affected by motor activity from peripheral nerve stumps with electrodes

## Slide 26: Conclusions
Improved performance in some subjects over short period may suggest further training may provide better feedback & control
May provide pain-free integration of artificial arm into amputee’s body in future

## Slide 27: Further Studies
Optimization of sensory stimulation paradigms
Optimal processing of motor control signals
Different training regimes
Improving operational characteristics of artificial arm
Nonvisual control of artificial arm

## Slide 28: Further Studies
Implementation of implanted bidirectional telemetry system
Implementation of viable permanent percutaneous connector system
Design constraints
  Weight
  Power supply