## Slide 1: Control of a humanoid robot using EEG

## Slide 2: Problem
EEG is low bandwidth
Hard to exercise fine grained control

## Slide 3: Solution
Use an autonomous robot
Provide various options for user to select from
Use P300 to detect which option is selected

## Slide 4: User Study
4 training sessions to train classifier for grids: 2x2, 2x3, 3x2
.25sec flash alternating between options
One binary classifier for P300
Spatial projection algorithm
  a multichannel time-series response to an event and projects all the channels to form a single time series that is maximally discriminative.

## Slide 5: Brain-Robot Interface
Robot offers image choices to the user
A border flashes alternating on images
User selects an option using P300 response

## Slide 6: Results
98.4% classification accuracy
97% accuracy without the spatial filter
Grid layout did not have a significant impact

## Slide 7: P3 example

## Slide 8: Number of Flashes
95% accuracy with 5 flashes
Using .25 sec flash, with 4 options, a command can be sent every 5 seconds

## Slide 9: Number of Flashes

## Slide 10: Generalizing Classification

## Slide 11: Training Time

## Slide 13: Discussion
New mode of interaction
Many potential uses