## Slide 1: CSE P 501 – Compilers
x86 Lite for Compiler Writers
Hal Perkins
Autumn 2011

## Slide 2: Agenda
Learn/review x86 architecture
  Core 32-bit part only for now
    Ignore crufty, backward-compatible things
    Look at x86-64 extensions later
  Suggest either 32- or 64-bit x86 as compiler target for project (tradeoffs either way)
    If you want to try something else (ARM, MIPS, ?), let’s talk
After we’ve reviewed the x86 we’ll look at how to map language constructs to code

## Slide 3: x86 Selected History
30 Years of x86
  1978: 8086 – 16-bit processor, segmentation
  1982: 80286 – protected mode, floating point
  1985: 80386 – 32-bit architecture, “general-purpose” register set, VM
  1993: Pentium – mmx
  1999: Pentium III – SSE
  2000: Pentium IV – SSE2, SSE3, HT, virtualization
  2006: Core Duo, Core 2 – Multicore, SSE4+, x86-64
  2008: Atom, i7, …
Many internal implementation changes, pipelining, concurrency, &c

## Slide 4: And It’s Backward-Compatible!
Current processors can run 8086 code (!)
  (You can get VisiCalc 1.0 on the web!)
 The Intel descriptions of the architecture are loaded down with modes and flags that obscure the modern, fairly simple 32-bit and 64-bit processor models
Modern processors have a RISC-like core
  Simple, register-register & load/store architecture
  Simple x86 instructions preferred; complex CICS instructions supported
    We’ll focus on the basic 32-bit core instructions for now

## Slide 5: x86 Assembler
The nice thing about standards…
Two main assembler languages for x86:
  Intel/Microsoft– what’s in the documentation
  GNU / AT&T syntax (Linux, OS X)
    Use gcc –S to generate examples from C/C++ code
  You can use either for your project
Slides use Intel descriptions
Brief information later on differences
  Main changes: dst,src reversed, data types in gnu opcodes, various syntactic annoyances

## Slide 6: Intel ASM Statements
Format is
  optLabel: opcode operands ; comment
  optLabel is an optional label
  opcode and operands make up the assembly language instruction
  Anything following a ‘;’ is a comment
Language is very free-form
  Comments and labels may appear on separate lines by themselves (we’ll take advantage of this)

## Slide 7: x86 Memory Model
8-bit bytes, byte addressable
16-, 32-, 64-bit words, doublewords, and quadwords
  Data should almost always be aligned on “natural” boundaries; huge performance penalty on modern processors if it isn’t
Little-endian – address of a 4-byte integer is address of low-order byte

## Slide 8: x86 Processor Registers
8 32-bit, mostly general purpose registers
  eax, ebx, ecx, edx, esi, edi, ebp (base pointer), esp (stack pointer)
Other registers, not directly addressable
  32-bit eflags register
    Holds condition codes, processor state, etc.
  32-bit “instruction pointer” eip
    Holds address of first byte of next instruction to execute

## Slide 9: Processor Fetch-Execute Cycle
Basic cycle (same as every processor you’ve ever seen)
  while (running) {
  fetch instruction beginning at eip address
  eip <- eip + instruction length
  execute instruction
  }
Sequential execution unless a jump stores a new “next instruction” address in eip

## Slide 10: Instruction Format
Typical data manipulation instruction
  opcode dst,src
Meaning is
  dst <- dst op src
Normally, one operand is a register, the other is a register, memory location, or integer constant
  Can’t have both operands in memory – can’t encode two separate memory addresses

## Slide 11: x86 Memory Stack
Register esp points to the “top” of stack
  Dedicated for this use; don’t use otherwise
  Points to the last 32-bit doubleword pushed onto the stack (not next “free” one)
  Should always be doubleword aligned
    It will start out this way, and will stay aligned unless your code does something bad
  Stack grows down

## Slide 12: Stack Instructions
push src
  esp <- esp – 4; memory[esp] <- src (e.g., push src onto the stack)
pop dst
  dst <- memory[esp]; esp <- esp + 4 (e.g., pop top of stack into dst and logically remove it from the stack)
These are highly optimized and heavily used
  32-bit function call protocol is stack-based
  32-bit x86 doesn’t have enough registers, so the stack is frequently used for temporary space

## Slide 13: Stack Frames
When a method is called, a stack frame is traditionally allocated on the top of the stack to hold its local variables
Frame is popped on method return
By convention, ebp (base pointer) points to a known offset into the stack frame
  Local variables referenced relative to ebp
  (This is often optimized to use esp-relative references instead. Frees up ebp, needs additional bookkeeping at compile time.)

## Slide 14: Operand Address Modes (1)
These should cover most of what we’ll need
  mov eax,17 ; store 17 in eax
  mov eax,ecx ; copy ecx to eax
  mov eax,[ebp-12] ; copy memory to eax
  mov [ebp+8],eax ; copy eax to memory
References to object fields work similarly – put the object’s memory address in a register and use that address plus field offset

## Slide 15: Operand Address Modes (2)
In full generality, a memory address can combine the contents of two registers (with one being scaled) plus a constant displacement:
  [basereg + index*scale + constant]
  Scale can be 2, 4, 8
Main use is for array subscripting
Example: suppose
  Array of 4-byte ints, address of the array A is in ecx, subscript i is in eax
  Code to store edx in A[i]
  mov [ecx+eax*4],edx ;; and we didn’t even use the offset!

## Slide 16: dword ptr – Intel assembler
Obscure, but sometimes necessary…
If the assembler can’t figure out the size of the operands to move, you can explicitly tell it to move 32 bits with the qualifier “dword ptr”
  mov dword ptr [eax+16],[ebp-8]
  Use this if the assembler complains; otherwise ignore
  Not an issue in GNU asembler – different opcode mnemonics for different operand sizes

## Slide 17: Basic Data Movement and Arithmetic Instructions
mov dst,src
  dst <- src
add dst,src
  dst <- dst + src
sub dst,src
  dst <- dst – src
inc dst
  dst <- dst + 1
dec dst
  dst <- dst - 1
neg dst
  dst <- - dst (2’s complement arithmetic negation)

## Slide 18: Integer Multiply and Divide
imul dst,src
  dst <- dst * src
  32-bit product
  dst must be a register
imul dst,src,imm8
  dst <- dst*src*imm8
  imm8 – 8 bit constant
  Obscure, but useful for optimizing array refs
  There are other mul instructions – see docs
idiv src
  Divide edx:eax by src (edx:eax holds sign-extended 64-bit value; cannot use other registers for division)
  eax <- quotient
  edx <- remainder
cdq
  edx:eax <- 64-bit sign extended copy of eax

## Slide 19: Bitwise Operations
and dst,src
  dst <- dst & src
or dst,src
  dst <- dst | src
xor dst,src
  dst <- dst ^ src
not dst
  dst <- ~ dst (logical or 1’s complement)

## Slide 20: Shifts and Rotates
shl dst,count
  dst shifted left count bits
shr dst,count
  dst <- dst shifted right count bits (0 fill)
sar dst,count
  dst <- dst shifted right count bits (sign bit fill)
rol dst,count
  dst <- dst rotated left count bits
ror dst,count
  dst <- dst rotated right count bits

## Slide 21: Uses for Shifts and Rotates
Can often be used to optimize multiplication and division by small constants
  If you’re interested, look at “Hacker’s Delight” by Henry Warren, A-W, 2003
    Lots of very cool bit fiddling and other algorithms
  But be careful – be sure semantics are OK
There are additional instructions that shift and rotate double words, use a calculated shift amount instead of a constant, etc.

## Slide 22: Load Effective Address
The unary & operator in C
  lea dst,src ; dst <- address of src
  dst must be a register
  Address of src includes any address arithmetic or indexing
  Useful to capture addresses for pointers, reference parameters, etc.
  Also useful for computing arithmetic expressions that match r1+scale*r2+const

## Slide 23: Control Flow - GOTO
At this level, all we have is goto and conditional goto
Loops and conditional statements are synthesized from these
Optimization note: random jumps play havoc with pipeline efficiency; much work is done in modern compilers and processors to minimize this impact

## Slide 24: Unconditional Jumps
jmp dst
  eip <- address of dst
  Assembly language notes:
    dst will be a label
    Can have multiple labels on separate lines preceding an instruction
      Convenient in compiler-generated asm lang.

## Slide 25: Conditional Jumps
Most arithmetic instructions set “condition code” bits in eflags to record information about the result (zero, non-zero, positive, etc.)
  True of add, sub, and, or; but not imul or idiv
Other instructions that set eflags
  cmp dst,src ; compare dst to src
  test dst,src ; calculate dst & src (logical ; and); doesn’t change either

## Slide 26: Conditional Jumps Following Arithmetic Operations
jz label ; jump if result == 0
jnz label ; jump if result != 0
jg label ; jump if result > 0
jng label ; jump if result <= 0
jge label ; jump if result >= 0
jnge label ; jump if result < 0
jl label ; jump if result < 0
jnl label ; jump if result >= 0
jle label ; jump if result <= 0
jnle label ; jump if result > 0
Obviously, the assembler is providing multiple opcode mnemonics for several of these instructions

## Slide 27: Compare and Jump Conditionally
Want: compare two operands and jump if a relationship holds between them
Would like to do this
  jmpcond op1,op2,label
but can’t, because 3-address instructions can’t be encoded in x86

## Slide 28: cmp and jcc
Instead, use a 2-instruction sequence
  cmp op1,op2
  jcc label
where jcc is a conditional jump that is taken if the result of the comparison matches the condition cc

## Slide 29: Conditional Jumps Following Arithmetic Operations
je label ; jump if op1 == op2
jne label ; jump if op1 != op2
jg label ; jump if op1 > op2
jng label ; jump if op1 <= op2
jge label ; jump if op1 >= op2
jnge label ; jump if op1 < op2
jl label ; jump if op1 < op2
jnl label ; jump if op1 >= op2
jle label ; jump if op1 <= op2
jnle label ; jump if op1 > op2
Again, the assembler is mapping more than one mnemonic to some machine instructions

## Slide 30: Function Call and Return
The x86 instruction set itself only provides for transfer of control (jump) and return
Stack is used to capture return address and recover it
Everything else – parameter passing, stack frame organization, register usage – is a matter of convention and not defined by the hardware

## Slide 31: call and ret Instructions
call label
  Push address of next instruction and jump
  esp <- esp – 4; memory[esp] <- eip eip <- address of label
ret
  Pop address from top of stack and jump
  eip <- memory[esp]; esp <- esp + 4
  WARNING! The word on the top of the stack had better be an address, not some leftover data

## Slide 32: enter and leave
Complex instructions for languages with nested procedures
  enter can be slow on current CPUs – best avoided
    i.e., don’t use it in your project
  leave is equivalent to
      mov esp,ebp
      pop ebp
    and is generated by many compilers. Fits in 1 byte, saves space. Not clear if it’s any faster.

## Slide 33: Win 32 C Function Call Conventions
Wintel code obeys the following conventions for C programs
  Note: calling conventions normally designed very early in the instruction set/ basic software design. Hard (e.g., basically impossible) to change later.
C++ augments these conventions to include the “this” pointer
We’ll use these conventions in our code

## Slide 34: Win32 C Register Conventions
These registers must be restored to their original values before a function returns, if they are altered during execution esp, ebp, ebx, esi, edi
  Traditional: push/pop from stack to save/restore
A function may use the other registers (eax, ecx, edx) without having to save/restore
A 32-bit function result is expected to be in eax when the function returns

## Slide 35: Call Site
Caller is responsible for
  Pushing arguments on the stack from right to left (allows implementation of varargs)
  Execute call instruction
  Pop arguments from stack after return
    For us, this means add 4*(# arguments) to esp after the return, since everything is either a 32-bit variable (int, bool), or a reference (pointer)

## Slide 36: Call Example
n = sumOf(17,42)
  push 42 ; push args
  push 17
  call sumOf ; jump &
  ; push addr
  add esp,8 ; pop args
  mov [ebp+offsetn],eax ; store result

## Slide 37: Callee
Called function must do the following
  Save registers if necessary
  Allocate stack frame for local variables
  Execute function body
  Ensure result of non-void function is in eax
  Restore any required registers if necessary
  Pop the stack frame
  Return to caller

## Slide 38: Win32 Function Prologue
The code that needs to be executed before the statements in the body of the function are executed is referred to as the prologue
For a Win32 function f, it looks like this:
  f: push ebp ; save old frame pointer
  mov ebp,esp ; new frame ptr is top of
  ; stack after arguments and
  ; return address are pushed
  sub esp,”# bytes needed”
  ; allocate stack frame (size
  ; must be multiple of 4)

## Slide 39: Win32 Function Epilogue
The epilogue is the code that is executed for a return statement (or if execution “falls off” the bottom of a void function)
For a Win32 function, it looks like this:
  mov eax,”function result”
  ; put result in eax if not already
  ; there (if non-void function)
  mov esp,ebp ; restore esp to old value
  ; before stack frame allocated
  pop ebp ; restore ebp to caller’s value
  ret ; return to caller

## Slide 40: Example Function
Source code
  int sumOf(int x, int y) {
  int a, int b;
  a = x;
  b = a + y;
  return b;
  }

## Slide 41: Stack Frame for sumOf
  int sumOf(int x, int y) {
  int a, int b;
  a = x;
  b = a + y;
  return b;
  }

## Slide 42: Assembly Language Version
;; int sumOf(int x, int y) {
;; int a, int b;
sumOf:
push ebp ; prologue
mov ebp,esp
sub esp, 8
;; a = x;
mov eax,[ebp+8]
mov [ebp-4],eax
;; b = a + y;
mov eax,[ebp-4]
add eax,[ebp+12]
mov [ebp-8],eax
;; return b;
mov eax,[ebp-8]
mov esp,ebp
pop ebp
ret
;; }

## Slide 43: Coming Attractions
Now that we’ve got a basic idea of the x86 instruction set, we need to map language constructs to x86
  Code Shape
Then on to basic code generation and execution
  And later, optimizations