## Slide 1: Practical Aspects of Modern Cryptography
Tolga Acar
Josh Benaloh
Autumn 2016

## Slide 2: Agenda
Hardware crypto devices
  Smart cards
  TPMs (v1.2 and v2.0)
  Hardware Security Modules
  Authentication Tokens

## Slide 4: What is a smart card?
Long history, invented in the 1970s
Integrated Circuit Cards - ICC
Initially used for pay phone systems in France
Most successful deployment: GSM cell phones
Payments: EMV
Strong User Authentication. Some examples:
  National eID programs in Asia and Europe
  DoD CAC cards

## Slide 5: Smart Cards
Pin | Description
VCC | Power supply input
RST | Reset signal from the interface device, or In combination with an internal reset control circuit (optional)
CLK | Clock signal (optional used by the card)
GND | Ground voltage
VPP | Programming voltage input (deprecated, optional)
I/O | Serial data I/O
C4 | Aux contact. USB devices D+
C8 | Aux contact. USB devices D-
ISO/IEC 7810 and 7816

## Slide 6: Smart Cards: typical
256 – 4KB RAM
8KB – 32KB ROM
1KB – 32KB EEPROM
CPU
  8-bit or 16-bit CPU (8051 is common) @ 16MHz
  32-bit RISC @ 25 – 32 MHz
Crypto processor: RSA, DES, 3DES, ECC, AES, SHAx
Atmel, Infineon, NXP, ST Microelectronics, and many others

## Slide 7: Credit Cards with Chip
1974
1977
1979
1984
1996
2007
Chip card description
uP chip card invention
Commercial smart cards
French chip card rollout
EMV
Contactless protocol
2008
CCPS: Contactless Comm. Protocol Spec. (L1)

## Slide 8: Benefits of smart cards
Provides secure storage for private keys & data
  Tamper resistant
  Cryptographically secure
Provides two factor authentication
  Something you have – The Card
  Something you know – The PIN (Also referred to as Card Holder Verification- CHV)
Programmable cards
  Ex.: JavaCards, .NET Cards

## Slide 9: Some Applications
Building access
User authentication (ID)
Banking and finance
Mobile communications
Pay phone cards
E-mail security
Transportation
Passports
Loyalty programs

## Slide 10: Possible eID scenarios
Woodgrove Bank
Michael
Smartcard + Reader / PIN pad
Web Banking
Domain Logon
Work Corp
Government eID Bank Smartcard …
Government Tax Agency
Abby
Email, IM, …
eID Issuance
Name Address Submit/sign form …

## Slide 11: Smart Card Management System
Register/Unregister
Adding/Removing from the system
Issue
Issuance and personalization for a smart card holder
Initialization
Activating for the first use by the card holder
Deactivation/Activation
Putting the card on hold and re-activating it
Lock/Unlock
Card holder access is blocked or unblocked
Revoke
Card credentials are revoked
Retire
Card holder is disconnected from the card
Delete
Permanent removal of the card from the system
Backup/Restore
Backup copy of the credentials on the card, and restore from a backup

## Slide 12: Hardware Security Modules
Physical computing device in different form factors
One or more crypto processors
Tamper-resistant
Bus snooping prevention
Side channel leakage protection
Self zeroization and destruction
No key export mode
FIPS 140 Level 3+ certification
SW Interfaces: PKCS#11, Java, CAPI, CNG, and proprietary

## Slide 13: Why HSM?
Compliance requirements
  FIPS 140 Level 3+
  Common Criteria (EAL3+)
All crypto keys are locked inside the HSM
  No cleartext keys outside the HSM
  Key operations via handles, key usage restrictions
High-value keys: significant negative impact from key compromise
Object types
  Asymmetric keys
  Symmetric keys
  Certificates
  Arbitrary data
Crypto processing offload
  TLS accelerators, cryptographic processing offload

## Slide 14: A Few Use Cases
Certificate Authorities: PKI
  CA private key is generated and stored in the HSM
Payments
  PCI: Payment Card Industry data protection
  PIN encryption
  EMV: Card Master Keys, key derivation
TLS
  Crypto processing offload: accelerator
  Private keys are generated and used in the HSM

## Slide 15: Net HSM, Security Worlds
Network attached HSM, sharable cryptographic resource
Multiple HSM devices sharing the same set of keys
  Each device has unique HW keys
  Common security world keys encrypted with device key
  Encrypted keys are stored in files
  Security World keys encrypt application keys
  Encrypted application keys are stored in files
Access cards (smart cards) are optionally required
  Required to add an HSM to a security world
Lights-out mode: no PIN, no smart card (accelerator mode)

## Slide 16
Expensive Moderate Inexpensive
Cost:
Very Secure More Secure Moderate (OS-Dependent)
Security:
Hard Easier Easy
Deployment:
HSM
Hardware Security Module
TPM based
Crypto
Software Crypto
No Hardware
TPM for Crypto
Following TPM sections include content from Shon Eizenhoefer, Paul England, David Wooten

## Slide 17: What Is A Trusted Platform Module (TPM)?
Smartcard-like module on the motherboard
Protects secrets
Performs cryptographic functions
  RSA, SHA-1/256, RNG, ECC, AES, others
Performs digital signature operations
Anchors chain of trust for keys and credentials
Protects itself against attacks
Holds Platform Measurements (hashes)
Can create, store and manage keys
  Provides a unique Endorsement Key (EK)
  Provides a unique Storage Root Key (SRK)
TPM 1.2 spec: www.trustedcomputinggroup.org

## Slide 18: TPM v1.2  v2.0
Algorithmic progression
  SHA-1 showing sign of weakness
  Shift from RSA to ECC
Mutual lack of trust across geographies
Need beyond user PCs
  Server use cases
  Too difficult to use (Owner  Security, Privacy, Platform)
V1.2 and v2.0 are not compatible
Notes: http://www.iaik.tugraz.at/content/about_iaik/events/ETISS_INTRUST_2013/ETISS/slides/ETISS-INTRUST-2013-LiqunChen.pdf

## Slide 19: TPM v1.2 and 2.0
 | V1.0 | V2.0
Architecture | Only one | Common and platform-specific: mandatory, optional, or banned
Cryptographic Algorithms | Required: RSA, SHA-1, MGF1, RNG, DAA, KeyGen Optional: AES, XOR Banned: 3DES | Required: SHA-1, SHA-256, RSA, ECC (BN-256, NIST P-256), HMAC, AES-128, MGF1, RNG, DAA-ECC, KeyGen, KDF
Storage Root Key | RSA-2048 with one hierarchy | Multiple keys and algorithms per hierarchy (three of them)

## Slide 20: TPMv2.0 Roots of Trust
Elements that must be trusted: malice is not detectable
  Measurement (RTM)
    Integrity relevant information (of CPU)
    Core Roots of Trust or Measurement is the first set of instructions executed by the CPU when a new trust chain is established (reset)
    These instructions send identity values to RTS
  Storage (RTS)
    Shielded TPM memory (e.g., keys)
  Reporting (RTR)
    Reports on RTS contents, i.e., signature over TPM contents
      PCR: Platform Configuration Registers (Quote)
      Audit logs
      Key properties

## Slide 21: TPMv2.0 Primary Seeds
Large random value stored persistently in the TPM
  Used to generate keys, seeds, and proof values
  Object Value = KDF(Primary Seed, Parameters)
EPS: Endorsement Primary Seed
  Generate Endorsement Keys (EK) – RTR Identity
PPS: Platform Primary Seed
  Hierarchy controlled by platform firmware (not OS)
SPS: Storage Primary Seed
  Hierarchies controlled by the platform owner
  Generates Storage Root Keys (SRK) for OS/App use

## Slide 22: TPM v2.0 Crypto Subsystem
Hash functions and HMAC
Asymmetric encryption and decryption
Asymmetric signing and signature verification
Symmetric encryption and decryption
  CTR, OFB, CBC, CFB, ECB
Key generation
  Key generation from the RNG
  Primary Key derivation from a seed with a KDF
RNG
KDF
  Hash-based (SP800-108 and SP800-56A)
  HMAC as the PRF

## Slide 23: TPM RNG
RNG consists of
  Entropy source and collector
    Collects entropy and removes bias
    Collected entropy is used to update the state register
  State register
    Input value to the mixing function
  Mixing function (e.g., a hash function)
    Typically implemented as a PRNG

## Slide 24: TPM RNG
RNG
DRBG
TPM2_StirRandom()
Entropy Source
Entropy
Random Bits
Random Numbers

## Slide 25: TPM Key Features
Platform measurements
  TPM can measure instruction sequences & store the results in Platform Configuration Registers (PCRs)
Encryption
  TPM can encrypt arbitrary data using TPM keys, or keys protected by TPM keys
Sealed Storage
  TPM can encrypt arbitrary data, using TPM keys or keys protected by TPM keys and under a set of PCR values
  Data can only be decrypted later under the same PCR configuration
Attestation (more later)

## Slide 26: Sealed Storage
Why is Sealed Storage useful?
Provides a mechanism for defending against boot-time attacks
Sealed Storage lets a TPM encrypt data to a specific set (or subset) of PCR values
Example: Full Volume Encryption (FVE)
  BitLocker™ Drive Encryption on Windows

## Slide 27: Booting w/ TPM measurements

## Slide 28: Secure Boot with TPM
Where does the public key trust come from?
  Databases
    Signature Database and Revoked Signature Database
      Signers or image hashes (UEFI app/driver, OS Loader)
    Key Enrollment Key database
      Database of signing keys to update the signature databases
Boot Sequence
  Boot manager  Anti-Malware  Kernel Drivers  Initialize User Mode processes

## Slide 29: Disk Layout And Key Storage
OS Volume Contains
Encrypted OS
Encrypted Page File
Encrypted Temp Files
Encrypted Data
Encrypted Hibernation File
Where’s the Encryption Key?
SRK (Storage Root Key) contained in TPM
SRK encrypts FVEK (Full Volume Encryption Key) protected by TPM/PIN/USB Storage Device
FVEK stored (encrypted by SRK) on hard drive in the OS Volume
System
OS Volume
System Volume Contains:
MBR, Boot manager, Boot Utilities
(Unencrypted, small)
3
2
FVEK
1
SRK

## Slide 30: TPM Attestation
Attestation is an authentication technology
  But more than “simple signing”
Attestation allows a TPM to sign data and a set (or subset) of the current PCR values
  TPM attests to a certain software configuration
  whatever was measured into those PCR registers is part of its digital signature
  Quoting

## Slide 31: TPM Attestation
Attestation | Attests to …
Endorsement Certificate | Genuine TPM, TPM specification compliance. Asymmetric key embedded in a TPM and a vouching credential
Platform Certificate | Contains a Root of Trust for Measurement, genuine TPM
Attestation Key Certificate | An asymmetric key pair protected in a genuine, but unidentified, TPM Typically relies on Endorsement and Platform Certificates
Key Attestation | Platform attestation to vouch for a TPM asymmetric key using an attestation key
Quote | Measurement to vouch for a software/firmware state, typically over a PCR using an attestation-key

## Slide 32: TPM Management
User has a difficult time understanding the TPM controls
    What is the difference between TPM enable and activate?
Security and privacy functions use the same controls
    Need to take ownership of TPM to use the Storage Root Key but that also enables Endorsement Key operations which are privacy sensitive.
PCR sealing model is brittle
    Makes it difficult to manage keys that rely on PCR values.
    System updates that change a PCR measurement can be very disruptive.

## Slide 33: PCR “Brittleness”
Many configuration changes leading to PCR changes are benign
  But still result in keys becoming unusable, etc.
Sometimes if you plan ahead you can prevent this
  E.g. seal to a future known good configuration
Sometimes we can fix this with smarter external software
  E.g. extend hashes of authorized signing keys and check certificates

## Slide 34: Ecosystem Issues
TPM/TCM are not interchangeable.
    No BIOS level abstraction for a security token (TPM/TCM) as there is for a disk (read/write logical blocks).
    Makes it hard to adopt boot code for alternative algorithms.
Trusted computing crosses national boundaries.
    Neither the TPM nor the TCM has the ability to meet both local and international cryptographic requirements at the same time.
  The sunset of SHA1 has demonstrated the importance of not being tied to a fixed set of algorithms.
    It will be a major upset to the ecosystem (chip, system, software) to switch to a new TPM with a new software interface.
Changing the TPM algorithms is going to cause a major upheaval in the ecosystem.

## Slide 35: Virtualization
Sharing a single physical platform among multiple virtual machines (VMs) with complete isolation among VMs
Benefits
  Consolidation of workloads, Fault tolerance, Extensibility, Ease of Management, Better security

## Slide 36: Virtualization
With increasing h/w support, performance degradation is becoming minimal
With multi-core, we can envision pervasive adoption
  Solutions available for server, client, and mobile platforms
  E.g., virtualized data centers (EC2, Azure)
  And, Dilbert running his office VM on home computer

## Slide 37: Virtual TPM
Challenge: physical TPM itself is hard to virtualize
  By design, TPM resists virtualization
TPM emulation
  Complete s/w emulation, TCG interface: vTPM [Berger06]
Para-virtualized TPM sharing [England08]
  Hypercall interface with Hv as mediator

## Slide 38: vTPM
VMM
TPM
Service VM
vTPM
Guest 0
Guest 1
vTPM

## Slide 39: vTPM
Pros
  Standard TCG interface
  High fidelity: full legacy support
  Vendors can add VM use-cases
    Migration, suspend/resume, rollback
Cons
  Low resistance to physical attack
  Reduced resistance to software attack
    Hypervisor is more complex and exposed than TPM embedded OS
  Trust model for TPM is complex
    Hypervisor security model influences vTPM security
VMM
TPM
Service VM
vTPM
Guest

## Slide 40: Para-Virtualized TPM Sharing
VMM
TPM
Guest 0
Guest 1
TPM Access Mediation
Guest 0 state
Guest 1 state

## Slide 41: Para-Virtualized TPM - Attestation
HvQuote(TCB, nonce)
TPM
PCR0
PCR1
…
Resettable PCR
VPCR0
VPCR1
Guest 0
Guest 1
VPCR0
VPCR1
VPCR1
PcrReset(15)
PcrExtend(15,VPCR1)
Quote((0,15), nonce)