## Slide 1: Parallel Computing on Manycore GPUs
Vinod Grover

## Slide 2: Generic Manycore Chip
• • •
Processor
Memory
Processor
Memory
Global Memory
Many processors each supporting many hardware threads
On-chip memory near processors (cache, RAM, or both)
Shared global memory space (external DRAM)

## Slide 3: GPU Evolution
High throughput computation
  933 GFLOP/s
High bandwidth memory
  102 GB/s
High availability to all
  ~100 million CUDA-capable GPUs sold
1999
GeForce 256
22 Million
Transistors
2002
GeForce4
63 Million
Transistors
2003
GeForce FX
130 Million
Transistors
2004
GeForce 6
222 Million
Transistors
1995
NV1
1 Million
Transistors
2005
GeForce 7
302 Million
Transistors
2008
GeForce GTX 200
1.4 Billion
Transistors
2006-2007
GeForce 8
754 Million
Transistors
Notes: Tesla C1060 @ 1.296 GHz: 933 GFLOP/s (78 double) and 102 GB/s (peak)

## Slide 4: Accelerating Computation
146X
36X
19X
17X
100X
Interactive visualization of volumetric white matter connectivity
Ionic placement for molecular dynamics simulation on GPU
Transcoding HD video stream to H.264
Simulation in Matlab using .mex file CUDA function
Astrophysics N-body simulation
149X
47X
20X
24X
30X
Financial simulation of LIBOR model with swaptions
GLAME@lab: An M-script API for linear Algebra operations on GPU
Ultrasound medical imaging for cancer diagnostics
Highly optimized object oriented molecular dynamics
Cmatch exact string matching to find similar proteins and gene sequences

## Slide 5: Lessons from Graphics Pipeline
Throughput is paramount
  must paint every pixel within frame time
Create, run, & retire lots of threads very rapidly
  measured 14.8 Gthread/s on increment() kernel
Use multithreading to hide latency
  1 stalled thread is OK if 100 are ready to run
Notes: bare minimum: 2 Mpixels * 60 fps * 2 = 240 Mthread/s

## Slide 6: NVIDIA GPU Architecture
Communication Fabric
Memory & I/O
Fixed Function Acceleration
240 scalar cores
On-chip memory
Texture units
GeForce GTX 280 / Tesla T10

## Slide 7: SM Multiprocessor
SM
DP
SFU
MT Issue
Inst. Cache
Const. Cache
SFU
Memory
SP
SP
SP
SP
SP
SP
SP
SP
8 scalar cores (SP) per SM
  16K 32-bit registers (64KB)
  usual ops: float, int, branch, …
  block-wide barrier in 1 instruction
Shared double precision unit
  IEEE 754 64-bit floating point
  fused multiply-add
  full-speed denorm. operands and results
Direct load/store to memory
  the usual linear sequence of bytes
  high bandwidth (~100 GB/sec)
Low-latency on-chip memory
  16KB available per SM
  shared amongst threads of a block
  supports thread communication
SM

## Slide 8: Key Architectural Ideas
Hardware multithreading
  HW resource allocation & thread scheduling
  HW relies on threads to hide latency
SIMT (Single Instruction Multiple Thread) execution
  threads run in groups of 32 called warps
  threads in a warp share instruction unit (IU)
  HW automatically handles divergence
Threads have all resources needed to run
  any warp not waiting for something can run
  context switching is (basically) free
SM
DP
SFU
MT Issue
Inst. Cache
Const. Cache
SFU
Memory
SP
SP
SP
SP
SP
SP
SP
SP

## Slide 9: Why is this different from a CPU?
Different goals produce different designs
  GPU assumes work load is highly parallel
  CPU must be good at everything, parallel or not
CPU: minimize latency experienced by 1 thread
  lots of big on-chip caches
  extremely sophisticated control
GPU: maximize throughput of all threads
  lots of big ALUs
  multithreading can hide latency … so skip the big caches
  simpler control, cost amortized over ALUs via SIMD

## Slide 10: CUDA: Scalable parallel programming
Augment C/C++ with minimalist abstractions
  let programmers focus on parallel algorithms
  not mechanics of a parallel programming language
Provide straightforward mapping onto hardware
  good fit to GPU architecture
  maps well to multi-core CPUs too
Scale to 100’s of cores & 10,000’s of parallel threads
  GPU threads are lightweight — create / switch is free
  GPU needs 1000’s of threads for full utilization

## Slide 11: Key Parallel Abstractions in CUDA
Hierarchy of concurrent threads
Lightweight synchronization primitives
Shared memory model for cooperating threads

## Slide 12: Hierarchy of concurrent threads
Parallel kernels composed of many threads
  all threads execute the same sequential program
Threads are grouped into thread blocks
  threads in the same block can cooperate
Threads/blocks have unique IDs
Thread t
t0 t1 … tB
Block b

## Slide 13: Example: Vector Addition Kernel
// Compute vector sum C = A+B
// Each thread performs one pair-wise addition
__global__
void vecAdd(float* A, float* B, float* C, int n)
{
int i = threadIdx.x + blockDim.x * blockIdx.x;
if(i<n) C[i] = A[i] + B[i];
}
int main()
{
// Run N/256 blocks of 256 threads each
vecAdd<<< N/256, 256>>>(d_A, d_B, d_C, n);
}
Device Code

## Slide 14: Example: Vector Addition Kernel
// Compute vector sum C = A+B
// Each thread performs one pair-wise addition
__global__
void vecAdd(float* A, float* B, float* C, int n)
{
int i = threadIdx.x + blockDim.x * blockIdx.x;
if(i<n) C[i] = A[i] + B[i];
}
int main()
{
// Run N/256 blocks of 256 threads each
vecAdd<<< N/256, 256>>>(d_A, d_B, d_C, n);
}
Host Code

## Slide 15: Example: Host code for vecAdd
// allocate and initialize host (CPU) memory
float *h_A = …, *h_B = …;
// allocate device (GPU) memory
float *d_A, *d_B, *d_C;
cudaMalloc( (void**) &d_A, N * sizeof(float));
cudaMalloc( (void**) &d_B, N * sizeof(float));
cudaMalloc( (void**) &d_C, N * sizeof(float));
// copy host memory to device
cudaMemcpy( d_A, h_A, N * sizeof(float), cudaMemcpyHostToDevice) );
cudaMemcpy( d_B, h_B, N * sizeof(float), cudaMemcpyHostToDevice) );
// execute the kernel on N/256 blocks of 256 threads each
vecAdd<<<N/256, 256>>>(d_A, d_B, d_C);

## Slide 16: Hierarchy of memory spaces
Per-thread local memory
Per-block shared memory
Per-device global memory
Thread
per-thread local memory
Block
per-block shared
memory
Kernel 0
. . .
per-device global
memory
. . .
Kernel 1
. . .

## Slide 17: CUDA Model of Parallelism
CUDA virtualizes the physical hardware
  thread is a virtualized scalar processor (registers, PC, state)
  block is a virtualized multiprocessor (threads, shared mem.)
Scheduled onto physical hardware without pre-emption
  threads/blocks launch & run to completion
  blocks should be independent
• • •
Block
Memory
Block
Memory
Global Memory

## Slide 18: Thread = virtualized scalar processor
Independent thread of execution
  has its own PC, variables (registers), processor state, etc.
  no implication about how threads are scheduled
CUDA threads might be physical threads
  as on NVIDIA GPUs
CUDA threads might be virtual threads
  might pick 1 block = 1 physical thread on multicore CPU

## Slide 19: Block = virtualized multiprocessor
Provides programmer flexibility
  freely choose processors to fit data
  freely customize for each kernel launch
Thread block = a (data) parallel task
  all blocks in kernel have the same entry point
  but may execute any code they want
Thread blocks of kernel must be independent tasks
  program valid for any interleaving of block executions

## Slide 20: Blocks must be independent
Any possible interleaving of blocks should be valid
  presumed to run to completion without pre-emption
  can run in any order … concurrently OR sequentially
Blocks may coordinate but not synchronize
  shared queue pointer: OK
  shared lock: BAD … can easily deadlock
Independence requirement gives scalability

## Slide 21: Example: Parallel Reduction
Summing up a sequence with 1 thread:
  int sum = 0;
  for(int i=0; i<N; ++i) sum += x[i];
Parallel reduction builds a summation tree
  each thread holds 1 element
  stepwise partial sums
  N threads need log N steps
  one possible approach: Butterfly pattern

## Slide 22: Example: Parallel Reduction
Summing up a sequence with 1 thread:
  int sum = 0;
  for(int i=0; i<N; ++i) sum += x[i];
Parallel reduction builds a summation tree
  each thread holds 1 element
  stepwise partial sums
  N threads need log N steps
  one possible approach: Butterfly pattern

## Slide 23: Parallel Reduction for 1 Block
// INPUT: Thread i holds value x_i
int i = threadIdx.x;
__shared__ int sum[blocksize];
// One thread per element
sum[i] = x_i; __syncthreads();
for(int bit=blocksize/2; bit>0; bit/=2)
{
int t=sum[i]+sum[i^bit]; __syncthreads();
sum[i]=t; __syncthreads();
}
// OUTPUT: Every thread now holds sum in sum[i]

## Slide 24: Final Thoughts
GPUs are throughput-oriented microprocessors
  manycore architecture
  massive hardware multithreading
  ubiquitous commodity hardware
CUDA programming model is simple yet powerful
  traditional scalar execution model with transparent SIMD
  simple extensions to existing sequential language
Many important research opportunities
  not to speak of the educational challenges

## Slide 25
Questions?
http://www.nvidia.com/CUDA
vgrover@nvidia.com