## Slide 1: CSE 311 Foundations of Computing I
Lecture 5, Boolean Logic and Predicates
Autumn 2012

## Slide 2: Announcements
Homework 2 available (Due October 10)

## Slide 3: Highlights from last lecture
Boolean algebra to circuit design
Boolean algebra
  a set of elements B = {0, 1}
  binary operations { + , • }
  and a unary operation { ’ }
  such that the following axioms hold:
1. the set B contains at least two elements: a, b 2. closure: a + b is in B a • b is in B 3. commutativity: a + b = b + a a • b = b • a 4. associativity: a + (b + c) = (a + b) + c a • (b • c) = (a • b) • c 5. identity: a + 0 = a a • 1 = a 6. distributivity: a + (b • c) = (a + b) • (a + c) a • (b + c) = (a • b) + (a • c) 7. complementarity: a + a’ = 1 a • a’ = 0
George Boole – 1854

## Slide 4: A simple example: 1-bit binary adder
Inputs: A, B, Carry-in
Outputs: Sum, Carry-out
A
B
Cin
Cout
S
A B Cin Cout S
0 0 0 0 0 1
0 1 0
0 1 1
1 0 0 1 0 1
1 1 0
1 1 1
0
1
1
0
1
0
0
1
0
0
0
1
0
1
1
1
Cout = A’ B Cin + A B’ Cin + A B Cin’ + A B Cin
S = A’ B’ Cin + A’ B Cin’ + A B’ Cin’ + A B Cin
A A A A A
B B B B B
S S S S S
Cin
Cout

## Slide 5: Cout = A’ B Cin + A B’ Cin + A B Cin’ + A B Cin

## Slide 6: Apply the theorems to simplify expressions
The theorems of Boolean algebra can simplify expressions
  e.g., full adder’s carry-out function
Cout = A’ B Cin + A B’ Cin + A B Cin’ + A B Cin
= A’ B Cin + A B’ Cin + A B Cin’ + A B Cin + A B Cin
= A’ B Cin + A B Cin + A B’ Cin + A B Cin’ + A B Cin
= (A’ + A) B Cin + A B’ Cin + A B Cin’ + A B Cin
= (1) B Cin + A B’ Cin + A B Cin’ + A B Cin
= B Cin + A B’ Cin + A B Cin’ + A B Cin + A B Cin
= B Cin + A B’ Cin + A B Cin + A B Cin’ + A B Cin
= B Cin + A (B’ + B) Cin + A B Cin’ + A B Cin
= B Cin + A (1) Cin + A B Cin’ + A B Cin
= B Cin + A Cin + A B (Cin’ + Cin)
= B Cin + A Cin + A B (1)
= B Cin + A Cin + A B
adding extra terms creates new factoring opportunities

## Slide 7: S = A’ B’ Cin + A’ B Cin’ + A B’ Cin’ + A B Cin

## Slide 8: A simple example: 1-bit binary adder
Inputs: A, B, Carry-in
Outputs: Sum, Carry-out
A
B
Cin
Cout
S
A B Cin Cout S
0 0 0 0 0 1
0 1 0
0 1 1
1 0 0 1 0 1
1 1 0
1 1 1
0
1
1
0
1
0
0
1
0
0
0
1
0
1
1
1
Cout = B Cin + A Cin + A B
S = A xor (B xor Cin)
A A A A A
B B B B B
S S S S S
Cin
Cout

## Slide 9: A 2-bit ripple-carry adder
A1
B1
Cout
Cin
Sum1
A
Sum
Cout
Cin
B
1-Bit Adder
A2
B2
Sum2
Cout
Cin
0

## Slide 10: Mapping truth tables to logic gates
Given a truth table:
  Write the Boolean expression
  Minimize the Boolean expression
  Draw as gates
  Map to available gates
A B C F
0 0 0 0
0 0 1 0
0 1 0 1
0 1 1 1
1 0 0 0
1 0 1 1
1 1 0 0
1 1 1 1
F = A’BC’+A’BC+AB’C+ABC
= A’B(C’+C)+AC(B’+B)
= A’B+AC
1
2
3
4

## Slide 11: Canonical forms
Truth table is the unique signature of a Boolean function
The same truth table can have many gate realizations
  we’ve seen this already
  depends on how good we are at Boolean simplification
Canonical forms
  standard forms for a Boolean expression
  we all come up with the same expression

## Slide 12: Sum-of-products canonical forms
Also known as disjunctive normal form
Also known as minterm expansion
A B C F F’ 0 0 0 0 1
0 0 1 1 0
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 0
F =
F’ = A’B’C’ + A’BC’ + AB’C’
F = 001 011 101 110 111
+ A’BC
+ AB’C
+ ABC’
+ ABC
A’B’C

## Slide 13: Sum-of-products canonical form (cont)
Product term (or minterm)
  ANDed product of literals – input combination for which output is true
  each variable appears exactly once, true or inverted (but not both)
short-hand notation for minterms of 3 variables
A B C minterms 0 0 0 A’B’C’ m0
0 0 1 A’B’C m1
0 1 0 A’BC’ m2
0 1 1 A’BC m3
1 0 0 AB’C’ m4
1 0 1 AB’C m5
1 1 0 ABC’ m6
1 1 1 ABC m7
F in canonical form: F(A, B, C) = m(1,3,5,6,7) = m1 + m3 + m5 + m6 + m7
= A’B’C + A’BC + AB’C + ABC’ + ABC
canonical form  minimal form F(A, B, C) = A’B’C + A’BC + AB’C + ABC + ABC’
      = (A’B’ + A’B + AB’ + AB)C + ABC’
      = ((A’ + A)(B’ + B))C + ABC’ = C + ABC’ = ABC’ + C
= AB + C

## Slide 14: Product-of-sums canonical form
Also known as conjunctive normal form
Also known as maxterm expansion
A B C F F’ 0 0 0 0 1
0 0 1 1 0
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 0
F = 000 010 100 F =
F’ = (A + B + C’) (A + B’ + C’) (A’ + B + C’) (A’ + B’ + C) (A’ + B’ + C’)
(A + B + C)
(A + B’ + C)
(A’ + B + C)

## Slide 15: Product-of-sums canonical form (cont)
Sum term (or maxterm)
  ORed sum of literals – input combination for which output is false
  each variable appears exactly once, true or inverted (but not both)
A B C maxterms 0 0 0 A+B+C M0
0 0 1 A+B+C’ M1
0 1 0 A+B’+C M2
0 1 1 A+B’+C’ M3
1 0 0 A’+B+C M4
1 0 1 A’+B+C’ M5
1 1 0 A’+B’+C M6
1 1 1 A’+B’+C’ M7
short-hand notation for maxterms of 3 variables
F in canonical form: F(A, B, C) = M(0,2,4) = M0 • M2 • M4
= (A + B + C) (A + B’ + C) (A’ + B + C)
canonical form  minimal form F(A, B, C) = (A + B + C) (A + B’ + C) (A’ + B + C)
      = (A + B + C) (A + B’ + C)
      (A + B + C) (A’ + B + C)
      = (A + C) (B + C)

## Slide 16: Predicate Calculus
Predicate or Propositional Function
  A function that returns a truth value
“x is a cat”
“x is prime”
“student x has taken course y”
“x > y”
“x + y = z”
Prime(65353)

## Slide 17: Quantifiers
 x P(x) : P(x) is true for every x in the domain
 x P(x) : There is an x in the domain for which P(x) is true
Relate  and  to  and 

## Slide 18: Statements with quantifiers
 x Even(x)
 x Odd(x)
 x (Even(x)  Odd(x))
 x (Even(x)  Odd(x))
 x Greater(x+1, x)
 x (Even(x)  Prime(x))
Even(x)
Odd(x)
Prime(x)
Greater(x,y)
Equal(x,y)
Domain:
Positive Integers

## Slide 19: Statements with quantifiers
 x  y Greater (y, x)
 x  y Greater (x, y)
 x  y (Greater(y, x)  Prime(y))
 x (Prime(x)  (Equal(x, 2)  Odd(x))
 x  y(Equal(x, y + 2)  Prime(x)  Prime(y))
Even(x)
Odd(x)
Prime(x)
Greater(x,y)
Equal(x,y)
Domain:
Positive Integers

## Slide 20: Statements with quantifiers
“There is an odd prime”
“If x is greater than two, x is not an even prime”
xyz ((Equal(z, x+y)  Odd(x)  Odd(y)) Even(z))
“There exists an odd integer that is the sum of two primes”
Even(x)
Odd(x)
Prime(x)
Greater(x,y)
Equal(x,y)
Domain:
Positive Integers

## Slide 21: Goldbach’s Conjecture
Every even integer greater than two can be expressed as the sum of two primes
Even(x)
Odd(x)
Prime(x)
Greater(x,y)
Equal(x,y)
Domain:
Positive Integers
xyz ((Greater(x, 2)  Even(x))  (Equal(x, y+z)  Prime(y)  Prime(z))