## Slide 1: The Hardware/Software Interface CSE351 Winter 2013
Buffer Overflow

## Slide 2: Buffer Overflow
Buffer overflows are possible because C doesn’t check array boundaries
Buffer overflows are dangerous because buffers for user input are often stored on the stack
  Probably the most common type of security vulnerability
Today we’ll go over:
  Address space layout
  Input buffers on the stack
  Overflowing buffers and injecting code
  Defenses against buffer overflows

## Slide 3: IA32 Linux Memory Layout
Stack
  Runtime stack (8MB limit)
Heap
  Dynamically allocated storage
  Allocated by malloc(), calloc(), new()
Data
  Statically allocated data
    Read-only: string literals
    Read/write: global arrays and variables
Text
  Executable machine instructions
  Read-only
Upper 2 hex digits = 8 bits of address
FF
00
Stack
Text
Data
Heap
08
8MB
not drawn to scale
Notes: The segment between addresses 0x00… and 0x08… is where shared libraries are mapped into the address space on IA32, I think.

## Slide 4: Memory Allocation Example
char big_array[1<<24]; /* 16 MB */
char huge_array[1<<28]; /* 256 MB */
int beyond;
char *p1, *p2, *p3, *p4;
int useless() { return 0; }
int main()
{
p1 = malloc(1 <<28); /* 256 MB */
p2 = malloc(1 << 8); /* 256 B */
p3 = malloc(1 <<28); /* 256 MB */
p4 = malloc(1 << 8); /* 256 B */
/* Some print statements ... */
}
FF
00
Stack
Text
Data
Heap
08
not drawn to scale
Where does everything go?

## Slide 5: IA32 Example Addresses
$esp 0xffffbcd0
p3 0x65586008
p1 0x55585008
p4 0x1904a110
p2 0x1904a008
&p2 0x18049760
beyond 0x08049744
big_array 0x18049780
huge_array 0x08049760
main() 0x080483c6
useless() 0x08049744
final malloc() 0x006be166
address range ~232
FF
00
Stack
Text
Data
Heap
08
80
not drawn to scale
malloc() is dynamically linked
address determined at runtime

## Slide 6: Internet Worm
These characteristics of the traditional IA32 Linux memory layout provide opportunities for malicious programs
  Stack grows “backwards” in memory
  Data and instructions both stored in the same memory
November, 1988
  Internet Worm attacks thousands of Internet hosts.
  How did it happen?
The Internet Worm was based on stack buffer overflow exploits!
  Many Unix functions do not check argument sizes
  Allows target buffers to overflow
Notes: http://en.wikipedia.org/wiki/Morris_worm

## Slide 7: String Library Code
Implementation of Unix function gets()
  What could go wrong in this code?
/* Get string from stdin */
char *gets(char *dest) { int c = getchar();
char *p = dest;
while (c != EOF && c != '\n') {
*p++ = c;
c = getchar();
}
*p = '\0';
return dest;
}

## Slide 8: String Library Code
Implementation of Unix function gets()
  No way to specify limit on number of characters to read
Similar problems with other Unix functions
  strcpy: Copies string of arbitrary length
  scanf, fscanf, sscanf, when given %s conversion specification
/* Get string from stdin */
char *gets(char *dest) { int c = getchar();
char *p = dest;
while (c != EOF && c != '\n') {
*p++ = c;
c = getchar();
}
*p = '\0';
return dest;
}
Notes: The man page for gets(3) now says “BUGS: Never use gets().”

## Slide 9: Vulnerable Buffer Code
int main() { printf("Type a string:"); echo(); return 0; }
/* Echo Line */ void echo() { char buf[4]; /* Way too small! */ gets(buf); puts(buf); }
unix>./bufdemo
Type a string:1234567
1234567
unix>./bufdemo
Type a string:12345678
Segmentation Fault
unix>./bufdemo
Type a string:123456789ABC
Segmentation Fault

## Slide 10: Buffer Overflow Disassembly
080484f0 <echo>:
80484f0: 55 push %ebp
80484f1: 89 e5 mov %esp,%ebp
80484f3: 53 push %ebx
80484f4: 8d 5d f8 lea 0xfffffff8(%ebp),%ebx
80484f7: 83 ec 14 sub $0x14,%esp
80484fa: 89 1c 24 mov %ebx,(%esp)
80484fd: e8 ae ff ff ff call 80484b0 <gets>
8048502: 89 1c 24 mov %ebx,(%esp)
8048505: e8 8a fe ff ff call 8048394 <puts@plt>
804850a: 83 c4 14 add $0x14,%esp
804850d: 5b pop %ebx
804850e: c9 leave
804850f: c3 ret
80485f2: e8 f9 fe ff ff call 80484f0 <echo>
80485f7: 8b 5d fc mov 0xfffffffc(%ebp),%ebx
80485fa: c9 leave
80485fb: 31 c0 xor %eax,%eax
80485fd: c3 ret
Notes: 0xfffffffc = -4
0xfffffff8 = -8
Why subtract 20 bytes from %esp? So that after call instruction, echo’s stack frame will occupy 4 + 4 + 20 + 4 = 32 bytes (16-byte aligned)

## Slide 11: Buffer Overflow Stack
echo:
pushl %ebp # Save %ebp on stack
movl %esp, %ebp
pushl %ebx # Save %ebx
leal -8(%ebp),%ebx # Compute buf as %ebp-8
subl $20, %esp # Allocate stack space
movl %ebx, (%esp) # Push buf addr on stack
call gets # Call gets
. . .
/* Echo Line */ void echo() { char buf[4]; /* Way too small! */ gets(buf); puts(buf); }
Return Address
Saved %ebp
%ebp
Stack Frame
for main
[3]
[2]
[1]
[0]
buf
Before call to gets
Saved %ebx
buf
Notes: Why subtract 20 bytes from %esp? So that after call instruction, echo’s stack frame will occupy 4 + 4 + 20 + 4 = 32 bytes (16-byte aligned)

## Slide 12: Buffer Overflow Stack Example
80485f2: call 80484f0 <echo>
80485f7: mov 0xfffffffc(%ebp),%ebx # Return Point
0xffffc638
buf
0xffffc658
Return Address
Saved %ebp
Stack Frame
for main
[3]
[2]
[1]
[0]
Stack Frame
for main
xx
xx
xx
xx
buf
58
c6
ff
ff
f7
85
04
08
Before call to gets
Before call to gets
Saved %ebx
Saved %ebx
buf
0xffffc630
Notes: 0xfffffffc = -4

## Slide 13: Buffer Overflow Example #1
Overflow buf, and corrupt saved %ebx, but no problem
0xffffc638
0xffffc658
Stack Frame
for main
34
33
32
31
buf
58
c6
ff
ff
f7
85
04
08
Input 1234567
00
37
36
35
buf
Stack Frame
for main
xx
xx
xx
xx
Before call to gets
Saved %ebx
58
c6
ff
ff
f7
85
04
08
0xffffc638
0xffffc658
0xffffc630
0xffffc630

## Slide 14: Buffer Overflow Example #2
Frame pointer corrupted
. . .
804850a: 83 c4 14 add $0x14,%esp # deallocate space
804850d: 5b pop %ebx # restore %ebx
804850e: c9 leave # movl %ebp, %esp; popl %ebp
804850f: c3 ret # Return
0xffffc638
0xffffc658
Stack Frame
for main
34
33
32
31
buf
58
c6
ff
00
f7
85
04
08
Input 12345678
38
37
36
35
buf
Stack Frame
for main
xx
xx
xx
xx
Before call to gets
Saved %ebx
58
c6
ff
ff
f7
85
04
08
0xffffc638
0xffffc658
0xffffc630
0xffffc630
Notes: [slide 10: code for main() that uses %ebp]

## Slide 15: Buffer Overflow Example #3
Return address corrupted
080485f2: call 80484f0 <echo>
080485f7: mov 0xfffffffc(%ebp),%ebx # Return Point
0xffffc638
0xffffc658
Stack Frame
for main
34
33
32
31
buf
43
42
41
39
f7
85
04
00
Input 123456789ABC
38
37
36
35
buf
Stack Frame
for main
xx
xx
xx
xx
Before call to gets
Saved %ebx
58
c6
ff
ff
f7
85
04
08
0xffffc638
0xffffc658
0xffffc630
0xffffc630

## Slide 16: Malicious Use of Buffer Overflow
Input string contains byte representation of executable code
Overwrite return address A with address of buffer (need to know B)
When bar() executes ret, will jump to exploit code (instead of A)
int bar() {
char buf[64];
gets(buf);
...
return ...;
}
void foo(){
bar();
...
}
Stack after call to gets()
B (was A)
return address A
foo stack frame
bar stack frame
B
exploit
code
pad
data written
by gets()

## Slide 17: Exploits Based on Buffer Overflows
Buffer overflow bugs allow remote machines to execute arbitrary code on victim machines
Internet worm
  Early versions of the finger server (fingerd) used gets() to read the argument sent by the client:
    finger droh@cs.cmu.edu
  Worm attacked fingerd server by sending phony argument:
    finger “exploit-code padding new-return-address”
    exploit code: executed a root shell on the victim machine with a direct TCP connection to the attacker

## Slide 18: Avoiding Overflow Vulnerability
Use library routines that limit string lengths
  fgets instead of gets (second argument to fgets sets limit)
  strncpy instead of strcpy
  Don’t use scanf with %s conversion specification
    Use fgets to read the string
    Or use %ns where n is a suitable integer
/* Echo Line */ void echo() { char buf[4]; /* Way too small! */ fgets(buf, 4, stdin); puts(buf); }

## Slide 19: System-Level Protections
Randomized stack offsets
  At start of program, allocate random amount of space on stack
  Makes it difficult for exploit to predict beginning of inserted code
Use techniques to detect stack corruption
Nonexecutable code segments
  Only allow code to execute from “text” sections of memory
  Do NOT execute code in stack, data, or heap regions
  Hardware support needed
FF
00
Stack
Text
Data
Heap
08
not drawn to scale