## Slide 1: The Hardware/Software Interface CSE351 Winter 2013
Virtual Memory I

## Slide 2: Roadmap
car *c = malloc(sizeof(car));
c->miles = 100;
c->gals = 17;
float mpg = get_mpg(c);
free(c);
Car c = new Car();
c.setMiles(100);
c.setGals(17);
float mpg = c.getMPG();
get_mpg:
pushq %rbp
movq %rsp, %rbp
...
popq %rbp
ret
Java:
C:
Assembly language:
Machine code:
0111010000011000
100011010000010000000010
1000100111000010
110000011111101000011111
Computer system:
OS:
Data & addressing
Integers & floats
Machine code & C
x86 assembly programming
Procedures & stacks
Arrays & structs
Memory & caches
Processes
Virtual memory
Memory allocation
Java vs. C

## Slide 3: Virtual Memory (VM)
Overview and motivation
VM as tool for caching
Address translation
VM as tool for memory management
VM as tool for memory protection

## Slide 4: Processes
Definition: A process is an instance of a running program
  One of the most important ideas in computer science
  Not the same as “program” or “processor”
Process provides each program with two key abstractions:
  Logical control flow
    Each process seems to have exclusive use of the CPU
  Private virtual address space
    Each process seems to have exclusive use of main memory
How are these illusions maintained?
  Process executions interleaved (multi-tasking) – last time
  Address spaces managed by virtual memory system – today!

## Slide 5: Virtual Memory (Previous Lectures)
Programs refer to virtual memory addresses
  movl (%ecx),%eax
  Conceptually memory is just a very large array of bytes
  Each byte has its own address
  System provides address space private to particular “process”
Allocation: Compiler and run-time system
  Where different program objects should be stored
  All allocation within single virtual address space
What problems does virtual memory solve?
FF∙∙∙∙∙∙F
00∙∙∙∙∙∙0

## Slide 6: Problem 1: How Does Everything Fit?
64-bit addresses:
16 Exabyte
Physical main memory:
Few Gigabytes
?
And there are many processes ….

## Slide 7: Problem 2: Memory Management
Physical main memory
What goes where?
stack
heap
.text
.data
…
Process 1
Process 2
Process 3
…
Process n
x

## Slide 8: Problem 3: How To Protect
Physical main memory
Process i
Process j
Problem 4: How To Share?
Physical main memory
Process i
Process j

## Slide 9: How would you solve those problems?

## Slide 10: Indirection
“Any problem in computer science can be solved by adding another level of indirection”
Without Indirection
With Indirection
Name
Thing
Name
Thing
Thing
Notes: Quote attributed to David Wheeler or Butler Lampson (http://en.wikipedia.org/wiki/Butler_Lampson)

## Slide 11: Indirection
Indirection: the ability to reference something using a name, reference, or container instead the value itself. A flexible mapping between a name and a thing allows changing the thing without notifying holders of the name.
Without Indirection
With Indirection
Examples: Domain Name Service (DNS) name->IP address, phone system (e.g., cell phone number portability), snail mail (e.g., mail forwarding), 911 (routed to local office), DHCP, call centers that route calls to available operators, etc.
Name
Thing
Name
Thing
Thing

## Slide 12: Solution: Level Of Indirection
Each process gets its own private virtual address space
Solves the previous problems
Physical memory
Virtual memory
Virtual memory
Process 1
Process n
mapping

## Slide 13: Address Spaces
Virtual address space: Set of N = 2n virtual addresses {0, 1, 2, 3, …, N-1}
Physical address space: Set of M = 2m physical addresses (n > m) {0, 1, 2, 3, …, M-1}
Every byte in main memory: one physical address; zero, one, or more virtual addresses

## Slide 14: Mapping
Virtual Address
Physical Memory
Disk
A virtual address can be mapped to either physical memory or disk.

## Slide 15: A System Using Physical Addressing
Used in “simple” systems like embedded microcontrollers in devices like cars, elevators, and digital picture frames
0:
1:
M-1:
Main memory
CPU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
4

## Slide 16: A System Using Virtual Addressing
Used in all modern desktops, laptops, servers
One of the great ideas in computer science
0:
1:
M-1:
Main memory
MMU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
CPU
Virtual address
(VA)
CPU Chip
4
4100

## Slide 17: VM and the Memory Hierarchy
Think of virtual memory as an array of N = 2n contiguous bytes stored on a disk
Then physical main memory (DRAM) is used as a cache for the virtual memory array
  The cache blocks are called pages (size is P = 2p bytes)
PP 2m-p-1
Physical memory
Empty
Empty
Uncached
VP 0
VP 1
VP 2n-p-1
Virtual memory
Unallocated
Cached
Uncached
Unallocated
Cached
Uncached
PP 0
PP 1
Empty
Cached
0
N-1
M-1
0
Virtual pages (VPs)
stored on disk
Physical pages (PPs)
cached in DRAM

## Slide 18: Memory Hierarchy: Core 2 Duo
Disk
Main Memory
L2 unified cache
L1
I-cache
L1
D-cache
CPU
Reg
2 B/cycle
8 B/cycle
16 B/cycle
1 B/30 cycles
Throughput:
Latency:
100 cycles
14 cycles
3 cycles
millions
~4 MB
32 KB
~4 GB
~500 GB
Not drawn to scale
L1/L2 cache: 64 B blocks
Miss penalty (latency): 33x
Miss penalty (latency): 10,000x

## Slide 19: DRAM Cache Organization
DRAM cache organization driven by the enormous miss penalty
  DRAM is about 10x slower than SRAM
  Disk is about 10,000x slower than DRAM
    (for first byte; faster for next byte)
Consequences?
  Block size?
  Associativity?
  Write-through or write-back?

## Slide 20: DRAM Cache Organization
DRAM cache organization driven by the enormous miss penalty
  DRAM is about 10x slower than SRAM
  Disk is about 10,000x slower than DRAM
    (for first byte; faster for next byte)
Consequences
  Large page (block) size: typically 4-8 KB, sometimes 4 MB
  Fully associative
    Any VP can be placed in any PP
    Requires a “large” mapping function – different from CPU caches
  Highly sophisticated, expensive replacement algorithms
    Too complicated and open-ended to be implemented in hardware
  Write-back rather than write-through

## Slide 21: Indexing into the “DRAM Cache”
How do we perform the VA -> PA translation?
0:
1:
M-1:
Main memory
MMU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
CPU
Virtual address
(VA)
CPU Chip
4
4100

## Slide 22: Address Translation: Page Tables
A page table (PT) is an array of page table entries (PTEs) that maps virtual pages to physical pages.
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory (disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
  How many page tables are in the system?
  One per process

## Slide 23: Address Translation With a Page Table
Virtual page number (VPN)
Virtual page offset (VPO)
Physical page number (PPN)
Physical page offset (PPO)
Virtual address (VA)
Physical address (PA)
Valid
Physical page number (PPN)
Page table base register
(PTBR)
Page table
Page table address
for process
Valid bit = 0:
page not in memory
(page fault)
In most cases, the hardware (the MMU) can perform this translation on its own, without software assistance
Notes: PTBR is another name for control register 3 (CR3) in x86: http://en.wikipedia.org/wiki/Control_register#CR3

## Slide 24: Page Hit
Page hit: reference to VM byte that is in physical memory
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 25: Page Fault
Page fault: reference to VM byte that is NOT in physical memory
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address
What happens when a page fault occurs?

## Slide 26: Fault Example: Page Fault
User writes to memory location
That portion (page) of user’s memory is currently on disk
Page handler must load page into physical memory
Returns to faulting instruction: mov is executed again!
Successful on second try
int a[1000];
main ()
{
a[500] = 13;
}
80483b7: c7 05 10 9d 04 08 0d movl $0xd,0x8049d10
User Process
OS
exception: page fault
Create page and
load into memory
returns
movl

## Slide 27: Handling Page Fault
Page miss causes page fault (an exception)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 28: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 29: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 30: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
Offending instruction is restarted: page hit!
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 31: Why does it work?

## Slide 32: Why does it work? Locality
Virtual memory works well because of locality
  Same reason that L1 / L2 / L3 caches work
The set of virtual pages that a program is “actively” accessing at any point in time is called its working set
  Programs with better temporal locality will have smaller working sets
If (working set size < main memory size):
  Good performance for one process after compulsory misses
If (SUM(working set sizes) > main memory size):
  Thrashing: Performance meltdown where pages are swapped (copied) in and out continuously