## Slide 1: Roadmap
car *c = malloc(sizeof(car));
c->miles = 100;
c->gals = 17;
float mpg = get_mpg(c);
free(c);
Car c = new Car();
c.setMiles(100);
c.setGals(17);
float mpg = c.getMPG();
get_mpg:
pushq %rbp
movq %rsp, %rbp
...
popq %rbp
ret
Java:
C:
Assembly language:
Machine code:
0111010000011000
100011010000010000000010
1000100111000010
110000011111101000011111
Computer system:
OS:
Memory & data
Integers & floats
Machine code & C
x86 assembly
Procedures & stacks
Arrays & structs
Memory & caches
Processes
Virtual memory
Memory allocation
Java vs. C

## Slide 2: Next x86 topics
x86 basics: registers
Move instructions, registers, and operands
Memory addressing modes
swap example
Arithmetic operations

## Slide 3: What Is A Register (again)?
A location in the CPU that stores a small amount of data, which can be accessed very quickly (once every clock cycle)
Registers have names, not addresses.
Registers are at the heart of assembly programming
  They are a precious commodity in all architectures, but especially x86

## Slide 4: x86-64 Integer Registers – 64 bits wide
%rsp
  Can reference low-order 4 bytes (also low-order 1 & 2 bytes)
%eax
%ebx
%ecx
%edx
%esi
%edi
%esp
%ebp
%r8d
%r9d
%r10d
%r11d
%r12d
%r13d
%r14d
%r15d
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp
Notes: Why is %rbp now general-purpose in x86-64? http://www.codemachine.com/article_x64deepdive.html

## Slide 5: Some History: IA32 Registers – 32 bits wide
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp
%ax
%cx
%dx
%bx
%si
%di
%sp
%bp
%ah
%ch
%dh
%bh
%al
%cl
%dl
%bl
16-bit virtual registers
(backwards compatibility)
general purpose
accumulate
counter
data
base
source
index
destination
index
stack
pointer
base
pointer
Name Origin
(mostly obsolete)

## Slide 6: Assembly Data Types
“Integer” data of 1, 2, 4, or 8 bytes
  Data values
  Addresses (untyped pointers)
Floating point data of 4, 8, or 10 bytes
No aggregate types such as arrays or structures
  Just contiguously allocated bytes in memory

## Slide 7: Three Basic Kinds of Instructions
Transfer data between memory and register
  Load data from memory into register
    %reg = Mem[address]
  Store register data into memory
    Mem[address] = %reg
Perform arithmetic function on register or memory data
  c = a + b; z = x << y; i = h & g;
Transfer control: what instruction to execute next
  Unconditional jumps to/from procedures
  Conditional branches
    Remember: memory is indexed just like an array[] of bytes!

## Slide 8: Moving Data
Moving Data
  movq Source, Dest:
Operand Types
  Immediate: Constant integer data
    Example: $0x400, $-533
    Like C constant, but prefixed with ‘$’
    Encoded with 1, 2, or 4 bytes
  Register: One of 16 integer registers
    Example: %rax, %r13
    But %rsp reserved for special use
    Others have special uses for particular instructions
  Memory: 8 consecutive bytes of memory at address given by register
    Simplest example: (%rax)
    Various other “address modes”
%rax
%rcx
%rdx
%rbx
%rsi
%rdi
%rsp
%rbp
%rN

## Slide 9: movq, movl, movw, movb
Moving Data
  movx Source, Dest
  x is one of {b, w, l, q}
  movq Source, Dest:
  Move 8-byte “quad word”
  movl Source, Dest:
  Move 4-byte “long word”
  movw Source, Dest:
  Move 2-byte “word”
  movb Source, Dest:
  Move 1-byte “byte”
Lots of these in typical code
confusing historical terms…
not the current machine word size

## Slide 10: movq Operand Combinations
Cannot do memory-memory transfer with a single instruction
movq
Imm
Reg
Mem
Reg
Mem
Reg
Mem
Reg
Source
Dest
C Analog
movq $0x4,%rax
var_a = 0x4;
movq $-147,(%rax)
*p_a = -147;
movq %rax,%rdx
var_d = var_a;
movq %rax,(%rdx)
*p_d = var_a;
movq (%rax),%rdx
var_d = *p_a;
Src,Dest
How would you do it?

## Slide 11: Memory vs. registers
What is the main difference?
Addresses vs. Names
Big vs. Small

## Slide 12: Memory Addressing Modes: Basic
Indirect (R) Mem[Reg[R]]
  Register R specifies the memory address
  Aha! Pointer dereferencing in C movq (%rcx),%rax
Displacement D(R) Mem[Reg[R]+D]
  Register R specifies a memory address
    (e.g. the start of some memory region)
  Constant displacement D specifies the offset from that address movq 8(%rbp),%rdx

## Slide 13: Example of Basic Addressing Modes
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret

## Slide 14: Understanding Swap()
%rdi
%rsi
%rax
%rdx
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
Memory
Register Value
%rdi xp
%rsi yp
%rax t0
%rdx t1
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
Registers

## Slide 15: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 16: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 17: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 18: Understanding Swap()
456
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 19: Understanding Swap()
456
123
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 20: Memory Addressing Modes: Basic
Indirect (R) Mem[Reg[R]]
  Register R specifies the memory address
  Aha! Pointer dereferencing in C movq (%rcx),%rax
Displacement D(R) Mem[Reg[R]+D]
  Register R specifies a memory address
    (e.g. the start of some memory region)
  Constant displacement D specifies the offset from that address movq 8(%rbp),%rdx

## Slide 21: Complete Memory Addressing Modes
Remember, the addresses used for accessing memory in mov (and other) instructions can be computed in several different ways
Most General Form:
D(Rb,Ri,S) Mem[Reg[Rb] + S*Reg[Ri] + D]
  D: Constant “displacement” value represented in 1, 2, or 4 bytes
  Rb: Base register: Any of the 16 integer registers
  Ri: Index register: Any, except for %rsp
  S: Scale: 1, 2, 4, or 8 (why these numbers?)
Special Cases: can use any combination of D, Rb, Ri and S
(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]] (S=1, D=0)
D(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]+D] (S=1)
(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]] (D=0)
Notes: See figure 3.3 in 3e textbook

## Slide 22: Address Computation Examples
%rdx
%rcx
0xf000
0x0100
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]]
D(,Ri,S) Mem[S*Reg[Ri]+D]
(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]]
D(Rb) Mem[Reg[Rb] +D]

## Slide 23: Address Computation Examples
%rdx
%rcx
0xf000
0x0100
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]]
D(,Ri,S) Mem[S*Reg[Ri]+D]
(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]]
D(Rb) Mem[Reg[Rb] +D]
0xf000 + 0x8 0xf008
0xf000 + 0x100 0xf100
0xf000 + 4*0x100 0xf400
2*0xf000 + 0x80 0x1e080

## Slide 24: Address Computation Instruction
leaq Src,Dest
  Src is address expression (Any of the formats we just discussed!)
  Dest is a register
  Set Dest to address computed by expression
    (lea stands for load effective address)
  Example: leaq (%rdx,%rcx,4), %rax
Uses
  Computing addresses without a memory reference
    E.g., translation of p = &x[i];
  Computing arithmetic expressions of the form x + k*i
    k = 1, 2, 4, or 8

## Slide 25: leaq vs. movq example
0x400
0xf
0x8
0x10
0x1
%rax
%rbx
%rcx
%rdx
0x4
0x100
Registers
Memory
leaq (%rdx,%rcx,4), %rax
movq (%rdx,%rcx,4), %rbx
leaq (%rdx), %rdi
movq (%rdx), %rsi
0x120
0x118
0x110
0x108
0x100
Address
%rdi
%rsi

## Slide 26: leaq vs. movq example (solution)
0x400
0xf
0x8
0x10
0x1
%rax
%rbx
%rcx
%rdx
0x4
0x100
Registers
Memory
leaq (%rdx,%rcx,4), %rax
movq (%rdx,%rcx,4), %rbx
leaq (%rdx), %rdi
movq (%rdx), %rsi
0x120
0x118
0x110
0x108
0x100
Address
%rdi
%rsi
0x110
0x8
0x100
0x1

## Slide 27: Some Arithmetic Operations
Two Operand (Binary) Instructions:
  Format Computation
  addq Src,Dest Dest = Dest + Src
  subq Src,Dest Dest = Dest - Src
  imulq Src,Dest Dest = Dest * Src
  shlq Src,Dest Dest = Dest << Src Also called salq
  sarq Src,Dest Dest = Dest >> Src Arithmetic
  shrq Src,Dest Dest = Dest >> Src Logical
  xorq Src,Dest Dest = Dest ^ Src
  andq Src,Dest Dest = Dest & Src
  orq Src,Dest Dest = Dest | Src
Watch out for argument order! (especially subq)
No distinction between signed and unsigned int (why?)
  except arithmetic vs. logical shift right

## Slide 28: Some Arithmetic Operations
One Operand (Unary) Instructions
  incq Dest Dest = Dest + 1 increment
  decq Dest Dest = Dest – 1 decrement
  negq Dest Dest = -Dest negate
  notq Dest Dest = ~Dest bitwise complement
See textbook section 3.5.5 for more instructions: mulq, cqto, idivq, divq

## Slide 29: The leaq Instruction
“lea” stands for load effective address
  Example: leaq (%rdx,%rcx,4), %rax
Does the leaq instruction go to memory?
“leaq – it just does math”
NO

## Slide 30: Using leaq for Arithmetic Expressions
Interesting Instructions
  leaq: address computation
  salq: shift
  imulq: multiplication
    But, only used once instead of twice
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax
addq %rdx, %rax
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx
leaq 4(%rdi,%rdx), %rcx
imulq %rcx, %rax
ret

## Slide 31: Understanding arith
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax # t1
addq %rdx, %rax # t2
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx # t4
leaq 4(%rdi,%rdx), %rcx # t5
imulq %rcx, %rax # rval
ret
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | t1, t2, rval
%rdx | t4
%rcx | t5

## Slide 32: Topics: control flow
Condition codes
Conditional and unconditional branches
Loops

## Slide 33: Conditionals and Control Flow
A conditional branch is sufficient to implement most control flow constructs offered in higher level languages
  if (condition) then {...} else {…}
  while (condition) {…}
  do {…} while (condition)
  for (initialization; condition; iterative) {...}
Unconditional branches implement some related control flow constructs
  break, continue
In x86, we’ll refer to branches as “jumps” (either conditional or unconditional)

## Slide 34: Jumping
jX Instructions
  Jump to different part of code depending on condition codes
  Takes address as argument
jX | Condition | Description
jmp | 1 | Unconditional
je | ZF | Equal / Zero
jne | ~ZF | Not Equal / Not Zero
js | SF | Negative
jns | ~SF | Nonnegative
jg | ~(SF^OF)&~ZF | Greater (Signed)
jge | ~(SF^OF) | Greater or Equal (Signed)
jl | (SF^OF) | Less (Signed)
jle | (SF^OF)¦ZF | Less or Equal (Signed)
ja | ~CF&~ZF | Above (unsigned)
jb | CF | Below (unsigned)

## Slide 35: Processor State (x86-64, Partial)
Information about currently executing program
  Temporary data ( %rax, … )
  Location of runtime stack ( %rsp )
  Location of current code control point ( %rip, … )
  Status of recent tests ( CF, ZF, SF, OF )
%rip
Registers
Current stack top
Instruction pointer
CF
ZF
SF
OF
Condition codes
%rsp
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 36: Condition Codes (Implicit Setting)
Implicitly set by arithmetic operations
  (think of it as side effect)
  Example: addq Src,Dest ↔ t = a+b
  Single bit registers
  CF Carry Flag (for unsigned) SF Sign Flag (for signed)
  ZF Zero Flag OF Overflow Flag (for signed)
  CF set if carry out from most significant bit (unsigned overflow)
  ZF set if t == 0
  SF set if t < 0 (as signed)
  OF set if two’s-complement (signed) overflow (a>0 && b>0 && t<0) || (a<0 && b<0 && t>=0)
Not set by leaq instruction (beware!)

## Slide 37: Condition Codes (Explicit Setting: Compare)
Explicit Setting by Compare Instruction
  cmpq Src2,Src1
  cmpq b,a like computing a-b without setting destination
  Single bit registers
  CF Carry Flag (for unsigned) SF Sign Flag (for signed)
  ZF Zero Flag OF Overflow Flag (for signed)
  CF set if carry out from most significant bit (used for unsigned comparisons)
  ZF set if a == b
  SF set if (a-b) < 0 (as signed)
  OF set if two’s complement (signed) overflow (a>0 && b<0 && (a-b)<0) || (a<0 && b>0 && (a-b)>0)
Notes: Src2 can be register, memory, or immediate; Src1 can be register or immediate

## Slide 38: Condition Codes (Explicit Setting: Test)
Explicit Setting by Test instruction
  testq Src2,Src1 testq b,a like computing a & b without setting destination
    Sets condition codes based on value of Src1 & Src2
    Useful to have one of the operands be a mask
  Single bit registers
  CF Carry Flag (for unsigned) SF Sign Flag (for signed)
  ZF Zero Flag OF Overflow Flag (for signed)
  ZF set if a&b == 0
  SF set if a&b < 0
  testq %rax, %rax
    Sets SF and ZF, check if rax is +,0,-

## Slide 39: Reading Condition Codes
SetX Instructions
  Set a low-order byte to 0 or 1 based on combinations of condition codes
  Does not alter remaining 7 bytes
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF^OF)&~ZF | Greater (Signed)
setge | ~(SF^OF) | Greater or Equal (Signed)
setl | (SF^OF) | Less (Signed)
setle | (SF^OF)¦ZF | Less or Equal (Signed)
seta | ~CF&~ZF | Above (unsigned)
setb | CF | Below (unsigned)

## Slide 40: x86-64 Integer Registers
%rsp
  Can reference low-order byte
%al
%bl
%cl
%dl
%sil
%dil
%spl
%bpl
%r8b
%r9b
%r10b
%r11b
%r12b
%r13b
%r14b
%r15b
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 41: Reading Condition Codes (Cont.)
cmpq %rsi, %rdi # Compare x:y
  setg %al # Set when >
  movzbl %al, %eax # Zero rest of %rax
ret
SetX Instructions:
  Set single byte to 0 or 1 based on combination of condition codes
  Operand is one of the byte registers (eg. al, dl) or a byte in memory
Set instruction does not alter remaining bytes in register
  Typically use movzbl to finish job - Sets upper 32 bits to zero
    Aside: In x86-64, any instruction that generates a 32-bit value for a register also sets the high-order portion of the register to 0.
int gt (long x, long y)
{
return x > y;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
What does each of these instructions do?
Notes: The order of the cmpq operands is backwards, unfortunately; first we do cmpq y, x, but then the setg is “true” if x > y. So, think of the cmpq as performing x – y, like a sub instruction, and then it makes more sense.

## Slide 42: Reading Condition Codes (Cont.)
cmpq %rsi, %rdi # Compare x:y
  setg %al # al = x > y
  movzbl %al, %eax # Zero rest of %rax
ret
SetX Instructions:
  Set single byte to 0 or 1 based on combination of condition codes
  Operand is one of the byte registers (eg. al, dl) or a byte in memory
Set instruction does not alter remaining bytes in register
  Typically use movzbl to finish job - Sets upper 32 bits to zero
    Aside: In x86-64, any instruction that generates a 32-bit value for a register also sets the high-order portion of the register to 0.
int gt (long x, long y)
{
return x > y;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
Notes: The order of the cmpq operands is backwards, unfortunately; first we do cmpq y, x, but then the setg is “true” if x > y. So, think of the cmpq as performing x – y, like a sub instruction, and then it makes more sense.

## Slide 43: Aside: movz and movs examples
    movzbl Src, RegisterDest Move with zero extension
    movsbl Src, RegisterDest Move with sign extension
    For use when copying a smaller source value to a larger destination
    Source can be memory or register; Destination must be a register
    movzSD – fills out remaining bytes of the destination with zeroes
    movsSD – fills out remaining bytes of the destination by sign extension, replicating the most significant bit of the source
    S – can be b=byte, w=16-bit word
    D – can be w=16-bit word, l=32-bit long word, q=64-bit quad word
    Note: In x86-64, any instruction that generates a 32-bit (long word) value for a register also sets the high-order portion of the register to 0.
    Good example in the “Aside” on p. 184 in 3e CS-APP (our text)

## Slide 44: Jumping
jX Instructions
  Jump to different part of code depending on condition codes
  Takes address as argument
jX | Condition | Description
jmp | 1 | Unconditional
je | ZF | Equal / Zero
jne | ~ZF | Not Equal / Not Zero
js | SF | Negative
jns | ~SF | Nonnegative
jg | ~(SF^OF)&~ZF | Greater (Signed)
jge | ~(SF^OF) | Greater or Equal (Signed)
jl | (SF^OF) | Less (Signed)
jle | (SF^OF)¦ZF | Less or Equal (Signed)
ja | ~CF&~ZF | Above (unsigned)
jb | CF | Below (unsigned)

## Slide 45: Conditional Branch Example (Old Style)
long absdiff
(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
absdiff:
cmpq %rsi, %rdi # x:y
jle .L4
movq %rdi, %rax
subq %rsi, %rax
ret
.L4: # x <= y
movq %rsi, %rax
subq %rdi, %rax
ret
Generation
  gcc –Og -S –fno-if-conversion control.c
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value

## Slide 46: Expressing with Goto Code
long absdiff
(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
long absdiff_j
(long x, long y)
{
long result;
int ntest = x <= y;
if (ntest) goto Else;
result = x-y;
goto Done;
Else:
result = y-x;
Done:
return result;
}
C allows “goto” as means of transferring control
  Closer to machine-level programming style
Generally considered bad coding style

## Slide 47: General Conditional Expression Translation (Using Branches)
C Code
val = Test ? Then-Expr : Else-Expr;
Goto Version
ntest = !Test;
if (ntest) goto Else;
val = Then_Expr;
goto Done;
Else:
val = Else_Expr;
Done:
. . .
  Test is expression returning integer
    = 0 interpreted as false
    0 interpreted as true
  Create separate code regions for then & else expressions
  Execute appropriate one
result = x>y ? x-y : y-x;
if (Test)
val = Then-Expr;
else
val = Else-Expr;
Example:

## Slide 48: Using Conditional Moves
C Code
val = Test
? Then_Expr
: Else_Expr;
Goto Version
result = Then_Expr;
else_val = Else_Expr;
nt = !Test;
if (nt) result = else_val;
return result;
Conditional Move Instructions
  cmovC src, dest
  Move value from src to dest if condition C holds
  Instruction supports:
    if (Test) Dest  Src
  Supported in post-1995 x86 processors
  GCC tries to use them
    But, only when known to be safe
Why is this useful?
  Branches are very disruptive to instruction flow through pipelines
  Conditional moves do not require control transfer

## Slide 49: Conditional Move Example
absdiff:
movq %rdi, %rax # x
subq %rsi, %rax # result = x-y
movq %rsi, %rdx
subq %rdi, %rdx # else_val = y-x
cmpq %rsi, %rdi # x:y
cmovle %rdx, %rax # if <=, result = else_val
ret
long absdiff
(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
Notes: More efficient than conditional branching (simple control flow)
But overhead: both branches are evaluated
cmov instructions available in IA32 since 1995, but not used by gcc unless –march=686 flag used. They are used regularly in x86-64.

## Slide 50: Bad Cases for Conditional Move
Expensive Computations
Both values get computed
Only makes sense when computations are very simple
val = Test(x) ? Hard1(x) : Hard2(x);
Risky Computations
Both values get computed
May have undesirable effects
val = p ? *p : 0;
Computations with side effects
Both values get computed
Must be side-effect free
val = x > 0 ? x*=7 : x+=3;

## Slide 51: Compiling Loops
How to compile other loops should be straightforward
  The only slightly tricky part is to be sure where the conditional branch occurs: top or bottom of the loop
while ( sum != 0 ) {
<loop body>
}
loopTop: cmpl $0, %eax
je loopDone
<loop body code>
jmp loopTop
loopDone:
Machine code:
C/Java code:

## Slide 52: Do-While Loop Example
C Code
long pcount_do(unsigned long x) {
long result = 0;
do {
result += x & 0x1;
x >>= 1;
} while (x);
return result;
}
Goto Version
long pcount_goto(unsigned long x) {
long result = 0;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
return result;
}
Count number of 1’s in argument x (“popcount”)
Use backward branch to continue looping
Only take branch when “while” condition holds

## Slide 53: Do-While Loop Compilation
Goto Version
movl $0, %eax # result = 0
.L2: # loop:
movq %rdi, %rdx
andl $1, %edx # t = x & 0x1
addq %rdx, %rax # result += t
shrq %rdi # x >>= 1
jne .L2 # if (x) goto loop
rep; ret
long pcount_goto(unsigned long x) {
long result = 0;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
return result;
}
Register | Use(s)
%rdi | Argument x
%rax | result

## Slide 54: General Do-While Loop Translation
C Code
do
Body
while (Test);
Goto Version
loop:
Body
if (Test)
goto loop
Body:
Test returns integer
  = 0 interpreted as false
   0 interpreted as true
{
Statement1;
Statement2;
…
Statementn;
}

## Slide 55: General While Loop - Translation #1
While version
while (Test)
Body
“Jump-to-middle” translation
Used with -Og
Goto Version
goto test;
loop:
Body
test:
if (Test)
goto loop;
done:

## Slide 56: While Loop Example – Translation #1
C Code
long pcount_while
(unsigned long x) {
long result = 0;
while (x) {
result += x & 0x1;
x >>= 1;
}
return result;
}
Jump to Middle Version
long pcount_goto_jtm
(unsigned long x) {
long result = 0;
goto test;
loop:
result += x & 0x1;
x >>= 1;
test:
if(x) goto loop;
return result;
}
Used with -Og
Compare to do-while version of function
Initial goto starts loop at test

## Slide 57: General While Loop - Translation #2
While version
while (Test)
Body
Do-While Version
if (!Test)
goto done;
do
Body
while(Test);
done:
“Do-while” conversion
Used with –O1
Goto Version
if (!Test)
goto done;
loop:
Body
if (Test)
goto loop;
done:

## Slide 58: While Loop Example – Translation #2
C Code
long pcount_while
(unsigned long x) {
long result = 0;
while (x) {
result += x & 0x1;
x >>= 1;
}
return result;
}
Do-While Version
long pcount_goto_dw
(unsigned long x) {
long result = 0;
if (!x) goto done;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
done:
return result;
}
Used with –O1
Compare to do-while version of function
Initial conditional guards entrance to loop

## Slide 59: For Loop Form
for (Init; Test; Update )
Body
General Form
#define WSIZE 8*sizeof(int)
long pcount_for
(unsigned long x)
{
size_t i;
long result = 0;
for (i = 0; i < WSIZE; i++)
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
return result;
}
i = 0
i < WSIZE
i++
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
Init
Test
Update
Body

## Slide 60: For Loop  While Loop
for (Init; Test; Update )
Body
For Version
Init;
while (Test ) {
Body
Update;
}
While Version

## Slide 61: For Loop-While Conversion
long pcount_for_while
(unsigned long x)
{
size_t i;
long result = 0;
i = 0;
while (i < WSIZE)
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
i++;
}
return result;
}
i = 0
i < WSIZE
i++
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
Init
Test
Update
Body

## Slide 62: For Loop Do-While Conversion
C Code
Initial test can be optimized away
long pcount_for
(unsigned long x)
{
size_t i;
long result = 0;
for (i = 0; i < WSIZE; i++)
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
return result;
}
Goto Version
long pcount_for_goto_dw
(unsigned long x) {
size_t i;
long result = 0;
i = 0;
if (!(i < WSIZE))
goto done;
loop:
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
i++;
if (i < WSIZE)
goto loop;
done:
return result;
}
Init
!Test
Body
Update
Test

## Slide 63: Switch Statement Example
Multiple case labels
  Here: 5 & 6
Fall through cases
  Here: 2
Missing cases
  Here: 4
long switch_eg
(long x, long y, long z)
{
long w = 1;
switch(x) {
case 1:
w = y*z;
break;
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
case 5:
case 6:
w -= z;
break;
default:
w = 2;
}
return w;
}

## Slide 64: Jump Table Structure
Code Block
0
Targ0:
Code Block
1
Targ1:
Code Block
2
Targ2:
Code Block
n–1
Targn-1:
•
•
•
Targ0
Targ1
Targ2
Targn-1
•
•
•
Jtab:
target = JTab[x];
goto target;
switch(x) {
case val_0:
Block 0
case val_1:
Block 1
• • •
case val_n-1:
Block n–1
}
Switch Form
Approximate Translation
Jump Table
Jump Targets

## Slide 65: Jump Table Structure
switch(x) {
case 1: <some code>
break;
case 2: <some code>
case 3: <some code>
break;
case 5:
case 6: <some code>
break;
default: <some code>
}
0
1
2
3
4
Jump
Table
Code
Blocks
Memory
We can use the jump table when x <= 6:
if (x <= 6)
target = JTab[x];
goto target;
else
goto default;
C code:
5
6

## Slide 66: Switch Statement Example
Setup:
long switch_eg(long x, long y, long z)
{
long w = 1;
switch(x) {
. . .
}
return w;
}
switch_eg:
movq %rdx, %rcx
cmpq $6, %rdi # x:6
ja .L8
jmp *.L4(,%rdi,8)
What range of values takes default?
Note that w not initialized here
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 67: Switch Statement Example
long switch_eg(long x, long y, long z)
{
long w = 1;
switch(x) {
. . .
}
return w;
}
Indirect jump
Jump table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
Setup:
switch_eg:
movq %rdx, %rcx
cmpq $6, %rdi # x:6
ja .L8 # Use default
jmp *.L4(,%rdi,8) # goto *JTab[x]
jump above
(like jg, but
unsigned)

## Slide 68: Assembly Setup Explanation
Table Structure
  Each target requires 8 bytes
  Base address at .L4
Jumping
  Direct: jmp .L8
  Jump target is denoted by label .L8
  Indirect: jmp *.L4(,%rdi,8)
  Start of jump table: .L4
  Must scale by factor of 8 (addresses are 8 bytes)
  Fetch target from effective Address .L4 + x*8
    Only for 0 ≤ x ≤ 6
Jump table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6

## Slide 69: Jump Table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
Jump table
switch(x) {
case 1: // .L3
w = y*z;
break;
case 2: // .L5
w = y/z;
/* Fall Through */
case 3: // .L9
w += z;
break;
case 5:
case 6: // .L7
w -= z;
break;
default: // .L8
w = 2;
}
declaring data, not instructions
8-byte memory alignment

## Slide 70: Code Blocks (x == 1)
.L3:
movq %rsi, %rax # y
imulq %rdx, %rax # y*z
ret
switch(x) {
case 1: // .L3
w = y*z;
break;
. . .
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 71: Handling Fall-Through
long w = 1;
. . .
switch(x) {
. . .
case 2: // .L5
w = y/z;
/* Fall Through */
case 3: // .L9
w += z;
break;
. . .
}
case 3:
w = 1;
case 2:
w = y/z;
goto merge;
merge:
w += z;

## Slide 72: Code Blocks (x == 2, x == 3)
.L5: # Case 2
movq %rsi, %rax # y in rax
cqto # Div prep
idivq %rcx # y/z
jmp .L6 # goto merge
.L9: # Case 3
movl $1, %eax # w = 1
.L6: # merge:
addq %rcx, %rax # w += z
ret
long w = 1;
. . .
switch(x) {
. . .
case 2: // .L5
w = y/z;
/* Fall Through */
case 3: // .L9
w += z;
break;
. . .
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 73: Code Blocks (x == 5, x == 6, default)
.L7: # Case 5,6
movl $1, %eax # w = 1
subq %rdx, %rax # w -= z
ret
.L8: # Default:
movl $2, %eax # 2
ret
switch(x) {
. . .
case 5: // .L7
case 6: // .L7
w -= z;
break;
default: // .L8
w = 2;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 74: Question
Would you implement this with a jump table?
Probably not:
  Don’t want a jump table with 52001 entries for only 4 cases (too big)
  about 200KB = 200,000 bytes
  text of this switch statement = about 200 bytes
switch(x) {
case 0: <some code>
break;
case 10: <some code>
break;
case 52000: <some code>
break;
default: <some code>
break;
}