## Slide 1: Roadmap
car *c = malloc(sizeof(car));
c->miles = 100;
c->gals = 17;
float mpg = get_mpg(c);
free(c);
Car c = new Car();
c.setMiles(100);
c.setGals(17);
float mpg = c.getMPG();
get_mpg:
pushq %rbp
movq %rsp, %rbp
...
popq %rbp
ret
Java:
C:
Assembly language:
Machine code:
0111010000011000
100011010000010000000010
1000100111000010
110000011111101000011111
Computer system:
OS:
Memory & data
Integers & floats
Machine code & C
x86 assembly
Procedures & stacks
Arrays & structs
Memory & caches
Processes
Virtual memory
Memory allocation
Java vs. C

## Slide 2: Virtual Memory (VM)
Overview and motivation
VM as tool for caching
Address translation
VM as tool for memory management
VM as tool for memory protection

## Slide 3: Again: Processes
Definition: A process is an instance of a running program
  One of the most important ideas in computer science
  Not the same as “program” or “processor”
Process provides each program with two key abstractions:
  Logical control flow
    Each process seems to have exclusive use of the CPU
  Private virtual address space
    Each process seems to have exclusive use of main memory
How are these illusions maintained?
  Process executions interleaved (multi-tasking) – done…
  Address spaces managed by virtual memory system – now!

## Slide 4: Memory as we know it so far… is virtual!
Programs refer to virtual memory addresses
  movl (%ecx),%eax
  Conceptually memory is just a very large array of bytes
  Each byte has its own address
  System provides address space private to particular “process”
Allocation: Compiler and run-time system
  Where different program objects should be stored
  All allocation within single virtual address space
But…
  We probably don’t have exactly 2w bytes of physical memory.
  We certainly don’t have 2w bytes of physical memory for every process.
  We have multiple processes that usually should not interfere with each other, but sometimes should share code or data.
FF∙∙∙∙∙∙F
00∙∙∙∙∙∙0

## Slide 5: Problem 1: How Does Everything Fit?
64-bit virtual addresses can address
several exabytes
(18,446,744,073,709,551,616 bytes)
Physical main memory offers
a few gigabytes
(e.g. 8,589,934,592 bytes)
?
1 virtual address space per process, with many processes…
(Actually, physical memory is smaller than the period at the end of this sentence compared to the virtual address space.)

## Slide 6: Problem 2: Memory Management
Physical main memory
What goes where?
stack
heap
.text
.data
…
Process 1
Process 2
Process 3
…
Process n
x
Each process has…
We have multiple processes:

## Slide 7: Problem 3: How To Protect
Physical main memory
Process i
Process j
Problem 4: How To Share?
Physical main memory
Process i
Process j

## Slide 8: How can we solve these problems?
Fitting a huge address space into a tiny physical memory
Managing the address spaces of multiple processes
Protecting processes from stepping on each other’s memory
Allowing processes to share common parts of memory

## Slide 9: Indirection
“Any problem in computer science can be solved by adding another level of indirection.” –David Wheeler, inventor of the subroutine (a.k.a. procedure)
Without Indirection
With Indirection
Name
Thing
Name
Thing
What if I want to move Thing?
Notes: Quote attributed to David Wheeler or Butler Lampson (http://en.wikipedia.org/wiki/Butler_Lampson)

## Slide 10: Indirection
Indirection: the ability to reference something using a name, reference, or container instead the value itself. A flexible mapping between a name and a thing allows changing the thing without notifying holders of the name.
Without Indirection
With Indirection
Examples of indirection:
  Domain Name Service (DNS): translation from name to IP address
  phone system: cell phone number portability
  snail mail: mail forwarding
  911: routed to local office
  Dynamic Host Configuration Protocol (DHCP): local network address assignment
  call centers: route calls to available operators, etc.
Name
Thing
Name
Thing
Thing

## Slide 11: Indirection in Virtual Memory
Each process gets its own private virtual address space
Solves the previous problems
Physical memory
Virtual memory
Virtual memory
Process 1
Process n
mapping

## Slide 12: Address Spaces
Virtual address space: Set of N = 2n virtual addresses {0, 1, 2, 3, …, N-1}
Physical address space: Set of M = 2m physical addresses (n >= m) {0, 1, 2, 3, …, M-1}
Every byte in main memory has:
  one physical address
  zero, one, or more virtual addresses

## Slide 13: Mapping
P2’s Virtual Address Space
Physical Memory
Disk
A virtual address can be mapped to either physical memory or disk.
P1’s Virtual Address Space

## Slide 14: A System Using Physical Addressing
Used in “simple” systems with (usually) just one process:
  embedded microcontrollers in devices like cars, elevators, and digital picture frames
0:
1:
M-1:
Main memory
CPU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
4

## Slide 15: Feb 25
Announcements
  HW 4 released today
  No class Friday: watch the video assignment and take the quizzes!
Today: virtual memory

## Slide 16: A System Using Virtual Addressing
Physical addresses are completely invisible to programs.
Used in all modern desktops, laptops, servers, smartphones…
One of the great ideas in computer science
0:
1:
M-1:
Main memory
MMU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
CPU
Virtual address
(VA)
CPU Chip
4
4100
Memory Management Unit

## Slide 17: Why Virtual Memory (VM)?
Efficient use of limited main memory (RAM)
  Use RAM as a cache for the parts of a virtual address space
    some non-cached parts stored on disk
    some (unallocated) non-cached parts stored nowhere
  Keep only active areas of virtual address space in memory
    transfer data back and forth as needed
Simplifies memory management for programmers
  Each process gets the same full, private linear address space
Isolates address spaces
  One process can’t interfere with another’s memory
    because they operate in different address spaces
  User process cannot access privileged information
    different sections of address spaces have different permissions

## Slide 18: VM and the Memory Hierarchy
Think of virtual memory as array of N = 2n contiguous bytes.
Pages of virtual memory are usually stored in physical memory, but sometimes spill to disk.
  Pages are another unit of aligned memory (size is P = 2p bytes)
  Each virtual page can be stored in any physical page.
PP 2m-p-1
Physical memory
Empty
Empty
Uncached
VP 0
VP 1
VP 2n-p-1
Virtual memory
Unallocated
Cached
Uncached
Unallocated
Cached
Uncached
PP 0
PP 1
Empty
Cached
0
2n-1
2m-1
0
Virtual pages (VP's)
stored on disk
Physical pages (PP's)
cached in DRAM
Disk

## Slide 19: or: Virtual Memory as DRAM Cache for Disk
Think of virtual memory as an array of N = 2n contiguous bytes stored on a disk.
Then physical main memory is used as a cache for the virtual memory array
  The cache blocks are called pages (size is P = 2p bytes)
PP 2m-p-1
Physical memory
Empty
Empty
Uncached
VP 0
VP 1
VP 2n-p-1
Virtual memory
Unallocated
Cached
Uncached
Unallocated
Cached
Uncached
PP 0
PP 1
Empty
Cached
0
N-1
M-1
0
Virtual pages (VPs)
stored on disk
Physical pages (PPs)
cached in DRAM

## Slide 20: Memory Hierarchy: Core 2 Duo
Disk
Main Memory
L2 unified cache
L1
I-cache
L1
D-cache
CPU
Reg
2 B/cycle
8 B/cycle
16 B/cycle
1 B/30 cycles
Throughput:
Latency:
100 cycles
14 cycles
3 cycles
millions
~4 MB
32 KB
~4 GB
~500 GB
Not drawn to scale
Miss penalty (latency): 33x
Miss penalty (latency): 10,000x
SRAM
Static Random Access Memory
DRAM
Dynamic Random Access Memory

## Slide 21: Virtual Memory Design Consequences
Large page size: typically 4-8 KB, sometimes up to 4 MB
Fully associative
  Any virtual page can be placed in any physical page
  Requires a “large” mapping function – different from CPU caches
Highly sophisticated, expensive replacement algorithms in OS
  Too complicated and open-ended to be implemented in hardware
Write-back rather than write-through

## Slide 22: Address Translation
How do we perform the virtual -> physical address translation?
0:
1:
M-1:
Main memory
MMU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
CPU
Virtual address
(VA)
CPU Chip
4
4100

## Slide 23: Address Translation: Page Tables
A page table is an array of page table entries (PTEs) that maps virtual pages to physical pages.
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory (disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
  How many page tables are in the system?
  One per process
stored in physical memory
managed by HW (MMU), OS

## Slide 24: Address Translation With a Page Table
Virtual page number (VPN)
Virtual page offset (VPO)
Physical page number (PPN)
Physical page offset (PPO)
Virtual address (VA)
Physical address (PA)
Valid
Physical page number (PPN)
Page table base register
(PTBR)
Page table
Page table address
for process
Valid bit = 0:
page not in memory
(page fault)
In most cases, the hardware (the MMU) can perform this translation on its own, without software assistance
This feels familiar…
Notes: PTBR is another name for control register 3 (CR3) in x86: http://en.wikipedia.org/wiki/Control_register#CR3

## Slide 25: Page Hit
Page hit: reference to VM byte that is in physical memory
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 26: Page Fault
Page fault: reference to VM byte that is NOT in physical memory
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address
What happens when a page fault occurs?

## Slide 27: Fault Example: Page Fault
User writes to memory location
That portion (page) of user’s memory is currently on disk
Page fault handler must load page into physical memory
Returns to faulting instruction: mov is executed again!
Successful on second try
int a[1000];
main ()
{
a[500] = 13;
}
80483b7: c7 05 10 9d 04 08 0d movl $0xd,0x8049d10
User Process
OS
exception: page fault
Create page and
load into memory
returns
movl

## Slide 28: Handling Page Fault
Page miss causes page fault (an exception)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 29: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 30: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 31: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
Offending instruction is restarted: page hit!
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 32: Why does VM work on RAM/disk? Locality.
Virtual memory works well for avoiding disk accesses because of locality
  Same reason that L1 / L2 / L3 caches work
The set of virtual pages that a program is “actively” accessing at any point in time is called its working set
If (working set size of one process < main memory size):
  Good performance for one process (after compulsory misses)
But if SUM(working set sizes of all processes) > main memory size:
  Thrashing: Performance meltdown where pages are swapped (copied) between memory and disk continuously. CPU always waiting or paging.
Notes:   Improving a program’s te
  Full quote: “Every problem in computer science can be solved by adding another level of indirection, but that usually will create another problem.”
  mporal locality can lead to a smaller working set (using data in one place in the program rather than many places).

## Slide 33: Simplifying Linking and Loading
Linking
  Each program has similar virtual address space
  Code, stack, and shared libraries always start at the same address
Loading
  execve() allocates virtual pages for .text and .data sections = creates PTEs marked as invalid
  The .text and .data sections are copied, page by page, on demand by the virtual memory system
Kernel virtual memory
Memory-mapped region for
shared libraries
Run-time heap
(created by malloc)
User stack
(created at runtime)
Unused
0
%esp
(stack
pointer)
Memory
invisible to
user code
brk
0xc0000000
0x08048000
0x40000000
Read/write segment
(.data, .bss)
Read-only segment
(.init, .text, .rodata)
Loaded
from
the
executable
file

## Slide 34: VM for Managing Multiple Processes
Key abstraction: each process has its own virtual address space
  It can view memory as a simple linear array
With virtual memory, this simple linear virtual address space need not be contiguous in physical memory
  Process needs to store data in another VP? Just map it to any PP!
Virtual Address Space for Process 1:
Physical
Address
Space (DRAM)
0
N-1
(e.g., read-only
library code)
Virtual Address Space for Process 2:
VP 1
VP 2
...
0
N-1
VP 1
VP 2
...
PP 2
PP 6
PP 8
...
0
M-1
Address
translation

## Slide 35: VM for Protection and Sharing
The mapping of VPs to PPs provides a simple mechanism to protect memory and to share memory between processes.
  Sharing: just map virtual pages in separate address spaces to the same physical page (here: PP 6)
  Protection: process simply can’t access physical pages to which none of its virtual pages are mapped (here: Process 2 can’t access PP 2).
Virtual Address Space for Process 1:
Physical
Address
Space (DRAM)
0
N-1
(e.g., read-only
library code)
Virtual Address Space for Process 2:
VP 1
VP 2
...
0
N-1
VP 1
VP 2
...
PP 2
PP 6
PP 8
...
0
M-1
Address
translation

## Slide 36: Memory Protection Within a Single Process
Can we use virtual memory to control read/write/execute permissions? How?

## Slide 37: Memory Protection Within a Single Process
Extend page table entries with permission bits
MMU checks these permission bits on every memory access
  If violated, raises exception and OS sends SIGSEGV signal to process (segmentation fault)
Process i:
Physical Page Num
WRITE
EXEC
PP 6
No
No
PP 4
No
Yes
PP 2
Yes
•
•
•
Process j:
No
READ
Yes
No
Yes
WRITE
EXEC
PP 9
Yes
No
PP 6
No
No
PP 11
Yes
No
READ
No
Yes
No
VP 0:
VP 1:
VP 2:
VP 0:
VP 1:
VP 2:
Physical
Address Space
PP 2
PP 4
PP 6
PP 8
PP 9
PP 11
Yes
Yes
Yes
Yes
Yes
Yes
Valid
Valid
Physical Page Num

## Slide 38: Terminology
context switch
  Switch between processes on the same CPU
page in
  Move pages of virtual memory from disk to physical memory
page out
  Move pages of virtual memory from physical memory to disk
thrash
  Total working set size of processes is larger than physical memory
  Most time is spent paging in and out instead of doing useful computation

## Slide 39: Address Translation: Page Hit
1) Processor sends virtual address to MMU (memory management unit)
2-3) MMU fetches PTE from page table in cache/memory (Uses PTBR to find beginning of page table for current process)
4) MMU sends physical address to cache/memory
5) Cache/memory sends data word to processor
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5
VA = Virtual Address PTEA = Page Table Entry Address PTE= Page Table Entry PA = Physical Address Data = Contents of memory stored at VA originally requested by CPU

## Slide 40: Address Translation: Page Fault
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in cache/memory
4) Valid bit is zero, so MMU triggers page fault exception
5) Handler identifies victim (and, if dirty, pages it out to disk)
6) Handler pages in new page and updates PTE in memory
7) Handler returns to original process, restarting faulting instruction
MMU
Cache/
Memory
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5
Disk
Page fault handler
Victim page
New page
Exception
6
7

## Slide 41: Hmm… Translation Sounds Slow!
The MMU accesses memory twice: once to first get the PTE for translation, and then again for the actual memory request from the CPU
  The PTEs may be cached in L1 like any other memory word
    But they may be evicted by other data references
    And a hit in the L1 cache still requires 1-3 cycles
What can we do to make this faster?

## Slide 42: Speeding up Translation with a TLB
Solution: add another cache!
Translation Lookaside Buffer (TLB):
  Small hardware cache in MMU
  Maps virtual page numbers to physical page numbers
  Contains complete page table entries for small number of pages
    Modern Intel processors: 128 or 256 entries in TLB
  Much faster than a page table lookup in cache/memory
Notes: “x86info -c” on Intel Core2 Duo CPU:
L1 Data TLB: 4KB pages, 4-way set associative, 16 entries
Data TLB: 4K pages, 4-way associative, 256 entries.
L1 Data TLB: 4MB pages, 4-way set associative, 16 entries
Data TLB: 4MB pages, 4-way associative, 32 entries

## Slide 43: TLB Hit
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
4
5
A TLB hit eliminates a memory access
TLB
VPN
3

## Slide 44: TLB Miss
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
5
6
TLB
VPN
4
PTEA
3
A TLB miss incurs an additional memory access (the PTE) Fortunately, TLB misses are rare.
Notes: Does a TLB miss require disk access?

## Slide 45: Simple Memory System Example (small)
Addressing
  14-bit virtual addresses
  12-bit physical address
  Page size = 64 bytes
13
12
11
10
9
8
7
6
5
4
3
2
1
0
11
10
9
8
7
6
5
4
3
2
1
0
VPO
PPO
PPN
VPN
Virtual Page Number
Virtual Page Offset
Physical Page Number
Physical Page Offset

## Slide 46: Simple Memory System Page Table
Only showing first 16 entries (out of 256 = 28)
What about a real address space? Read more in the book…
1
0D
0F
1
11
0E
1
2D
0D
0
–
0C
0
–
0B
1
09
0A
1
17
09
1
13
08
Valid
PPN
VPN
0
–
07
0
–
06
1
16
05
0
–
04
1
02
03
1
33
02
0
–
01
1
28
00
Valid
PPN
VPN

## Slide 47: Simple Memory System TLB
16 entries total
4 sets
4-way associative
13
12
11
10
9
8
7
6
5
4
3
2
1
0
virtual page offset
virtual page number
TLB index
TLB tag
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set
TLB ignores page offset. Why?

## Slide 48: Simple Memory System Cache
16 lines, 4-byte block size
Physically addressed
Direct mapped
11
10
9
8
7
6
5
4
3
2
1
0
physical page offset
physical page number
cache offset
cache index
cache tag
03
DF
C2
11
1
16
7
–
–
–
–
0
31
6
1D
F0
72
36
1
0D
5
09
8F
6D
43
1
32
4
–
–
–
–
0
36
3
08
04
02
00
1
1B
2
–
–
–
–
0
15
1
11
23
11
99
1
19
0
B3
B2
B1
B0
Valid
Tag
Index
–
–
–
–
0
14
F
D3
1B
77
83
1
13
E
15
34
96
04
1
16
D
–
–
–
–
0
12
C
–
–
–
–
0
0B
B
3B
DA
15
93
1
2D
A
–
–
–
–
0
2D
9
89
51
00
3A
1
24
8
B3
B2
B1
B0
Valid
Tag
Index

## Slide 49: Current state of caches/tables
03
DF
C2
11
1
16
7
–
–
–
–
0
31
6
1D
F0
72
36
1
0D
5
09
8F
6D
43
1
32
4
–
–
–
–
0
36
3
08
04
02
00
1
1B
2
–
–
–
–
0
15
1
11
23
11
99
1
19
0
B3
B2
B1
B0
Valid
Tag
Index
–
–
–
–
0
14
F
D3
1B
77
83
1
13
E
15
34
96
04
1
16
D
–
–
–
–
0
12
C
–
–
–
–
0
0B
B
3B
DA
15
93
1
2D
A
–
–
–
–
0
2D
9
89
51
00
3A
1
24
8
B3
B2
B1
B0
Valid
Tag
Index
Cache
1
0D
0F
1
11
0E
1
2D
0D
0
–
0C
0
–
0B
1
09
0A
1
17
09
1
13
08
Valid
PPN
VPN
0
–
07
0
–
06
1
16
05
0
–
04
1
02
03
1
33
02
0
–
01
1
28
00
Valid
PPN
VPN
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set
TLB
Page table (partial)

## Slide 50: Current state of caches/tables
03
DF
C2
11
1
16
7
–
–
–
–
0
31
6
1D
F0
72
36
1
0D
5
09
8F
6D
43
1
32
4
–
–
–
–
0
36
3
08
04
02
00
1
1B
2
–
–
–
–
0
15
1
11
23
11
99
1
19
0
B3
B2
B1
B0
Valid
Tag
Index
–
–
–
–
0
14
F
D3
1B
77
83
1
13
E
15
34
96
04
1
16
D
–
–
–
–
0
12
C
–
–
–
–
0
0B
B
3B
DA
15
93
1
2D
A
–
–
–
–
0
2D
9
89
51
00
3A
1
24
8
B3
B2
B1
B0
Valid
Tag
Index
Cache
1
0D
0F
1
11
0E
1
2D
0D
0
–
0C
0
–
0B
1
09
0A
1
17
09
1
13
08
Valid
PPN
VPN
0
–
07
0
–
06
1
16
05
0
–
04
1
02
03
1
33
02
0
–
01
1
28
00
Valid
PPN
VPN
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set
TLB
Page table (partial)

## Slide 51: Address Translation Example #1
Virtual Address: 0x03D4
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO ___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
1
0
1
0
1
1
1
1
0
0
0
0

## Slide 52: Address Translation Example #1
Virtual Address: 0x03D4
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO ___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
1
0
1
0
1
1
1
1
0
0
0
0
0x0F
3
0x03
Y
N
0x0D
0
0
0
1
0
1
0
1
1
0
1
0
0
0x5
0x0D
Y
0x36

## Slide 53: Address Translation Example #2
Virtual Address: 0x0B8F
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO ___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
1
1
1
1
0
0
0
1
1
1
0
1
0
0

## Slide 54: Address Translation Example #2
Virtual Address: 0x0B8F
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO ___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
1
1
1
1
0
0
0
1
1
1
0
1
0
0
0x2E
2
0x0B
N
?
TBD

## Slide 55: Address Translation Example #3
Virtual Address: 0x0020
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
0
0
0
1
0
0
0
0
0
0
0
0

## Slide 56: Address Translation Example #3
Virtual Address: 0x0020
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0x00
0
0x00
N
N
0x28
0
0
0
0
0
0
0
0
0
1
1
1
0
0x8
0x28
N
Mem

## Slide 57: Servicing a Page Fault
Disk
(1) Processor signals disk controller
  Read block of length P starting at disk address X
  Store starting at memory address Y
(2) Read occurs
  Direct Memory Access (DMA)
  Under control of I/O controller
(3) Controller signals completion
  Interrupts processor
  OS resumes suspended process
Disk
Memory-I/O bus
Processor
Cache
Memory
I/O
controller
Reg
(2) Direct Memory Address Transfer
(1) Initiate Block Read
(3) Read Done

## Slide 58: Summary
Programmer’s view of virtual memory
  Each process has its own private linear address space
  Cannot be corrupted by other processes
System view of virtual memory
  Uses memory efficiently by caching virtual memory pages
    Efficient only because of locality
  Simplifies memory management and sharing
  Simplifies protection by providing a convenient interpositioning point to check permissions

## Slide 59: Memory System Summary
L1/L2 Memory Cache
  Purely a speed-up technique
  Behavior invisible to application programmer and (mostly) OS
  Implemented totally in hardware
Virtual Memory
  Supports many OS-related functions
    Process creation, task switching, protection
  Operating System (software)
    Allocates/shares physical memory among processes
    Maintains high-level tables tracking memory type, source, sharing
    Handles exceptions, fills in hardware-defined mapping tables
  Hardware
    Translates virtual addresses via mapping tables, enforcing permissions
    Accelerates mapping via translation cache (TLB)

## Slide 60: Memory System – Who controls what?
L1/L2 Memory Cache
  Controlled by hardware
  Programmer cannot control it
  Programmer can write code in a way that takes advantage of it
Virtual Memory
  Controlled by OS and hardware
  Programmer cannot control mapping to physical memory
  Programmer can control sharing and some protection
    via OS functions (not in CSE 351)