## Slide 1: Caches II CSE 351 Autumn 2016
Instructor:
Justin Hsia
Teaching Assistants:
Chris Ma
Hunter Zahn John Kaltenbach Kevin Bi
Sachin Mehta
Suraj Bhat
Thomas Neuman
Waylon Huang Xi Liu Yufang Sun
https://what-if.xkcd.com/111/

## Slide 2: Administrivia
Lab 3 due Thursday
Midterm grades
  Unadjusted average currently right around 65%
    All scores will be adjusted up by 6 points in Catalyst
  Regrade requests open on Gradescope until end of Thursday
    It is possible for your grade to go down
    Make sure you submit separate requests for each portion of a question (e.g. Q5A and Q5B) – these may go to different graders!
Chart: CSE351 Au16 Midterm
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55
Frequency | 0 | 0 | 0 | 3 | 3 | 16 | 25 | 59 | 52 | 36 | 19 | 5

## Slide 3: An Example Memory Hierarchy
registers
on-chip L1
cache (SRAM)
main memory
(DRAM)
local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
remote secondary storage
(distributed file systems, web servers)
Local disks hold files retrieved from disks on remote network servers
Main memory holds disk blocks retrieved from local disks
off-chip L2
cache (SRAM)
L1 cache holds cache lines retrieved from L2 cache
CPU registers hold words retrieved from L1 cache
L2 cache holds cache lines retrieved from main memory
Smaller,
faster,
costlier
per byte
Notes: Implemented with different technologies!
  disks, solid-state
  DRAM: little wells that drain slowly, refreshed periodically
  SRAM: flip-flops, little logic gates that feedback with each other, faster but uses more power!
That’s why they’re different sizes and costs

## Slide 4: Making memory accesses fast!
Cache basics
Principle of locality
Memory hierarchies
Cache organization
  Direct-mapped (sets; index + tag)
  Associativity (ways)
  Replacement policy
  Handling writes
Program optimizations that consider caches
Notes: Divide addresses into “index” and “tag”

## Slide 5: Cache Organization (1)
Block Size (): unit of transfer between and Mem
  Given in bytes and always a power of 2 (e.g. 64 B)
  Blocks consist of adjacent bytes (differ in address by 1)
    Spatial locality!
Notes: Just like withinBlock() from Lab 1!

## Slide 6: Cache Organization (1)
Block Size (): unit of transfer between and Mem
  Given in bytes and always a power of 2 (e.g. 64 B)
  Blocks consist of adjacent bytes (differ in address by 1)
    Spatial locality!
Offset field
  Low-order bits of address tell you which byte within a block
    (address) mod = lowest bits of address
  (address) modulo (# of bytes in a block)
Block Number
Block Offset
-bit address:
(refers to byte in memory)
bits
bits
Notes: Just like withinBlock() from Lab 1!

## Slide 7: Cache Organization (2)
Cache Size (): amount of data the can store
  Cache can only hold so much data (subset of next level)
  Given in bytes () or number of blocks ()
  Example: = 32 KiB = 512 blocks if using 64-B blocks
Where should data go in the cache?
  We need a mapping from memory addresses to specific locations in the cache to make checking the cache for an address fast
What is a data structure that provides fast lookup?
  Hash table!

## Slide 8: Aside: Hash Tables for Fast Lookup
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 
Insert: 5
27
34
102
119
Apply hash function to map data to “buckets”
Notes: hash(27) % N (10) = 7…

## Slide 9: Place Data in Cache by Hashing Address
Block Addr | Block Data |  |  | 
0000 |  |  |  | 
0001 |  |  |  | 
0010 |  |  |  | 
0011 |  |  |  | 
0100 |  |  |  | 
0101 |  |  |  | 
0110 |  |  |  | 
0111 |  |  |  | 
1000 |  |  |  | 
1001 |  |  |  | 
1010 |  |  |  | 
1011 |  |  |  | 
1100 |  |  |  | 
1101 |  |  |  | 
1110 |  |  |  | 
1111 |  |  |  | 
Memory
Cache
Index | Block Data |  |  | 
00 |  |  |  | 
01 |  |  |  | 
10 |  |  |  | 
11 |  |  |  | 
Map to cache index from block address
  Use next bits
  (block address) mod (# blocks in cache)
  Lets adjacent blocks fit in cache simultaneously!
Here = 4 B
and = 4

## Slide 10: Place Data in Cache by Hashing Address
Block Addr | Block Data |  |  | 
0000 |  |  |  | 
0001 |  |  |  | 
0010 |  |  |  | 
0011 |  |  |  | 
0100 |  |  |  | 
0101 |  |  |  | 
0110 |  |  |  | 
0111 |  |  |  | 
1000 |  |  |  | 
1001 |  |  |  | 
1010 |  |  |  | 
1011 |  |  |  | 
1100 |  |  |  | 
1101 |  |  |  | 
1110 |  |  |  | 
1111 |  |  |  | 
Memory
Cache
Index | Block Data |  |  | 
00 |  |  |  | 
01 |  |  |  | 
10 |  |  |  | 
11 |  |  |  | 
Collision!
  This might confuse the cache later when we access the data
  Solution?
Here = 4 B
and = 4

## Slide 11: Tags Differentiate Blocks in Same Index
Block Addr | Block Data |  |  | 
0000 |  |  |  | 
0001 |  |  |  | 
0010 |  |  |  | 
0011 |  |  |  | 
0100 |  |  |  | 
0101 |  |  |  | 
0110 |  |  |  | 
0111 |  |  |  | 
1000 |  |  |  | 
1001 |  |  |  | 
1010 |  |  |  | 
1011 |  |  |  | 
1100 |  |  |  | 
1101 |  |  |  | 
1110 |  |  |  | 
1111 |  |  |  | 
Memory
Cache
Index | Tag |  | Block Data |  |  | 
00 | 00 |  |  |  |  | 
01 |  |  |  |  |  | 
10 | 01 |  |  |  |  | 
11 | 01 |  |  |  |  | 
Tag = rest of address bits
  bits =
  Check this during a cache lookup
Here = 4 B
and = 4

## Slide 12: Checking for a Requested Address
CPU sends address request for chunk of data
  Address and requested data are not the same thing!
    Analogy: your friend ≠ his or her phone number
TIO address breakdown:
  Index field tells you where to look in cache
  Tag field lets you check that data is the block you want
  Offset field selects specified start byte within block
  Note: and sizes will change based on hash function
Tag ()
Offset ()
-bit address:
Block Number
Index ()

## Slide 13: Cache Puzzle #1
What can you infer from the following behavior?
  Cache starts empty, also known as a cold cache
  Access (addr: hit/miss) stream:
    (14: miss), (15: hit), (16: miss)
Minimum block size?
Maximum block size?
Notes: Lab 4!

## Slide 14: Direct-Mapped Cache
Block Addr | Block Data |  |  | 
00 00 |  |  |  | 
00 01 |  |  |  | 
00 10 |  |  |  | 
00 11 |  |  |  | 
01 00 |  |  |  | 
01 01 |  |  |  | 
01 10 |  |  |  | 
01 11 |  |  |  | 
10 00 |  |  |  | 
10 01 |  |  |  | 
10 10 |  |  |  | 
10 11 |  |  |  | 
11 00 |  |  |  | 
11 01 |  |  |  | 
11 10 |  |  |  | 
11 11 |  |  |  | 
Memory
Cache
Index | Tag |  | Block Data |  |  | 
00 | 00 |  |  |  |  | 
01 | 11 |  |  |  |  | 
10 | 01 |  |  |  |  | 
11 | 01 |  |  |  |  | 
Hash function: (block address) mod (# of blocks in cache)
  Each memory address maps to exactly one index in the cache
  Fast (and simpler) to find an address
Here = 4 B
and = 4

## Slide 15: Direct-Mapped Cache Problem
Block Addr | Block Data |  |  | 
00 00 |  |  |  | 
00 01 |  |  |  | 
00 10 |  |  |  | 
00 11 |  |  |  | 
01 00 |  |  |  | 
01 01 |  |  |  | 
01 10 |  |  |  | 
01 11 |  |  |  | 
10 00 |  |  |  | 
10 01 |  |  |  | 
10 10 |  |  |  | 
10 11 |  |  |  | 
11 00 |  |  |  | 
11 01 |  |  |  | 
11 10 |  |  |  | 
11 11 |  |  |  | 
Memory
Cache
Index | Tag |  | Block Data |  |  | 
00 | ?? |  |  |  |  | 
01 | ?? |  |  |  |  | 
10 |  |  |  |  |  | 
11 | ?? |  |  |  |  | 
What happens if we access the following addresses?
  8, 24, 8, 24, 8, …?
  Conflict in cache (misses!)
  Rest of cache goes unused
Solution?
Here = 4 B
and = 4
Notes: Conflict! Rest of cache unused!

## Slide 16: Associativity
What if we could store data in any place in the cache?
  More complicated hardware = more power consumed, slower
So we combine the two ideas:
  Each address maps to exactly one set
  Each set can store block in more than one way
0
1
2
3
4
5
6
7
0
1
2
3
Set
0
1
Set
1-way:
8 sets,
1 block each
2-way:
4 sets,
2 blocks each
4-way:
2 sets,
4 blocks each
0
Set
8-way:
1 set,
8 blocks
direct mapped
fully associative
Notes: “Where is address 2?”

## Slide 17: Cache Organization (3)
Associativity (): # of ways for each set
  Such a cache is called an “-way set associative cache”
  We now index into cache sets, of which there are
  Use lowest = bits of block address
    Direct-mapped: = 1, so = as we saw previously
    Fully associative: = , so = 0 bits
Decreasing associativity
Fully associative
(only one set)
Direct mapped
(only one way)
Increasing associativity
Selects the set
Used for tag comparison
Selects the byte from block
Tag ()
Index ()
Offset ()

## Slide 18: Example Placement
Where would data from address 0x1833 be placed?
  Binary: 0b 0001 1000 0011 0011
= ?
block size: | 16 B
capacity: | 8 blocks
address: | 16 bits
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Direct-mapped
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
Set | Tag | Data
0 |  | 
1 |  | 
2-way set associative
4-way set associative
Tag ()
Offset ()
-bit address:
Index ()
=
=
= ––
= ?
= ?
Notes: 18

## Slide 19: Example Placement
Where would data from address 0x1833 be placed?
  Binary: 0b 0001 1000 0011 0011
= 3
block size: | 16 B
capacity: | 8 blocks
address: | 16 bits
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Direct-mapped
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
Set | Tag | Data
0 |  | 
1 |  | 
2-way set associative
4-way set associative
Tag ()
Offset ()
-bit address:
Index ()
=
=
= ––
= 2
= 1
Notes: 19

## Slide 20: Block Replacement
Any empty block in the correct set may be used to store block
If there are no empty blocks, which one should we replace?
  No choice for direct-mapped caches
  Caches typically use something close to least recently used (LRU) (hardware usually implements “not most recently used”)
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Direct-mapped
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
Set | Tag | Data
0 |  | 
1 |  | 
2-way set associative
4-way set associative

## Slide 21: Cache Puzzle #2
What can you infer from the following behavior?
  Cache starts empty, also known as a cold cache
  Access (addr: hit/miss) stream:
    (10: miss), (12: miss), (10: miss)
Associativity?
Number of sets?
Notes: How much associativity is there?
  None! first access kicked the other out, so 1-way
How many sets?
  10 & 12 map to same thing
  1010 & 1100

## Slide 22: General Cache Organization (, , )
= blocks/lines per set
= # sets
=
set
“line” (block plus management bits)
0
1
2
B-1
tag
V
valid bit
= bytes per block
Cache size:
data bytes
(doesn’t include V or Tag)
Notes: valid bit so we know if this has been initialized

## Slide 23: Notation Changes
We are using different variable names from previous quarters
  Please be aware of this when you look at past exam questions or are watching videos
Variable | This Quarter | Previous Quarters
Block size |  | B
Cache size |  | ---
Associativity |  | E
Address width |  | m
Tag field width |  | t
Index field width |  | k, s
Offset field width |  | n, b
Number of Sets |  | S
Variable | This Quarter | Previous Quarters
Block size |  | B
Cache size |  | ---
Associativity |  | E
Address width |  | m
Tag field width |  | t
Index field width |  | k, s
Offset field width |  | n, b
Number of Sets |  | S