## Slide 1: Caches III CSE 351 Autumn 2016
Instructor:
Justin Hsia
Teaching Assistants:
Chris Ma Hunter Zahn John Kaltenbach Kevin Bi
Sachin Mehta Suraj Bhat Thomas Neuman Waylon Huang
Xi Liu Yufang Sun
http://xkcd.com/908/

## Slide 2: Administrivia
Lab 3 due Friday
  1 late day = Sunday @ 5pm
No lecture on Friday – Veteran’s Day!
Midterm Regrades due end of Thursday

## Slide 3: Cache Read
0
1
2
B-1
tag
v
bits
bits
bits
Address of byte in memory:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset
valid bit
= # sets
=
= blocks/lines per set
= bytes per block

## Slide 4: Example: Direct-Mapped Cache ( = 1)
Direct-mapped: One line per set
Block Size = 8 B
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set
= sets

## Slide 5: Example: Direct-Mapped Cache ( = 1)
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match?: yes = hit
valid? +
block offset
Direct-mapped: One line per set
Block Size = 8 B

## Slide 6: Example: Direct-Mapped Cache ( = 1)
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match?: yes = hit
valid? +
int (4 B) is here
block offset
No match? Then old line gets evicted and replaced
This is why we want alignment!
Direct-mapped: One line per set
Block Size = 8 B

## Slide 7: Example: Set-Associative Cache ( = 2)
bits
0…01
100
Address of short int:
find set
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
2-way: Two lines per set
Block Size = 8 B

## Slide 8: Example: Set-Associative Cache ( = 2)
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
bits
0…01
100
compare both
valid? +
match: yes = hit
block offset
tag
2-way: Two lines per set
Block Size = 8 B
Address of short int:

## Slide 9: Example: Set-Associative Cache ( = 2)
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
bits
0…01
100
valid? +
match: yes = hit
block offset
short int (2 B) is here
No match?
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …
compare both
Address of short int:
2-way: Two lines per set
Block Size = 8 B
Notes: Do CAMERA demo here.

## Slide 10: Types of Cache Misses: 3 C’s!
Compulsory (cold) miss
  Occurs on first access to a block
Conflict miss
  Conflict misses occur when the cache is large enough, but multiple data objects all map to the same slot
    e.g., referencing blocks 0, 8, 0, 8, ... could miss every time
  Direct-mapped caches have more conflict misses than -way set-associative (where > 1)
Capacity miss
  Occurs when the set of active cache blocks (the working set) is larger than the cache (just won’t fit, even if cache was fully-associative)
  Note: Fully-associative only has Compulsory and Capacity misses

## Slide 11: Core i7: Associativity
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
slower, but
more likely
to hit
Block/line size: 64 bytes for all
L1 i-cache and d-cache:
  32 KiB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KiB, 8-way,
  Access: 11 cycles
L3 unified cache:
  8 MiB, 16-way,
  Access: 30-40 cycles
Notes: cat /sys/devices/system/cpu/cpu0/cache/index0/ways_of_associativity
Practice: how many sets in L1?
  32 kB / 64 B/block = 512 lines
  512 blocks / 8 ways = 64 sets

## Slide 12: What about writes?
Multiple copies of data exist:
  L1, L2, possibly L3, main memory
What to do on a write-hit?
  Write-through: write immediately to memory and all caches in-between
  Write-back: defer write to memory until line is evicted (replaced)
    Must track which cache lines have been modified (“dirty bit”)
What to do on a write-miss?
  Write-allocate: (“fetch on write”) load into cache, update line in cache
    Good if more writes or reads to the location follow
  No-write-allocate: (“write around”) just write immediately to memory
Typical caches:
  Write-back + Write-allocate, usually
  Write-through + No-write-allocate, occasionally
Notes: Why? Reuse is common
  Typically you would read, then write (incr)
  Or after you initialize a value (say, to 0), likely read and write it again soon

## Slide 13: Write-back, write-allocate example
0xBEEF
Cache
Memory
G
0xCAFE
0xBEEF
0
F
G
dirty bit
tag (there is only one set in this tiny cache, so the tag is the entire block address!)
In this example we are sort of ignoring block offsets. Here a block holds 2 bytes (16 bits, 4 hex digits).
Normally a block would be much bigger and thus there would be multiple items per block. While only one item in that block would be written at a time, the entire line would be brought into cache.
Contents of memory stored at address G

## Slide 14: Write-back, write-allocate example
0xBEEF
Cache
Memory
G
0xCAFE
0xBEEF
0
F
G
mov 0xFACE, F
dirty bit

## Slide 15: Write-back, write-allocate example
0xBEEF
U
0
0xCAFE
Cache
Memory
F
0xCAFE
0xBEEF
F
G
dirty bit
0xCAFE
0
Step 1: Bring F into cache
mov 0xFACE, F

## Slide 16: Write-back, write-allocate example
0xBEEF
U
0
0xCAFE
Cache
Memory
F
0xCAFE
0xBEEF
F
G
dirty bit
0xFACE
1
Step 2: Write 0xFACE to cache only and set dirty bit
mov 0xFACE, F

## Slide 17: Write-back, write-allocate example
0xBEEF
U
0
0xCAFE
Cache
Memory
F
0xCAFE
0xBEEF
F
G
mov 0xFEED, F
dirty bit
0xFACE
1
Write hit!
Write 0xFEED to cache only
mov 0xFACE, F

## Slide 18: Write-back, write-allocate example
0xBEEF
U
0
0xCAFE
Cache
Memory
F
0xCAFE
0xBEEF
F
G
mov G, %rax
dirty bit
0xFEED
1
mov 0xFEED, F
mov 0xFACE, F

## Slide 19: Write-back, write-allocate example
0xBEEF
Cache
Memory
G
0xFEED
0xBEEF
0
F
G
dirty bit
1. Write F back to memory since it is dirty 2. Bring G into the cache so we can copy it into %rax
mov G, %rax
mov 0xFEED, F
mov 0xFACE, F

## Slide 20: Where else is caching used?
Software caches are more flexible
  File system buffer caches, browser caches, etc.
  Content-delivery networks (CDN): cache for the Internet (e.g. Netflix)
Some design differences
  Almost always fully-associative
    so, no placement restrictions
    index structures like hash tables are common (for placement)
  More complex replacement policies
    misses are very expensive when disk or network involved
    worth thousands of cycles to avoid them
  Not necessarily constrained to single “block” transfers
    may fetch or write-back in larger units, opportunistically

## Slide 21: Optimizations for the Memory Hierarchy
Write code that has locality!
  Spatial: access data contiguously
  Temporal: make sure access to the same data is not too far apart in time
How can you achieve locality?
  Adjust memory accesses in code (software) to improve miss rate (MR)
    Requires knowledge of both how caches work as well as your system’s parameters
  Proper choice of algorithm
  Loop transformations

## Slide 22: Example: Matrix Multiplication
C
=
×
A
B
ai*
b*j
cij
Notes: Subscript indices given in (row,col).

## Slide 23: Matrices in Memory
How do cache blocks fit into this scheme?
  Row major matrix in memory:
Cache blocks
COLUMN of matrix (blue) is spread among cache blocks shown in red

## Slide 24: Naïve Matrix Multiply
# move along rows of A
for (i = 0; i < n; i++)
# move along columns of B
for (j = 0; j < n; j++)
# EACH k loop reads row of A, col of B
# Also read & write c(i,j) n times
for (k = 0; k < n; k++)
c[i*n+j] += a[i*n+k] * b[k*n+j];
C(i,j)
A(i,:)
B(:,j)
C(i,j)
Notes: Note the += leads to an additional read of matrix C

## Slide 25: Cache Miss Analysis (Naïve)
Scenario Parameters:
  Square matrix (), elements are doubles
  Cache block size = 64 B = 8 doubles
  Cache size (much smaller than )
First iteration:
  misses
  Afterwards in cache: (schematic)
8 doubles wide
misses
misses
Ignoring
matrix c

## Slide 26: Cache Miss Analysis (Naïve)
Scenario Parameters:
  Square matrix (), elements are doubles
  Cache block size = 64 B = 8 doubles
  Cache size (much smaller than )
Other iterations:
  Again: misses
Total misses:
8 wide
once per element
Ignoring
matrix c

## Slide 27: Linear Algebra to the Rescue (1)
Can get the same result of a matrix multiplication by splitting the matrices into smaller submatrices (matrix “blocks”)
For example, multiply two 4×4 matrices:

## Slide 28: Linear Algebra to the Rescue (2)
Matrices of size , split into 4 blocks of size (=)
C22 = A21B12 + A22B22 + A23B32 + A24B42 = k A2k*Bk2
Multiplication operates on small “block” matrices
  Choose size so that they fit in the cache!
  This technique called “cache blocking”
C11
C12
C13
C14
C21
C22
C23
C24
C31
C32
C43
C34
C41
C42
C43
C44
A11
A12
A13
A14
A21
A22
A23
A24
A31
A32
A33
A34
A41
A42
A43
A144
B11
B12
B13
B14
B21
B22
B23
B24
B32
B32
B33
B34
B41
B42
B43
B44

## Slide 29: Blocked Matrix Multiply
Blocked version of the naïve algorithm:
  = block matrix size (assume divides evenly)
# move by rxr BLOCKS now
for (i = 0; i < n; i += r)
for (j = 0; j < n; j += r)
for (k = 0; k < n; k += r)
# block matrix multiplication
for (ib = i; ib < i+r; ib++)
for (jb = j; jb < j+r; jb++)
for (kb = k; kb < k+r; kb++)
c[ib*n+jb] += a[ib*n+kb]*b[kb*n+jb];

## Slide 30: Cache Miss Analysis (Blocked)
Scenario Parameters:
  Cache block size = 64 B = 8 doubles
  Cache size (much smaller than )
  Three blocks () fit into cache:
First (block) iteration:
  misses per block
  Afterwards in cache (schematic)
/ blocks
elements per block, 8 per cache block
/ blocks in row and column
Ignoring
matrix c
Notes: 3B2 < C: need to be able to fit three full blocks in the cache (one for c, one for a, one for b) while executing the algorithm

## Slide 31: Cache Miss Analysis (Blocked)
Scenario Parameters:
  Cache block size = 64 B = 8 doubles
  Cache size (much smaller than )
  Three blocks () fit into cache:
Other (block) iterations:
  Same as first iteration
Total misses:
Ignoring
matrix c
/ blocks

## Slide 32: Matrix Multiply Summary
Naïve:
Blocked:
  If = 8, difference is 4*8 * 9/8 = 36x
  If = 16, difference is 4*16 * 9/8 = 72x
Blocking optimization only works if the blocks fit in the cache
  Suggests largest possible block size up to limit
Matrix multiplication has inherent temporal locality:
  Input data: 32, computation 23
  Every array element used times!
  But program has to be written properly
Notes: 3B2 < C: need to be able to fit three full blocks in the cache (one for c, one for a, one for b) while executing the algorithm

## Slide 33: Matrix Multiply Visualization
Here = 100, = 32 KiB, = 30
Naïve:
Blocked:
≈ 1,020,000
cache misses
≈ 90,000
cache misses

## Slide 34: Cache-Friendly Code
Programmer can optimize for cache performance
  How data structures are organized
  How data are accessed
    Nested loop structure
    Blocking is a general technique
All systems favor “cache-friendly code”
  Getting absolute optimum performance is very platform specific
    Cache size, cache block size, associativity, etc.
  Can get most of the advantage with generic code
    Keep working set reasonably small (temporal locality)
    Use small strides (spatial locality)
    Focus on inner loop code

## Slide 35: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11
128m | 8350 | 4750 | 3096 | 2286 | 1817 | 1512 | 1293 | 1131 | 1055 | 995 | 945 | 900
64m | 8352 | 4750 | 3092 | 2287 | 1816 | 1510 | 1291 | 1129 | 1051 | 989 | 938 | 894
32m | 8406 | 4787 | 3098 | 2289 | 1823 | 1512 | 1295 | 1133 | 1052 | 989 | 938 | 892
16m | 8556 | 4990 | 3204 | 2376 | 1891 | 1579 | 1356 | 1198 | 1127 | 1070 | 1028 | 994
8m | 8998 | 5447 | 3570 | 2643 | 2104 | 1743 | 1477 | 1300 | 1217 | 1158 | 1128 | 1096
4m | 11494 | 7921 | 5664 | 4319 | 3524 | 2991 | 2592 | 2298 | 2208 | 2148 | 2117 | 2077
2m | 12297 | 8417 | 5940 | 4573 | 3734 | 3174 | 2763 | 2446 | 2349 | 2272 | 2213 | 2160
1024k | 12422 | 8398 | 5971 | 4569 | 3740 | 3172 | 2756 | 2446 | 2351 | 2271 | 2209 | 2162
512k | 12432 | 8472 | 5950 | 4573 | 3726 | 3165 | 2758 | 2447 | 2341 | 2267 | 2210 | 2162
256k | 12564 | 10037 | 8679 | 7175 | 5915 | 5022 | 4345 | 3856 | 3895 | 3981 | 4001 | 4404
128k | 12711 | 10750 | 10271 | 8649 | 7525 | 6374 | 5482 | 4854 | 4901 | 4933 | 4917 | 4924
64k | 12687 | 10689 | 10208 | 8768 | 7570 | 6352 | 5460 | 4830 | 4885 | 4885 | 4823 | 4868
Core i7 Haswell
2.1 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
Slopes
of spatial locality
Ridges
of temporal locality
L1
Mem
L2
L3
Aggressive prefetching
Notes: Increase stride size = less spatial locality = drop in throughput
Increase working set size = less temporal locality = fall out of respective caches
All caches on-chip

## Slide 36: Learning About Your Machine
Linux:
  lscpu
  ls /sys/devices/system/cpu/cpu0/cache/index0/
    Ex: cat /sys/devices/system/cpu/cpu0/cache/index*/size
  cat /proc/cpuinfo | grep cache | sort | uniq
Windows:
  wmic memcache get <query> (all values in KB)
  Ex: wmic memcache get MaxCacheSize
Modern processor specs: http://www.7-cpu.com/
Notes: Linux Demo: type, level, size, ways_of_associativity
Windows Demo: Purpose, MaxCacheSize, BlockSize, Associativity