## Slide 1: Virtual Memory III CSE 351 Autumn 2018
Instructor:
Justin Hsia
Teaching Assistants:
Akshat Aggarwal
An Wang
Andrew Hu
Brian Dai
Britt Henderson
James Shin
Kevin Bi
Kory Watson
Riley Germundson
Sophie Tian
Teagan Horkan
https://xkcd.com/648/

## Slide 2: Administrivia
Lab 4 due Monday (11/26)
Homework 5 due next Friday (11/30)
“Virtual section” on virtual memory released
  3 PDFs: VM overview, worksheet, and solutions
  Linked in the code section of today’s lecture
  See Piazza post for links and videos

## Slide 3: Quick Review
What do Page Tables map?
Where are Page Tables located?
How many Page Tables are there?
Can your process tell if a page fault has occurred?
True / False: Virtual Addresses that are contiguous will always be contiguous in physical memory
TLB stands for _______________________ and stores _______________

## Slide 4: Address Translation
VM is complicated, but also elegant and effective
  Level of indirection to provide isolated memory & caching
  TLB as a cache of page tables avoids two trips to memory for every memory access
Virtual Address
TLB
Lookup
Check the
Page Table
Update
TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
TLB Miss
TLB Hit
Page not
in Mem
Access
Denied
Access
Permitted
Protection
Fault
SIGSEGV
Page
in Mem
Check cache
Find in Disk
Find in Mem
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 5: Simple Memory System Example (small)
Addressing
  14-bit virtual addresses
  12-bit physical address
  Page size = 64 bytes
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
Virtual Page Number
Virtual Page Offset
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
Physical Page Number
Physical Page Offset

## Slide 6: Simple Memory System: Page Table
Only showing first 16 entries (out of _____)
  Note: showing 2 hex digits for PPN even though only 6 bits
  Note: other management bits not shown, but part of PTE
VPN | PPN | Valid
0 | 28 | 1
1 | – | 0
2 | 33 | 1
3 | 02 | 1
4 | – | 0
5 | 16 | 1
6 | – | 0
7 | – | 0
VPN | PPN | Valid
8 | 13 | 1
9 | 17 | 1
A | 09 | 1
B | – | 0
C | – | 0
D | 2D | 1
E | – | 0
F | 0D | 1
Notes: Size of page table = 2^(n-p) entries

## Slide 7: Simple Memory System: TLB
16 entries total
4-way set associative
13
12
11
10
9
8
7
6
5
4
3
2
1
0
virtual page offset
virtual page number
TLB index
TLB tag
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set
Why does the TLB ignore the page offset?
Notes: Calculate VPN for valid TLB entry using Tag & Set

## Slide 8: Simple Memory System: Cache
Direct-mapped with = 4 B, = 16
Physically addressed
11
10
9
8
7
6
5
4
3
2
1
0
physical page offset
physical page number
cache offset
cache index
cache tag
Note: It is just coincidence that the PPN is the same width as the cache Tag
Index | Tag | Valid | B0 | B1 | B2 | B3
0 | 19 | 1 | 99 | 11 | 23 | 11
1 | 15 | 0 | – | – | – | –
2 | 1B | 1 | 00 | 02 | 04 | 08
3 | 36 | 0 | – | – | – | –
4 | 32 | 1 | 43 | 6D | 8F | 09
5 | 0D | 1 | 36 | 72 | F0 | 1D
6 | 31 | 0 | – | – | – | –
7 | 16 | 1 | 11 | C2 | DF | 03
Index | Tag | Valid | B0 | B1 | B2 | B3
8 | 24 | 1 | 3A | 00 | 51 | 89
9 | 2D | 0 | – | – | – | –
A | 2D | 1 | 93 | 15 | DA | 3B
B | 0B | 0 | – | – | – | –
C | 12 | 0 | – | – | – | –
D | 16 | 1 | 04 | 96 | 34 | 15
E | 13 | 1 | 83 | 77 | 1B | D3
F | 14 | 0 | – | – | – | –

## Slide 9: Current State of Memory System
Cache:
TLB:
Page table (partial):
Index | Tag | V | B0 | B1 | B2 | B3
0 | 19 | 1 | 99 | 11 | 23 | 11
1 | 15 | 0 | – | – | – | –
2 | 1B | 1 | 00 | 02 | 04 | 08
3 | 36 | 0 | – | – | – | –
4 | 32 | 1 | 43 | 6D | 8F | 09
5 | 0D | 1 | 36 | 72 | F0 | 1D
6 | 31 | 0 | – | – | – | –
7 | 16 | 1 | 11 | C2 | DF | 03
Index | Tag | V | B0 | B1 | B2 | B3
8 | 24 | 1 | 3A | 00 | 51 | 89
9 | 2D | 0 | – | – | – | –
A | 2D | 1 | 93 | 15 | DA | 3B
B | 0B | 0 | – | – | – | –
C | 12 | 0 | – | – | – | –
D | 16 | 1 | 04 | 96 | 34 | 15
E | 13 | 1 | 83 | 77 | 1B | D3
F | 14 | 0 | – | – | – | –
Set | Tag | PPN | V | Tag | PPN | V | Tag | PPN | V | Tag | PPN | V
0 | 03 | – | 0 | 09 | 0D | 1 | 00 | – | 0 | 07 | 02 | 1
1 | 03 | 2D | 1 | 02 | – | 0 | 04 | – | 0 | 0A | – | 0
2 | 02 | – | 0 | 08 | – | 0 | 06 | – | 0 | 03 | – | 0
3 | 07 | – | 0 | 03 | 0D | 1 | 0A | 34 | 1 | 02 | – | 0
VPN | PPN | V
0 | 28 | 1
1 | – | 0
2 | 33 | 1
3 | 02 | 1
4 | – | 0
5 | 16 | 1
6 | – | 0
7 | – | 0
VPN | PPN | V
8 | 13 | 1
9 | 17 | 1
A | 09 | 1
B | – | 0
C | – | 0
D | 2D | 1
E | – | 0
F | 0D | 1
Notes: TLB and Cache are separate pieces of hardware; page table stored in memory
Show correlation between TLB & page table (VPN 0x0D and 0x0F in particular)

## Slide 10: Memory Request Example #1
Virtual Address: 0x03D4
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
1
9
1
8
1
7
1
6
0
5
1
4
0
3
1
2
0
1
0
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Hit, Cache Hit

## Slide 11: Memory Request Example #2
Virtual Address: 0x038F
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
1
9
1
8
1
7
0
6
0
5
0
4
1
3
1
2
1
1
1
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Miss, page fault

## Slide 12: Memory Request Example #3
Virtual Address: 0x0020
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
0
9
0
8
0
7
0
6
1
5
0
4
0
3
0
2
0
1
0
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Miss, Page Table Hit, Cache Miss

## Slide 13: Memory Request Example #4
Virtual Address: 0x036B
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
1
9
1
8
0
7
1
6
1
5
0
4
1
3
0
2
1
1
1
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Hit, Cache Hit

## Slide 14: Memory Overview
Disk
Main memory
(DRAM)
Cache
CPU
Page
Page
Line
Block
requested 32-bits
movl 0x8043ab, %rdi
TLB
MMU

## Slide 15: Page Table Reality
Just one issue… the numbers don’t work out for the story so far!
The problem is the page table for each process:
  Suppose 64-bit VAs, 8 KiB pages, 8 GiB physical memory
  How many page table entries is that?
  About how long is each PTE?
  Moral: Cannot use this naïve implementation of the virtual→physical page mapping – it’s way too big
This is extra (non-testable) material
Notes: 2^64/2^13 = 2^51
PPN = 20 bits; plus Valid, R/W/X; so ~ 3 B per PTE
So each page table takes up 2^52 + 2^51 B!

## Slide 16: A Solution: Multi-level Page Tables
Page table base register
(PTBR)
VPN 1
0
p-1
n-1
VPO
VPN 2
...
VPN k
PPN
0
p-1
m-1
PPO
PPN
Virtual Address
Physical Address
...
...
Level 1
page table
Level 2
page table
Level k
page table
TLB
PTE
VPN
→
PTE
VPN
→
PTE
VPN
→
This is called a page walk
This is extra (non-testable) material

## Slide 17: Multi-level Page Tables
A tree of depth where each node at depth has up to children if part of the VPN has bits
Hardware for multi-level page tables inherently more complicated
  But it’s a necessary complexity – 1-level does not fit
Why it works: Most subtrees are not used at all, so they are never created and definitely aren’t in physical memory
  Parts created can be evicted from cache/memory when not being used
  Each node can have a size of ~1-100KB
But now for a -level page table, a TLB miss requires cache/memory accesses
  Fine so long as TLB misses are rare – motivates larger TLBs
This is extra (non-testable) material

## Slide 18: Practice VM Question
Our system has the following properties
  1 MiB of physical address space
  4 GiB of virtual address space
  32 KiB page size
  4-entry fully associative TLB with LRU replacement
Fill in the following blanks:
________ | Entries in a page table | ________ | Minimum bit-width of PTBR
________ | TLBT bits | ________ | Max # of valid entries in a page table

## Slide 19: Practice VM Question
One process uses a page-aligned square matrix mat[] of 32-bit integers in the code shown below:
#define MAT_SIZE = 2048
for(int i = 0; i < MAT_SIZE; i++)
mat[i*(MAT_SIZE+1)] = i;
What is the largest stride (in bytes) between successive memory accesses (in the VA space)?

## Slide 20: Practice VM Question
One process uses a page-aligned square matrix mat[] of 32-bit integers in the code shown below:
#define MAT_SIZE = 2048
for(int i = 0; i < MAT_SIZE; i++)
mat[i*(MAT_SIZE+1)] = i;
Assuming all of mat[] starts on disk, what are the following hit rates for the execution of the for-loop?
________ | TLB Hit Rate | ________ | Page Table Hit Rate

## Slide 21
For Fun: DRAMMER Security Attack
Why are we talking about this?
  Recent: Announced in October 2016; Google released Android patch on November 8, 2016
  Relevant: Uses your system’s memory setup to gain elevated privileges
    Ties together some of what we’ve learned about virtual memory and processes
  Interesting: It’s a software attack that uses only hardware vulnerabilities and requires no user permissions
BONUS SLIDES

## Slide 22: Underlying Vulnerability: Row Hammer
Dynamic RAM (DRAM) has gotten denser over time
  DRAM cells physically closer and use smaller charges
  More susceptible to “disturbance errors” (interference)
DRAM capacitors need to be “refreshed” periodically (~64 ms)
  Lose data when loss of power
  Capacitors accessed in rows
Rapid accesses to one row can flip bits in an adjacent row!
  ~ 100K to 1M times
By Dsimic (modified), CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=38868341

## Slide 23: Row Hammer Exploit
Force constant memory access
  Read then flush the cache
  clflush – flush cache line
    Invalidates cache line containing the specified address
    Not available in all machines or environments
  Want addresses X and Y to fall in activation target row(s)
    Good to understand how banks of DRAM cells are laid out
The row hammer effect was discovered in 2014
  Only works on certain types of DRAM (2010 onwards)
  These techniques target x86 machines
hammertime:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
jmp hammertime

## Slide 24: Consequences of Row Hammer
Row hammering process can affect another process via memory
  Circumvents virtual memory protection scheme
  Memory needs to be in an adjacent row of DRAM
Worse: privilege escalation
  Page tables live in memory!
  Hope to change PPN to access other parts of memory, or change permission bits
  Goal: gain read/write access to a page containing a page table, hence granting process read/write access to all of physical memory

## Slide 25: Effectiveness?
Doesn’t seem so bad – random bit flip in a row of physical memory
  Vulnerability affected by system setup and physical condition of memory cells
Improvements:
  Double-sided row hammering increases speed & chance
  Do system identification first (e.g. Lab 4)
    Use timing to infer memory row layout & find “bad” rows
    Allocate a huge chunk of memory and try many addresses, looking for a reliable/repeatable bit flip
  Fill up memory with page tables first
    fork extra processes; hope to elevate privileges in any page table

## Slide 26: What’s DRAMMER?
No one previously made a huge fuss
  Prevention: error-correcting codes, target row refresh, higher DRAM refresh rates
  Often relied on special memory management features
  Often crashed system instead of gaining control
Research group found a deterministic way to induce row hammer exploit in a non-x86 system (ARM)
  Relies on predictable reuse patterns of standard physical memory allocators
  Universiteit Amsterdam, Graz University of Technology, and University of California, Santa Barbara

## Slide 27: DRAMMER Demo Video
It’s a shell, so not that sexy-looking, but still interesting
  Apologies that the text is so small on the video
Notes: https://youtu.be/x6hL-obNhAw

## Slide 28: How did we get here?
Computing industry demands more and faster storage with lower power consumption
Ability of user to circumvent the caching system
  clflush is an unprivileged instruction in x86
  Other commands exist that skip the cache
Availability of virtual to physical address mapping
  Example: /proc/self/pagemap on Linux (not human-readable)
Google patch for Android (Nov. 8, 2016)
  Patched the ION memory allocator

## Slide 29: More reading for those interested
DRAMMER paper: https://vvdveen.com/publications/drammer.pdf
Google Project Zero: https://googleprojectzero.blogspot.com/2015/03/exploiting-dram-rowhammer-bug-to-gain.html
First row hammer paper: https://users.ece.cmu.edu/~yoonguk/papers/kim-isca14.pdf
Wikipedia: https://en.wikipedia.org/wiki/Row_hammer

## Slide 30: Quick Review Answers
What do Page Tables map?
  VPN PPN or disk address
Where are Page Tables located?
  In physical memory
How many Page Tables are there?
  One per process
Can your program tell if a page fault has occurred?
  Nope, but it has to wait a long time
What is thrashing?
  Constantly paging out and paging in
True / False: Virtual Addresses that are contiguous will always be contiguous in physical memory
  Could fall across a page boundary
TLB stands for Translation Lookaside Buffer and stores page table entries