## Slide 1: Integers II CSE 351 Summer 2018
Instructor:
Justin Hsia
Teaching Assistants:
Josie Lee Natalie Andreeva Teagan Horkan
http://xkcd.com/1953/

## Slide 2: Administrivia
Lab 1a due Friday (6/29)
Lab 1b due next Thursday (7/5)
  Bonus slides at the end of today’s lecture have relevant examples
Homework 2 released today, due two Wed from now (7/11)
  Can start on Integers, will need to wait for Assembly

## Slide 3: Integers
Binary representation of integers
  Unsigned and signed
  Casting in C
Consequences of finite width representations
  Overflow, sign extension
Shifting and arithmetic operations
Notes: 3

## Slide 4: Arithmetic Overflow
When a calculation produces a result that can’t be represented in the current encoding scheme
  Integer range limited by fixed width
  Can occur in both the positive and negative directions
C and Java ignore overflow exceptions
  You end up with a bad value in your program and no warning/indication… oops!
Bits | Unsigned | Signed
0000 | 0 | 0
0001 | 1 | 1
0010 | 2 | 2
0011 | 3 | 3
0100 | 4 | 4
0101 | 5 | 5
0110 | 6 | 6
0111 | 7 | 7
1000 | 8 | -8
1001 | 9 | -7
1010 | 10 | -6
1011 | 11 | -5
1100 | 12 | -4
1101 | 13 | -3
1110 | 14 | -2
1111 | 15 | -1

## Slide 5: Overflow: Unsigned
Addition: drop carry bit ()
Subtraction: borrow ()
15
+ 2
17
1
1111
+ 0010
10001
0000
0001
0011
1111
1110
1100
1011
1010
1000
0111
0110
0100
0010
0101
1001
1101
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Unsigned
1
- 2
-1
15
10001
- 0010
1111
because of
modular arithmetic

## Slide 6: Overflow: Two’s Complement
Addition: () + () = () result?
Subtraction: () + () = ()?
0000
0001
0011
1111
1110
1100
1011
1010
1000
0111
0110
0100
0010
0101
1001
1101
0
+ 1
+ 2
+ 3
+ 4
+ 5
+ 6
+ 7
– 8
– 7
– 6
– 5
– 4
– 3
– 2
– 1
For signed: overflow if operands have same sign and result’s sign is different
Two’s Complement
6
+ 3
9
-7
0110
+ 0011
1001
-7
- 3
-10
6
1001
- 0011
0110

## Slide 7: Sign Extension
What happens if you convert a signed integral data type to a larger one?
  e.g. char short int long
4-bit 8-bit Example:
  Positive Case
    Add 0’s?
  Negative Case?
4-bit: | 0010 | = | +2
8-bit: | ????0010 | = | ?
00000010
+2
✓

## Slide 8: Peer Instruction Question
Which of the following 8-bit numbers has the same signed value as the 4-bit number 0b1100?
  Underlined digit = MSB
  Vote at http://PollEv.com/justinh
0b 0000 1100
0b 1000 1100
0b 1111 1100
0b 1100 1100
We’re lost…

## Slide 9: Sign Extension
Task: Given a -bit signed integer , convert it to +-bit signed integer with the same value
Rule: Add copies of sign bit
  Let be the -th digit of in binary
copies of MSB
• • •
• • •
• • •
• • •
original
Notes: General algorithm for any number of bits

## Slide 10: Sign Extension Example
Convert from smaller to larger integral data types
C automatically performs sign extension
  Java too
short int x = 12345;
int ix = (int) x;
short int y = -12345;
int iy = (int) y;
Var | Decimal | Hex | Binary
x | 12345 | 30 39 | 00110000 00111001
ix | 12345 | 00 00 30 39 | 00000000 00000000 00110000 00111001
y | -12345 | CF C7 | 11001111 11000111
iy | -12345 | FF FF CF C7 | 11111111 11111111 11001111 11000111

## Slide 11: Integers
Binary representation of integers
  Unsigned and signed
  Casting in C
Consequences of finite width representations
  Overflow, sign extension
Shifting and arithmetic operations
Notes: 11

## Slide 12: Shift Operations
Left shift (x<<n) bit vector x by n positions
  Throw away (drop) extra bits on left
  Fill with 0s on right
Right shift (x>>n) bit-vector x by n positions
  Throw away (drop) extra bits on right
  Logical shift (for unsigned values)
    Fill with 0s on left
  Arithmetic shift (for signed values)
    Replicate most significant bit on left
    Maintains sign of x
Notes: Useful operator when working with bit representations
Especially Lab 1
1001

## Slide 13: Shift Operations
Left shift (x<<n)
  Fill with 0s on right
Right shift (x>>n)
  Logical shift (for unsigned values)
    Fill with 0s on left
  Arithmetic shift (for signed values)
    Replicate most significant bit on left
Notes:
  Shifts by n<0 or nw (bit width of x) are undefined
  In C: behavior of >> is determined by compiler
    In gcc / C lang, depends on data type of x (signed/unsigned)
  In Java: logical shift is >>> and arithmetic shift is >>
 | x | 0010 0010
 | x<<3 | 0001 0000
logical: | x>>2 | 0000 1000
arithmetic: | x>>2 | 0000 1000
 | x | 1010 0010
 | x<<3 | 0001 0000
logical: | x>>2 | 0010 1000
arithmetic: | x>>2 | 1110 1000

## Slide 14: Shifting Arithmetic?
What are the following computing?
  x>>n
    0b 0100 >> 1 = 0b 0010
    0b 0100 >> 2 = 0b 0001
    Divide by 2n
  x<<n
    0b 0001 << 1 = 0b 0010
    0b 0001 << 2 = 0b 0100
    Multiply by 2n
Shifting is faster than general multiply and divide operations
Notes: 0100 (4) >> 1 = 0010 (2)
0001 (1) << 2 = 0100 (4)

## Slide 15: Left Shift Arithmetic 8-bit Example
No difference in left shift operation for unsigned and signed numbers (just manipulates bits)
  Difference comes during interpretation: x*2n?
x = 25; 00011001 =
L1=x<<2; 0001100100 =
L2=x<<3; 00011001000 =
L3=x<<4; 000110010000 =
25 25
100 100
-56 200
-112 144
Signed Unsigned
signed overflow
unsigned overflow
signed overflow

## Slide 16: Right Shift Arithmetic 8-bit Example
Reminder: C operator >> does logical shift on unsigned values and arithmetic shift on signed values
  Logical Shift: x/2n?
xu = 240u; 11110000 =
R1u=xu>>3; 00011110000 =
R2u=xu>>5; 0000011110000 =
240
30
7
rounding (down)

## Slide 17: Right Shift Arithmetic 8-bit Example
Reminder: C operator >> does logical shift on unsigned values and arithmetic shift on signed values
  Arithmetic Shift: x/2n?
xs = -16; 11110000 =
R1s=xu>>3; 11111110000 =
R2s=xu>>5; 1111111110000 =
-16
-2
-1
rounding (down)

## Slide 18: Peer Instruction Question
Assume we are using 8-bit arithmetic:
  x == (unsigned char) x
  x >= 128U
  x != (x>>2)<<2
  x == -x
    Hint: there are two solutions
  (x < 128U) && (x > 0x3F)
For the following expressions, find a value of signed char x, if there exists one, that makes the expression TRUE. Compare with your neighbor(s)!

## Slide 19: Unsigned Multiplication in C
Standard Multiplication Function
  Ignores high order bits
Implements Modular Arithmetic
  UMultw(u , v) = u · v mod 2w
• • •
• • •
u
v
*
• • •
u · v
• • •
True Product: bits
Operands: bits
Discard bits: bits
UMultw(u , v)
• • •

## Slide 20: Multiplication with shift and add
Operation u<<k gives u*2k
  Both signed and unsigned
Examples:
  u<<3 == u * 8
  u<<5 - u<<3 == u * 24
  Most machines shift and add faster than multiply
    Compiler generates this code automatically
• • •
u
2k
*
u · 2k
True Product: bits
Operands: bits
Discard bits: bits
UMultw(u , 2k)
0
0
1
0
0
0
•••
•••
k
• • •
0
0
0
•••
TMultw(u , 2k)
0
0
0
•••
•••

## Slide 21: Number Representation Revisited
What can we represent in one word?
  Signed and Unsigned Integers
  Characters (ASCII)
  Addresses
How do we encode the following:
  Real numbers (e.g. 3.14159)
  Very large numbers (e.g. 6.02×1023)
  Very small numbers (e.g. 6.626×10-34)
  Special numbers (e.g. ∞, NaN)
Floating
Point

## Slide 22: Floating Point Topics
Fractional binary numbers
IEEE floating-point standard
Floating-point operations and rounding
Floating-point in C
There are many more details that we won’t cover
  It’s a 58-page standard…
Notes: Start by talking about representing fractional numbers in binary in general
Then about the IEEE Standard for floating point representation, operations,
Will not cover:
  All the details of the 58-page spec
  Or expect you to perform operations
Want to show you how floating point values are represented
  To give you a sense of the kinds of things that can go wrong with them

## Slide 23: Representation of Fractions
“Binary Point,” like decimal point, signifies boundary between integer and fractional parts:
Example 6-bit representation:
Example: 10.10102 = 1×21 + 1×2-1 + 1×2-3 = 2.62510
Binary point numbers that match the 6-bit format above range from 0 (00.00002) to 3.9375 (11.11112)
xx.yyyy
21
20
2-1
2-2
2-3
2-4

## Slide 24: Scientific Notation (Decimal)
Normalized form: exactly one digit (non-zero) to left of decimal point
Alternatives to representing 1/1,000,000,000
  Normalized: 1.0×10-9
  Not normalized: 0.1×10-8,10.0×10-10
6.0210 × 1023
radix (base)
decimal point
exponent
mantissa

## Slide 25: Scientific Notation (Binary)
Computer arithmetic that supports this called floating point due to the “floating” of the binary point
  Declare such variable in C as float (or double)
1.012 × 2-1
radix (base)
mantissa
exponent
binary point

## Slide 26: Scientific Notation Translation
Convert from scientific notation to binary point
  Shift the decimal until the exponent disappears
    Example: 1.011224 = 101102 = 2210
    Example: 1.01122-2 = 0.010112 = 0.3437510
Convert from binary point to normalized scientific notation
  Distribute exponent until binary point is to the right of a single digit
    Example: 1101.0012 = 1.1010012×23
Practice: Convert 11.37510 to normalized binary scientific notation
Practice: Convert 1/5 to binary
Notes: Fraction like 1/3 needs an infinite number of digits to be represented, even in base 10!

## Slide 27: Summary
Sign and unsigned variables in C
  Bit pattern remains the same, just interpreted differently
  Strange things can happen with our arithmetic when we convert/cast between sign and unsigned numbers
    Type of variables affects behavior of operators (shifting, comparison)
We can only represent so many numbers in bits
  When we exceed the limits, arithmetic overflow occurs
  Sign extension tries to preserve value when expanding
Shifting is a useful bitwise operator
  Right shifting can be arithmetic (sign) or logical (0)
  Can be used in multiplication with constant or bit masking

## Slide 28
Some examples of using shift operators in combination with bitmasks, which you may find helpful for Lab 1. We will try to cover these in lecture or section if we have the time.
Extract the 2nd most significant byte of an int
Extract the sign bit of a signed int
Conditionals as Boolean expressions
BONUS SLIDES

## Slide 29: Using Shifts and Masks
Extract the 2nd most significant byte of an int:
  First shift, then mask: (x>>16) & 0xFF
  Or first mask, then shift: (x & 0xFF0000)>>16
0xFF | 00000000 | 00000000 | 00000000 | 11111111
(x>>16) & 0xFF | 00000000 | 00000000 | 00000000 | 00000010
x>>16 | 00000000 | 00000000 | 00000001 | 00000010
x | 00000001 | 00000010 | 00000011 | 00000100
x & 0xFF0000 | 00000000 | 00000010 | 00000000 | 00000000
(x&0xFF0000)>>16 | 00000000 | 00000000 | 00000000 | 00000010
0xFF0000 | 00000000 | 11111111 | 00000000 | 00000000
x | 00000001 | 00000010 | 00000011 | 00000100

## Slide 30: Using Shifts and Masks
Extract the sign bit of a signed int:
  First shift, then mask: (x>>31) & 0x1
    Assuming arithmetic shift here, but this works in either case
    Need mask to clear 1s possibly shifted in
x | 00000001 | 00000010 | 00000011 | 00000100
x>>31 | 00000000 | 00000000 | 00000000 | 00000000
0x1 | 00000000 | 00000000 | 00000000 | 00000001
(x>>31) & 0x1 | 00000000 | 00000000 | 00000000 | 00000000
x | 10000001 | 00000010 | 00000011 | 00000100
x>>31 | 11111111 | 11111111 | 11111111 | 11111111
0x1 | 00000000 | 00000000 | 00000000 | 00000001
(x>>31) & 0x1 | 00000000 | 00000000 | 00000000 | 00000001
0
0
1
1

## Slide 31: Using Shifts and Masks
Conditionals as Boolean expressions
  For int x, what does (x<<31)>>31 do?
  Can use in place of conditional:
    In C: if(x) {a=y;} else {a=z;} equivalent to a=x?y:z;
    a=(((x<<31)>>31)&y) | (((!x<<31)>>31)&z);
x=!!123 | 00000000 | 00000000 | 00000000 | 00000001
x<<31 | 10000000 | 00000000 | 00000000 | 00000000
(x<<31)>>31 | 11111111 | 11111111 | 11111111 | 11111111
!x | 00000000 | 00000000 | 00000000 | 00000000
!x<<31 | 00000000 | 00000000 | 00000000 | 00000000
(!x<<31)>>31 | 00000000 | 00000000 | 00000000 | 00000000
Notes: Use !! to force to 0/1