## Slide 1: Memory, Data, & Addressing I CSE 351 Winter 2018
Instructor:
Mark Wyse
Teaching Assistants:
Kevin Bi
Parker DeWilde
Emily Furst
Sarah House
Waylon Huang
Vinny Palaniappan
http://xkcd.com/953/
Notes: Close the doors!

## Slide 2: Administrivia
Pre-Course Survey due tonight @ 11:59pm
Lab 0 due Monday (1/8)
Homework 1 due Wednesday (1/10)
All course materials can be found on the website/schedule
Course Overloads – fill out the Google Form linked in lecture 1!
Make sure you’re also enrolled in CSE391 (EEs and non-majors included!)
Notes: Overloads: handled by CSE advising, fill out the form, they will decide who gets spots.
If not in course yet, don’t worry, you will get a fair chance to submit these assignments.

## Slide 3: Roadmap
car *c = malloc(sizeof(car));
c->miles = 100;
c->gals = 17;
float mpg = get_mpg(c);
free(c);
Car c = new Car();
c.setMiles(100);
c.setGals(17);
float mpg = c.getMPG();
get_mpg:
pushq %rbp
movq %rsp, %rbp
...
popq %rbp
ret
Java:
C:
Assembly language:
Machine code:
0111010000011000
100011010000010000000010
1000100111000010
110000011111101000011111
Computer system:
OS:
Memory & data
Integers & floats
x86 assembly
Procedures & stacks
Executables
Arrays & structs
Memory & caches
Processes
Virtual memory
Memory allocation
Java vs. C
Notes: Today we’ll be talking about the basic execution model, and focusing on how data gets stored in memory and addressed

## Slide 4: Hardware: Logical View
CPU
Memory
Disks
Net
USB
Etc.
Bus
Notes: CPU: all computations done here (workhorse)
Memory: big array of bytes, (local storage)
Big pipe between CPU and memory, in order to keep CPU fed
Bus: connect everything else to each other
  Bus just means you broadcast on it (to everyone)
  Same root as the other kind of “bus”
  “interconnection”
Disks bigger storage, slower, farther away, persistent
Network, etc.

## Slide 5: Hardware: Physical View
CPU
(socket)
Bus connections
I/O controller
Storage connections
Memory

## Slide 6: Hardware: 351 View (version 0)
CPU executes instructions; memory stores data
To execute an instruction, the CPU must:
  fetch an instruction;
  fetch the data used by the instruction; and, finally,
  execute the instruction on the data…
  which may result in writing data back to memory
Memory
CPU
?
data
instructions
Notes: The CPU and Memory are what this course focuses on.
Instructions = “constant fetching”
Data = “load” and “store”

## Slide 7: Hardware: 351 View (version 1)
The CPU holds instructions temporarily in the instruction cache
The CPU holds data temporarily in a fixed number of registers
Instruction and operand fetching is hardware-controlled
Data movement is programmer-controlled (in assembly)
We’ll learn about the instructions the CPU executes – take CSE/EE 469 and 470 to find out how it actually executes them
Memory
data
instructions
CPU
take 470…
registers
i-cache
this week…
Notes: How it executes is architecture and microarchitecture of the CPU
  Out-of-order, speculative execution
  If you’ve been keeping up with the Meltdown and Spectre CPU bugs

## Slide 8: Hardware: 351 View (version 1)
The CPU holds instructions temporarily in the instruction cache
The CPU holds data temporarily in a fixed number of registers
Instruction and operand fetching is hardware-controlled
Data movement is programmer-controlled (in assembly)
We’ll learn about the instructions the CPU executes – take CSE/EE 469 and 470 to find out how it actually executes them
Memory
data
instructions
CPU
take 470…
registers
i-cache
this week…
How are data and instructions represented?
How does a program find its data in memory?

## Slide 9: Question 1:
Binary Encoding!
Memory
data
instructions
CPU
take 470…
registers
i-cache
this week…
How are data and instructions represented?
Notes: Okay so first…

## Slide 10: Question 1: Some Additional Details
Because storage is finite in reality, everything is stored as “fixed” length
  Data is moved and manipulated in fixed-length chunks
  Multiple fixed lengths (e.g. 1 byte, 4 bytes, 8 bytes)
  Leading zeros now must be included up to “fill out” the fixed length
Example: the “eight-bit” representation of the number 4 is 0b00000100
Least Significant Bit (LSB)
Most Significant Bit (MSB)
Notes: Extra 0’s = “padding”
MSB = 2^n-1, “most weight”
LSB = 2^0, “least weight”

## Slide 11: Question 2:
Memory
data
instructions
CPU
take 470…
registers
i-cache
this week…
How does a program find its data in memory?

## Slide 12: Byte-Oriented Memory Organization
Conceptually, memory is a single, large array of bytes, each with a unique address (index)
  The value of each byte in memory can be read and written
Programs refer to bytes in memory by their addresses
  Domain of possible addresses = address space
But not all values fit in a single byte… (e.g. 351)
  Many operations actually use multi-byte values
We can store addresses as data to “remember” where other data is in memory
00•••0
FF•••F
 |  |  |  |  |  | • • • |  |  |  |  |  | 
Notes: Each byte can be read and written
Address space determined by how many bits in the address
00…….0 = “lowest address”
FF……F = “highest address”
So what if things don’t fit in a single byte?
How many things does 1 byte allow us to address?
Last bullet = “pointers”!!

## Slide 13: Peer Instruction Question
If we choose to use 8-bit addresses, how big is our address space?
  i.e. How much space can we “refer to” using our addresses?
256 bits
256 bytes
8 bits
8 bytes
We’re lost…
Notes: Answer: B. 256 bytes
  8 bits can represent 2^8 things, each addr is a byte
  Byte Addressable Memory!
Ink out the answer

## Slide 14: Machine “Words”
Instructions encoded into machine code (0’s and 1’s)
  Historically (still true in some assembly languages), all instructions were exactly the size of a word
Word size bounds the size of the address space
  word size = address size = register size
  word size = bits addresses
Current x86 systems use 64-bit (8-byte) words
  Potential address space: addresses 264 bytes  1.8 x 1019 bytes = 18 billion billion bytes = 18 EB (exabytes)
  Actual physical address space: 48 bits
Notes:     Instead, we typically talk about addresses in terms of “words”
      Use same word size anywhere that you typically store addresses
      Word size is a “design decision”
    You could count the world population with 33 fingers (using population number of 7.454 billion)

## Slide 15: Word-Oriented Memory Organization
Addresses still specify locations of bytes in memory
  Addresses of successive words differ by word size (in bytes): e.g. 4 (32-bit) or 8 (64-bit)
  Address of word 0, 1, … 10?
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
32-bit
Words
Bytes
0x0C
0x0D
0x0E
0x0F
64-bit
Words
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr.
(hex)
Notes: What do we use to address bigger chunks of bytes?

## Slide 16: Word-Oriented Memory Organization
Addresses still specify locations of bytes in memory
  Addresses of successive words differ by word size (in bytes): e.g. 4 (32-bit) or 8 (64-bit)
  Address of word 0, 1, … 10?
Address of word = address of first byte in word
  The address of any chunk of memory is given by the address of the first byte
  Alignment
32-bit
Words
Bytes
64-bit
Words
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
0000
0004
0008
0012
0000
0008
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
0x0C
0x0D
0x0E
0x0F
Addr.
(hex)
Notes: Use the first byte of the word
Still count by bytes
Aside: isn’t this wasteful?
  Yes, but remember how much we can address with 64 bits? Probably don’t need to worry too much.

## Slide 17: A Picture of Memory (64-bit view)
A “64-bit (8-byte) word-aligned” view of memory:
  In this type of picture, each row is composed of 8 bytes
  Each cell is a byte
  A 64-bit pointer will fit on one row
0x00
0x
0x
0x
0x
0x
0x
0x
0x
0x
0x04
0x05
0x06
0x07
0x00
0x01
0x02
0x03
one word
Address
Notes: 0x00 = “beginning of memory”
In this course, we’ll be doing everything in 64-bits
What’s the second row’s address going to be?
  0x08
Third?
  0x10

## Slide 18: A Picture of Memory (64-bit view)
A “64-bit (8-byte) word-aligned” view of memory:
  In this type of picture, each row is composed of 8 bytes
  Each cell is a byte
  A 64-bit pointer will fit on one row
0x00
0x08
0x10
0x18
0x20
0x28
0x30
0x38
0x40
0x48
Address
one word
0x04
0x05
0x06
0x07
0x00
0x01
0x02
0x03
0x0D
0x0E
0x0F
0x0C
0x09
0x0A
0x0B
0x08
Notes: 16’s digit is the digit after the x

## Slide 19: Addresses and Pointers
An address is a location in memory
A pointer is a data object that holds an address
  Address can point to any data
Value 351 stored at address 0x08
  35110 = 15F16 = 0x 00 ... 00 01 5F
Pointer stored at 0x38 points to address 0x08
0x00
0x08
0x10
0x18
0x20
0x28
0x30
0x38
0x40
0x48
Address
00
00
00
00
00
00
01
5F
00
00
00
00
00
00
00
08
64-bit example
(pointers are 64-bits wide)
big-endian
Notes: Note that everything is just padded with extra 0s
15F16 = 1 x 16^2 + 5 x 16^1 + 15 x 16^0 = 256 * 80 * 15

## Slide 20: Addresses and Pointers
An address is a location in memory
A pointer is a data object that holds an address
  Address can point to any data
Pointer stored at 0x48 points to address 0x38
  Pointer to a pointer!
Is the data stored at 0x08 a pointer?
  Could be, depending on how you use it
0x00
0x08
0x10
0x18
0x20
0x28
0x30
0x38
0x40
0x48
Address
00
00
00
00
00
00
01
5F
00
00
00
00
00
00
00
08
00
00
00
00
00
00
00
38
64-bit example
(pointers are 64-bits wide)
big-endian
Notes: Note that everything is just padded with extra 0s

## Slide 21: Data Representations
Sizes of data types (in bytes)
To use “bool” in C, you must #include <stdbool.h>
Java Data Type | C Data Type | 32-bit (old) | x86-64
boolean | bool | 1 | 1
byte | char | 1 | 1
char |  | 2 | 2
short | short int | 2 | 2
int | int | 4 | 4
float | float | 4 | 4
 | long int | 4 | 8
double | double | 8 | 8
long | long | 8 | 8
 | long double | 8 | 16
(reference) | pointer * | 4 | 8
(reference) | pointer * | 4 | 8
address size = word size
Notes: This mapping is mostly an arbitrary historical artifact except for address sizes.
We will focus on x86-64
Ink – cross out 32-bit column

## Slide 22: More on Memory Alignment in x86-64
For good memory system performance, Intel recommends data be aligned
  However the x86-64 hardware will work correctly regardless of alignment of data
  Design choice: x86-64 instructions are variable bytes long
Aligned: Primitive object of bytes must have an address that is a multiple of
  More about alignment later in the course
 | Type
1 | char
2 | short
4 | int, float
8 | long, double, pointers
 | Type
1 | char
2 | short
4 | int, float
8 | long, double, pointers
Notes: Alignment: used to reduce the number of memory system transactions
  More transactions may lower performance (may not be noticeable, though)
Padding used in structs, will come back to this later.

## Slide 23: Byte Ordering
How should bytes within a word be ordered in memory?
  Example: store the 4-byte (32-bit) int: 0x a1 b2 c3 d4
By convention, ordering of bytes called endianness
  The two options are big-endian and little-endian
    In which address does the least significant byte go?
    Based on Gulliver’s Travels: tribes cut eggs on different sides (big, little)
Notes: In which address does LSB go? “Biggest or littlest?”
Question: anyone know where term ‘Endian’ comes from?
Byte ordering only applies when working with multi-byte data!!
  Only applies intra-data
  Ordering of items in an array is preserved, but the ordering of bytes within each entry in array will differ

## Slide 24: Byte Ordering
Big-endian (SPARC, z/Architecture)
  Least significant byte has highest address
Little-endian (x86, x86-64)
  Least significant byte has lowest address
Bi-endian (ARM, PowerPC)
  Endianness can be specified as big or little (default)
Example: 4-byte data 0xa1b2c3d4 at address 0x100
0x100
0x101
0x102
0x103
01
23
45
67
0x100
0x101
0x102
0x103
67
45
23
01
Big-Endian
Little-Endian
a1
b2
c3
d4
d4
c3
b2
a1
Notes: Big Endian
  Most significant is first
Little Endian
  Looks backwards
  x86 is Little Endian!!! This will probably be confusing for a while; it still gets me occasionally.
  Let’s look at some more examples…
Trick: L-L-L
  Little endian = LSB = Lowest address

## Slide 25: Byte Ordering Examples
39
30
00
00
IA32, x86-64 (little-endian)
00
00
00
00
39
30
00
00
64-bit
x86-64
39
30
00
00
32-bit
IA32
30
39
00
00
SPARC (big-endian)
30
39
00
00
32-bit
SPARC
30
39
00
00
64-bit
SPARC
00
00
00
00
int x = 12345;
// or x = 0x3039;
long int y = 12345;
// or y = 0x3039;
(A long int is the size of a word)
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
Notes: Long = 4 bytes on 32-bit, 8 bytes on 64-bit machine

## Slide 26: Peer Instruction Question:
We store the value 0x 01 02 03 04 as a word at address 0x100 in a big-endian, 64-bit machine
What is the byte of data stored at address 0x104?
0x04
0x40
0x01
0x10
We’re lost…
0x104
0x105
0x106
0x107
0x100
0x101
0x102
0x103
64-bit
SPARC
Notes: Answer: C
Ink it out, similar to last slide
First, pad 0x01020304 to be a 64-bit word: 0x 00 00 00 00 01 02 03 04
Now, store this 64-bit word to address 0x100, on a big-endian machine
Recall previous slide, it will look like the SPARC 64-bit diagram.
Occupies addresses 0x100 through 0x107, and the LSB is in the highest address (0x107)

## Slide 27: Endianness
Endianness only applies to memory storage
Often programmer can ignore endianness because it is handled for you
  Bytes wired into correct place when reading or storing from memory (hardware)
  Compiler and assembler generate correct behavior (software)
Endianness still shows up:
  Logical issues: accessing different amount of data than how you stored it (e.g. store int, access byte as a char)
  Need to know exact values to debug memory errors
  Manual translation to and from machine code (in 351)
Notes: You will encounter endianness first hand in the programming labs!!!
  Lab 3 in particular

## Slide 28: Summary
Memory is a long, byte-addressed array
  Word size bounds the size of the address space and memory
  Different data types use different number of bytes
  Address of chunk of memory given by address of lowest byte in chunk
  Object of bytes is aligned if it has an address that is a multiple of
Pointers are data objects that hold addresses
Endianness determines memory storage order for multi-byte data