## Slide 1: x86-64 Programming I CSE 351 Winter 2018
Instructor:
Mark Wyse
Teaching Assistants:
Kevin Bi
Parker DeWilde
Emily Furst
Sarah House
Waylon Huang
Vinny Palaniappan
http://www.smbc-comics.com/?id=2999

## Slide 2: Administrivia
Homework 2 due Wednesday (1/24)
  x86-64 part extended until Monday, January 29
Lab 2 (x86-64) released today (1/22)
  Due on Friday, February 2 @ 11:59 pm
Don’t forget to read the book!
  Ch. 3 will be very helpful!

## Slide 3: x86-64 Programming I
Operand types
Moving data
Arithmetic operations
Memory addressing modes
  swap example
Address computation instruction (lea)

## Slide 4: Operand types
Immediate: Constant integer data
  Examples: $0x400, $-533
  Like C literal, but prefixed with ‘$’
  Encoded with 1, 2, 4, or 8 bytes depending on the instruction
Register: 1 of 16 integer registers
  Examples: %rax, %r13
  But %rsp reserved for special use
  Others have special uses for particular instructions
Memory: Consecutive bytes of memory at a computed address
  Simplest example: (%rax)
  Various other “address modes”
%rax
%rcx
%rdx
%rbx
%rsi
%rdi
%rsp
%rbp
%rN
Notes: These are the types of operands an assembly instruction can use
Not all instructions can use all types!
Not all combinations can be used
  E.g., no memory to memory moves

## Slide 5: Moving Data
General form: mov_ source, destination
  Missing letter (_) specifies size of operands
  Note that due to backwards-compatible support for 8086 programs (16-bit machines!), “word” means 16 bits = 2 bytes in x86 instruction names
  Lots of these in typical code
movb src, dst
  Move 1-byte “byte”
movw src, dst
  Move 2-byte “word”
movl src, dst
  Move 4-byte “long word”
movq src, dst
  Move 8-byte “quad word”

## Slide 6: movq Operand Combinations
 | Source | Dest | Src, Dest | C Analog
movq | Imm | Reg | movq $0x4, %rax | 
 |  | Mem | movq $-147, (%rax) | 
 | Reg | Reg | movq %rax, %rdx | 
 |  | Mem | movq %rax, (%rdx) | 
 | Mem | Reg | movq (%rax), %rdx | 
Cannot do memory-memory transfer with a single instruction
  How would you do it?
var_a = 0x4;
*p_a = -147;
var_d = var_a;
*p_d = var_a;
var_d = *p_a;
Notes: Memory to Memory:
  Memory to Reg, then Reg to Memory

## Slide 7: Some Arithmetic Operations
Binary (two-operand) Instructions:
  Beware argument order!
  No distinction between signed and unsigned
    Only arithmetic vs. logical shifts
  How do you implement “r3 = r1 + r2”?
Format | Computation | 
addq src, dst | dst = dst + src | (dst += src)
subq src, dst | dst = dst – src | 
imulq src, dst | dst = dst * src | signed mult
sarq src, dst | dst = dst >> src | Arithmetic
shrq src, dst | dst = dst >> src | Logical
shlq src, dst | dst = dst << src | (same as salq)
xorq src, dst | dst = dst ^ src | 
andq src, dst | dst = dst & src | 
orq src, dst | dst = dst ¦ src | 
Maximum of one memory operand
operand size specifier
Notes: Src and dst can be Imm, Reg, or Mem
Ink: circle or -> “operation”
Operand size specifier (b, w, l, q)
r3 = r1 + r2
  mov r1, r3
  add r2, r3

## Slide 8: Some Arithmetic Operations
Unary (one-operand) Instructions:
See CSPP Section 3.5.5 for more instructions: mulq, cqto, idivq, divq
Format | Computation | 
incq dst | dst = dst + 1 | increment
decq dst | dst = dst – 1 | decrement
negq dst | dst = –dst | negate
notq dst | dst = ~dst | bitwise complement
Notes: Why have a different inc operator?
  Smaller bit representation!
  Maybe faster implementation

## Slide 9: Arithmetic Example
long simple_arith(long x, long y)
{
long t1 = x + y;
long t2 = t1 * 3;
return t2;
}
Register | Use(s)
%rdi | 1st argument (x)
%rsi | 2nd argument (y)
%rax | return value
y += x;
y *= 3;
long r = y;
return r;
simple_arith:
addq %rdi, %rsi
imulq $3, %rsi
movq %rsi, %rax
ret
Notes: Function calling convention (get to it later) says which registers to use for arguments and return value
Compiler knows
  Arithmetic ops are like “+=“
  And it doesn’t need intermediate values anyway
  So it transforms it to...
Under Register/Use -> convention!
Must return in %rax
Ink: circle t1 and t2: don’t actually need new variables

## Slide 10: Example of Basic Addressing Modes
void swap(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret
Notes: Remind AT&T syntax: src, dst

## Slide 11: Understanding swap()
%rdi
%rsi
%rax
%rdx
Registers
Memory
Register Variable
%rdi ⇔ xp
%rsi ⇔ yp
%rax ⇔ t0
%rdx ⇔ t1
void swap(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret

## Slide 12: Understanding swap()
0x120
0x118
0x110
0x108
0x100
Word
Address
%rdi
%rsi
%rax
%rdx
0x120
0x100
Registers
Memory
123
456
123
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
Notes: But actually, pointers are just addresses!
Showing here 8-byte words of memory, addresses jump by 8

## Slide 13: Understanding swap()
0x120
0x118
0x110
0x108
0x100
Word
Address
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
Registers
Memory
123
456
123
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret

## Slide 14: Understanding swap()
0x120
0x118
0x110
0x108
0x100
Word
Address
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
123
456
123
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret

## Slide 15: Understanding swap()
0x120
0x118
0x110
0x108
0x100
Word
Address
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
123
456
456
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret

## Slide 16: Understanding swap()
0x120
0x118
0x110
0x108
0x100
Word
Address
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
123
123
456
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret

## Slide 17: Memory Addressing Modes: Basic
Indirect: (R) Mem[Reg[R]]
  Data in register R specifies the memory address
  Like pointer dereference in C
  Example: movq (%rcx), %rax
Displacement: D(R) Mem[Reg[R]+D]
  Data in register R specifies the start of some memory region
  Constant displacement D specifies the offset from that address
  Example: movq 8(%rbp), %rdx

## Slide 18: Complete Memory Addressing Modes
General:
  D(Rb,Ri,S) Mem[Reg[Rb]+Reg[Ri]*S+D]
    Rb: Base register (any register)
    Ri: Index register (any register except %rsp)
    S: Scale factor (1, 2, 4, 8) – why these numbers?
    D: Constant displacement value (a.k.a. immediate)
Special cases (see CSPP Figure 3.3 on p.181)
  D(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]+D] (S=1)
  (Rb,Ri,S) Mem[Reg[Rb]+Reg[Ri]*S] (D=0)
  (Rb,Ri) Mem[Reg[Rb]+Reg[Ri]] (S=1,D=0)
  (,Ri,S) Mem[Reg[Ri]*S] (Rb=0,D=0)
Notes: Syntax for memory operands can be more complex
Designed to do things that are common with pointers
D: displacement, add a constant
Rb: base pointer
Ri: index into array
S: scale the index (pointer arithmetic needs to scale by the size of the pointer target)
  compiler keeps track of what the pointer points to and scales accordingly
  int x[] x[i]
  ith element of an array of ints: Ri=i, S=4 (bytes)
See figure 3.3 in 3e textbook

## Slide 19: Address Computation Examples
%rdx
%rcx
0xf000
0x0100
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
D(Rb,Ri,S)
Mem[Reg[Rb]+Reg[Ri]*S+D]
Notes: 0xF008
0xF100
0xF400
0x1E080
  0xF000 * 2 = 0xF000 << 1 = 0x1E000

## Slide 20: Address Computation Instruction
leaq src, dst
  “lea” stands for load effective address
  src is address expression (any of the formats we’ve seen)
  dst is a register
  Sets dst to the address computed by the src expression (does not go to memory! – it just does math)
  Example: leaq (%rdx,%rcx,4), %rax
Uses:
  Computing addresses without a memory reference
    e.g. translation of p = &x[i];
  Computing arithmetic expressions of the form x+k*i+d
    Though k can only be 1, 2, 4, or 8
Notes: Those address calculations always go to memory except in one special case

## Slide 21: Example: lea vs. mov
0x120
0x118
0x110
0x108
0x100
Word
Address
Memory
123
0x10
0x1
0x400
0xF
0x8
Registers
%rax
%rbx
%rcx
%rdx
0x4
0x100
%rdi
%rsi
leaq (%rdx,%rcx,4), %rax
movq (%rdx,%rcx,4), %rbx
leaq (%rdx), %rdi
movq (%rdx), %rsi
Notes: 0x110
0x8
0x100
0x1
Yellow box: annotate lines for dsts
  Addr
  Data
  Addr
  Data

## Slide 22: Arithmetic Example
Interesting Instructions
  leaq: “address” computation
  salq: shift
  imulq: multiplication
    Only used once!
long arith(long x, long y, long z)
{
long t1 = x + y;
long t2 = z + t1;
long t3 = x + 4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
Register | Use(s)
%rdi | 1st argument (x)
%rsi | 2nd argument (y)
%rdx | 3rd argument (z)
arith:
leaq (%rdi,%rsi), %rax
addq %rdx, %rax
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx
leaq 4(%rdi,%rdx), %rcx
imulq %rcx, %rax
ret
Notes: Just jumping back to an arithmetic example now that we’ve covered lea to show how the compiler often generates lea instead of add, and sal (shift) instead of multiplication
y*48 becomes:
  leaq (%rsi,%rsi,2), %rdx == y*2+y == y*3
  salq $4, %rdx == (y*3) << 4 == (y*3)*2^4 == (y*3)*16
Use imulq when operand is dynamic (we don’t know at compile time what we’re multiplying by)

## Slide 23: Arithmetic Example
long arith(long x, long y, long z)
{
long t1 = x + y;
long t2 = z + t1;
long t3 = x + 4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
Register | Use(s)
%rdi | x
%rsi | y
%rdx | z, t4
%rax | t1, t2, rval
%rcx | t5
arith:
leaq (%rdi,%rsi), %rax # rax/t1 = x + y
addq %rdx, %rax # rax/t2 = t1 + z
leaq (%rsi,%rsi,2), %rdx # rdx = 3 * y
salq $4, %rdx # rdx/t4 = (3*y) * 16
leaq 4(%rdi,%rdx), %rcx # rcx/t5 = x + t4 + 4
imulq %rcx, %rax # rax/rval = t5 * t2
ret
Notes: Just jumping back to an arithmetic example now that we’ve covered lea to show how the compiler often generates lea instead of add, and sal (shift) instead of multiplication
y*48 becomes:
  leaq (%rsi,%rsi,2), %rdx == y*2+y == y*3
  salq $4, %rdx == (y*3) << 4 == (y*3)*2^4 == (y*3)*16
Use imulq when operand is dynamic (we don’t know at compile time what we’re multiplying by)

## Slide 24: Peer Instruction Question
Which of the following x86-64 instructions correctly calculates %rax=9*%rdi?
leaq (,%rdi,9), %rax
movq (,%rdi,9), %rax
leaq (%rdi,%rdi,8), %rax
movq (%rdi,%rdi,8), %rax
We’re lost…
Notes: C: remember that leaq can be used to perform arithmetic!
  leaq performs an address calculation, but does not dereference the address
  C gives: %rax = %rdi + %rdi * 8 = %rdi * 9
A:
  A is wrong because the scale factor can only be 1, 2, 4, or 8
B or D:
  B is wrong for the same reason as A, using a bad scale factor
  D is wrong because it computes the address %rdi * 9 then fetches the data at that address and stores it in %rax

## Slide 25: Summary
Operands: Assembly operands include immediates, registers, and data at a specified memory location.
Memory Addressing Modes: The addresses used for accessing memory in mov (and other) instructions can be computed in several different ways
  Base register, index register, scale factor, and displacement map well to pointer arithmetic operations
lea is address calculation instruction
  Does NOT actually go to memory
  Used to compute addresses or some arithmetic expressions