## Slide 1: Procedures & Executables CSE 351 Winter 2018
Instructor:
Mark Wyse
Teaching Assistants:
Kevin Bi
Parker DeWilde
Emily Furst
Sarah House
Waylon Huang
Vinny Palaniappan
https://xkcd.com/1537/

## Slide 2: Administrative
Lab 2 due Friday (2/2)
Lab 1 grading – see Piazza post
Midterm next Monday (2/5)
  Check Piazza this week for last minute announcements
  Bring your UW Student ID (Husky Card)
  Review session 2:00-4:00pm on Saturday (2/3) in EEB 125

## Slide 3: Procedures
Stack Structure
Calling Conventions
  Passing control
  Passing data
  Managing local data
Register Saving Conventions
Illustration of Recursion

## Slide 4: Register Saving Conventions
When procedure yoo calls who:
  yoo is the caller
  who is the callee
Can registers be used for temporary storage?
  No! Contents of register %rdx overwritten by who!
  This could be trouble – something should be done. Either:
    Caller should save %rdx before the call (and restore it after the call)
    Callee should save %rdx before using it (and restore it before returning)
yoo:
• • •
movq $15213, %rdx
call who
addq %rdx, %rax
• • •
ret
who:
• • •
subq $18213, %rdx
• • •
ret
?

## Slide 5: Register Saving Conventions
“Caller-saved” registers
  It is the caller’s responsibility to save any important data in these registers before calling another procedure (i.e. the callee can freely change data in these registers)
  Caller saves values in its stack frame before calling Callee, then restores values after the call
“Callee-saved” registers
  It is the callee’s responsibility to save any data in these registers before using the registers (i.e. the caller assumes the data will be the same across the callee procedure call)
  Callee saves values in its stack frame before using, then restores them before returning to caller

## Slide 6: x86-64 Linux Register Usage, part 1
%rax
  Return value
  Also caller-saved & restored
  Can be modified by procedure
%rdi, ..., %r9
  Arguments
  Also caller-saved & restored
  Can be modified by procedure
%r10, %r11
  Caller-saved & restored
  Can be modified by procedure
%rax
%rdx
%rcx
Return value
%r8
%r9
%r10
%r11
%rdi
%rsi
Arguments
Caller-saved
temporaries

## Slide 7: x86-64 Linux Register Usage, part 2
%rbx, %r12, %r13, %r14
  Callee-saved
  Callee must save & restore
%rbp
  Callee-saved
  Callee must save & restore
  May be used as frame pointer
  Can mix & match
%rsp
  Special form of callee save
  Restored to original value upon exit from procedure
%rbx
%rsp
Callee-saved
Temporaries
Special
%rbp
%r12
%r13
%r14

## Slide 8: x86-64 64-bit Registers: Usage Conventions
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
Callee saved
Callee saved
Callee saved
Callee saved
Caller saved
Caller Saved
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rsp
%rbp
Callee saved
Callee saved
Stack pointer
Return value - Caller saved
Argument #4 - Caller saved
Argument #1 - Caller saved
Argument #3 - Caller saved
Argument #2 - Caller saved
Argument #6 - Caller saved
Argument #5 - Caller saved

## Slide 9: Callee-Saved Example (step 1)
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $351, 8(%rsp)
movl $100, %esi
leaq 8(%rsp), %rdi
call increment
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 351;
long v2 = increment(&v1, 100);
return x+v2;
}
Initial Stack Structure
%rsp
. . .
ret addr
Resulting Stack Structure
351
Unused
%rsp
. . .
ret addr
%rsp+8
Saved %rbx
Notes: Modified example from earlier
  Now call_incr takes an argument, long x, which is used in computing its result
  x is in %rdi
  Need to save it somewhere: use a callee-saved register
But call_incr is a callee, too!
  Have to save %rbx for whoever called call_incr2

## Slide 10: Callee-Saved Example (step 2)
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $351, 8(%rsp)
movl $100, %esi
leaq 8(%rsp), %rdi
call increment
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
Pre-return Stack Structure
%rsp
. . .
Rtn address
Stack Structure
351
Unused
%rsp
. . .
Rtn address
%rsp+8
Saved %rbx
long call_incr2(long x) {
long v1 = 351;
long v2 = increment(&v1, 100);
return x+v2;
}
Notes: Can you think of another way we could have done this?
Push %rdi onto the stack
Why did the compiler choose this way?
  In this case it’s a wash, but if we ever use %rbx again, then it was worth it

## Slide 11: Why Caller and Callee Saved?
We want one calling convention to simply separate implementation details between caller and callee
In general, neither caller-save nor callee-save is “best”:
  If caller isn’t using a register, caller-save is better
  If callee doesn’t need a register, callee-save is better
  If “do need to save”, callee-save generally makes smaller programs
    Functions are called from multiple places
So… “some of each” and compiler tries to “pick registers” that minimize amount of saving/restoring
Notes: Remember: access to memory is slow

## Slide 12: Register Conventions Summary
Caller-saved register values need to be pushed onto the stack before making a procedure call only if the Caller needs that value later
  Callee may change those register values
Callee-saved register values need to be pushed onto the stack only if the Callee intends to use those registers
  Caller expects unchanged values in those registers
Don’t forget to restore/pop the values later!

## Slide 13: Procedures
Stack Structure
Calling Conventions
  Passing control
  Passing data
  Managing local data
Register Saving Conventions
Illustration of Recursion

## Slide 14: Recursive Function
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x&1)+pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
shrq %rdi
call pcount_r
andl $1, %ebx
addq %rbx, %rax
popq %rbx
.L6:
rep ret
Compiler Explorer:
https://godbolt.org/g/W8DxeR
Compiled with -O1 for brevity instead of -Og
Try -O2 instead!

## Slide 15: Recursive Function: Base Case
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x&1)+pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
shrq %rdi
call pcount_r
andl $1, %ebx
addq %rbx, %rax
popq %rbx
.L6:
rep ret
Register | Use(s) | Type
%rdi | x | Argument
%rax | Return value | Return value
Trick because some AMD hardware doesn’t like jumping to ret
Notes: First: look at the test:
  test if %rdi == 0
  If it does, then jump to the ret
Note: share ret between both cases, so set rax=0 before jump
Rep; ret is just because some HW doesn‘t like jumping to ret

## Slide 16: Recursive Function: Callee Register Save
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x&1)+pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
shrq %rdi
call pcount_r
andl $1, %ebx
addq %rbx, %rax
popq %rbx
.L6:
rep ret
Register | Use(s) | Type
%rdi | x | Argument
. . .
rtn <main+?>
saved %rbx
%rsp
Need original value of x after recursive call to pcount_r.
“Save” by putting in %rbx (callee saved), but need to save old value of %rbx before you change it.
The Stack
Notes: %rdi (x) is argument for both pcount_r instances (recursive caller and callee).
Choosing “to save”

## Slide 17: Recursive Function: Call Setup
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
shrq %rdi
call pcount_r
andl $1, %ebx
addq %rbx, %rax
popq %rbx
.L6:
rep ret
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x&1)+pcount_r(x >> 1);
}
Register | Use(s) | Type
%rdi | x (new) | Argument
%rbx | x (old) | Callee saved
. . .
rtn <main+?>
saved %rbx
%rsp
The Stack

## Slide 18: Recursive Function: Call
Register | Use(s) | Type
%rax | Recursive call return value | Return value
%rbx | x (old) | Callee saved
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x&1)+pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
shrq %rdi
call pcount_r
andl $1, %ebx
addq %rbx, %rax
popq %rbx
.L6:
rep ret
. . .
rtn <main+?>
saved %rbx
rtn <pcount_r+22>
. . .
%rsp
The Stack
Notes: Draw out example if x = 0b100

## Slide 19: Recursive Function: Result
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x&1)+pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
shrq %rdi
call pcount_r
andl $1, %ebx
addq %rbx, %rax
popq %rbx
.L6:
rep ret
Register | Use(s) | Type
%rax | Return value | Return value
%rbx | x&1 | Callee saved
. . .
rtn <main+?>
saved %rbx
%rsp
The Stack

## Slide 20: Recursive Function: Completion
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x&1)+pcount_r(x >> 1);
}
pcount_r:
movl $0, %eax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
shrq %rdi
call pcount_r
andl $1, %ebx
addq %rbx, %rax
popq %rbx
.L6:
rep ret
Register | Use(s) | Type
%rax | Return value | Return value
%rbx | Previous %rbx value | Callee restored
. . .
rtn <main+?>
saved %rbx
%rsp
The Stack

## Slide 21: Observations About Recursion
Works without any special consideration
  Stack frames mean that each function call has private storage
    Saved registers & local variables
    Saved return pointer
  Register saving conventions prevent one function call from corrupting another’s data
    Unless the code explicitly does so (e.g. buffer overflow)
  Stack discipline follows call / return pattern
    If P calls Q, then Q returns before P
    Last-In, First-Out (LIFO)
Also works for mutual recursion (P calls Q; Q calls P)

## Slide 22: x86-64 Stack Frames
Many x86-64 procedures have a minimal stack frame
  Only return address is pushed onto the stack when procedure is called
A procedure needs to grow its stack frame when it:
  Has too many local variables to hold in caller-saved registers
  Has local variables that are arrays or structs
  Uses & to compute the address of a local variable
  Calls another function that takes more than six arguments
  Is using caller-saved registers and then calls a procedure
  Modifies/uses callee-saved registers

## Slide 23: x86-64 Procedure Summary
Important Points
  Procedures are a combination of instructions and conventions
    Conventions prevent functions from disrupting each other
  Stack is the right data structure for procedure call/return
    If P calls Q, then Q returns before P
  Recursion handled by normal calling conventions
Heavy use of registers
  Faster than using memory
  Use limited by data size and conventions
Minimize use of the Stack
Return Addr
Saved
Registers
+
Local
Variables
Argument
Build
Old %rbp
Arguments
7+
Caller
Frame
%rbp
(Optional)
%rsp

## Slide 24: Roadmap
car *c = malloc(sizeof(car));
c->miles = 100;
c->gals = 17;
float mpg = get_mpg(c);
free(c);
Car c = new Car();
c.setMiles(100);
c.setGals(17);
float mpg = c.getMPG();
get_mpg:
pushq %rbp
movq %rsp, %rbp
...
popq %rbp
ret
Java:
C:
Assembly language:
Machine code:
0111010000011000
100011010000010000000010
1000100111000010
110000011111101000011111
Computer system:
OS:
Memory & data
Integers & floats
x86 assembly
Procedures & stacks
Executables
Arrays & structs
Memory & caches
Processes
Virtual memory
Memory allocation
Java vs. C

## Slide 25: Building an Executable from a C File
Code in files p1.c p2.c
Compile with command: gcc -Og p1.c p2.c -o p
  Put resulting machine code in file p
Run with command: ./p
text
text
binary
binary
Compiler (gcc –Og -S)
Assembler (gcc -c or as)
Linker (gcc or ld)
C program (p1.c p2.c)
Asm program (p1.s p2.s)
Object program (p1.o p2.o)
Executable program (p)
Static libraries (.a)
Loader (the OS)

## Slide 26: Compiler
Input: Higher-level language code (e.g. C, Java)
  foo.c
Output: Assembly language code (e.g. x86, ARM, MIPS)
  foo.s
First there’s a preprocessor step to handle #directives
  Macro substitution, plus other specialty directives
  If curious/interested: http://tigcc.ticalc.org/doc/cpp.html
Super complex, whole courses devoted to these!
Compiler optimizations
  “Level” of optimization specified by capital ‘O’ flag (e.g. -Og, -O3)
  Options: https://gcc.gnu.org/onlinedocs/gcc/Optimize-Options.html

## Slide 27: Compiling Into Assembly
C Code (sum.c)
x86-64 assembly (gcc –Og –S sum.c)
  Generates file sum.s (see https://godbolt.org/g/o34FHp)
Warning: You may get different results with other versions of gcc and different compiler settings
void sumstore(long x, long y, long *dest) {
long t = x + y;
*dest = t;
}
sumstore(long, long, long*):
addq %rdi, %rsi
movq %rsi, (%rdx)
ret
Notes: https://godbolt.org/g/5hQk8a

## Slide 28: Assembler
Input: Assembly language code (e.g. x86, ARM, MIPS)
  foo.s
Output: Object files (e.g. ELF, COFF)
  foo.o
  Contains object code and information tables
Reads and uses assembly directives
  e.g. .text, .data, .quad
  x86: https://docs.oracle.com/cd/E26502_01/html/E28388/eoiyg.html
Produces “machine language”
  Does its best, but object file is not a completed binary
Example: gcc -c foo.s
Notes: ELF = executable and linkable format
COFF = common object file format

## Slide 29: Producing Machine Language
Simple cases: arithmetic and logical operations, shifts, etc.
  All necessary information is contained in the instruction itself
What about the following?
  Conditional jump
  Accessing static data (e.g. global var or jump table)
  call
Addresses and labels are problematic because final executable hasn’t been constructed yet!
  So how do we deal with these in the meantime?

## Slide 30: Object File Information Tables
Symbol Table holds list of “items” that may be used by other files
  Non-local labels – function names for call
  Static Data – variables & literals that might be accessed across files
Relocation Table holds list of “items” that this file needs the address of later (currently undetermined)
  Any label or piece of static data referenced in an instruction in this file
    Both internal and external
Each file has its own symbol and relocation tables

## Slide 31: Object File Format
object file header: size and position of the other pieces of the object file
text segment: the machine code
data segment: data in the source file (binary)
relocation table: identifies lines of code that need to be “handled”
symbol table: list of this file’s labels and data that can be referenced
debugging information
More info: ELF format
  http://www.skyfree.org/linux/references/ELF_Format.pdf

## Slide 32: Linker
Input: Object files (e.g. ELF, COFF)
  foo.o
Output: executable binary program
  a.out
Combines several object files into a single executable (linking)
Enables separate compilation/assembling of files
  Changes to one file do not require recompiling of whole program

## Slide 33: Linking
Take text segment from each .o file and put them together
Take data segment from each .o file, put them together, and concatenate this onto end of text segments
Resolve References
  Go through Relocation Table; handle each entry
object file 1
info 1
data 1
text 1
object file 2
info 2
data 2
text 2
Linker
a.out
Relocated data 1
Relocated data 2
Relocated text 1
Relocated text 2

## Slide 34: Disassembling Object Code
Disassembled:
Disassembler (objdump -d sum)
  Useful tool for examining object code (man 1 objdump)
  Analyzes bit pattern of series of instructions
  Produces approximate rendition of assembly code
  Can run on either a.out (complete executable) or .o file
0000000000400536 <sumstore>:
400536: 48 01 fe add %rdi,%rsi
400539: 48 89 32 mov %rsi,(%rdx)
40053c: c3 retq

## Slide 35: What Can be Disassembled?
Anything that can be interpreted as executable code
Disassembler examines bytes and attempts to reconstruct assembly source
% objdump -d WINWORD.EXE
WINWORD.EXE: file format pei-i386
No symbols in "WINWORD.EXE".
Disassembly of section .text:
30001000 <.text>:
30001000: 55 push %ebp
30001001: 8b ec mov %esp,%ebp
30001003: 6a ff push $0xffffffff
30001005: 68 90 10 00 30 push $0x30001090
3000100a: 68 91 dc 4c 30 push $0x304cdc91
Reverse engineering forbidden by
Microsoft End User License Agreement

## Slide 36: Loader
Input: executable binary program, command-line arguments
  ./a.out arg1 arg2
Output: <program is run>
Loader duties primarily handled by OS/kernel
  More about this when we learn about processes
Memory sections (Instructions, Static Data, Stack) are set up
Registers are initialized