## Slide 1: Caches I CSE 351 Winter 2018
Instructor:
Mark Wyse
Teaching Assistants:
Kevin Bi
Parker DeWilde
Emily Furst
Sarah House
Waylon Huang
Vinny Palaniappan
http://xkcd.com/1353/
Alt text: I looked at some of the data dumps from vulnerable sites, and it was ... bad. I saw emails, passwords, password hints. SSL keys and session cookies. Important servers brimming with visitor IPs. Attack ships on fire off the shoulder of Orion, c-beams glittering in the dark near the Tannhäuser Gate. I should probably patch OpenSSL.

## Slide 2: Administrative
Lab 3 due Friday (2/16)
Midterm grades released later today
  Mean: 69%
  Median: 71%
  StDev: 13%
  Regrade requests done on Gradescope and due Friday (2/16)
Notes: Midterm average goal was ~75%

## Slide 3: Roadmap
car *c = malloc(sizeof(car));
c->miles = 100;
c->gals = 17;
float mpg = get_mpg(c);
free(c);
Car c = new Car();
c.setMiles(100);
c.setGals(17);
float mpg = c.getMPG();
get_mpg:
pushq %rbp
movq %rsp, %rbp
...
popq %rbp
ret
Java:
C:
Assembly language:
Machine code:
0111010000011000
100011010000010000000010
1000100111000010
110000011111101000011111
Computer system:
OS:
Memory & data
Integers & floats
x86 assembly
Procedures & stacks
Executables
Arrays & structs
Memory & caches
Processes
Virtual memory
Memory allocation
Java vs. C

## Slide 4: How does execution time grow with SIZE?
int array[SIZE];
int sum = 0;
for (int i = 0; i < 200000; i++) {
for (int j = 0; j < SIZE; j++) {
sum += array[j];
}
}
SIZE
Time
Plot
Notes: What should we expect for this experiment?
  Expect linear

## Slide 5: Actual Data
SIZE
Time
Data set > cache size
Data set < cache size
Notes: Knee in the curve
  After some size threshold
  Memory “wall”
Steeper slope = execution time grows faster
Fits in cache, doesn’t fit in cache

## Slide 6: Making memory accesses fast!
Cache basics
Principle of locality
Memory hierarchies
Cache organization
Program optimizations that consider caches

## Slide 7: Processor-Memory Gap
Chart: Year
| 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005
uProc | 1 | 1.35 | 1.82 | 2.46 | 3.32 | 4.48 | 6.05 | 8.17 | 12.67 | 19.63 | 30.43 | 47.17 | 73.11 | 113.32 | 175.65 | 272.26 | 422.01 | 654.11 | 1013.88 | 1571.51 | 2435.84 | 3775.55 | 5852.1 | 9070.75 | 9500 | 10000
DRAM | 1 | 1.07 | 1.15 | 1.23 | 1.31 | 1.4 | 1.5 | 1.61 | 1.72 | 1.84 | 1.97 | 2.1 | 2.25 | 2.41 | 2.58 | 2.76 | 2.95 | 3.16 | 3.38 | 3.62 | 3.87 | 4.14 | 4.43 | 4.74 | 5.07 | 5.43
“Moore’s Law”
Processor-Memory
Performance Gap (grows 50%/year)
1989 first Intel CPU with cache on chip
1998 Pentium III has two cache levels on chip
µProc
55%/year
(2X/1.5yr)
DRAM
7%/year
(2X/10yrs)
Notes: Earlier in course, we briefly talked about technology scaling

## Slide 8: Problem: Processor-Memory Bottleneck
Main Memory
CPU
Reg
Processor performance
doubled about
every 18 months
Bus latency / bandwidth
evolved much slower
Core 2 Duo:
Can process at least
256 Bytes/cycle
Core 2 Duo:
Bandwidth
2 Bytes/cycle
Latency
100-200 cycles (30-60ns)
Problem: lots of waiting on memory
cycle: single machine step (fixed-time)
Notes: What is a cycle
Only 2 hard problems in computer science: cache invalidation, naming things, and off-by-one errors.
Okay, so if one bite takes ~5-10 seconds
  Going to memory: 15-30 minutes: going to grocery store

## Slide 9: Problem: Processor-Memory Bottleneck
Main Memory
CPU
Reg
Processor performance
doubled about
every 18 months
Bus latency / bandwidth
evolved much slower
Core 2 Duo:
Can process at least
256 Bytes/cycle
Core 2 Duo:
Bandwidth
2 Bytes/cycle
Latency
100-200 cycles (30-60ns)
Solution: caches
Cache
cycle: single machine step (fixed-time)
Notes: Have your avocados and eat them too

## Slide 10: Cache 💰
Pronunciation: “cash”
  We abbreviate this as “$”
English: A hidden storage space for provisions, weapons, and/or treasures
Computer: Memory with short access time used for the storage of frequently or recently used instructions (i-cache/I$) or data (d-cache/D$)
  More generally: Used to optimize data transfers between any system elements with different characteristics (network interface cache, I/O cache, etc.)

## Slide 11: General Cache Mechanics
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
Larger, slower, cheaper memory.
Viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive memory
Caches a subset of the blocks
Notes: Note: these are not bytes: blocks

## Slide 12: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!
Data is returned to CPU
Notes: 1. access cache
2. return on hit

## Slide 13: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)
Data is returned to CPU
Notes: 1. access cache
2. miss
3. fill block to cache with fetch from memory
3. return data to CPU

## Slide 14: Why Caches Work
Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time
How do caches take advantage of this?
block
block

## Slide 15: Example: Any Locality?
Data:
  Temporal: sum referenced in each iteration
  Spatial: array a[] accessed in stride-1 pattern
Instructions:
  Temporal: cycle through loop repeatedly
  Spatial: reference instructions in sequence
sum = 0;
for (i = 0; i < n; i++) {
sum += a[i];
}
return sum;

## Slide 16: Locality Example #1
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}

## Slide 17: Locality Example #1
Access Pattern:
stride = ?
M = 3, N=4
Note: 76 is just one possible starting address of array a
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}
76
92
108
Layout in Memory
a[0][0] |  | a[0][1] |  | a[0][2] |  | a[0][3]
a[1][0] |  | a[1][1] |  | a[1][2] |  | a[1][3]
a[2][0] |  | a[2][1] |  | a[2][2] |  | a[2][3]
a [0] [0] | a [0] [1] | a [0] [2] | a [0] [3] | a [1] [0] | a [1] [1] | a [1] [2] | a [1] [3] | a [2] [0] | a [2] [1] | a [2] [2] | a [2] [3]
1) | a[0][0]
2) | a[0][1]
3) | a[0][2]
4) | a[0][3]
5) | a[1][0]
6) | a[1][1]
7) | a[1][2]
8) | a[1][3]
9) | a[2][0]
10) | a[2][1]
11) | a[2][2]
12) | a[2][3]
Notes: Stride-1

## Slide 18: Locality Example #2
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}
Notes: Now, flip the iteration over rows and columns
Iterate the columns first

## Slide 19: Locality Example #2
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}
76
92
108
Layout in Memory
a [0] [0] | a [0] [1] | a [0] [2] | a [0] [3] | a [1] [0] | a [1] [1] | a [1] [2] | a [1] [3] | a [2] [0] | a [2] [1] | a [2] [2] | a [2] [3]
M = 3, N=4
a[0][0] |  | a[0][1] |  | a[0][2] |  | a[0][3]
a[1][0] |  | a[1][1] |  | a[1][2] |  | a[1][3]
a[2][0] |  | a[2][1] |  | a[2][2] |  | a[2][3]
Access Pattern:
stride = ?
1) | a[0][0]
2) | a[1][0]
3) | a[2][0]
4) | a[0][1]
5) | a[1][1]
6) | a[2][1]
7) | a[0][2]
8) | a[1][2]
9) | a[2][2]
10) | a[0][3]
11) | a[1][3]
12) | a[2][3]
Notes: Stride-4 in this example
Stride-N in general

## Slide 20: Locality Example #3
What is wrong with this code?
How can it be fixed?
int sum_array_3D(int a[M][N][L])
{
int i, j, k, sum = 0;
for (i = 0; i < N; i++)
for (j = 0; j < L; j++)
for (k = 0; k < M; k++)
sum += a[k][i][j];
return sum;
}
a[2][0][0] |  | a[2][0][1] |  | a[2][0][2] |  | a[2][0][3]
a[2][1][0] |  | a[2][1][1] |  | a[2][1][2] |  | a[2][1][3]
a[2][2][0] |  | a[2][2][1] |  | a[2][2][2] |  | a[2][2][3]
a[1][0][0] |  | a[1][0][1] |  | a[1][0][2] |  | a[1][0][3]
a[1][1][0] |  | a[1][1][1] |  | a[1][1][2] |  | a[1][1][3]
a[1][2][0] |  | a[1][2][1] |  | a[1][2][2] |  | a[1][2][3]
a[0][0][0] |  | a[0][0][1] |  | a[0][0][2] |  | a[0][0][3]
a[0][1][0] |  | a[0][1][1] |  | a[0][1][2] |  | a[0][1][3]
a[0][2][0] |  | a[0][2][1] |  | a[0][2][2] |  | a[0][2][3]
m = 0
m = 1
m = 2
Notes: M = grids
N = rows
L = columns

## Slide 21: Locality Example #3
int sum_array_3D(int a[M][N][L])
{
int i, j, k, sum = 0;
for (i = 0; i < N; i++)
for (j = 0; j < L; j++)
for (k = 0; k < M; k++)
sum += a[k][i][j];
return sum;
}
What is wrong with this code?
How can it be fixed?
Layout in Memory (M = ?, N = 3, L = 4)
a [0] [0] [0] | a [0] [0] [1] | a [0] [0] [2] | a [0] [0] [3] | a [0] [1] [0] | a [0] [1] [1] | a [0] [1] [2] | a [0] [1] [3] | a [0] [2] [0] | a [0] [2] [1] | a [0] [2] [2] | a [0] [2] [3]
a [1] [0] [0] | a [1] [0] [1] | a [1] [0] [2] | a [1] [0] [3] | a [1] [1] [0] | a [1] [1] [1] | a [1] [1] [2] | a [1] [1] [3] | a [1] [2] [0] | a [1] [2] [1] | a [1] [2] [2] | a [1] [2] [3]
76
92
108
124
140
156
172
Notes: Grid 0, Grid 1
i -> stride-L
j -> stride-1
k -> stride-N*L

## Slide 22: Cache Performance Metrics
Huge difference between a cache hit and a cache miss
  Could be 100x speed difference between accessing cache and main memory (measured in clock cycles)
Miss Rate (MR)
  Fraction of memory references not found in cache (misses / accesses) = 1 - Hit Rate
Hit Time (HT)
  Time to deliver a block in the cache to the processor
    Includes time to determine whether the block is in the cache
Miss Penalty (MP)
  Additional time required because of a miss

## Slide 23: Cache Performance
Two things hurt the performance of a cache:
  Miss rate and miss penalty
  Average Memory Access Time (AMAT): average time to access memory considering both hits and misses
  AMAT = Hit time + Miss rate × Miss penalty
  (abbreviated AMAT = HT + MR × MP)
99% hit rate twice as good as 97% hit rate!
  Assume HT of 1 clock cycle and MP of 100 clock cycles
  97%: AMAT =
  99%: AMAT =
Notes: 97: 1 + 0.03*100 = 4 clock cycles
99: 1 + 0.01*100 = 2 clock cycles

## Slide 24: Peer Instruction Question
Processor specs: 200 ps clock, MP of 50 clock cycles, MR of 0.02 misses/instruction, and HT of 1 clock cycle
  AMAT = HT + MR*MP =
Which improvement would be best?
  190 ps clock
  Miss penalty of 40 clock cycles
  MR of 0.015 misses/instruction
Notes: AMAT = 1 + 0.02 * 50 = 2 cycles = 400 ps
A (faster CPU): 380 ps
B (faster Memory, smaller Memory): 360 ps
C (write better code): 350 ps
Answer: C

## Slide 25: Can we have more than one cache?
Why would we want to do that?
  Avoid going to memory!
Typical performance numbers:
  Miss Rate
    L1 MR = 3-10%
    L2 MR = Quite small (e.g. < 1%), depending on parameters, etc.
  Hit Time
    L1 HT = 4 clock cycles
    L2 HT = 10 clock cycles
  Miss Penalty
    P = 50-200 cycles for missing in L2 & going to main memory
    Trend: increasing!
Notes: 1. optimize L1 for fast Hit Time (HT)
2. optimize L2 for low Miss Rate (MR)

## Slide 26: Memory Hierarchies
Some fundamental and enduring properties of hardware and software systems:
  Faster storage technologies almost always cost more per byte and have lower capacity
  The gaps between memory technology speeds are widening
    True for: registers ↔ cache, cache ↔ DRAM, DRAM ↔ disk, etc.
  Well-written programs tend to exhibit good locality
These properties complement each other beautifully
  They suggest an approach for organizing memory and storage systems known as a memory hierarchy

## Slide 27: An Example Memory Hierarchy
registers
on-chip L1
cache (SRAM)
main memory
(DRAM)
local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
remote secondary storage
(distributed file systems, web servers)
off-chip L2
cache (SRAM)
Smaller,
faster,
costlier
per byte
<1 ns
1 ns
5-10 ns
100 ns
150,000 ns
10,000,000 ns (10 ms)
1-150 ms
SSD
Disk
Notes: Going to SSD is like walking down to California to get an avocado
Disk is like waiting a year for a new crop of avocados
Going across the world is like waiting for an avocado tree to grow up from a seed…

## Slide 28: Summary
Memory Hierarchy
  Successively higher levels contain “most used” data from lower levels
  Exploits temporal and spatial locality
  Caches are intermediate storage levels used to optimize data transfers between any system elements with different characteristics
Cache Performance
  Ideal case: found in cache (hit)
  Bad case: not found in cache (miss), search in next level
  Average Memory Access Time (AMAT) = HT + MR × MP
    Hurt by Miss Rate and Miss Penalty

## Slide 29: Aside: Units and Prefixes
Here focusing on large numbers (exponents > 0)
Note that 103 ≈ 210
SI prefixes are ambiguous if base 10 or 2
IEC prefixes are unambiguously base 2
Notes: Disk capacity SI to IEC conversion
512 GB = 512 * 10^9
  So, actual size is 512 * 10 ^9 / (2^30) Bytes = 477 GiB