## Slide 1: Caches II CSE 351 Winter 2018
Instructor:
Mark Wyse
Teaching Assistants:
Kevin Bi
Parker DeWilde
Emily Furst
Sarah House
Waylon Huang
Vinny Palaniappan

## Slide 2: Administrative
Lab 3 due Friday (2/16)
Homework 4 released today (Structs, Caches)
Midterm Regrade Requests due Friday (2/16)

## Slide 3: An Example Memory Hierarchy
registers
on-chip L1
cache (SRAM)
main memory
(DRAM)
local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
remote secondary storage
(distributed file systems, web servers)
Local disks hold files retrieved from disks on remote network servers
Main memory holds disk blocks retrieved from local disks
on-chip L2
cache (SRAM)
L1 cache holds cache lines retrieved from L2 cache
CPU registers hold words retrieved from L1 cache
L2 cache holds cache lines retrieved from main memory
Smaller,
faster,
costlier
per byte
Notes: Implemented with different technologies!
  disks, solid-state
  DRAM: little wells that drain slowly, refreshed periodically
  SRAM: flip-flops, little logic gates that feedback with each other, faster but uses more power!
That’s why they’re different sizes and costs

## Slide 4: An Example Memory Hierarchy
registers
on-chip L1
cache (SRAM)
main memory
(DRAM)
local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
remote secondary storage
(distributed file systems, web servers)
on-chip L2
cache (SRAM)
explicitly program-controlled (e.g. refer to exactly %rax, %rbx)
Smaller,
faster,
costlier
per byte
program sees “memory”;
hardware manages caching
transparently
Notes: So, why haven’t we seen caches before now in this class?
  Because they’re designed to be architecturally transparent!

## Slide 5: Memory Hierarchies
Fundamental idea of a memory hierarchy:
  For each level k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1
Why do memory hierarchies work?
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit
Big Idea: The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top

## Slide 6: Making memory accesses fast!
Cache basics
Principle of locality
Memory hierarchies
Cache organization
  Direct-mapped (sets; index + tag)
  Associativity (ways)
  Replacement policy
  Handling writes
Program optimizations that consider caches
Notes: Divide addresses into “index” and “tag”

## Slide 7: Cache Organization
Fundamental Equation:
Cache Size (): total capacity (Bytes) of cache
Block Size (): unit of transfer between and Mem
Sets (): collection of blocks
  Cache can be thought of as an “array of sets”
Associativity (): number of cache blocks per set
Address Bits (): number of bits in address

## Slide 8: Cache Organization (1)
Block Size (): unit of transfer between and Mem
  Given in bytes and always a power of 2 (e.g. 64 Bytes)
  Blocks consist of adjacent bytes (differ in address by 1)
    Spatial locality!
Offset field
  Low-order bits of address tell you which byte within a block
    (address) mod = lowest bits of address
  (address) modulo (# of bytes in a block)
Block Number
Block Offset
-bit address:
(refers to byte in memory)
bits
bits

## Slide 9: Cache Organization (2)
Cache Size (): amount of data the can store
  Cache can only hold so much data (subset of next level)
  Given in bytes () or number of blocks ()
  Example: = 32 KB = 512 blocks if using 64-Byte blocks
Where should data go in the cache?
  We need a mapping from memory addresses to specific locations in the cache to make checking the cache for an address fast
What is a data structure that provides fast lookup?
  Hash table!

## Slide 10: Review: Hash Tables for Fast Lookup
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 
Insert: 5
27
34
102
119
Apply hash function to map data to “buckets”
Notes: Example: mod 10
Goals of Hash Function:
Fast and simple calculation
Use all buckets “well”
hash(27) % N (10) = 7…

## Slide 11: Place Data in Cache by Hashing Address
Map to cache set index from block address
  Use next bits
  (block address) mod (# blocks in cache)
Block Addr | Block Data |  |  | 
0000 |  |  |  | 
0001 |  |  |  | 
0010 |  |  |  | 
0011 |  |  |  | 
0100 |  |  |  | 
0101 |  |  |  | 
0110 |  |  |  | 
0111 |  |  |  | 
1000 |  |  |  | 
1001 |  |  |  | 
1010 |  |  |  | 
1011 |  |  |  | 
1100 |  |  |  | 
1101 |  |  |  | 
1110 |  |  |  | 
1111 |  |  |  | 
Memory
Cache
Index | Block Data |  |  | 
00 |  |  |  | 
01 |  |  |  | 
10 |  |  |  | 
11 |  |  |  | 
Here = 4 B
and = 4
Notes: Assume 6-bit addresses. Show how to split into Index and Offset fields.

## Slide 12: Place Data in Cache by Hashing Address
Map to cache index from block address
  Lets adjacent blocks fit in cache simultaneously!
    Consecutive blocks go in consecutive cache indices
Block Addr | Block Data |  |  | 
0000 |  |  |  | 
0001 |  |  |  | 
0010 |  |  |  | 
0011 |  |  |  | 
0100 |  |  |  | 
0101 |  |  |  | 
0110 |  |  |  | 
0111 |  |  |  | 
1000 |  |  |  | 
1001 |  |  |  | 
1010 |  |  |  | 
1011 |  |  |  | 
1100 |  |  |  | 
1101 |  |  |  | 
1110 |  |  |  | 
1111 |  |  |  | 
Memory
Cache
Index | Block Data |  |  | 
00 |  |  |  | 
01 |  |  |  | 
10 |  |  |  | 
11 |  |  |  | 
Here = 4 B
and = 4

## Slide 13: Place Data in Cache by Hashing Address
Collision!
  This might confuse the cache later when we access the data
  Solution?
Block Addr | Block Data |  |  | 
0000 |  |  |  | 
0001 |  |  |  | 
0010 |  |  |  | 
0011 |  |  |  | 
0100 |  |  |  | 
0101 |  |  |  | 
0110 |  |  |  | 
0111 |  |  |  | 
1000 |  |  |  | 
1001 |  |  |  | 
1010 |  |  |  | 
1011 |  |  |  | 
1100 |  |  |  | 
1101 |  |  |  | 
1110 |  |  |  | 
1111 |  |  |  | 
Memory
Cache
Index | Block Data |  |  | 
00 |  |  |  | 
01 |  |  |  | 
10 |  |  |  | 
11 |  |  |  | 
Here = 4 B
and = 4

## Slide 14: Tags Differentiate Blocks in Same Index
Tag = rest of address bits
  bits =
  Check this during a cache lookup
Block Addr | Block Data |  |  | 
0000 |  |  |  | 
0001 |  |  |  | 
0010 |  |  |  | 
0011 |  |  |  | 
0100 |  |  |  | 
0101 |  |  |  | 
0110 |  |  |  | 
0111 |  |  |  | 
1000 |  |  |  | 
1001 |  |  |  | 
1010 |  |  |  | 
1011 |  |  |  | 
1100 |  |  |  | 
1101 |  |  |  | 
1110 |  |  |  | 
1111 |  |  |  | 
Memory
Cache
Index | Tag |  | Block Data |  |  | 
00 | 00 |  |  |  |  | 
01 |  |  |  |  |  | 
10 | 01 |  |  |  |  | 
11 | 01 |  |  |  |  | 
Here = 4 B
and = 4
Notes: Use a tag to differentiate between cache blocks that map to same Set (Index)

## Slide 15: Checking for a Requested Address
CPU sends address request for chunk of data
  Address and requested data are not the same thing!
    Analogy: your friend ≠ his or her phone number
TIO address breakdown:
  Index field tells you where to look in cache
  Tag field lets you check that data is the block you want
  Offset field selects specified start byte within block
  Note: and sizes will change based on hash function
Tag ()
Offset ()
-bit address:
Block Number
Index ()

## Slide 16: Direct-Mapped Cache
Hash function: (block address) mod (# of blocks in cache)
  Each memory address maps to exactly one index in the cache
  Fast (and simpler) to find an address
Block Addr | Block Data |  |  | 
00 00 |  |  |  | 
00 01 |  |  |  | 
00 10 |  |  |  | 
00 11 |  |  |  | 
01 00 |  |  |  | 
01 01 |  |  |  | 
01 10 |  |  |  | 
01 11 |  |  |  | 
10 00 |  |  |  | 
10 01 |  |  |  | 
10 10 |  |  |  | 
10 11 |  |  |  | 
11 00 |  |  |  | 
11 01 |  |  |  | 
11 10 |  |  |  | 
11 11 |  |  |  | 
Memory
Cache
Index | Tag |  | Block Data |  |  | 
00 | 00 |  |  |  |  | 
01 | 11 |  |  |  |  | 
10 | 01 |  |  |  |  | 
11 | 01 |  |  |  |  | 
Here = 4 B
and = 4

## Slide 17: Direct-Mapped Cache Problem
What happens if we access the following addresses?
  8, 24, 8, 24, 8, …?
  Conflict in cache (misses!)
  Rest of cache goes unused
Solution?
Block Addr | Block Data |  |  | 
00 00 |  |  |  | 
00 01 |  |  |  | 
00 10 |  |  |  | 
00 11 |  |  |  | 
01 00 |  |  |  | 
01 01 |  |  |  | 
01 10 |  |  |  | 
01 11 |  |  |  | 
10 00 |  |  |  | 
10 01 |  |  |  | 
10 10 |  |  |  | 
10 11 |  |  |  | 
11 00 |  |  |  | 
11 01 |  |  |  | 
11 10 |  |  |  | 
11 11 |  |  |  | 
Memory
Cache
Index | Tag |  | Block Data |  |  | 
00 | ?? |  |  |  |  | 
01 | ?? |  |  |  |  | 
10 |  |  |  |  |  | 
11 | ?? |  |  |  |  | 
Here = 4 B
and = 4
Notes: Conflict! Rest of cache unused!

## Slide 18: Associativity
What if we could store data in any place in the cache?
  More complicated hardware = more power consumed, slower
So we combine the two ideas:
  Each address maps to exactly one set
  Each set can store block in more than one way
0
1
2
3
4
5
6
7
0
1
2
3
Set
0
1
Set
1-way:
8 sets,
1 block each
2-way:
4 sets,
2 blocks each
4-way:
2 sets,
4 blocks each
0
Set
8-way:
1 set,
8 blocks
direct mapped
fully associative
Notes: Solution to conflicts with direct mapped caches is cache with higher associativity
“Where is address 2?”

## Slide 19: Cache Organization (3)
Associativity (): # of ways for each set
  Such a cache is called an “-way set associative cache”
  We now index into cache sets, of which there are
  Use lowest = bits of block address
    Direct-mapped: = 1, so = as we saw previously
    Fully associative: = , so = 0 bits
Decreasing associativity
Fully associative
(only one set)
Direct mapped
(only one way)
Increasing associativity
Selects the set
Used for tag comparison
Selects the byte from block
Tag ()
Index ()
Offset ()

## Slide 20: Example Placement
Where would data from address 0x1833 be placed?
  Binary: 0b 0001 1000 0011 0011
= ?
block size: | 16 B
capacity: | 8 blocks
address: | 16 bits
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Direct-mapped
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
Set | Tag | Data
0 |  | 
1 |  | 
2-way set associative
4-way set associative
Tag ()
Offset ()
-bit address:
Index ()
=
=
= ––
= ?
= ?
Notes: b = log2(B) = log2(16) = 4
s = log2(C/B/E) = log2(8/E)
E = 1 -> s = 3
E = 2 -> s = 2
E = 4 -> s = 1

## Slide 21: Block Replacement
Any empty block in the correct set may be used to store block
If there are no empty blocks, which one should we replace?
  No choice for direct-mapped caches
  Caches typically use something close to least recently used (LRU) (hardware usually implements “not most recently used”)
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Direct-mapped
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
Set | Tag | Data
0 |  | 
1 |  | 
2-way set associative
4-way set associative
Notes: Optimal = block used furthest in future
but, this is not possible to compute, so use an approximation
Approximation = LRU
Or, not most recently used
Or, pseudo-LRU

## Slide 22: General Cache Organization (, , )
= blocks/lines per set
= # sets
=
set
“line” (block plus management bits)
0
1
2
B-1
Tag
V
valid bit
= bytes per block
Cache size:
data bytes
(doesn’t include V or Tag)
Notes: “Layers” of a cache:
Block (data)
Line (data + management bits)
Set (many lines based on associativity)
Cache (many sets based on cache size & associativity)
Valid bit lets us know if this line has been initialized (“is valid”).

## Slide 23: Notation Review
We just introduced a lot of new variable names!
  Please be mindful of block size notation when you look at past exam questions or are watching videos
Variable | This Quarter | Formulas
Block size |  | 
Cache size |  | 
Associativity |  | 
Number of Sets |  | 
Address space |  | 
Address width |  | 
Tag field width |  | 
Index field width |  | 
Offset field width |  | 
Variable | This Quarter | Formulas
Block size |  | 
Cache size |  | 
Associativity |  | 
Number of Sets |  | 
Address space |  | 
Address width |  | 
Tag field width |  | 
Index field width |  | 
Offset field width |  | 

## Slide 24: Cache Read
0
1
2
B-1
tag
v
bits
bits
bits
Address of byte in memory:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set is valid and has matching tag: hit
Locate data starting at offset
valid bit
= # sets
=
= blocks/lines per set
= bytes per block

## Slide 25: Example: Direct-Mapped Cache ( = 1)
Direct-mapped: One line per set
Block Size = 8 Bytes
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set
= sets

## Slide 26: Example: Direct-Mapped Cache ( = 1)
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match?: yes = hit
valid? +
block offset
Direct-mapped: One line per set
Block Size = 8 Bytes

## Slide 27: Example: Direct-Mapped Cache ( = 1)
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match?: yes = hit
valid? +
int (4 B) is here
block offset
No match? Then old line gets evicted and replaced
This is why we want alignment!
Direct-mapped: One line per set
Block Size = 8 Bytes

## Slide 28: Example: Set-Associative Cache ( = 2)
bits
0…01
100
Address of short int:
find set
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
2-way: Two lines per set
Block Size = 8 Bytes

## Slide 29: Example: Set-Associative Cache ( = 2)
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
bits
0…01
100
compare both
valid? +
match: yes = hit
block offset
tag
2-way: Two lines per set
Block Size = 8 Bytes
Address of short int:

## Slide 30: Example: Set-Associative Cache ( = 2)
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
bits
0…01
100
valid? +
match: yes = hit
block offset
short int (2 B) is here
No match?
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …
compare both
Address of short int:
2-way: Two lines per set
Block Size = 8 Bytes
Notes: Do CAMERA demo here.

## Slide 31: Cache Puzzle #1
Based on the following behavior, which of the following block sizes is NOT possible for our cache?
  Cache starts empty, also known as a cold cache
  Access (addr: hit/miss) stream:
    (14: miss), (15: hit), (16: miss)
4 bytes
8 bytes
16 bytes
32 bytes
We’re lost…
Notes: Lab 4!
Answer: D

## Slide 32: Cache Puzzle #1
Based on the following behavior, which of the following block sizes is NOT possible for our cache?
  Cache starts empty, also known as a cold cache
  Access (addr: hit/miss) stream:
    (14: miss), (15: hit), (16: miss)
4 bytes
8 bytes
16 bytes
32 bytes
We’re lost…
Notes: Lab 4!
Answer: D

## Slide 33: Peer Instruction Question
We have a cache of size 2 KB with block size of 128 B. If our cache has 2 sets, what is its associativity?
2
4
8
16
We’re lost…
If addresses are 16 bits wide, how wide is the Tag field?
Notes: Answer: C