## Slide 1: Caches III CSE 351 Winter 2018
Instructor:
Mark Wyse
Teaching Assistants:
Kevin Bi
Parker DeWilde
Emily Furst
Sarah House
Waylon Huang
Vinny Palaniappan
https://what-if.xkcd.com/111/

## Slide 2: Administrative
Midterm regrade requests due today
Lab 3 due today!
HW 4 out, due Friday, February 23
No lecture on Monday – President’s Day!
  OH also cancelled

## Slide 3: Making memory accesses fast!
Cache basics
Principle of locality
Memory hierarchies
Cache organization
  Direct-mapped (sets; index + tag)
  Associativity (ways)
  Replacement policy
  Handling writes
Program optimizations that consider caches
Notes: Divide addresses into “index” and “tag”

## Slide 4: General Cache Organization (, , )
= blocks/lines per set
= # sets
=
set
“line” (block plus management bits)
0
1
2
B-1
Tag
V
valid bit
= bytes per block
Cache size:
data bytes
(doesn’t include V or Tag)
Notes: “Layers” of a cache:
Block (data)
Line (data + management bits)
Set (many lines based on associativity)
Cache (many sets based on cache size & associativity)
Valid bit lets us know if this line has been initialized (“is valid”).

## Slide 5: Notation Review
We just introduced a lot of new variable names!
  Please be mindful of block size notation when you look at past exam questions or are watching videos
Variable | This Quarter | Formulas
Block size |  | 
Cache size |  | 
Associativity |  | 
Number of Sets |  | 
Address space |  | 
Address width |  | 
Tag field width |  | 
Index field width |  | 
Offset field width |  | 
Variable | This Quarter | Formulas
Block size |  | 
Cache size |  | 
Associativity |  | 
Number of Sets |  | 
Address space |  | 
Address width |  | 
Tag field width |  | 
Index field width |  | 
Offset field width |  | 

## Slide 6: Cache Read
0
1
2
B-1
tag
v
bits
bits
bits
Address of byte in memory:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set is valid and has matching tag: hit
Locate data starting at offset
valid bit
= # sets
=
= blocks/lines per set
= bytes per block

## Slide 7: Types of Cache Misses: 3 C’s!
Compulsory (cold) miss
  Occurs on first access to a block
Conflict miss
  Conflict misses occur when the cache is large enough, but multiple data objects all map to the same slot
    e.g. referencing blocks 0, 8, 0, 8, ... could miss every time
  Direct-mapped caches have more conflict misses than -way set-associative (where > 1)
Capacity miss
  Occurs when the set of active cache blocks (the working set) is larger than the cache (just won’t fit, even if cache was fully-associative)
  Note: Fully-associative only has Compulsory and Capacity misses

## Slide 8: What about writes?
Multiple copies of data exist:
  L1, L2, possibly L3, main memory
What to do on a write-hit?
  Write-through: write immediately to next level
  Write-back: defer write to next level until line is evicted (replaced)
    Must track which cache lines have been modified (“dirty bit”)
What to do on a write-miss?
  Write-allocate: (“fetch on write”) load into cache, update line in cache
    Good if more writes or reads to the location follow
  No-write-allocate: (“write around”) just write immediately to memory
Typical caches:
  Write-back + Write-allocate, usually
  Write-through + No-write-allocate, occasionally
Notes: Why? Reuse is common
Typically you would read, then write (incr)
Or after you initialize a value (say, to 0), likely read and write it again soon
We will study: Write-Back + Write-Allocate
Take 469/470 to learn more about caches and cache optimizations

## Slide 9: Write-back, write-allocate example
0xBEEF
Cache
Memory
G
0xCAFE
0xBEEF
0
F
G
dirty bit
tag (there is only one set in this tiny cache, so the tag is the entire block address!)
In this example we are sort of ignoring block offsets. Here a block holds 2 bytes (16 bits, 4 hex digits).
Normally a block would be much bigger and thus there would be multiple items per block. While only one item in that block would be written at a time, the entire line would be brought into cache.
Contents of memory stored at address G
Notes: Note: not showing valid bit, but assume it is set (1) for all of example

## Slide 10: Write-back, write-allocate example
0xBEEF
Cache
Memory
G
0xCAFE
0xBEEF
0
F
G
mov 0xFACE, F
dirty bit
Notes: Write miss
Check cache for F -> miss
  Block G is not dirty, so data in cache is same as data in memory
Fetch block into $, then write

## Slide 11: Write-back, write-allocate example
0xBEEF
U
0
0xCAFE
Cache
Memory
F
0xCAFE
0xBEEF
F
G
dirty bit
0xCAFE
0
Step 1: Bring F into cache
mov 0xFACE, F

## Slide 12: Write-back, write-allocate example
0xBEEF
U
0
0xCAFE
Cache
Memory
F
0xCAFE
0xBEEF
F
G
dirty bit
0xFACE
1
Step 2: Write 0xFACE to cache only and set dirty bit
mov 0xFACE, F
Notes: Perform the write of 0xFACE into F in the $
Set the dirty bit because using write-back and writing new data to $

## Slide 13: Write-back, write-allocate example
0xBEEF
U
0
0xCAFE
Cache
Memory
F
0xCAFE
0xBEEF
F
G
mov 0xFEED, F
dirty bit
0xFACE
1
Write hit!
Write 0xFEED to cache only
mov 0xFACE, F
Notes: Write hit example
F is in $
But, write a new value into the block
F remains dirty (dirty bit = 1)

## Slide 14: Write-back, write-allocate example
0xBEEF
U
0
0xCAFE
Cache
Memory
F
0xCAFE
0xBEEF
F
G
mov G, %rax
dirty bit
0xFEED
1
mov 0xFEED, F
mov 0xFACE, F
Notes: Read miss

## Slide 15: Write-back, write-allocate example
0xBEEF
Cache
Memory
G
0xFEED
0xBEEF
0
F
G
dirty bit
1. Write F back to memory since it is dirty 2. Bring G into the cache so we can copy it into %rax
mov G, %rax
mov 0xFEED, F
mov 0xFACE, F
Notes: Write back F to memory since it was dirty
Load G to $ (read miss)
  Dirty bit remains unset (0) since data in $ is same as data in memory

## Slide 16: Optimizations for the Memory Hierarchy
Write code that has locality!
  Spatial: access data contiguously
  Temporal: make sure access to the same data is not too far apart in time
How can you achieve locality?
  Adjust memory accesses in code (software) to improve miss rate (MR)
    Requires knowledge of both how caches work as well as your system’s parameters
  Proper choice of algorithm
  Loop transformations

## Slide 17: Example: Matrix Multiplication
C
=
×
A
B
ai*
b*j
cij
Notes: Subscript indices given in (row,col).

## Slide 18: Matrices in Memory
How do cache blocks fit into this scheme?
  Row major matrix in memory:
Cache blocks
COLUMN of matrix (blue) is spread among cache blocks shown in red

## Slide 19: Naïve Matrix Multiply
# move along rows of A
for (i = 0; i < n; i++)
# move along columns of B
for (j = 0; j < n; j++)
# EACH k loop reads row of A, col of B
# Also read & write c(i,j) n times
for (k = 0; k < n; k++)
c[i*n+j] += a[i*n+k] * b[k*n+j];
C(i,j)
A(i,:)
B(:,j)
C(i,j)
Notes: Note the += leads to an additional read of matrix C
Read A
Read B
Read C
Write C (guaranteed hit due to read of C)

## Slide 20: Cache Miss Analysis (Naïve)
Scenario Parameters:
  Square matrix (), elements are doubles
  Cache block size = 64 B = 8 doubles
  Cache size (much smaller than )
Each iteration:
  misses
Ignoring
matrix c
Notes: Each cache block holds 8 matrix elements
A has good spatial locality
Stride 1
B has poor spatial locality
Stride n
By the time element n+1 is accessed, block has been kicked out of $
Iteration:
A = n/8
B = n

## Slide 21: Cache Miss Analysis (Naïve)
Scenario Parameters:
  Square matrix (), elements are doubles
  Cache block size = 64 B = 8 doubles
  Cache size (much smaller than )
Each iteration:
  misses
  Afterwards in cache: (schematic)
8 doubles wide
Ignoring
matrix c
Notes: Red portions show the blocks that are remaining in the $

## Slide 22: Cache Miss Analysis (Naïve)
Scenario Parameters:
  Square matrix (), elements are doubles
  Cache block size = 64 B = 8 doubles
  Cache size (much smaller than )
Each iteration:
  misses
Total misses:
Ignoring
matrix c
once per element

## Slide 23: Linear Algebra to the Rescue (1)
Can get the same result of a matrix multiplication by splitting the matrices into smaller submatrices (matrix “blocks”)
For example, multiply two 4×4 matrices:
This is extra (non-testable) material

## Slide 24: Linear Algebra to the Rescue (2)
Matrices of size , split into 4 blocks of size (=)
C22 = A21B12 + A22B22 + A23B32 + A24B42 = k A2k*Bk2
Multiplication operates on small “block” matrices
  Choose size so that they fit in the cache!
  This technique called “cache blocking”
C11
C12
C13
C14
C21
C22
C23
C24
C31
C32
C43
C34
C41
C42
C43
C44
A11
A12
A13
A14
A21
A22
A23
A24
A31
A32
A33
A34
A41
A42
A43
A144
B11
B12
B13
B14
B21
B22
B23
B24
B32
B32
B33
B34
B41
B42
B43
B44
This is extra (non-testable) material

## Slide 25: Blocked Matrix Multiply
Blocked version of the naïve algorithm:
  = block matrix size (assume divides evenly)
# move by rxr BLOCKS now
for (i = 0; i < n; i += r)
for (j = 0; j < n; j += r)
for (k = 0; k < n; k += r)
# block matrix multiplication
for (ib = i; ib < i+r; ib++)
for (jb = j; jb < j+r; jb++)
for (kb = k; kb < k+r; kb++)
c[ib*n+jb] += a[ib*n+kb]*b[kb*n+jb];
Notes: 6 nested loops seems inefficient, but leads to faster code!
Outer three loops: loop over block matrices
Inner three loops: loop within block matrices

## Slide 26: Cache Miss Analysis (Blocked)
Scenario Parameters:
  Cache block size = 64 B = 8 doubles
  Cache size (much smaller than )
  Three blocks () fit into cache:
Each block iteration:
  misses per block
/ blocks
elements per block, 8 per cache block
/ blocks in row and column
Ignoring
matrix c
Notes: 3r2 < C: need to be able to fit three full blocks in the cache (one for c, one for a, one for b) while executing the algorithm

## Slide 27: Cache Miss Analysis (Blocked)
Scenario Parameters:
  Cache block size = 64 B = 8 doubles
  Cache size (much smaller than )
  Three blocks () fit into cache:
Each block iteration:
  misses per block
  Afterwards in cache (schematic)
/ blocks
elements per block, 8 per cache block
/ blocks in row and column
Ignoring
matrix c
Notes: 3r2 < C: need to be able to fit three full blocks in the cache (one for c, one for a, one for b) while executing the algorithm

## Slide 28: Cache Miss Analysis (Blocked)
Scenario Parameters:
  Cache block size = 64 B = 8 doubles
  Cache size (much smaller than )
  Three blocks () fit into cache:
Each block iteration:
  misses per block
Total misses:
/ blocks
elements per block, 8 per cache block
/ blocks in row and column
Ignoring
matrix c
Notes: 3r2 < C: need to be able to fit three full blocks in the cache (one for c, one for a, one for b) while executing the algorithm

## Slide 29: Cache-Friendly Code
Programmer can optimize for cache performance
  How data structures are organized
  How data are accessed
    Nested loop structure
    Blocking is a general technique
All systems favor “cache-friendly code”
  Getting absolute optimum performance is very platform specific
    Cache size, cache block size, associativity, etc.
  Can get most of the advantage with generic code
    Keep working set reasonably small (temporal locality)
    Use small strides (spatial locality)
    Focus on inner loop code
Notes: Generic Code -> good rules of thumb

## Slide 30: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11
128m | 8350 | 4750 | 3096 | 2286 | 1817 | 1512 | 1293 | 1131 | 1055 | 995 | 945 | 900
64m | 8352 | 4750 | 3092 | 2287 | 1816 | 1510 | 1291 | 1129 | 1051 | 989 | 938 | 894
32m | 8406 | 4787 | 3098 | 2289 | 1823 | 1512 | 1295 | 1133 | 1052 | 989 | 938 | 892
16m | 8556 | 4990 | 3204 | 2376 | 1891 | 1579 | 1356 | 1198 | 1127 | 1070 | 1028 | 994
8m | 8998 | 5447 | 3570 | 2643 | 2104 | 1743 | 1477 | 1300 | 1217 | 1158 | 1128 | 1096
4m | 11494 | 7921 | 5664 | 4319 | 3524 | 2991 | 2592 | 2298 | 2208 | 2148 | 2117 | 2077
2m | 12297 | 8417 | 5940 | 4573 | 3734 | 3174 | 2763 | 2446 | 2349 | 2272 | 2213 | 2160
1024k | 12422 | 8398 | 5971 | 4569 | 3740 | 3172 | 2756 | 2446 | 2351 | 2271 | 2209 | 2162
512k | 12432 | 8472 | 5950 | 4573 | 3726 | 3165 | 2758 | 2447 | 2341 | 2267 | 2210 | 2162
256k | 12564 | 10037 | 8679 | 7175 | 5915 | 5022 | 4345 | 3856 | 3895 | 3981 | 4001 | 4404
128k | 12711 | 10750 | 10271 | 8649 | 7525 | 6374 | 5482 | 4854 | 4901 | 4933 | 4917 | 4924
64k | 12687 | 10689 | 10208 | 8768 | 7570 | 6352 | 5460 | 4830 | 4885 | 4885 | 4823 | 4868
Core i7 Haswell
2.1 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
Slopes
of spatial locality
Ridges
of temporal locality
L1
Mem
L2
L3
Aggressive prefetching
Notes: Increase stride size = less spatial locality = drop in throughput
Increase working set size = less temporal locality = fall out of respective caches
All caches on-chip

## Slide 31: Matrix Multiply Visualization
Here = 100, = 32 KB, = 30
Naïve:
Blocked:
≈ 1,020,000
cache misses
≈ 90,000
cache misses

## Slide 32: Anatomy of a Cache Question
Cache questions come in a few flavors:
  TIO Address Breakdown
  For fixed cache parameters, analyze the performance of the given code/sequence
  For given code/sequence, how does changing your cache parameters affect performance?
  Average Memory Access Time (AMAT)

## Slide 33: Example Cache Parameters Problem
1 MB address space, 125 cycles to go to memory. Fill in the following table:
Cache Size | 4 KB
Block Size | 16 B
Associativity | 4-way
Hit Time | 3 cycles
Miss Rate | 20%
Write Policy | Write-through
Replacement Policy | LRU
Tag Bits | 
Index Bits | 
Offset Bits | 
AMAT | 
10
6
4
AMAT = 3 + 0.2 * 125 = 28
Notes: 1 MB = 2^20 Bytes -> m = 20 bits
Miss Penalty (MP) = 125 cycles

## Slide 34: Peer Instruction Question
We have a cache of size 2 KB with block size of 128 B. If our cache has 2 sets, what is its associativity?
2
4
8
16
We’re lost…
If addresses are 16 bits wide, how wide is the Tag field?
Notes: Answer: C
2 KB = 2^11 B
128 B = 2^7 B
C/B = 2^(11-7) = 2^4 = 16 Blocks
E = Blocks/Sets = 16/2 = 8
t = m – s – b = 16 – log2(2) – log2(128) = 16 – 1 – 7 = 8 bits for tag

## Slide 35: Peer Instruction Question
Which of the following cache statements is FALSE?
We can reduce compulsory misses by decreasing our block size
We can reduce conflict misses by increasing associativity
A write-back cache will save time for code with good temporal locality on writes
A write-through cache will always match data with the memory hierarchy level below it
We’re lost…
Notes: Answer: A
A smaller block size pulls fewer bytes into $ on a miss, so this would increase compulsory misses
B: true, since higher associativity gives more options to place bocks before eviction
C: true, since frequently used blocks are rarely evicted, so fewer write-backs occur
D: true, since the main goal of a write-through cache is to keep its data consistent with the level below

## Slide 36: Example Code Analysis Problem
Assuming the cache starts cold (all blocks invalid), calculate the miss rate for the following loop:
  = 20 bits, = 4 KB, = 16 B, = 4
#define AR_SIZE 2048
int int_ar[AR_SIZE], sum=0; // &int_ar=0x80000
for (int i=0; i<AR_SIZE; i++)
sum += int_ar[i];
for (int j=AR_SIZE-1; j>=0; j--)
sum += int_ar[i];
Notes: AR_SIZE 2048 = 2^11 ints = 2^13 Bytes
C = 2^12 Bytes = half of int_ar[]
m = 20: t = 10, s = 6, b = 4
Overall miss rate = ¾ * (¼) + ¼ * 0 = 3/16

## Slide 37: Example Code Analysis Problem
Assuming the cache starts cold (all blocks invalid), calculate the miss rate for the following loop:
  = 20 bits, = 4 KB, = 16 B, = 4
#define AR_SIZE 2048
int int_ar[AR_SIZE], sum=0; // &int_ar=0x80000
for (int i=0; i<AR_SIZE; i++)
sum += int_ar[i];
for (int j=AR_SIZE-1; j>=0; j--)
sum += int_ar[i];
Notes: AR_SIZE 2048 = 2^11 ints = 2^13 Bytes
C = 2^12 Bytes = half of int_ar[]
m = 20: t = 10, s = 6, b = 4
Overall miss rate = ¾ * (¼) + ¼ * 0 = 3/16

## Slide 38: Suggested Problems
CS:APP 3rd
  Practice Problems 6.12-15
AU16 Final Question F5

## Slide 39: Learning About Your Machine
Linux:
  lscpu
  ls /sys/devices/system/cpu/cpu0/cache/index0/
    Ex: cat /sys/devices/system/cpu/cpu0/cache/index*/size
Windows:
  wmic memcache get <query> (all values in KB)
  Ex: wmic memcache get MaxCacheSize
Modern processor specs: http://www.7-cpu.com/
Notes: Linux Demo: type, level, size, ways_of_associativity
Windows Demo: Purpose, MaxCacheSize, BlockSize, Associativity