## Slide 1: Meltdown CSE 351 Winter 2018
Instructor:
Mark Wyse
Teaching Assistants:
Kevin Bi
Parker DeWilde
Emily Furst
Sarah House
Waylon Huang
Vinny Palaniappan
*thanks to Eddie Yan for a subset/skeleton of the slides

## Slide 2: Computer Architecture – The Basics
Address Translation
  Memory addresses in our program are virtual and require a translation
int myArray[42]; // software address: 0xdead00a8
// physical address: 0xffff00a8

## Slide 3: Computer Architecture – The Basics
Caching
  CPUs have caches that speed up memory access!
  Typically physically addressed (after address translation)
Assume access below is valid and memory page is in DRAM
int x = myArray[42]; //goes to DRAM, slooooow...
int y = myArray[42]; //goes to Cache, 1 CPU cycle
Cache/memory accesses can be timed by user programs!

## Slide 4: Computer Architecture – The Basics
Out-of-Order Execution
  Modern CPUs can run Out-of-Order (OoO)
These lines can run in parallel!
  Computation for d and e are independent
  These operations may be executed by CPU in any order
int d = a + b + fac(c);
int e = a + b + c;
return d + e;

## Slide 5: Computer Architecture – The Basics
Speculation
  Modern, high-performance processors can execute instructions (statements) speculatively
Consider this code:
assert(idx < len);
result = data[idx];

## Slide 6: Computer Architecture – The Basics
Speculation
  Modern, high-performance processors can execute instructions (statements) speculatively
Consider this code:
  The second line can execute before the check completes!
assert(idx < len);
result = data[idx];

## Slide 7: Computer Architecture – The Basics
Speculation
  Modern, high-performance processors can execute instructions (statements) speculatively
CPU often does something more like:
result = data[idx];
if (idx >= len)
// assert should have fired!
// CPU rolls back state
do_assert();

## Slide 8: Flush + Reload
Starting with a empty (cold) cache, an attacker can use timing information to determine if a cache block was loaded by the victim
Notes: Assume the two processes are accessing valid virtual addresses that map to a shared memory page and reside in the same cache block.

## Slide 9: Meltdown - Assumptions
All of physical memory is mapped to kernel addresses in user process
  Start address (VA in user process) of physical memory is known, Ak
  Physical memory is K bytes total, and mapped directly, [Ak … (Ak + K – 1)]
An exception (illegal memory access) can be handled/suppressed
Kernel Address Space Layout Randomization not used
  Similar to randomizing start address of stack, kernel data structure start address can be randomized
Notes: All of the assumptions are valid, or can easily be handled in real systems!
True in Linux
  Start address is deterministic or easily found
Easy to do: fork a child process to do the illegal access, use TSX, install a signal handler, etc.
Easy to defeat if used (Sec 5.2 of Meltdown paper)

## Slide 10: Meltdown – Data Structures/Variables
Two important data structures/variables
char probe_array[256 * 4096]; // 256 * 4KB = 256 pages
char* kernelAddr = {Ak … (Ak + K – 1)};
Notes: probeArray is an array of 256 * 4096 entries
  Lives in user address space (e.g., the heap), so we can always access this array
kernelAddr will be used to read a byte of physical memory by selecting the appropriate kernel address. Attempting to access kernelAddr will result in a illegal memory access, raising an exception in the user process

## Slide 11: Meltdown – Toy Example
1 raise_exception();
2 // the line below is never reached
3 access(probe_array[data * 4096]);
Assume data is a value between 0 – 255, and value is unknown
Assume a cold cache

## Slide 12: Meltdown – Toy Example
1 raise_exception();
2 // the line below is never reached
3 access(probe_array[data * 4096]);
Assume the CPU executes the probe_array access Speculatively, loading the element of the array into the cache.
Even though the exception is raised and the architectural state is “rolled back”, the CPU still caches the memory access!

## Slide 13: Meltdown – Toy Example
After the speculative memory access, access all the elements of the probe array, looking for an unusually fast access (i.e., a cached access):
The Page tells us what the value of data was!
Notes: Iterate over values of data from 0 – 255, accessing probe_array[data*4096]

## Slide 14: Meltdown – Toy Example
So, what did we accomplish?
  data was an unknown value between 0 – 255
  Based on the value of data, we speculatively loaded a cache line from probe_array[data*4096]
  After the exception is handled/suppressed, iterate values of data from 0 – 255, and use timing code to determine if probe_array[data*4096] is a cache hit.
If cache hit detected for a particular value of data, we learned the value of data!

## Slide 15: Meltdown – the Exploit
Goal: attempt to read physical memory by exploiting speculative and OoO execution, and the fact that all of physical memory is mapped to kernel addresses (virtual addresses) in a user process
Question: if user process accesses a kernel address, an illegal memory access occurs, raising an exception. Does the CPU still speculatively perform the illegal load? And can we determine the value loaded?
Yes!

## Slide 16: Meltdown – the Exploit
1 // rcx = kernel address (kernelAddr)
2 // rbx = probe_array
3 retry:
4 movb (%rcx), %al // move a byte to %al (%rax)
5 shl 0xc, %rax // multiply by 4096 (<< 12)
6 jz retry // retry if byte was 0**
7 mov (%rbx,%rax), %rbx // access probe_array[%al*4096]
** 0 is a special case, ignore for now
* Assume cold cache
Notes: This is the core of the exploit.

## Slide 17: Meltdown – the Exploit
1 // rcx = kernel address (kernelAddr)
2 // rbx = probe_array
3 retry:
4 movb (%rcx), %al // WILL RAISE AN EXCEPTION!
5 shl 0xc, %rax
6 jz retry
7 mov (%rbx,%rax), %rbx
Notes: This is the core of the exploit.

## Slide 18: Meltdown – the Exploit
1 // rcx = kernel address (kernelAddr)
2 // rbx = probe_array
3 retry:
4 movb (%rcx), %al // WILL RAISE AN EXCEPTION!
5 shl 0xc, %rax // But, lines 5-7 executed
6 jz retry // speculatively!
7 mov (%rbx,%rax), %rbx
Notes: This is the core of the exploit.

## Slide 19: Meltdown – the Exploit
1 // rcx = kernel address (kernelAddr)
2 // rbx = probe_array
3 retry:
4 movb (%rcx), %al // WILL RAISE AN EXCEPTION!
5 shl 0xc, %rax // But, lines 5-7 executed
6 jz retry // speculatively!
7 mov (%rbx,%rax), %rbx // Races with Exception!
Notes: This is the core of the exploit.

## Slide 20: Meltdown – the Exploit
1 // rcx = kernel address (kernelAddr)
2 // rbx = probe_array
3 retry:
4 movb (%rcx), %al // move a byte to %al (%rax)
5 shl 0xc, %rax // multiply by 4096 (<< 12)
6 jz retry // retry if byte was 0
7 mov (%rbx,%rax), %rbx // access probe_array[%al*4096]
So, what did we do? Attempt to load a byte from kernel memory (this is illegal for our user process!). Then, use that loaded byte in a speculative access to the probe_array, loading a cache line to our cold cache.
How do we determine what the byte was?
Notes: This is the core of the exploit.

## Slide 21: Meltdown – the Exploit
After the speculative memory access, access elements of the probe array, looking for an unusually fast access:
Access probe_array[data * 4096], timing the access for a cache hit. If hit detected, the value of data is the byte read from the kernel address!!!

## Slide 22: Meltdown – Explained
Race between raising exception for illegal kernel address access (from user process) and the probe array access.
  Race is due to OoO and speculative execution in the CPU
If the exception wins the race, the register %rax is zeroed to prevent leaking information
If the probe array access wins the race, a cache line is loaded from memory. The line to load is determined by the value of the illegal load (byte %al) and uses %rax before it is zeroed by the exception.
We can find the cache line that hits in the probe array on a second access, which tells us the value of the byte %al we loaded illegally!

## Slide 23: Meltdown – the Exploit – what about 0?
1 // rcx = kernel address (kernelAddr)
2 // rbx = probe_array
3 retry:
4 movb (%rcx), %al // move a byte to %al (%rax)
5 shl 0xc, %rax // multiply by 4096 (<< 12)
6 jz retry // retry if byte was 0**
7 mov (%rbx,%rax), %rbx // access probe_array[%al*4096]
** %rax will be 0 if the Exception wins the race with the probe_array access. Thus, if a zero is seen, try again. Either, a non-zero byte is used to perform the speculative access, or don’t perform the speculative access at all! Then, when scanning probe_array, no hits will occur, and we can be reasonably confident the byte was 0.
Notes: This is the core of the exploit.

## Slide 24: Meltdown - Summary
Allows a user process to read all of physical memory on the system, which is mapped in kernel addresses and by extension in user process address space
Speculative execution occurs in the exploit (leak arises from CPU speculating in the attacker’s code)

## Slide 25: Meltdown - Mitigation
Meltdown relies on the kernel address space being mapped into user process address space, and all of physical memory being mapped to kernel address space.
KAISER (patch by Gruss et al.) implements a stronger isolation between kernel and user space. It leaves physical memory unmapped in kernel address space.
Or, use an AMD processor, which doesn’t bypass memory protection during speculative execution.