## Slide 1: Caches IV CSE 351 Autumn 2019
Instructor: Teaching Assistants:
Justin Hsia Andrew Hu Antonio Castelli Cosmo Wang
Diya Joy Ivy Yu Kaelin Laundry
Maurice Montag Melissa Birchfield Millicent Li
Suraj Jagadeesh
http://xkcd.com/908/

## Slide 2: Administrivia
Lab 3 due tonight
  Late days count as normal: Sunday is 1 day, Monday is 2
No lecture Monday – Veteran’s Day!
Lab 4 released over the long weekend
  Cache parameter puzzles and code optimizations
hw16 due Wednesday (11/13)

## Slide 3: What about writes?
Multiple copies of data may exist:
  multiple levels of cache and main memory
What to do on a write-hit?
  Write-through: write immediately to next level
  Write-back: defer write to next level until line is evicted (replaced)
    Must track which cache lines have been modified (“dirty bit”)
What to do on a write-miss?
  Write allocate: (“fetch on write”) load into cache, then execute the write-hit policy
    Good if more writes or reads to the location follow
  No-write allocate: (“write around”) just write immediately to next level
Typical caches:
  Write-back + Write allocate, usually
  Write-through + No-write allocate, occasionally
Notes: Why? Reuse is common
  Typically you would read, then write (incr)
  Or after you initialize a value (say, to 0), likely read and write it again soon

## Slide 4: Write-back, Write Allocate Example
Note: While unrealistic, this example assumes that all requests have offset 0 and are for a block’s worth of data.
0xBEEF
Cache:
G
0
1
Valid
Dirty
Tag
Block Contents
Memory:
0xCAFE
0xBEEF
F
G
●
●
●
●
●
●
●
●
●
Block
Num
There is only one set in this tiny cache,
so the tag is the entire block number!

## Slide 5: Write-back, Write Allocate Example
0xBEEF
Cache:
G
0
1
Valid
Dirty
Tag
Block Contents
Memory:
0xCAFE
0xBEEF
F
G
●
●
●
●
●
●
●
●
●
Block
Num
1) mov 0xFACE, F
Step 1: Bring F into cache
Write Miss!

## Slide 6: Write-back, Write Allocate Example
0xCAFE
Cache:
F
0
1
Valid
Dirty
Tag
Block Contents
Memory:
0xCAFE
0xBEEF
F
G
●
●
●
●
●
●
●
●
●
Block
Num
1) mov 0xFACE, F
Step 1: Bring F into cache
Step 2: Write 0xFACE to cache only and set the dirty bit
Write Miss

## Slide 7: Write-back, Write Allocate Example
0xFACE
Cache:
F
1
1
Valid
Dirty
Tag
Block Contents
Memory:
0xCAFE
0xBEEF
F
G
●
●
●
●
●
●
●
●
●
Block
Num
1) mov 0xFACE, F
Step 1: Bring F into cache
Step 2: Write 0xFACE to cache only and set the dirty bit
Write Miss

## Slide 8: Write-back, Write Allocate Example
0xFACE
Cache:
F
1
1
Valid
Dirty
Tag
Block Contents
Memory:
0xCAFE
0xBEEF
F
G
●
●
●
●
●
●
●
●
●
Block
Num
1) mov 0xFACE, F
Step: Write 0xFEED to cache only (and set the dirty bit)
2) mov 0xFEED, F
Write Miss
Write Hit!

## Slide 9: Write-back, Write Allocate Example
0xFEED
Cache:
F
1
1
Valid
Dirty
Tag
Block Contents
Memory:
0xCAFE
0xBEEF
F
G
●
●
●
●
●
●
●
●
●
Block
Num
1) mov 0xFACE, F
2) mov 0xFEED, F
Write Miss
Write Hit

## Slide 10: Write-back, Write Allocate Example
0xFEED
Cache:
F
1
1
Valid
Dirty
Tag
Block Contents
Memory:
0xCAFE
0xBEEF
F
G
●
●
●
●
●
●
●
●
●
Block
Num
1) mov 0xFACE, F
2) mov 0xFEED, F
3) mov G, %ax
Write Miss
Write Hit
Read Miss!
Step 1: Write F back to memory since it is dirty

## Slide 11: Write-back, Write Allocate Example
0xFEED
Cache:
F
1
1
Valid
Dirty
Tag
Block Contents
Memory:
0xFEED
0xBEEF
F
G
●
●
●
●
●
●
●
●
●
Block
Num
1) mov 0xFACE, F
2) mov 0xFEED, F
3) mov G, %ax
Write Miss
Write Hit
Read Miss
Step 1: Write F back to memory since it is dirty
Step 2: Bring G into the cache so that we can copy it into %ax
0
G
0xBEEF

## Slide 12: Cache Simulator
Want to play around with cache parameters and policies? Check out our cache simulator!
  https://courses.cs.washington.edu/courses/cse351/cachesim/
Way to use:
  Take advantage of “explain mode” and navigable history to test your own hypotheses and answer your own questions
  Self-guided Cache Sim Demo posted along with Section 7
  Will be used in hw17 – Lab 4 Preparation

## Slide 13: Polling Question
Which of the following cache statements is FALSE?
  Vote at http://PollEv.com/justinh
We can reduce compulsory misses by decreasing our block size
We can reduce conflict misses by increasing associativity
A write-back cache will save time for code with good temporal locality on writes
A write-through cache will always match data with the memory hierarchy level below it
We’re lost…

## Slide 14: Optimizations for the Memory Hierarchy
Write code that has locality!
  Spatial: access data contiguously
  Temporal: make sure access to the same data is not too far apart in time
How can you achieve locality?
  Adjust memory accesses in code (software) to improve miss rate (MR)
    Requires knowledge of both how caches work as well as your system’s parameters
  Proper choice of algorithm
  Loop transformations

## Slide 15: Example: Matrix Multiplication
C
=
×
A
B
ai*
b*j
cij
Notes: Subscript indices given in (row,col).

## Slide 16: Matrices in Memory
How do cache blocks fit into this scheme?
  Row major matrix in memory:
Cache blocks
COLUMN of matrix (blue) is spread among cache blocks shown in red

## Slide 17: Naïve Matrix Multiply
# move along rows of A
for (i = 0; i < n; i++)
# move along columns of B
for (j = 0; j < n; j++)
# EACH k loop reads row of A, col of B
# Also read & write c(i,j) n times
for (k = 0; k < n; k++)
c[i*n+j] += a[i*n+k] * b[k*n+j];
C(i,j)
A(i,:)
B(:,j)
C(i,j)
Notes: Note the += leads to an additional read of matrix C

## Slide 18: Cache Miss Analysis (Naïve)
Scenario Parameters:
  Square matrix (), elements are doubles
  Cache block size = 64 B = 8 doubles
  Cache size (much smaller than )
Each iteration:
  misses
Ignoring
matrix c

## Slide 19: Cache Miss Analysis (Naïve)
Scenario Parameters:
  Square matrix (), elements are doubles
  Cache block size = 64 B = 8 doubles
  Cache size (much smaller than )
Each iteration:
  misses
  Afterwards in cache: (schematic)
8 doubles wide
Ignoring
matrix c

## Slide 20: Cache Miss Analysis (Naïve)
Scenario Parameters:
  Square matrix (), elements are doubles
  Cache block size = 64 B = 8 doubles
  Cache size (much smaller than )
Each iteration:
  misses
Total misses:
Ignoring
matrix c
once per product matrix element

## Slide 21: Linear Algebra to the Rescue (1)
Can get the same result of a matrix multiplication by splitting the matrices into smaller submatrices (matrix “blocks”)
For example, multiply two 4×4 matrices:
This is extra (non-testable) material

## Slide 22: Linear Algebra to the Rescue (2)
Matrices of size , split into 4 blocks of size (=)
C22 = A21B12 + A22B22 + A23B32 + A24B42 = k A2k*Bk2
Multiplication operates on small “block” matrices
  Choose size so that they fit in the cache!
  This technique called “cache blocking”
C11
C12
C13
C14
C21
C22
C23
C24
C31
C32
C43
C34
C41
C42
C43
C44
A11
A12
A13
A14
A21
A22
A23
A24
A31
A32
A33
A34
A41
A42
A43
A144
B11
B12
B13
B14
B21
B22
B23
B24
B32
B32
B33
B34
B41
B42
B43
B44
This is extra (non-testable) material

## Slide 23: Blocked Matrix Multiply
Blocked version of the naïve algorithm:
  = block matrix size (assume divides evenly)
# move by rxr BLOCKS now
for (i = 0; i < n; i += r)
for (j = 0; j < n; j += r)
for (k = 0; k < n; k += r)
# block matrix multiplication
for (ib = i; ib < i+r; ib++)
for (jb = j; jb < j+r; jb++)
for (kb = k; kb < k+r; kb++)
c[ib*n+jb] += a[ib*n+kb]*b[kb*n+jb];

## Slide 24: Cache Miss Analysis (Blocked)
Scenario Parameters:
  Cache block size = 64 B = 8 doubles
  Cache size (much smaller than )
  Three blocks () fit into cache:
Each block iteration:
  misses per block
/ blocks
elements per block, 8 per cache block
/ blocks in row and column
Ignoring
matrix c
Notes: 3r2 < C: need to be able to fit three full blocks in the cache (one for c, one for a, one for b) while executing the algorithm

## Slide 25: Cache Miss Analysis (Blocked)
Scenario Parameters:
  Cache block size = 64 B = 8 doubles
  Cache size (much smaller than )
  Three blocks () fit into cache:
Each block iteration:
  misses per block
  Afterwards in cache (schematic)
/ blocks
elements per block, 8 per cache block
/ blocks in row and column
Ignoring
matrix c
Notes: 3r2 < C: need to be able to fit three full blocks in the cache (one for c, one for a, one for b) while executing the algorithm

## Slide 26: Cache Miss Analysis (Blocked)
Scenario Parameters:
  Cache block size = 64 B = 8 doubles
  Cache size (much smaller than )
  Three blocks () fit into cache:
Each block iteration:
  misses per block
Total misses:
/ blocks
elements per block, 8 per cache block
/ blocks in row and column
Ignoring
matrix c
Notes: 3r2 < C: need to be able to fit three full blocks in the cache (one for c, one for a, one for b) while executing the algorithm

## Slide 27: Matrix Multiply Visualization
Here = 100, = 32 KiB, = 30
Naïve:
Blocked:
≈ 1,020,000
cache misses
≈ 90,000
cache misses

## Slide 28: Cache-Friendly Code
Programmer can optimize for cache performance
  How data structures are organized
  How data are accessed
    Nested loop structure
    Blocking is a general technique
All systems favor “cache-friendly code”
  Getting absolute optimum performance is very platform specific
    Cache size, cache block size, associativity, etc.
  Can get most of the advantage with generic code
    Keep working set reasonably small (temporal locality)
    Use small strides (spatial locality)
    Focus on inner loop code

## Slide 29: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11
128m | 8350 | 4750 | 3096 | 2286 | 1817 | 1512 | 1293 | 1131 | 1055 | 995 | 945 | 900
64m | 8352 | 4750 | 3092 | 2287 | 1816 | 1510 | 1291 | 1129 | 1051 | 989 | 938 | 894
32m | 8406 | 4787 | 3098 | 2289 | 1823 | 1512 | 1295 | 1133 | 1052 | 989 | 938 | 892
16m | 8556 | 4990 | 3204 | 2376 | 1891 | 1579 | 1356 | 1198 | 1127 | 1070 | 1028 | 994
8m | 8998 | 5447 | 3570 | 2643 | 2104 | 1743 | 1477 | 1300 | 1217 | 1158 | 1128 | 1096
4m | 11494 | 7921 | 5664 | 4319 | 3524 | 2991 | 2592 | 2298 | 2208 | 2148 | 2117 | 2077
2m | 12297 | 8417 | 5940 | 4573 | 3734 | 3174 | 2763 | 2446 | 2349 | 2272 | 2213 | 2160
1024k | 12422 | 8398 | 5971 | 4569 | 3740 | 3172 | 2756 | 2446 | 2351 | 2271 | 2209 | 2162
512k | 12432 | 8472 | 5950 | 4573 | 3726 | 3165 | 2758 | 2447 | 2341 | 2267 | 2210 | 2162
256k | 12564 | 10037 | 8679 | 7175 | 5915 | 5022 | 4345 | 3856 | 3895 | 3981 | 4001 | 4404
128k | 12711 | 10750 | 10271 | 8649 | 7525 | 6374 | 5482 | 4854 | 4901 | 4933 | 4917 | 4924
64k | 12687 | 10689 | 10208 | 8768 | 7570 | 6352 | 5460 | 4830 | 4885 | 4885 | 4823 | 4868
Core i7 Haswell
2.1 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
Slopes
of spatial locality
Ridges
of temporal locality
L1
Mem
L2
L3
Aggressive prefetching
Notes: Increase stride size = less spatial locality = drop in throughput
Increase working set size = less temporal locality = fall out of respective caches
All caches on-chip

## Slide 30: Learning About Your Machine
Linux:
  lscpu
  ls /sys/devices/system/cpu/cpu0/cache/index0/
    Example: cat /sys/devices/system/cpu/cpu0/cache/index*/size
Windows:
  wmic memcache get <query> (all values in KB)
  Example: wmic memcache get MaxCacheSize
Modern processor specs: http://www.7-cpu.com/
Notes: Linux Demo: type, level, size, ways_of_associativity
Windows Demo: Purpose, MaxCacheSize, BlockSize, Associativity

## Slide 31: Write-back, Write Allocate Example
0xBEEF
Cache:
G
0
1
Valid
Dirty
Tag
Block Contents
Memory:
0xCAFE
0xBEEF
F
G
●
●
●
●
●
●
●
●
●
Block
Num
1) mov 0xFACE, F
2) mov 0xFEED, F
3) mov G, %ax

## Slide 32: Cache Miss Analysis Comparison
Scenario Parameters:
  Square matrix () of doubles
  Cache size and three blocks () fit into cache:
Naïve:
Blocked:
Ignoring
matrix c
/ blocks
Scenario Parameters:
  Cache block size = 64 B = 8 doubles

## Slide 33: Exceptions - Handout
An exception is transfer of control to the operating system (OS) kernel in response to some event (i.e. change in processor state)
  Kernel is the memory-resident part of the OS
  Examples: division by 0, page fault, I/O request completes, Ctrl-C
How does the system know where to jump to in the OS?
User Code
OS Kernel Code
exception
exception processing by exception handler, then:
current_instr
next_instr
event

## Slide 34: Notes Diagrams
User Code
OS Kernel Code
exception
exception processing by exception handler, then:
return to current_instr,
return to next_instr, OR
abort
current_instr
next_instr
event