## Slide 1: Caches II CSE 351 Spring 2019
Instructor:
Ruth Anderson
Teaching Assistants:
Gavin Cai Jack Eggleston John Feltrup Britt Henderson Richard Jiang Jack Skalitzky Sophie Tian Connie Wang Sam Wolfson Casey Xing Chin Yeoh

## Slide 2: Administrivia
Lab 3, due Wednesday (5/15)
Homework 4 , due Wed (5/22) (Structs, Caches)
Midterm Grading completed
  You should have received an email from Gradescope
  Solutions posted on website
  Rubric and grades will be found on Gradescope
  Regrade requests will be open for a short time after grade release via Gradescope

## Slide 3: Memory Hierarchies
Some fundamental and enduring properties of hardware and software systems:
  Faster storage technologies almost always cost more per byte and have lower capacity
  The gaps between memory technology speeds are widening
    True for: registers ↔ cache, cache ↔ DRAM, DRAM ↔ disk, etc.
  Well-written programs tend to exhibit good locality
These properties complement each other beautifully
  They suggest an approach for organizing memory and storage systems known as a memory hierarchy
    For each level k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1

## Slide 4: An Example Memory Hierarchy
registers
on-chip L1
cache (SRAM)
main memory
(DRAM)
local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
remote secondary storage
(distributed file systems, web servers)
Local disks hold files retrieved from disks on remote network servers
Main memory holds disk blocks retrieved from local disks
off-chip L2
cache (SRAM)
L1 cache holds cache lines retrieved from L2 cache
CPU registers hold words retrieved from L1 cache
L2 cache holds cache lines retrieved from main memory
Smaller,
faster,
costlier
per byte
Notes: Implemented with different technologies!
  disks, solid-state
  DRAM: little wells that drain slowly, refreshed periodically
  SRAM: flip-flops, little logic gates that feedback with each other, faster but uses more power!
That’s why they’re different sizes and costs

## Slide 5: An Example Memory Hierarchy
registers
on-chip L1
cache (SRAM)
main memory
(DRAM)
local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
remote secondary storage
(distributed file systems, web servers)
off-chip L2
cache (SRAM)
explicitly program-controlled (e.g. refer to exactly %rax, %rbx)
Smaller,
faster,
costlier
per byte
program sees “memory”;
hardware manages caching
transparently
Notes: So, why haven’t we seen caches before now in this class?
  Because they’re designed to be architecturally transparent!

## Slide 6: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
Block size: 64 bytes for all caches
L1 i-cache and d-cache:
  32 KiB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KiB, 8-way,
  Access: 11 cycles
L3 unified cache:
  8 MiB, 16-way,
  Access: 30-40 cycles
Notes: cat /sys/devices/system/cpu/cpu0/cache/index0/ways_of_associativity

## Slide 7: Making memory accesses fast!
Cache basics
Principle of locality
Memory hierarchies
Cache organization
  Direct-mapped (sets; index + tag)
  Associativity (ways)
  Replacement policy
  Handling writes
Program optimizations that consider caches
Notes: Divide addresses into “index” and “tag”

## Slide 8: Cache Organization (1)
Block Size (): unit of transfer between and Mem
  Given in bytes and always a power of 2 (e.g. 64 B)
  Blocks consist of adjacent bytes (differ in address by 1)
    Spatial locality!
Note: The textbook uses “B” for block size
Notes: Just like withinBlock() from Lab 1!

## Slide 9: Cache Organization (1)
Block Size (): unit of transfer between and Mem
  Given in bytes and always a power of 2 (e.g. 64 B)
  Blocks consist of adjacent bytes (differ in address by 1)
    Spatial locality!
Offset field
  Low-order bits of address tell you which byte within a block
    (address) mod = lowest bits of address
  (address) modulo (# of bytes in a block)
Block Number
Block Offset
-bit address:
(refers to byte in memory)
bits
bits
Note: The textbook uses “b” for offset bits
Notes: Just like withinBlock() from Lab 1!

## Slide 10: Peer Instruction Question
If we have 6-bit addresses and block size = 4 B, which block and byte does 0x15 refer to?
  Vote at: http://PollEv.com/rea
  Block Num Block Offset
1 1
1 5
5 1
5 5
We’re lost…

## Slide 11: Cache Organization (2)
Cache Size (): amount of data the can store
  Cache can only hold so much data (subset of next level)
  Given in bytes () or number of blocks ()
  Example: = 32 KiB = 512 blocks if using 64-B blocks
Where should data go in the cache?
  We need a mapping from memory addresses to specific locations in the cache to make checking the cache for an address fast
What is a data structure that provides fast lookup?
  Hash table!

## Slide 12: Review: Hash Tables for Fast Lookup
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 
Insert: 5
27
34
102
119
Apply hash function to map data to “buckets”
Notes: hash(27) % N (10) = 7…

## Slide 13: Place Data in Cache by Hashing Address
Map to cache index from block address
  Use next bits
  (block address) mod (# blocks in cache)
Block Num | Block Data |  |  | 
0000 |  |  |  | 
0001 |  |  |  | 
0010 |  |  |  | 
0011 |  |  |  | 
0100 |  |  |  | 
0101 |  |  |  | 
0110 |  |  |  | 
0111 |  |  |  | 
1000 |  |  |  | 
1001 |  |  |  | 
1010 |  |  |  | 
1011 |  |  |  | 
1100 |  |  |  | 
1101 |  |  |  | 
1110 |  |  |  | 
1111 |  |  |  | 
Memory
Cache
Index | Block Data |  |  | 
00 |  |  |  | 
01 |  |  |  | 
10 |  |  |  | 
11 |  |  |  | 
Here = 4 B
and = 4
Notes: Assume 6-bit addresses. Show how to split into Index and Offset fields.

## Slide 14: Place Data in Cache by Hashing Address
Map to cache index from block address
  Lets adjacent blocks fit in cache simultaneously!
    Consecutive blocks go in consecutive cache indices
Block Addr | Block Data |  |  | 
0000 |  |  |  | 
0001 |  |  |  | 
0010 |  |  |  | 
0011 |  |  |  | 
0100 |  |  |  | 
0101 |  |  |  | 
0110 |  |  |  | 
0111 |  |  |  | 
1000 |  |  |  | 
1001 |  |  |  | 
1010 |  |  |  | 
1011 |  |  |  | 
1100 |  |  |  | 
1101 |  |  |  | 
1110 |  |  |  | 
1111 |  |  |  | 
Memory
Cache
Index | Block Data |  |  | 
00 |  |  |  | 
01 |  |  |  | 
10 |  |  |  | 
11 |  |  |  | 
Here = 4 B
and = 4

## Slide 15: Practice Question
6-bit addresses, block size = 4 B, and our cache holds = 4 blocks.
A request for address 0x2A results in a cache miss. Which index does this block get loaded into and which 3 other addresses are loaded along with it?
  No voting for this question

## Slide 16: Place Data in Cache by Hashing Address
Collision!
  This might confuse the cache later when we access the data
  Solution?
Block Addr | Block Data |  |  | 
0000 |  |  |  | 
0001 |  |  |  | 
0010 |  |  |  | 
0011 |  |  |  | 
0100 |  |  |  | 
0101 |  |  |  | 
0110 |  |  |  | 
0111 |  |  |  | 
1000 |  |  |  | 
1001 |  |  |  | 
1010 |  |  |  | 
1011 |  |  |  | 
1100 |  |  |  | 
1101 |  |  |  | 
1110 |  |  |  | 
1111 |  |  |  | 
Memory
Cache
Index | Block Data |  |  | 
00 |  |  |  | 
01 |  |  |  | 
10 |  |  |  | 
11 |  |  |  | 
Here = 4 B
and = 4

## Slide 17: Tags Differentiate Blocks in Same Index
Tag = rest of address bits
  bits =
  Check this during a cache lookup
Block Addr | Block Data |  |  | 
0000 |  |  |  | 
0001 |  |  |  | 
0010 |  |  |  | 
0011 |  |  |  | 
0100 |  |  |  | 
0101 |  |  |  | 
0110 |  |  |  | 
0111 |  |  |  | 
1000 |  |  |  | 
1001 |  |  |  | 
1010 |  |  |  | 
1011 |  |  |  | 
1100 |  |  |  | 
1101 |  |  |  | 
1110 |  |  |  | 
1111 |  |  |  | 
Memory
Cache
Index | Tag |  | Block Data |  |  | 
00 | 00 |  |  |  |  | 
01 |  |  |  |  |  | 
10 | 01 |  |  |  |  | 
11 | 01 |  |  |  |  | 
Here = 4 B
and = 4
Notes: Possible analogies for Tag:
Hash by first name, tag by last name
Hash by 7-digit phone number, tag by area code

## Slide 18: Checking for a Requested Address
CPU sends address request for chunk of data
  Address and requested data are not the same thing!
    Analogy: your friend ≠ his or her phone number
TIO address breakdown:
  Index field tells you where to look in cache
  Tag field lets you check that data is the block you want
  Offset field selects specified start byte within block
  Note: and sizes will change based on hash function
Tag ()
Offset ()
-bit address:
Block Number
Index ()

## Slide 19: Cache Puzzle
Based on the following behavior, which of the following block sizes is NOT possible for our cache?
  Cache starts empty, also known as a cold cache
  Access (addr: hit/miss) stream:
    (14: miss), (15: hit), (16: miss)
4 bytes
8 bytes
16 bytes
32 bytes
We’re lost…
Vote at http://pollev.com/rea
Notes: Lab 4!

## Slide 20: Direct-Mapped Cache
Hash function: (block address) mod (# of blocks in cache)
  Each memory address maps to exactly one index in the cache
  Fast (and simpler) to find an address
Block Addr | Block Data |  |  | 
00 00 |  |  |  | 
00 01 |  |  |  | 
00 10 |  |  |  | 
00 11 |  |  |  | 
01 00 |  |  |  | 
01 01 |  |  |  | 
01 10 |  |  |  | 
01 11 |  |  |  | 
10 00 |  |  |  | 
10 01 |  |  |  | 
10 10 |  |  |  | 
10 11 |  |  |  | 
11 00 |  |  |  | 
11 01 |  |  |  | 
11 10 |  |  |  | 
11 11 |  |  |  | 
Memory
Cache
Index | Tag |  | Block Data |  |  | 
00 | 00 |  |  |  |  | 
01 | 11 |  |  |  |  | 
10 | 01 |  |  |  |  | 
11 | 01 |  |  |  |  | 
Here = 4 B
and = 4

## Slide 21: Direct-Mapped Cache Problem
What happens if we access the following addresses?
  8, 24, 8, 24, 8, …?
  Conflict in cache (misses!)
  Rest of cache goes unused
Solution?
Block Addr | Block Data |  |  | 
00 00 |  |  |  | 
00 01 |  |  |  | 
00 10 |  |  |  | 
00 11 |  |  |  | 
01 00 |  |  |  | 
01 01 |  |  |  | 
01 10 |  |  |  | 
01 11 |  |  |  | 
10 00 |  |  |  | 
10 01 |  |  |  | 
10 10 |  |  |  | 
10 11 |  |  |  | 
11 00 |  |  |  | 
11 01 |  |  |  | 
11 10 |  |  |  | 
11 11 |  |  |  | 
Memory
Cache
Index | Tag |  | Block Data |  |  | 
00 | ?? |  |  |  |  | 
01 | ?? |  |  |  |  | 
10 |  |  |  |  |  | 
11 | ?? |  |  |  |  | 
Here = 4 B
and = 4
Notes: Conflict! Rest of cache unused!

## Slide 22: Associativity
What if we could store data in any place in the cache?
  More complicated hardware = more power consumed, slower
So we combine the two ideas:
  Each address maps to exactly one set
  Each set can store block in more than one way
0
1
2
3
4
5
6
7
0
1
2
3
Set
0
1
Set
1-way:
8 sets,
1 block each
2-way:
4 sets,
2 blocks each
4-way:
2 sets,
4 blocks each
0
Set
8-way:
1 set,
8 blocks
direct mapped
fully associative
Notes: “Where is address 2?”