## Slide 1: Virtual Memory III CSE 351 Spring 2019
Instructor:
Ruth Anderson
Teaching Assistants:
Gavin Cai Jack Eggleston John Feltrup Britt Henderson Richard Jiang Jack Skalitzky Sophie Tian Connie Wang Sam Wolfson Casey Xing Chin Yeoh

## Slide 2: Administrivia
Lab 4, due Fri (5/24)
Homework 5 is out!
  Processes and Virtual Memory
  Due Friday, May 31
Error on last week’s section handout
  Incorrect variable names for caches

## Slide 3: Quick Review
What do Page Tables map?
Where are Page Tables located?
How many Page Tables are there?
Can your process tell if a page fault has occurred?
True / False: Virtual Addresses that are contiguous will always be contiguous in physical memory
TLB stands for _______________________ and stores _______________

## Slide 4: Address Translation: Page Hit
1) Processor sends virtual address to MMU (memory management unit)
2-3) MMU fetches PTE from page table in cache/memory (Uses PTBR to find beginning of page table for current process)
4) MMU sends physical address to cache/memory requesting data
5) Cache/memory sends data to processor
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5
VA = Virtual Address PTEA = Page Table Entry Address PTE= Page Table Entry PA = Physical Address Data = Contents of memory stored at VA originally requested by CPU

## Slide 5: Address Translation: Page Fault
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in cache/memory
4) Valid bit is zero, so MMU triggers page fault exception
5) Handler identifies victim (and, if dirty, pages it out to disk)
6) Handler pages in new page and updates PTE in memory
7) Handler returns to original process, restarting faulting instruction
MMU
Cache/
Memory
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5
Disk
Page fault handler
Victim page
New page
Exception
6
7
Notes: First 3 steps are the same

## Slide 6: Hmm… Translation Sounds Slow
The MMU accesses memory twice: once to get the PTE for translation, and then again for the actual memory request
  The PTEs may be cached in L1 like any other memory word
    But they may be evicted by other data references
    And a hit in the L1 cache still requires 1-3 cycles
What can we do to make this faster?
  “Any problem in computer science can be solved by adding another level of indirection.” – David Wheeler, inventor of the subroutine
  “And all of the new problems that creates can be solved by adding another cache.” - Sam Wolfson, inventor of this quote

## Slide 7: Speeding up Translation with a TLB
Translation Lookaside Buffer (TLB):
  Small hardware cache in MMU
  Maps virtual page numbers to physical page numbers
  Contains complete page table entries for small number of pages
    Modern Intel processors have 128 or 256 entries in TLB
  Much faster than a page table lookup in cache/memory
TLB
PTE
VPN
→
PTE
VPN
→
PTE
VPN
→
Notes: “The architecture of the IBM System/370” R.P. Case and A. Padegs Communications of the ACM. 21:1, 73-96, January 1978.
Perhaps the first paper to use the term translation lookaside buffer. The name arises from the historical name for a cache, which was a lookaside buffer as called by those developing the Atlas system at the University of Manchester; a cache of address translations thus became a translation lookaside buffer. Even though the term lookaside buffer fell out of favor, TLB seems to have stuck, for whatever reason.
“x86info -c” on Intel Core2 Duo CPU:
L1 Data TLB: 4KB pages, 4-way set associative, 16 entries
Data TLB: 4K pages, 4-way associative, 256 entries.
L1 Data TLB: 4MB pages, 4-way set associative, 16 entries
Data TLB: 4MB pages, 4-way associative, 32 entries

## Slide 8: TLB Hit
A TLB hit eliminates a memory access!
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
4
5
TLB
VPN
3
TLB
PTE
VPN
→
PTE
VPN
→
PTE
VPN
→
Notes: Check the TLB for the VPN mapping before going to memory.

## Slide 9: TLB Miss
A TLB miss incurs an additional memory access (the PTE)
  Fortunately, TLB misses are rare
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
5
6
TLB
VPN
4
PTEA
3
TLB
PTE
VPN
→
PTE
VPN
→
PTE
VPN
→
Notes: Does a TLB miss require disk access?
TLB miss updates the TLB entry so it won’t miss in the future

## Slide 10: Fetching Data on a Memory Read
Check TLB
  Input: VPN, Output: PPN
  TLB Hit: Fetch translation, return PPN
  TLB Miss: Check page table (in memory)
    Page Table Hit: Load page table entry into TLB
    Page Fault: Fetch page from disk to memory, update corresponding page table entry, then load entry into TLB
Check cache
  Input: physical address, Output: data
  Cache Hit: Return data value to processor
  Cache Miss: Fetch data value from memory, store it in cache, return it to processor
Notes: Note: caches use physical addresses!

## Slide 11: Address Translation
VM is complicated, but also elegant and effective
  Level of indirection to provide isolated memory & caching
  TLB as a cache of page tables avoids two trips to memory for every memory access
Virtual Address
TLB
Lookup
Check the
Page Table
Update
TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
TLB Miss
TLB Hit
Page not
in Mem
Access
Denied
Access
Permitted
Protection
Fault
SIGSEGV
Page
in Mem
Check cache
Find in Disk
Find in Mem
Notes: Need to restart instruction.
Soft and hard page faults.
Are you allowed to access this page?
Nice “overview” of the entire process.

## Slide 12: Simple Memory System Example (small)
Addressing
  14-bit virtual addresses
  12-bit physical address
  Page size = 64 bytes
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
Virtual Page Number
Virtual Page Offset
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
Physical Page Number
Physical Page Offset
Notes: VA space is 2^14B. (n=14)
PA space is 2^12B (n=12) (how much memory we actually have)
Page offset width is 6 bits
What does that mean…? (animation)
N bits of VA
M bits of PA
2^(n-p) pages in virtual address space
2^(m-p) pages in physical mem

## Slide 13: Simple Memory System: Page Table
Only showing first 16 entries (out of _____)
  Note: showing 2 hex digits for PPN even though only 6 bits
  Note: other management bits not shown, but part of PTE
VPN | PPN | Valid
0 | 28 | 1
1 | – | 0
2 | 33 | 1
3 | 02 | 1
4 | – | 0
5 | 16 | 1
6 | – | 0
7 | – | 0
VPN | PPN | Valid
8 | 13 | 1
9 | 17 | 1
A | 09 | 1
B | – | 0
C | – | 0
D | 2D | 1
E | – | 0
F | 0D | 1
Notes: Size of page table = 2^(n-p) entries
n = 14 (virtual address length)
p = 6 (2^6 = 64, which is page size)
Need an entry for every page!

## Slide 14: Simple Memory System: TLB
16 entries total
4-way set associative
13
12
11
10
9
8
7
6
5
4
3
2
1
0
virtual page offset
virtual page number
TLB index
TLB tag
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set
Why does the TLB ignore the page offset?
Notes: How many sets? 16 entries total, 4 way assoc., 4 sets  2 set bits (same as TLB index)
Why ignore offset? Because there’s no need – only one entry per set (PPN).
Calculate VPN for valid TLB entry using Tag & Set
- Tag 3, set 1, 000 0011 | 01 =>VPN 0x0D, PPN 0x2D (show that it matches memory system on prev slide)

## Slide 15: Simple Memory System: Cache
Direct-mapped with = 4 B, = 16
Physically addressed
11
10
9
8
7
6
5
4
3
2
1
0
physical page offset
physical page number
cache offset
cache index
cache tag
Note: It is just coincidence that the PPN is the same width as the cache Tag
Index | Tag | Valid | B0 | B1 | B2 | B3
0 | 19 | 1 | 99 | 11 | 23 | 11
1 | 15 | 0 | – | – | – | –
2 | 1B | 1 | 00 | 02 | 04 | 08
3 | 36 | 0 | – | – | – | –
4 | 32 | 1 | 43 | 6D | 8F | 09
5 | 0D | 1 | 36 | 72 | F0 | 1D
6 | 31 | 0 | – | – | – | –
7 | 16 | 1 | 11 | C2 | DF | 03
Index | Tag | Valid | B0 | B1 | B2 | B3
8 | 24 | 1 | 3A | 00 | 51 | 89
9 | 2D | 0 | – | – | – | –
A | 2D | 1 | 93 | 15 | DA | 3B
B | 0B | 0 | – | – | – | –
C | 12 | 0 | – | – | – | –
D | 16 | 1 | 04 | 96 | 34 | 15
E | 13 | 1 | 83 | 77 | 1B | D3
F | 14 | 0 | – | – | – | –
Notes: Split up cache as usual into CT, CI, CO
In this example, assume that block size is 4 bytes, so need 2 bits
Coincidence that CT is same width as PPN

## Slide 16: Current State of Memory System
Cache:
TLB:
Page table (partial):
Index | Tag | V | B0 | B1 | B2 | B3
0 | 19 | 1 | 99 | 11 | 23 | 11
1 | 15 | 0 | – | – | – | –
2 | 1B | 1 | 00 | 02 | 04 | 08
3 | 36 | 0 | – | – | – | –
4 | 32 | 1 | 43 | 6D | 8F | 09
5 | 0D | 1 | 36 | 72 | F0 | 1D
6 | 31 | 0 | – | – | – | –
7 | 16 | 1 | 11 | C2 | DF | 03
Index | Tag | V | B0 | B1 | B2 | B3
8 | 24 | 1 | 3A | 00 | 51 | 89
9 | 2D | 0 | – | – | – | –
A | 2D | 1 | 93 | 15 | DA | 3B
B | 0B | 0 | – | – | – | –
C | 12 | 0 | – | – | – | –
D | 16 | 1 | 04 | 96 | 34 | 15
E | 13 | 1 | 83 | 77 | 1B | D3
F | 14 | 0 | – | – | – | –
Set | Tag | PPN | V | Tag | PPN | V | Tag | PPN | V | Tag | PPN | V
0 | 03 | – | 0 | 09 | 0D | 1 | 00 | – | 0 | 07 | 02 | 1
1 | 03 | 2D | 1 | 02 | – | 0 | 04 | – | 0 | 0A | – | 0
2 | 02 | – | 0 | 08 | – | 0 | 06 | – | 0 | 03 | – | 0
3 | 07 | – | 0 | 03 | 0D | 1 | 0A | 34 | 1 | 02 | – | 0
VPN | PPN | V
0 | 28 | 1
1 | – | 0
2 | 33 | 1
3 | 02 | 1
4 | – | 0
5 | 16 | 1
6 | – | 0
7 | – | 0
VPN | PPN | V
8 | 13 | 1
9 | 17 | 1
A | 09 | 1
B | – | 0
C | – | 0
D | 2D | 1
E | – | 0
F | 0D | 1
Notes: TLB and Cache are separate pieces of hardware; page table stored in memory
Show correlation between TLB & page table (VPN 0x0D and 0x0F in particular)
TLB index is 2 bits
0x0D = 0000 1101 (set 1 with tag 0x03) maps to PPN 0x2D
0x0F = 0000 1111 (set 3 with tag 0x03) maps to PPN 0x0D

## Slide 17: Memory Request Example #1
Virtual Address: 0x03D4
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
1
9
1
8
1
7
1
6
0
5
1
4
0
3
1
2
0
1
0
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Hit, Cache Hit
VPN: 0x0F, TLBT: 0x3, TLBI: 0x3, TLB Hit: yes, page fault: no, PPN: 0x0D (check valid bit, confirm that matches page table)
Copy offset to physical address, total should be: 0b00 1101 0101 00
CT: 0x0D, CI: 0x5, CO: 0x0, data: 0x36 (check valid bit!)

## Slide 18: Memory Request Example #2
Virtual Address: 0x038F
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
1
9
1
8
1
7
0
6
0
5
0
4
1
3
1
2
1
1
1
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Miss, page fault
VPN: 0x0E, TLBT: 0x03, TLBI: 0x2, TLB Hit: no, check the page table, page fault 

## Slide 19: Memory Request Example #3
Virtual Address: 0x0020
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
0
9
0
8
0
7
0
6
1
5
0
4
0
3
0
2
0
1
0
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Miss, Page Table Hit, Cache Miss
VPN: 0x00, TLBT: 0x0, TLBI: 0x0, TLB Hit: no, page fault: no, PPN: 0x28 (check valid bit)
Physical address: 0b10 1000 1000 00
CT: 0x28, CI: 0x8, CO: 0x2, cache hit: no (tag doesn’t match), data returned (shrug)?

## Slide 20: Memory Request Example #4
Virtual Address: 0x036B
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
1
9
1
8
0
7
1
6
1
5
0
4
1
3
0
2
1
1
1
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Hit, Cache Hit

## Slide 21: Memory Overview
Disk
Main memory
(DRAM)
Cache
CPU
Page
Page
Line
Block
requested 32-bits
movl 0x8043ab, %rdi
TLB
MMU
Notes: We have pages, move pages in and out of memory.
Segment pages into smaller blocks of data
Move blocks in and out of caches
Cache returns data requested to the CPU (

## Slide 22: Page Table Reality
Just one issue… the numbers don’t work out for the story so far!
The problem is the page table for each process:
  Suppose 64-bit VAs, 8 KiB pages, 8 GiB physical memory
  How many page table entries is that?
  About how long is each PTE?
  Moral: Cannot use this naïve implementation of the virtual→physical page mapping – it’s way too big
This is extra (non-testable) material
Notes: Page table entries: 2^64/2^13 (8KiB) = 2^(n-p) = 2^51
PPN = 20 bits (m=33, 33-p = 33-13); plus Valid, R/W/X; so ~ 3 B per PTE
So each page table takes up 2^52 + 2^51 B! (same as 2^51 * 3 = 2^51 + 2^51 + 2^51)
This is on the order of pebibytes

## Slide 23: A Solution: Multi-level Page Tables
Page table base register
(PTBR)
VPN 1
0
p-1
n-1
VPO
VPN 2
...
VPN k
PPN
0
p-1
m-1
PPO
PPN
Virtual Address
Physical Address
...
...
Level 1
page table
Level 2
page table
Level k
page table
TLB
PTE
VPN
→
PTE
VPN
→
PTE
VPN
→
This is called a page walk
This is extra (non-testable) material
Notes: Split up virtual address into chunks
Walk down “arrays of pointers” via pieces of the VPN, starting from MSBs and going down to LSBs
Example: only 4 virtual pages, so 2 bits (write all combos out)
  Draw out tree, 2 entries -> 2 * 2 entries
  Use upper bit as VPN 1 field
    If 0, in bottom half
    If 1, in top half
  Use lower bit to actually discover PPN, based on which array we ended up in with higher bit
If only using the top two entries, can avoid allocating entire bottom half of table
Since most addresses are never allocated, actually much more efficient

## Slide 24: Multi-level Page Tables
A tree of depth where each node at depth has up to children if part of the VPN has bits
Hardware for multi-level page tables inherently more complicated
  But it’s a necessary complexity – 1-level does not fit
Why it works: Most subtrees are not used at all, so they are never created and definitely aren’t in physical memory
  Parts created can be evicted from cache/memory when not being used
  Each node can have a size of ~1-100KB
But now for a -level page table, a TLB miss requires cache/memory accesses
  Fine so long as TLB misses are rare – motivates larger TLBs
This is extra (non-testable) material

## Slide 25: Practice VM Question
Our system has the following properties
  1 MiB of physical address space
  4 GiB of virtual address space
  32 KiB page size
  4-entry fully associative TLB with LRU replacement
Fill in the following blanks:
________ | Entries in a page table | ________ | Minimum bit-width of page table base register (PTBR)
________ | TLBT bits | ________ | Max # of valid entries in a page table
Notes: Physical address space = m = 20 bits
Virtual address space = n = 32 bits
Page size = p =15 bits
Entries in page table: 2^n-p = 32-15 = 2^17
Minimum bit with of PTBR: 20 bits (size of physical address space; in reality probably just 64 bits)
VPN width = n-p = TLBT + TLBI
1 TLB set since fully associative, so 0 index bits, so 17 bit tag (full size of VPN)
Valid entry means that page exists in PA space, total num of physical pages = 2^(m-p) = 2^5

## Slide 26: Practice VM Question
One process uses a page-aligned square matrix mat[] of 32-bit integers in the code shown below:
#define MAT_SIZE = 2048
for(int i = 0; i < MAT_SIZE; i++)
mat[i*(MAT_SIZE+1)] = i;
What is the largest stride (in bytes) between successive memory accesses (in the VA space)?
Notes: Page aligned: starting address at page offset of 0
i=0, idx=0
i=1, idx=2049
i=2, idx=2*2049
Stride = 2049 elements = 2049*4 (sizeof int)=8196B
What is it doing? Setting diagonals of matrix to i (draw a diagram of matrix)

## Slide 27: Practice VM Question
One process uses a page-aligned square matrix mat[] of 32-bit integers in the code shown below:
#define MAT_SIZE = 2048
for(int i = 0; i < MAT_SIZE; i++)
mat[i*(MAT_SIZE+1)] = i;
Assuming all of mat[] starts on disk, what are the following hit rates for the execution of the for-loop?
________ | TLB Hit Rate | ________ | Page Table Hit Rate
Notes: 2048=2^11
Recall: page size is 32 KiB = 2^15 bytes.
1 memory access occurring inside of loop, addresses are never revisited
Each row accessed once
First row will be a miss, next will be a hit if on the page
How many rows fit in a page?
  How manys int in a page? Pages hold 2^15 bytes = 2^15/2^2 = 2^13 ints
  How many ints in a row? 2^11
  How many rows in each page? 2^13/2^11 = 2^2 = 4
each row accessed once
  Miss, hit, hit, hit
  Miss, hit, hit, hit
  Overall: 75% TLB hit rate
Only need to check page table when mapping is not in the TLB. So page table hit rate is 0%, since all of the matrix starts on disk
  nothing in the page table that is not also in the TLB
  Only read each address once

## Slide 28
For Fun: DRAMMER Security Attack
Why are we talking about this?
  Recent(ish): Announced in October 2016; Google released Android patch on November 8, 2016
  Relevant: Uses your system’s memory setup to gain elevated privileges
    Ties together some of what we’ve learned about virtual memory and processes
  Interesting: It’s a software attack that uses only hardware vulnerabilities and requires no user permissions
BONUS SLIDES

## Slide 29: Underlying Vulnerability: Row Hammer
Dynamic RAM (DRAM) has gotten denser over time
  DRAM cells physically closer and use smaller charges
  More susceptible to “disturbance errors” (interference)
DRAM capacitors need to be “refreshed” periodically (~64 ms)
  Lose data when loss of power
  Capacitors accessed in rows
Rapid accesses to one row can flip bits in an adjacent row!
  ~ 100K to 1M times
By Dsimic (modified), CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=38868341

## Slide 30: Row Hammer Exploit
Force constant memory access
  Read then flush the cache
  clflush – flush cache line
    Invalidates cache line containing the specified address
    Not available in all machines or environments
  Want addresses X and Y to fall in activation target row(s)
    Good to understand how banks of DRAM cells are laid out
The row hammer effect was discovered in 2014
  Only works on certain types of DRAM (2010 onwards)
  These techniques target x86 machines
hammertime:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
jmp hammertime

## Slide 31: Consequences of Row Hammer
Row hammering process can affect another process via memory
  Circumvents virtual memory protection scheme
  Memory needs to be in an adjacent row of DRAM
Worse: privilege escalation
  Page tables live in memory!
  Hope to change PPN to access other parts of memory, or change permission bits
  Goal: gain read/write access to a page containing a page table, hence granting process read/write access to all of physical memory

## Slide 32: Effectiveness?
Doesn’t seem so bad – random bit flip in a row of physical memory
  Vulnerability affected by system setup and physical condition of memory cells
Improvements:
  Double-sided row hammering increases speed & chance
  Do system identification first (e.g. Lab 4)
    Use timing to infer memory row layout & find “bad” rows
    Allocate a huge chunk of memory and try many addresses, looking for a reliable/repeatable bit flip
  Fill up memory with page tables first
    fork extra processes; hope to elevate privileges in any page table

## Slide 33: What’s DRAMMER?
No one previously made a huge fuss
  Prevention: error-correcting codes, target row refresh, higher DRAM refresh rates
  Often relied on special memory management features
  Often crashed system instead of gaining control
Research group found a deterministic way to induce row hammer exploit in a non-x86 system (ARM)
  Relies on predictable reuse patterns of standard physical memory allocators
  Universiteit Amsterdam, Graz University of Technology, and University of California, Santa Barbara

## Slide 34: DRAMMER Demo Video
It’s a shell, so not that sexy-looking, but still interesting
  Apologies that the text is so small on the video
Notes: https://youtu.be/x6hL-obNhAw

## Slide 35: How did we get here?
Computing industry demands more and faster storage with lower power consumption
Ability of user to circumvent the caching system
  clflush is an unprivileged instruction in x86
  Other commands exist that skip the cache
Availability of virtual to physical address mapping
  Example: /proc/self/pagemap on Linux (not human-readable)
Google patch for Android (Nov. 8, 2016)
  Patched the ION memory allocator

## Slide 36: More reading for those interested
DRAMMER paper: https://vvdveen.com/publications/drammer.pdf
Google Project Zero: https://googleprojectzero.blogspot.com/2015/03/exploiting-dram-rowhammer-bug-to-gain.html
First row hammer paper: https://users.ece.cmu.edu/~yoonguk/papers/kim-isca14.pdf
Wikipedia: https://en.wikipedia.org/wiki/Row_hammer

## Slide 37: Quick Review Answers
What do Page Tables map?
  VPN PPN or disk address
Where are Page Tables located?
  In physical memory
How many Page Tables are there?
  One per process
Can your program tell if a page fault has occurred?
  Nope, but it has to wait a long time
What is thrashing?
  Constantly paging out and paging in
True / False: Virtual Addresses that are contiguous will always be contiguous in physical memory
  Could fall across a page boundary
TLB stands for Translation Lookaside Buffer and stores page table entries