## Slide 1: Memory Allocation II CSE 351 Spring 2019
Instructor:
Ruth Anderson
Teaching Assistants:
Gavin Cai Jack Eggleston John Feltrup Britt Henderson Richard Jiang Jack Skalitzky Sophie Tian Connie Wang Sam Wolfson Casey Xing Chin Yeoh
http://xkcd.com/1909/

## Slide 2: Administrivia
Homework 5, due Friday (5/31)
  Processes and Virtual Memory
Lab 5, released Wed Evening, due Friday (6/7)
  Memory Allocation
  Recommended that you watch the Lab 5 helper videos
  Sunday 6/9 is last day Lab 5 may be submitted (if one late day is used)
Final Exam: Wed, 6/12, 12:30-2:20 pm in KNE 130

## Slide 3: Peer Instruction Question
Which allocation strategy and requests remove external fragmentation in this Heap? B3 was the last fulfilled request.
  http://pollev.com/rea
Best-fit: malloc(50), malloc(50)
(A)
First-fit:
malloc(50), malloc(30)
(B)
Next-fit: malloc(30), malloc(50)
(C)
Next-fit: malloc(50), malloc(30)
(D)
B1
B3
B2
10
10
50
50
50
30
Start of heap
payload
size

## Slide 4: Implicit List: Allocating in a Free Block
Allocating in a free block: splitting
  Since allocated space might be smaller than free space, we might want to split the block
void split(ptr b, int bytes) { // bytes = desired block size
int newsize = ((bytes+15) >> 4) << 4; // round up to multiple of 16
int oldsize = *b; // why not mask out low bit?
*b = newsize; // initially unallocated
if (newsize < oldsize)
*(b+newsize) = oldsize - newsize; // set length in remaining
} // part of block (UNSCALED +)
Assume ptr points to a free block and has unscaled pointer arithmetic
malloc(24):
ptr b = find(24+8)
split(b, 24+8)
allocate(b)
Free word
Allocated word
Newly-allocated word
16|1
16|1
48|0
b
16|0
16|1
16|1
32|1
Notes: Note that we add 4 to the malloc request size to account for the header
Why not mask out? Bit must be 0, otherwise it's not a free block!

## Slide 5: Implicit List: Freeing a Block
Simplest implementation just clears “allocated” flag
  void free(ptr p) {*(p-WORD) &= -2;}
  But can lead to “false fragmentation”
p
Oops! There is enough free space, but the allocator won’t be able to find it
16|0
16|1
16|1
32|1
Free word
Allocated word
Block of interest
16|0
16|1
16|1
32|0
malloc(40)
free(p)

## Slide 6: Implicit List: Coalescing with Next
Join (coalesce) with next block if also free
How do we coalesce with the previous block?
void free(ptr p) { // p points to payload ptr b = p – WORD; // b points to block header
*b &= -2; // clear allocated bit ptr next = b + *b; // find next block (UNSCALED +) if ((*next & 1) == 0) // if next block is not allocated, *b += *next; // add its size to this block }
logically gone
16|0
16|1
16|1
32|1
16|0
16|1
16|1
48|0
free(p)
p
Free word
Allocated word
Block of interest

## Slide 7: Implicit List: Bidirectional Coalescing
Boundary tags [Knuth73]
  Replicate header at “bottom” (end) of free blocks
  Allows us to traverse backwards, but requires extra space
  Important and general technique!
Footer
32/0
32/0
32/1
32/1
48/0
32/1
48/0
32/1
Header
size
payload and padding
a
size
a
Format of allocated and free blocks:
a = 1: allocated block
a = 0: free block
size: block size (in bytes)
payload: application data
(allocated blocks only)
Boundary tags

## Slide 8: Constant Time Coalescing
Allocated
Allocated
Allocated
Free
Free
Allocated
Free
Free
Block being freed
Case 1
Case 2
Case 3
Case 4

## Slide 9: Constant Time Coalescing
m1 | 1
m1 | 1
n | 1
n | 1
m2 | 1
m2 | 1
m1 | 1
m1 | 1
n | 0
n | 0
m2 | 1
m2 | 1
Case 1
m1 | 1
m1 | 1
n | 1
n | 1
m2 | 0
m2 | 0
m1 | 1
m1 | 1
n+m2 | 0
n+m2 | 0
Case 2
m1 | 0
m1 | 0
n | 1
n | 1
m2 | 1
m2 | 1
n+m1 | 0
n+m1 | 0
m2 | 1
m2 | 1
Case 3
m1 | 0
m1 | 0
n | 1
n | 1
m2 | 0
m2 | 0
n+m1+m2 | 0
n+m1+m2 | 0
Case 4

## Slide 10: Implicit Free List Review Questions
What is the block header? What do we store and how?
What are boundary tags and why do we need them?
When we coalesce free blocks, how many neighboring blocks do we need to check on either side? Why is this?
If I want to check the size of the -th block forward from the current block, how many memory accesses do I make?
32/0
32/0
32/1
32/1
48/0
32/1
48/0
32/1

## Slide 11: Keeping Track of Free Blocks
Implicit free list using length – links all blocks using math
  No actual pointers, and must check each block if allocated or free
Explicit free list among only the free blocks, using pointers
Segregated free list
  Different free lists for different size “classes”
Blocks sorted by size
  Can use a balanced binary tree (e.g. red-black tree) with pointers within each free block, and the length used as a key
40
32
16
48
40
32
16
48
= 8-byte box (free)
= 8-byte box (allocated)

## Slide 12: Explicit Free Lists
Use list(s) of free blocks, rather than implicit list of all blocks
  The “next” free block could be anywhere in the heap
    So we need to store next/previous pointers, not just sizes
  Since we only track free blocks, so we can use “payload” for pointers
  Still need boundary tags (header/footer) for coalescing
size
a
size
a
next
prev
Free block:
size
payload and
padding
a
size
a
Allocated block:
(same as implicit free list)
Notes: Storing pointers in the “payload” section of a free block could require a larger minimum block size, possibly increasing internal fragmentation.

## Slide 13: Doubly-Linked Lists
Linear
  Needs head/root pointer
  First node prev pointer is NULL
  Last node next pointer is NULL
  Good for first-fit, best-fit
Circular
  Still have pointer to tell you which node to start with
  No NULL pointers (term condition is back at starting point)
  Good for next-fit, best-fit
Root
⋅⋅⋅
Start
⋅⋅⋅

## Slide 14: Explicit Free Lists
Logically: doubly-linked list
Physically: blocks can be in any order
A
B
C
32
32
32
32
48
48
32
32
32
32
Forward (next) links
Back (prev) links
A
B
C

## Slide 15: Allocating From Explicit Free Lists
Note: These diagrams are not very specific about where inside a block a pointer points. In reality we would always point to one place (e.g. start/header of a block).
Before
After
(with splitting)
= malloc(…)
Notes: 4 pointers updated, same number of list nodes.
Don’t forget to update boundary tags for both the allocated and new free blocks!

## Slide 16: Allocating From Explicit Free Lists
Note: These diagrams are not very specific about where inside a block a pointer points. In reality we would always point to one place (e.g. start/header of a block).
Before
After
(fully allocated)
= malloc(…)
Notes: 2 pointers updated, one fewer list node.
Don’t forget to create the boundary tags for the allocated block!

## Slide 17: Freeing With Explicit Free Lists
Insertion policy: Where in the free list do you put the newly freed block?
  LIFO (last-in-first-out) policy
    Insert freed block at the beginning (head) of the free list
    Pro: simple and constant time
    Con: studies suggest fragmentation is worse than the alternative
  Address-ordered policy
    Insert freed blocks so that free list blocks are always in address order:
    address(previous) < address(current) < address(next)
    Con: requires linear-time search
    Pro: studies suggest fragmentation is better than the alternative

## Slide 18: Coalescing in Explicit Free Lists
Neighboring free blocks are already part of the free list
  Remove old block from free list
  Create new, larger coalesced block
  Add new block to free list (insertion policy)
How do we tell if a neighboring block if free?
Block being freed
Allocated
Allocated
Case 1
Allocated
Free
Case 2
Free
Allocated
Case 3
Free
Free
Case 4

## Slide 19: Freeing with LIFO Policy (Case 1)
Insert the freed block at the root of the list
Before
After
Root
Boundary tags not shown, but don’t forget about them!
free( )
Root
Notes: Note: all blue “next” pointers and red “previous” pointers should probably point to either the header or footer of the next/previous block – it shouldn’t matter which (I think), as long as it’s done consistently. The diagrams on this slide and on the next few do not always show pointers to the exact word for the block header/footer.

## Slide 20: Freeing with LIFO Policy (Case 2)
Splice successor block out of list, coalesce both memory blocks, and insert the new block at the root of the list
Boundary tags not shown, but don’t forget about them!
Before
Root
free( )
After
Root
Notes: Note: all blue “next” pointers and red “previous” pointers should probably point to either the header or footer of the next/previous block – it shouldn’t matter which (I think), as long as it’s done consistently. The diagrams on this slide and on the next few do not always show pointers to the exact word for the block header/footer.

## Slide 21: Freeing with LIFO Policy (Case 3)
Splice predecessor block out of list, coalesce both memory blocks, and insert the new block at the root of the list
Boundary tags not shown, but don’t forget about them!
Before
Root
free( )
After
Root
Notes: Note: all blue “next” pointers and red “previous” pointers should probably point to either the header or footer of the next/previous block – it shouldn’t matter which (I think), as long as it’s done consistently. The diagrams on this slide and on the next few do not always show pointers to the exact word for the block header/footer.

## Slide 22: Freeing with LIFO Policy (Case 4)
Splice predecessor and successor blocks out of list, coalesce all 3 memory blocks, and insert the new block at the root of the list
Boundary tags not shown, but don’t forget about them!
Before
Root
free( )
After
Root

## Slide 23: Do we always need the boundary tags?
Lab 5 suggests no…
size
a
size
a
next
prev
Free block:
size
payload and
padding
a
size
a
Allocated block:
(same as implicit free list)

## Slide 24: Explicit List Summary
Comparison with implicit list:
  Block allocation is linear time in number of free blocks instead of all blocks
    Much faster when most of the memory is full
  Slightly more complicated allocate and free since we need to splice blocks in and out of the list
  Some extra space for the links (2 extra pointers needed for each free block)
    Increases minimum block size, leading to more internal fragmentation
Most common use of explicit lists is in conjunction with segregated free lists
  Keep multiple linked lists of different size classes, or possibly for different types of objects

## Slide 25
The following slides are about the SegList Allocator, for those curious. You will NOT be expected to know this material.
BONUS SLIDES

## Slide 26: SegList Allocator
Have an array of free lists for various size classes
To allocate a block of size :
  Search appropriate free list for block of size
  If an appropriate block is found:
    [Optional] Split block and place free fragment on appropriate list
  If no block is found, try the next larger class
    Repeat until block is found
If no block is found:
  Request additional heap memory from OS (using sbrk)
  Place remainder of additional heap memory as a single free block in appropriate size class

## Slide 27: SegList Allocator
Have an array of free lists for various size classes
To free a block:
  Mark block as free
  Coalesce (if needed)
  Place on appropriate class list

## Slide 28: SegList Advantages
Higher throughput
  Search is log time for power-of-two size classes
Better memory utilization
  First-fit search of seglist approximates a best-fit search of entire heap
  Extreme case: Giving every block its own size class is no worse than best-fit search of an explicit list
  Don’t need to use space for block size for the fixed-size classes

## Slide 29: Freeing with LIFO Policy (Explicit Free List)
 | Predecessor Block | Successor Block | Change in Nodes in Free List | Number of Pointers Updated
Case 1 | Allocated | Allocated |  | 
Case 2 | Allocated | Free |  | 
Case 3 | Free | Allocated |  | 
Case 4 | Free | Free |  |