## Slide 1: Caches III CSE 351 Winter 2019
https://what-if.xkcd.com/111/
Instructors:
Max Willsey
Luis Ceze
Teaching Assistants:
Britt Henderson
Lukas Joswiak
Josie Lee
Wei Lin
Daniel Snitkovsky
Luis Vega
Kory Watson
Ivy Yu

## Slide 2: Administrivia
Lab 3 due today (Friday)
Lab 4 out this weekend
HW 4 is released, due next Friday (03/01)
Last day for regrade requests!
Extra OH today
  Me – 12:00-1:30pm – CSE 280
  Lukas – 2:30pm-close – 2nd floor breakout
Cache sim!

## Slide 3: Making memory accesses fast!
Cache basics
Principle of locality
Memory hierarchies
Cache organization
  Direct-mapped (sets; index + tag)
  Associativity (ways)
  Replacement policy
  Handling writes
Program optimizations that consider caches
Notes: Divide addresses into “index” and “tag”

## Slide 4: Checking for a Requested Address
CPU sends address request for chunk of data
  Address and requested data are not the same thing!
    Analogy: your friend ≠ his or her phone number
TIO address breakdown:
  Index field tells you where to look in cache
  Tag field lets you check that data is the block you want
  Offset field selects specified start byte within block
  Note: and sizes will change based on hash function
Tag ()
Offset ()
-bit address:
Block Number
Index ()
Notes: Tio = uncle in spanish
Go through steps
What determines the size?
– k – block size (K)
s – num blocks in cache
t - rest
Why are they in this order?
Offset must be last
You want index to ”change fast” to minimize collision
If you swapped tag and index, adjacent blocks would collide (jump forward two slides)

## Slide 5: Direct-Mapped Cache
Hash function: index bits
  Each memory address maps to exactly one index in the cache
  Fast (and simpler) to find an address
Block Addr | Block Data |  |  | 
00 00 |  |  |  | 
00 01 |  |  |  | 
00 10 |  |  |  | 
00 11 |  |  |  | 
01 00 |  |  |  | 
01 01 |  |  |  | 
01 10 |  |  |  | 
01 11 |  |  |  | 
10 00 |  |  |  | 
10 01 |  |  |  | 
10 10 |  |  |  | 
10 11 |  |  |  | 
11 00 |  |  |  | 
11 01 |  |  |  | 
11 10 |  |  |  | 
11 11 |  |  |  | 
Memory
Cache
Index | Tag |  | Block Data |  |  | 
00 | 00 |  |  |  |  | 
01 | 11 |  |  |  |  | 
10 | 01 |  |  |  |  | 
11 | 01 |  |  |  |  | 
Here = 4 B
and = 4

## Slide 6: Direct-Mapped Cache Problem
What happens if we access the following addresses?
  8, 24, 8, 24, 8, …?
  Conflict in cache (misses!)
  Rest of cache goes unused
Solution?
Block Addr | Block Data |  |  | 
00 00 |  |  |  | 
00 01 |  |  |  | 
00 10 |  |  |  | 
00 11 |  |  |  | 
01 00 |  |  |  | 
01 01 |  |  |  | 
01 10 |  |  |  | 
01 11 |  |  |  | 
10 00 |  |  |  | 
10 01 |  |  |  | 
10 10 |  |  |  | 
10 11 |  |  |  | 
11 00 |  |  |  | 
11 01 |  |  |  | 
11 10 |  |  |  | 
11 11 |  |  |  | 
Memory
Cache
Index | Tag |  | Block Data |  |  | 
00 | ?? |  |  |  |  | 
01 | ?? |  |  |  |  | 
10 |  |  |  |  |  | 
11 | ?? |  |  |  |  | 
Here = 4 B
and = 4
Notes: Conflict! Rest of cache unused!

## Slide 7: Associativity
What if we could store data in any place in the cache?
  More complicated hardware = more power consumed, slower
So we combine the two ideas:
  Each address maps to exactly one set
  Each set can store block in more than one way
0
1
2
3
4
5
6
7
0
1
2
3
Set
0
1
Set
1-way:
8 sets,
1 block each
2-way:
4 sets,
2 blocks each
4-way:
2 sets,
4 blocks each
0
Set
8-way:
1 set,
8 blocks
direct mapped
fully associative
Notes: “Where is address 2?”

## Slide 8: Cache Organization (3)
Associativity (): # of ways for each set
  Such a cache is called an “-way set associative cache”
  We now index into cache sets, of which there are
  Use lowest = bits of block address
    Direct-mapped: = 1, so = as we saw previously
    Fully associative: = , so = 0 bits
Decreasing associativity
Fully associative
(only one set)
Direct mapped
(only one way)
Increasing associativity
Selects the set
Used for tag comparison
Selects the byte from block
Tag ()
Index ()
Offset ()
Note: The textbook uses “b” for offset bits
Notes: Assume a fixed cache size

## Slide 9: Example Placement
Where would data from address 0x1833 be placed?
  Binary: 0b 0001 1000 0011 0011
= ?
block size: | 16 B
capacity: | 8 blocks
address: | 16 bits
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Direct-mapped
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
Set | Tag | Data
0 |  | 
1 |  | 
2-way set associative
4-way set associative
Tag ()
Offset ()
-bit address:
Index ()
=
=
= ––
= ?
= ?
Notes: 9
k = 4
E = 1; s = 3; idx = 3
E = 2; s = 2; idx = 3
E = 4; s = 1; idx = 1

## Slide 10: Block Replacement
Any empty block in the correct set may be used to store block
If there are no empty blocks, which one should we replace?
  No choice for direct-mapped caches
  Caches typically use something close to least recently used (LRU) (hardware usually implements “not most recently used”)
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Direct-mapped
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
Set | Tag | Data
0 |  | 
1 |  | 
2-way set associative
4-way set associative

## Slide 11: Peer Instruction Question
We have a cache of size 2 KiB with block size of 128 B. If our cache has 2 sets, what is its associativity?
2
4
8
16
We’re lost…
If addresses are 16 bits wide, how wide is the Tag field?
Notes: C = 2^11 B
K = 2^7 B
2^4 = 16 blocks
16 / 2 = 8 E
k = 7; s = 1; t = 16 – 7 – 1 = 8

## Slide 12: General Cache Organization (, , )
= blocks/lines per set
= # sets
=
set
“line” (block plus management bits)
0
1
2
K-1
Tag
V
valid bit
= bytes per block
Cache size:
data bytes
(doesn’t include V or Tag)
Notes: “Layers” of a cache:
Block (data)
Line (data + management bits)
Set (many lines based on associativity)
Cache (many sets based on cache size & associativity)
Valid bit lets us know if this line has been initialized (“is valid”).

## Slide 13: Notation Review
We just introduced a lot of new variable names!
  Please be mindful of block size notation when you look at past exam questions or are watching videos
Variable | This Quarter | Formulas
Block size | ( in book) | 
Cache size |  | 
Associativity |  | 
Number of Sets |  | 
Address space |  | 
Address width |  | 
Tag field width |  | 
Index field width |  | 
Offset field width | ( in book) | 
Variable | This Quarter | Formulas
Block size |  | 
Cache size |  | 
Associativity |  | 
Number of Sets |  | 
Address space |  | 
Address width |  | 
Tag field width |  | 
Index field width |  | 
Offset field width |  | 
Notes: Review this on your own
DON’T MEMORIZE FORUMLAS

## Slide 14: Example Cache Parameters Problem
4 KiB address space, 125 cycles to go to memory. Fill in the following table:
Cache Size | 256 B
Block Size | 32 B
Associativity | 2-way
Hit Time | 3 cycles
Miss Rate | 20%
Tag Bits | 
Index Bits | 
Offset Bits | 
AMAT | 
Notes: Tag bits = 5
Index bits = 2
Offset bits = 5
AMAT = 3 + 0.2(125) = 28 cycles

## Slide 15: Cache Read
0
1
2
K-1
tag
v
bits
bits
bits
Address of byte in memory:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set is valid and has matching tag: hit
Locate data starting at offset
valid bit
= # sets
=
= blocks/lines per set
= bytes per block

## Slide 16: Example: Direct-Mapped Cache ( = 1)
Direct-mapped: One line per set
Block Size = 8 B
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set
= sets

## Slide 17: Example: Direct-Mapped Cache ( = 1)
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match?: yes = hit
valid? +
block offset
Direct-mapped: One line per set
Block Size = 8 B

## Slide 18: Example: Direct-Mapped Cache ( = 1)
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match?: yes = hit
valid? +
int (4 B) is here
block offset
No match? Then old line gets evicted and replaced
This is why we want alignment!
Direct-mapped: One line per set
Block Size = 8 B

## Slide 19: Example: Set-Associative Cache ( = 2)
bits
0…01
100
Address of short int:
find set
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
2-way: Two lines per set
Block Size = 8 B
Notes: 1 fewer s bit, 2x fewer sets

## Slide 20: Example: Set-Associative Cache ( = 2)
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
bits
0…01
100
compare both
valid? +
match: yes = hit
block offset
tag
2-way: Two lines per set
Block Size = 8 B
Address of short int:

## Slide 21: Example: Set-Associative Cache ( = 2)
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
bits
0…01
100
valid? +
match: yes = hit
block offset
short int (2 B) is here
No match?
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …
compare both
Address of short int:
2-way: Two lines per set
Block Size = 8 B

## Slide 22: Types of Cache Misses: 3 C’s!
Compulsory (cold) miss
  Occurs on first access to a block
Conflict miss
  Conflict misses occur when the cache is large enough, but multiple data objects all map to the same slot
    e.g. referencing blocks 0, 8, 0, 8, ... could miss every time
  Direct-mapped caches have more conflict misses than -way set-associative (where > 1)
  Note: Fully-associative only has Compulsory and Capacity misses
Capacity miss
  Occurs when the set of active cache blocks (the working set) is larger than the cache (just won’t fit, even if cache was fully-associative)

## Slide 23: Example Code Analysis Problem
Assuming the cache starts cold (all blocks invalid) and sum is stored in a register, calculate the miss rate:
  = 12 bits, = 256 B, = 32 B, = 2
#define SIZE 8
long ar[SIZE][SIZE], sum = 0; // &ar=0x800
for (int i = 0; i < SIZE; i++)
for (int j = 0; j < SIZE; j++)
sum += ar[i][j];
Notes: k = 5 bits
256 / 32 = 8 blocks
8 / 2 = 4 sets
s = 2 bits
t = 12 – 5 – 2 = 5 bits
0x800 = 0b 1000 0000 0000
8 bytes per elem
4 longs fit in a block
¼ miss rate (missed are compulsory)

## Slide 24: What about writes?
Multiple copies of data exist:
  L1, L2, possibly L3, main memory
What to do on a write-hit?
  Write-through: write immediately to next level
  Write-back: defer write to next level until line is evicted (replaced)
    Must track which cache lines have been modified (“dirty bit”)
What to do on a write-miss?
  Write-allocate: (“fetch on write”) load into cache, update line in cache
    Good if more writes or reads to the location follow
  No-write-allocate: (“write around”) just write immediately to memory
Typical caches:
  Write-back + Write-allocate, usually
  Write-through + No-write-allocate, occasionally
Notes: Why? Reuse is common
  Typically you would read, then write (incr)
  Or after you initialize a value (say, to 0), likely read and write it again soon

## Slide 25: Write-back, write-allocate example
0xBEEF
Cache
Memory
G
0xCAFE
0xBEEF
0
F
G
dirty bit
tag (there is only one set in this tiny cache, so the tag is the entire block address!)
In this example we are sort of ignoring block offsets. Here a block holds 2 bytes (16 bits, 4 hex digits).
Normally a block would be much bigger and thus there would be multiple items per block. While only one item in that block would be written at a time, the entire line would be brought into cache.
Contents of memory stored at address G
Notes: Valid bit not shown
Tiny cache, 1 set, tag is G
Dirty bit because write back

## Slide 26: Write-back, write-allocate example
0xBEEF
Cache
Memory
G
0xCAFE
0xBEEF
0
F
G
mov 0xFACE, F
dirty bit
Notes: Miss, need to maybe write back
But not dirty, so I don’t have to
Pull in F

## Slide 27: Write-back, write-allocate example
0xBEEF
U
0
0xCAFE
Cache
Memory
F
0xCAFE
0xBEEF
F
G
dirty bit
0xCAFE
0
Step 1: Bring F into cache
mov 0xFACE, F
Notes: Pull in F, then write

## Slide 28: Write-back, write-allocate example
0xBEEF
U
0
0xCAFE
Cache
Memory
F
0xCAFE
0xBEEF
F
G
dirty bit
0xFACE
1
Step 2: Write 0xFACE to cache only and set dirty bit
mov 0xFACE, F
Notes: Write, make dirty (write-back)

## Slide 29: Write-back, write-allocate example
0xBEEF
U
0
0xCAFE
Cache
Memory
F
0xCAFE
0xBEEF
F
G
mov 0xFEED, F
dirty bit
0xFACE
1
Write hit!
Write 0xFEED to cache only
mov 0xFACE, F
Notes: Another write hit, don’t need to go to mem

## Slide 30: Write-back, write-allocate example
0xBEEF
U
0
0xCAFE
Cache
Memory
F
0xCAFE
0xBEEF
F
G
mov G, %rax
dirty bit
0xFEED
1
mov 0xFEED, F
mov 0xFACE, F
Notes: Read miss, and my line is dirty! Write back

## Slide 31: Write-back, write-allocate example
0xBEEF
Cache
Memory
G
0xFEED
0xBEEF
0
F
G
dirty bit
1. Write F back to memory since it is dirty 2. Bring G into the cache so we can copy it into %rax
mov G, %rax
mov 0xFEED, F
mov 0xFACE, F

## Slide 32: Peer Instruction Question
Which of the following cache statements is FALSE?
We can reduce compulsory misses by decreasing our block size
We can reduce conflict misses by increasing associativity
A write-back cache will save time for code with good temporal locality on writes
A write-through cache will always match data with the memory hierarchy level below it
We’re lost…
Notes: A
A: smaller block size pulls fewer bytes into $ on miss
B: more options to place blocks before need to evict
C: freq used blocks rarely get evicted, so fewer write-backs
D: yes, write-through!