## Slide 1: Virtual Memory I CSE 351 Winter 2019
https://xkcd.com/1495/
Instructors:
Max Willsey
Luis Ceze
Teaching Assistants:
Britt Henderson
Lukas Joswiak
Josie Lee
Wei Lin
Daniel Snitkovsky
Luis Vega
Kory Watson
Ivy Yu

## Slide 2: Roadmap
car *c = malloc(sizeof(car));
c->miles = 100;
c->gals = 17;
float mpg = get_mpg(c);
free(c);
Car c = new Car();
c.setMiles(100);
c.setGals(17);
float mpg = c.getMPG();
get_mpg:
pushq %rbp
movq %rsp, %rbp
...
popq %rbp
ret
Java:
C:
Assembly language:
Machine code:
0111010000011000
100011010000010000000010
1000100111000010
110000011111101000011111
Computer system:
OS:
Memory & data
Integers & floats
x86 assembly
Procedures & stacks
Executables
Arrays & structs
Memory & caches
Processes
Virtual memory
Memory allocation
Java vs. C

## Slide 3: Virtual Memory (VM*)
Overview and motivation
VM as a tool for caching
Address translation
VM as a tool for memory management
VM as a tool for memory protection
*Not to be confused with “Virtual Machine” which is a whole other thing.
Warning: Virtual memory is pretty complex, but crucial for understanding how processes work and for debugging performance

## Slide 4: Memory as we know it so far… is virtual!
Programs refer to virtual memory addresses
  movq (%rdi),%rax
  Conceptually memory is just a very large array of bytes
  System provides private address space to each process
Allocation: Compiler and run-time system
  Where different program objects should be stored
  All allocation within single virtual address space
But…
  We probably don’t have bytes of physical memory
  We certainly don’t have bytes of physical memory for every process
  Processes should not interfere with one another
    Except in certain cases where they want to share code or data
0xFF∙∙∙∙∙∙F
0x00∙∙∙∙∙∙0

## Slide 5: Problem 1: How Does Everything Fit?
64-bit virtual addresses can address
several exabytes
(18,446,744,073,709,551,616 bytes)
Physical main memory offers
a few gigabytes
(e.g. 8,589,934,592 bytes)
?
1 virtual address space per process, with many processes…
(Not to scale; physical memory would be smaller than the period at the end of this sentence compared to the virtual address space.)

## Slide 6: Problem 2: Memory Management
Physical main memory
What goes where?
stack
heap
.text
.data
…
Process 1
Process 2
Process 3
…
Process n
x
Each process has…
We have multiple processes:

## Slide 7: Problem 3: How To Protect
Physical main memory
Process i
Process j
Problem 4: How To Share?
Physical main memory
Process i
Process j

## Slide 8: How can we solve these problems?
“Any problem in computer science can be solved by adding another level of indirection.” – David Wheeler, inventor of the subroutine
Without Indirection
With Indirection
What if I want to move Thing?
P2
Thing
P1
P3
P2
Thing
P3
P1
NewThing
NewThing
Notes: Quote attributed to David Wheeler or Butler Lampson (http://en.wikipedia.org/wiki/Butler_Lampson)

## Slide 9: Indirection
Indirection: The ability to reference something using a name, reference, or container instead of the value itself. A flexible mapping between a name and a thing allows changing the thing without notifying holders of the name.
  Adds some work (now have to look up 2 things instead of 1)
  But don’t have to track all uses of name/address (single source!)
Examples:
  Phone system: cell phone number portability
  Domain Name Service (DNS): translation from name to IP address
  Call centers: route calls to available operators, etc.
  Dynamic Host Configuration Protocol (DHCP): local network address assignment

## Slide 10: Indirection in Virtual Memory
Each process gets its own private virtual address space
Solves the previous problems!
Physical memory
Virtual memory
Virtual memory
Process 1
Process
mapping

## Slide 11: Address Spaces
Virtual address space: Set of virtual addr
  {0, 1, 2, 3, …, -1}
Physical address space: Set of physical addr
  {0, 1, 2, 3, …, -1}
Every byte in main memory has:
  one physical address (PA)
  zero, one, or more virtual addresses (VAs)

## Slide 12: Mapping
A virtual address (VA) can be mapped to either physical memory or disk
  Unused VAs may not have a mapping
  VAs from different processes may map to same location in memory/disk
Process 2’s Virtual
Address Space
Physical Memory
Disk
Process 1’s Virtual
Address Space
“Swap Space”

## Slide 13: A System Using Physical Addressing
Used in “simple” systems with (usually) just one process:
  Embedded microcontrollers in devices like cars, elevators, and digital picture frames
0:
1:
M-1:
Main memory
CPU
2:
3:
4:
5:
6:
7:
Physical address (PA)
Data (int/float)
8:
...
0x4

## Slide 14: A System Using Virtual Addressing
Physical addresses are completely invisible to programs
  Used in all modern desktops, laptops, servers, smartphones…
  One of the great ideas in computer science
0:
1:
M-1:
Main memory
MMU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data (int/float)
8:
...
CPU
Virtual address
(VA)
CPU Chip
0x4
0x4100
Memory Management Unit

## Slide 15: Why Virtual Memory (VM)?
Efficient use of limited main memory (RAM)
  Use RAM as a cache for the parts of a virtual address space
    Some non-cached parts stored on disk
    Some (unallocated) non-cached parts stored nowhere
  Keep only active areas of virtual address space in memory
    Transfer data back and forth as needed
Simplifies memory management for programmers
  Each process “gets” the same full, private linear address space
Isolates address spaces (protection)
  One process can’t interfere with another’s memory
    They operate in different address spaces
  User process cannot access privileged information
    Different sections of address spaces have different permissions
Notes: Adds disks to memory hierarchy
Simplifies memory for processes & programmers
Security/protection

## Slide 16: VM and the Memory Hierarchy
Think of virtual memory as array of contiguous bytes
Pages of virtual memory are usually stored in physical memory, but sometimes spill to disk
  Pages are another unit of aligned memory (size is bytes)
  Each virtual page can be stored in any physical page (no fragmentation!)
VP 0
VP 1
VP 2n-p-1
Virtual memory
Unallocated
Unallocated
0
2n-1
PP 2m-p-1
Physical memory
Empty
Empty
PP 0
PP 1
Empty
2m-1
0
Virtual pages (VP's)
Disk
Physical pages (PP's)
“Swap Space”
Notes: Swap space: https://www.linux.com/news/all-about-linux-swap-space

## Slide 17: or: Virtual Memory as DRAM Cache for Disk
Think of virtual memory as an array of contiguous bytes stored on a disk
Then physical main memory is used as a cache for the virtual memory array
  These “cache blocks” are called pages (size is bytes)
PP 2m-p-1
Physical memory
Empty
Empty
Uncached
VP 0
VP 1
VP 2n-p-1
Virtual memory
Unallocated
Cached
Uncached
Unallocated
Cached
Uncached
PP 0
PP 1
Empty
Cached
0
N-1
M-1
0
Virtual pages (VPs)
“stored on disk”
Physical pages (PPs)
cached in DRAM

## Slide 18: Memory Hierarchy: Core 2 Duo
Disk
Main Memory
L2 unified cache
L1
I-cache
L1
D-cache
CPU
Reg
2 B/cycle
8 B/cycle
16 B/cycle
1 B/30 cycles
Throughput:
Latency:
100 cycles
14 cycles
3 cycles
millions
~4 MB
32 KB
~8 GB
~500 GB
Not drawn to scale
Miss Penalty
(latency)
33x
Miss Penalty
(latency)
10,000x
SRAM
Static Random Access Memory
DRAM
Dynamic Random Access Memory

## Slide 19: Virtual Memory Design Consequences
Large page size: typically 4-8 KiB or 2-4 MiB
  Can be up to 1 GiB (for “Big Data” apps on big computers)
  Compared with 64-byte cache blocks
Fully associative
  Any virtual page can be placed in any physical page
  Requires a “large” mapping function – different from CPU caches
Highly sophisticated, expensive replacement algorithms in OS
  Too complicated and open-ended to be implemented in hardware
Write-back rather than write-through
  Really don’t want to write to disk every time we modify something in memory
  Some things may never end up on disk (e.g. stack for short-lived process)

## Slide 20: Why does VM work on RAM/disk?
Avoids disk accesses because of locality
  Same reason that L1 / L2 / L3 caches work
The set of virtual pages that a program is “actively” accessing at any point in time is called its working set
  If (working set of one process ≤ physical memory):
    Good performance for one process (after compulsory misses)
  If (working sets of all processes > physical memory):
    Thrashing: Performance meltdown where pages are swapped between memory and disk continuously (CPU always waiting or paging)
    This is why your computer can feel faster when you add RAM
Notes:   Improving a program’s temporal locality can lead to a smaller working set (using data in one place in the program rather than many places).
  Full quote: “Every problem in computer science can be solved by adding another level of indirection, but that usually will create another problem.”

## Slide 21: Virtual Memory (VM)
Overview and motivation
VM as a tool for caching
Address translation
VM as a tool for memory management
VM as a tool for memory protection

## Slide 22: Address Translation
0:
1:
M-1:
Main memory
MMU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data (int/float)
8:
...
CPU
Virtual address
(VA)
CPU Chip
0x4
0x4100
Memory Management Unit
How do we perform the virtual physical address translation?

## Slide 23: Address Translation: Page Tables
CPU-generated address can be split into:
  Request is Virtual Address (VA), want Physical Address (PA)
  Note that Physical Offset = Virtual Offset (page-aligned)
Use lookup table that we call the page table (PT)
  Replace Virtual Page Number (VPN) for Physical Page Number (PPN) to generate Physical Address
  Index PT using VPN: page table entry (PTE) stores the PPN plus management bits (e.g. Valid, Dirty, access rights)
  Has an entry for every virtual page – why?
Virtual Page Number
Page Offset
-bit address:

## Slide 24: Page Table Diagram
Page tables stored in physical memory
  Too big to fit elsewhere – managed by MMU & OS
How many page tables in the system?
  One per process
Page Table
(DRAM)
null
null
0
1
0
0
1
1
0
1
Valid
PPN/Disk Addr
PTE 0: 0
PTE 7: 7
PTE 1: 1
PTE 2: 2
PTE 3: 3
PTE 4: 4
PTE 5: 5
PTE 6: 6
...
...
Virtual memory (DRAM/disk)
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual page #
Physical memory
(DRAM)
PP 0
PP 3
PP 2
PP 1
VP 1
VP 2
VP 7
VP 4
Physical page #
Notes: Space allocated for pages in disk called Swap Space

## Slide 25: Page Table Address Translation
CPU
Virtual page number (VPN)
Virtual page offset (VPO)
Physical page number (PPN)
Physical page offset (PPO)
Virtual address (VA)
Physical address (PA)
Valid
PPN
Page table base register
(PTBR)
Page table
Page table address
for process
Valid bit = 0:
page not in memory
(page fault)
In most cases, the MMU can perform this translation without software assistance
Notes: PTBR is another name for control register 3 (CR3) in x86: http://en.wikipedia.org/wiki/Control_register#CR3

## Slide 26: Page Hit
Page hit: VM reference is in physical memory
Page Table (DRAM)
null
null
0
1
0
0
1
1
0
1
Valid
PPN/Disk Addr
PTE 0
PTE 7
...
...
Virtual address
Example: Page size = 4 KiB
0x00740b
Virtual Addr:
VPN:
PPN:
Physical Addr:
Physical memory
(DRAM)
PP 0
PP 3
VP 1
VP 2
VP 7
VP 4
Virtual memory (DRAM/disk)
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Notes: 4kB page = 2^12
  3 hex digits

## Slide 27: Page Fault
Page fault: VM reference is NOT in physical memory
Page Table (DRAM)
null
null
0
1
0
0
1
1
0
1
Valid
PPN/Disk Addr
PTE 0
PTE 7
...
...
Physical memory
(DRAM)
PP 0
PP 3
VP 1
VP 2
VP 7
VP 4
Virtual memory (DRAM/disk)
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address
Example: Page size = 4 KiB
Provide a virtual address request (in hex) that results in this particular page fault:
Virtual Addr:

## Slide 28: Page Fault Exception
User writes to memory location
That portion (page) of user’s memory is currently on disk
Page fault handler must load page into physical memory
Returns to faulting instruction: mov is executed again!
  Successful on second try
int a[1000];
int main ()
{
a[500] = 13;
}
80483b7: c7 05 10 9d 04 08 0d movl $0xd,0x8049d10
User code
OS Kernel code
exception: page fault
Create page and
load into memory
returns
movl
handle_page_fault:

## Slide 29: Handling a Page Fault
Page miss causes page fault (an exception)
Page Table (DRAM)
null
null
0
1
0
0
1
1
0
1
Valid
PPN/Disk Addr
PTE 0
PTE 7
...
...
Physical memory
(DRAM)
PP 0
PP 3
VP 1
VP 2
VP 7
VP 4
Virtual memory (DRAM/disk)
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 30: Handling a Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
Page Table (DRAM)
null
null
0
1
0
0
1
1
0
1
Valid
PPN/Disk Addr
PTE 0
PTE 7
...
...
Physical memory
(DRAM)
PP 0
PP 3
VP 1
VP 2
VP 7
VP 4
Virtual memory (DRAM/disk)
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address
Notes: Check dirty bit on eviction!

## Slide 31: Handling a Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
Page Table (DRAM)
null
null
0
1
0
0
1
1
1
0
Valid
PPN/Disk Addr
PTE 0
PTE 7
...
...
Physical memory
(DRAM)
PP 0
PP 3
VP 1
VP 2
VP 7
VP 3
Virtual memory (DRAM/disk)
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 32: Handling a Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
Offending instruction is restarted: page hit!
Page Table (DRAM)
null
null
0
1
0
0
1
1
1
0
Valid
PPN/Disk Addr
PTE 0
PTE 7
...
...
Physical memory
(DRAM)
PP 0
PP 3
VP 1
VP 2
VP 7
VP 3
Virtual memory (DRAM/disk)
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 33: Peer Instruction Question
How many bits wide are the following fields?
  16 KiB pages
  48-bit virtual addresses
  16 GiB physical memory
34 24
(A)
32 18
(B)
30 20
(C)
34 20
(D)
VPN PPN

## Slide 34: Virtual Memory (VM)
Overview and motivation
VM as a tool for caching
Address translation
VM as a tool for memory management
VM as a tool for memory protection

## Slide 35: VM for Managing Multiple Processes
Key abstraction: each process has its own virtual address space
  It can view memory as a simple linear array
With virtual memory, this simple linear virtual address space need not be contiguous in physical memory
  Process needs to store data in another VP? Just map it to any PP!
Virtual Address Space for Process 1:
Physical
Address
Space (DRAM)
0
N-1
(e.g., read-only
library code)
Virtual Address Space for Process 2:
VP 1
VP 2
...
0
N-1
VP 1
VP 2
...
PP 2
PP 6
PP 8
...
0
M-1
Address
translation

## Slide 36: Simplifying Linking and Loading
Linking
  Each program has similar virtual address space
  Code, Data, and Heap always start at the same addresses
Loading
  execve allocates virtual pages for .text and .data sections & creates PTEs marked as invalid
  The .text and .data sections are copied, page by page, on demand by the virtual memory system
Kernel virtual memory
Memory-mapped region for
shared libraries
Run-time heap
(created by malloc)
User stack
(created at runtime)
Unused
0
%rsp
(stack
pointer)
Memory
invisible to
user code
brk
0x400000
Read/write segment
(.data, .bss)
Read-only segment
(.init, .text, .rodata)
Loaded
from the
executable
file

## Slide 37: VM for Protection and Sharing
The mapping of VPs to PPs provides a simple mechanism to protect memory and to share memory between processes
  Sharing: map virtual pages in separate address spaces to the same physical page (here: PP 6)
  Protection: process can’t access physical pages to which none of its virtual pages are mapped (here: Process 2 can’t access PP 2)
Virtual Address Space for Process 1:
Physical
Address
Space (DRAM)
0
N-1
(e.g., read-only
library code)
Virtual Address Space for Process 2:
VP 1
VP 2
...
0
N-1
VP 1
VP 2
...
PP 2
PP 6
PP 8
...
0
M-1
Address
translation

## Slide 38: Memory Protection Within Process
VM implements read/write/execute permissions
  Extend page table entries with permission bits
  MMU checks these permission bits on every memory access
    If violated, raises exception and OS sends SIGSEGV signal to process (segmentation fault)
•
•
•
Physical
Address Space
PP 2
PP 4
PP 6
PP 8
PP 9
PP 11
Process i:
PPN
WRITE
EXEC
PP 6
No
No
PP 4
No
Yes
PP 2
Yes
No
READ
Yes
Yes
Yes
VP 0:
VP 1:
VP 2:
Yes
Yes
Yes
Valid
Process j:
WRITE
EXEC
PP 9
Yes
No
PP 6
No
No
PP 11
Yes
No
READ
Yes
Yes
Yes
VP 0:
VP 1:
VP 2:
Yes
Yes
Yes
Valid
PPN
Notes: Why no Dirty bit? Typically handled by OS.

## Slide 39: Review Question
What should the permission bits be for pages from the following sections of virtual memory?
Section | Read | Write | Execute
Stack |  |  | 
Heap |  |  | 
Static Data |  |  | 
Literals |  |  | 
Instructions |  |  | 

## Slide 40: Address Translation: Page Hit
1) Processor sends virtual address to MMU (memory management unit)
2-3) MMU fetches PTE from page table in cache/memory (Uses PTBR to find beginning of page table for current process)
4) MMU sends physical address to cache/memory requesting data
5) Cache/memory sends data to processor
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5
VA = Virtual Address PTEA = Page Table Entry Address PTE= Page Table Entry PA = Physical Address Data = Contents of memory stored at VA originally requested by CPU

## Slide 41: Address Translation: Page Fault
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in cache/memory
4) Valid bit is zero, so MMU triggers page fault exception
5) Handler identifies victim (and, if dirty, pages it out to disk)
6) Handler pages in new page and updates PTE in memory
7) Handler returns to original process, restarting faulting instruction
MMU
Cache/
Memory
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5
Disk
Page fault handler
Victim page
New page
Exception
6
7

## Slide 42: Hmm… Translation Sounds Slow
The MMU accesses memory twice: once to get the PTE for translation, and then again for the actual memory request
  The PTEs may be cached in L1 like any other memory word
    But they may be evicted by other data references
    And a hit in the L1 cache still requires 1-3 cycles
What can we do to make this faster?
  Solution: add another cache! 🎉

## Slide 43: Speeding up Translation with a TLB
Translation Lookaside Buffer (TLB):
  Small hardware cache in MMU
  Maps virtual page numbers to physical page numbers
  Contains complete page table entries for small number of pages
    Modern Intel processors have 128 or 256 entries in TLB
  Much faster than a page table lookup in cache/memory
TLB
PTE
VPN
→
PTE
VPN
→
PTE
VPN
→
Notes: “The architecture of the IBM System/370” R.P. Case and A. Padegs Communications of the ACM. 21:1, 73-96, January 1978.
Perhaps the first paper to use the term translation lookaside buffer. The name arises from the historical name for a cache, which was a lookaside buffer as called by those developing the Atlas system at the University of Manchester; a cache of address translations thus became a translation lookaside buffer. Even though the term lookaside buffer fell out of favor, TLB seems to have stuck, for whatever reason.
“x86info -c” on Intel Core2 Duo CPU:
L1 Data TLB: 4KB pages, 4-way set associative, 16 entries
Data TLB: 4K pages, 4-way associative, 256 entries.
L1 Data TLB: 4MB pages, 4-way set associative, 16 entries
Data TLB: 4MB pages, 4-way associative, 32 entries

## Slide 44: TLB Hit
A TLB hit eliminates a memory access!
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
4
5
TLB
VPN
3
TLB
PTE
VPN
→
PTE
VPN
→
PTE
VPN
→

## Slide 45: TLB Miss
A TLB miss incurs an additional memory access (the PTE)
  Fortunately, TLB misses are rare
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
5
6
TLB
VPN
4
PTEA
3
TLB
PTE
VPN
→
PTE
VPN
→
PTE
VPN
→
Notes: Does a TLB miss require disk access?

## Slide 46: Fetching Data on a Memory Read
Check TLB
  Input: VPN, Output: PPN
  TLB Hit: Fetch translation, return PPN
  TLB Miss: Check page table (in memory)
    Page Table Hit: Load page table entry into TLB
    Page Fault: Fetch page from disk to memory, update corresponding page table entry, then load entry into TLB
Check cache
  Input: physical address, Output: data
  Cache Hit: Return data value to processor
  Cache Miss: Fetch data value from memory, store it in cache, return it to processor

## Slide 47: Address Translation
Virtual Address
TLB
Lookup
Check the
Page Table
Update
TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
TLB Miss
TLB Hit
Page not
in Mem
Access
Denied
Access
Permitted
Protection
Fault
SIGSEGV
Page
in Mem
Check cache
Find in Disk
Find in Mem
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 48: Context Switching Revisited
What needs to happen when the CPU switches processes?
  Registers:
    Save state of old process, load state of new process
    Including the Page Table Base Register (PTBR)
  Memory:
    Nothing to do! Pages for processes already exist in memory/disk and protected from each other
  TLB:
    Invalidate all entries in TLB – mapping is for old process’ VAs
  Cache:
    Can leave alone because storing based on PAs – good for shared data

## Slide 49: Summary of Address Translation Symbols
Basic Parameters
  Number of addresses in virtual address space
  Number of addresses in physical address space
  Page size (bytes)
Components of the virtual address (VA)
  VPO Virtual page offset
  VPN Virtual page number
  TLBI TLB index
  TLBT TLB tag
Components of the physical address (PA)
  PPO Physical page offset (same as VPO)
  PPN Physical page number

## Slide 50: Virtual Memory Summary
Programmer’s view of virtual memory
  Each process has its own private linear address space
  Cannot be corrupted by other processes
System view of virtual memory
  Uses memory efficiently by caching virtual memory pages
    Efficient only because of locality
  Simplifies memory management and sharing
  Simplifies protection by providing permissions checking

## Slide 51: Memory System Summary
Memory Caches (L1/L2/L3)
  Purely a speed-up technique
  Behavior invisible to application programmer and (mostly) OS
  Implemented totally in hardware
Virtual Memory
  Supports many OS-related functions
    Process creation, task switching, protection
  Operating System (software)
    Allocates/shares physical memory among processes
    Maintains high-level tables tracking memory type, source, sharing
    Handles exceptions, fills in hardware-defined mapping tables
  Hardware
    Translates virtual addresses via mapping tables, enforcing permissions
    Accelerates mapping via translation cache (TLB)