## Slide 1: Virtual Memory III CSE 351 Winter 2019
https://xkcd.com/648/
Instructors:
Max Willsey
Luis Ceze
Teaching Assistants:
Britt Henderson
Lukas Joswiak
Josie Lee
Wei Lin
Daniel Snitkovsky
Luis Vega
Kory Watson
Ivy Yu

## Slide 2: Administrivia
Lab 4 due today (March 4)
Lab 5, HW 5 coming soon
Collaboration means the discussion of the problem
  not the specifics of your solution

## Slide 3: Quick Review
What is VM useful for?
What do Page Tables map?
Where are Page Tables located?
How many Page Tables are there?
Can your process tell if a page fault has occurred?
True / False: Virtual Addresses that are contiguous will always be contiguous in physical memory
TLB stands for _______________________ and stores _______________
Notes: Protection, sharing, virtualization (pretending you own it all), caching
VPN -> PPN (or disk address)
Phyiscal memory
One per process
No, except for timing
No!!! That’s the whole point
Translation lookaside buffer stores PTEs

## Slide 4: Address Translation: Page Hit
1) Processor sends virtual address to MMU (memory management unit)
2-3) MMU fetches PTE from page table in cache/memory (Uses PTBR to find beginning of page table for current process)
4) MMU sends physical address to cache/memory requesting data
5) Cache/memory sends data to processor
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5
VA = Virtual Address PTEA = Page Table Entry Address PTE= Page Table Entry PA = Physical Address Data = Contents of memory stored at VA originally requested by CPU
Notes: VA = VPN + PO
PTEA = PTBR + VPN
PTE = PPN + management
PA = PPN + PO

## Slide 5: Address Translation: Page Fault
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in cache/memory
4) Valid bit is zero, so MMU triggers page fault exception
5) Handler identifies victim (and, if dirty, pages it out to disk)
6) Handler pages in new page and updates PTE in memory
7) Handler returns to original process, restarting faulting instruction
MMU
Cache/
Memory
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5
Disk
Page fault handler
Victim page
New page
Exception
6
7
Notes: Same thing but valid bit zero,
Evict, retry

## Slide 6: Hmm… Translation Sounds Slow
The MMU accesses memory twice for a page hit
  1. get the PTE for translation
  2. again for the actual memory request
  The PTEs may be cached in L1 like any other memory word
    But they may be evicted by other data references
    And a hit in the L1 cache still requires 1-3 cycles
What can we do to make this faster?
  Solution: add another cache! 💰💸

## Slide 7: Speeding up Translation with a TLB
Translation Lookaside Buffer (TLB):
  Small hardware cache in MMU
  Maps virtual page numbers to physical page numbers
  Contains complete page table entries for small number of pages
    Modern Intel processors have 128 or 256 entries in TLB
  Much faster than a page table lookup in cache/memory
TLB
PTE
VPN
→
PTE
VPN
→
PTE
VPN
→
Notes: “The architecture of the IBM System/370” R.P. Case and A. Padegs Communications of the ACM. 21:1, 73-96, January 1978.
Perhaps the first paper to use the term translation lookaside buffer. The name arises from the historical name for a cache, which was a lookaside buffer as called by those developing the Atlas system at the University of Manchester; a cache of address translations thus became a translation lookaside buffer. Even though the term lookaside buffer fell out of favor, TLB seems to have stuck, for whatever reason.
“x86info -c” on Intel Core2 Duo CPU:
L1 Data TLB: 4KB pages, 4-way set associative, 16 entries
Data TLB: 4K pages, 4-way associative, 256 entries.
L1 Data TLB: 4MB pages, 4-way set associative, 16 entries
Data TLB: 4MB pages, 4-way associative, 32 entries

## Slide 8: TLB Hit
A TLB hit eliminates a memory access!
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
4
5
TLB
VPN
3
TLB
PTE
VPN
→
PTE
VPN
→
PTE
VPN
→
Notes: Instead of going to memory for PTE, we go to TLB

## Slide 9: TLB Miss
A TLB miss incurs an additional memory access (the PTE)
  Fortunately, TLB misses are rare
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
5
6
TLB
VPN
4
PTEA
3
TLB
PTE
VPN
→
PTE
VPN
→
PTE
VPN
→
Notes: Does a TLB miss require disk access? Not necessarily

## Slide 10: Fetching Data on a Memory Read
Check TLB
  Input: VPN, Output: PPN
  TLB Hit: Fetch translation, return PPN
  TLB Miss: Check page table (in memory)
    Page Table Hit: Load page table entry into TLB
    Page Fault: Fetch page from disk to memory, update corresponding page table entry, then load entry into TLB
Check cache
  Input: physical address, Output: data
  Cache Hit: Return data value to processor
  Cache Miss: Fetch data value from memory, store it in cache, return it to processor

## Slide 11: Address Translation
Virtual Address
TLB
Lookup
Check the
Page Table
Update
TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
TLB Miss
TLB Hit
Page not
in Mem
Access
Denied
Access
Permitted
Protection
Fault
SIGSEGV
Page
in Mem
Check cache
Find in Disk
Find in Mem
Notes: Need to restart instruction.
Soft and hard page faults.
Protection check takes a PTE

## Slide 12: Context Switching Revisited
What needs to happen when the CPU switches processes?
  Registers:
    Save state of old process, load state of new process
    Including the Page Table Base Register (PTBR)
  Memory:
    Nothing to do! Pages for processes already exist in memory/disk and protected from each other
  TLB:
    Invalidate all entries in TLB – mapping is for old process’ VAs
  Cache:
    Can leave alone because storing based on PAs – good for shared data

## Slide 13: Simple Memory System Example (small)
Addressing
  14-bit virtual addresses
  12-bit physical address
  Page size = 64 bytes
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
Virtual Page Number
Virtual Page Offset
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
Physical Page Number
Physical Page Offset
Notes: 14-bit va = 16kb va space
12-bit va = 4kb va space
64 B page = 6 bit PO

## Slide 14: Simple Memory System: Page Table
Only showing first 16 entries (out of _____)
  Note: showing 2 hex digits for PPN even though only 6 bits
  Note: other management bits not shown, but part of PTE
VPN | PPN | Valid
0 | 28 | 1
1 | – | 0
2 | 33 | 1
3 | 02 | 1
4 | – | 0
5 | 16 | 1
6 | – | 0
7 | – | 0
VPN | PPN | Valid
8 | 13 | 1
9 | 17 | 1
A | 09 | 1
B | – | 0
C | – | 0
D | 2D | 1
E | – | 0
F | 0D | 1
Notes: Size of page table = 2^(n-p) entries
14 bit VA, 6 bit PO, so 2^8 = 256 entries

## Slide 15: Simple Memory System: TLB
16 entries total
4-way set associative
13
12
11
10
9
8
7
6
5
4
3
2
1
0
virtual page offset
virtual page number
TLB index
TLB tag
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set
Why does the TLB ignore the page offset?
Notes: Calculate VPN for valid TLB entry using Tag & Set
16 / 4 = 4 sets, so two index bits
No offset bits, TLB doesn’t do offsets

## Slide 16: Simple Memory System: Cache
Direct-mapped with = 4 B, = 16
Physically addressed
11
10
9
8
7
6
5
4
3
2
1
0
physical page offset
physical page number
cache offset
cache index
cache tag
Note: It is just coincidence that the PPN is the same width as the cache Tag
Index | Tag | Valid | B0 | B1 | B2 | B3
0 | 19 | 1 | 99 | 11 | 23 | 11
1 | 15 | 0 | – | – | – | –
2 | 1B | 1 | 00 | 02 | 04 | 08
3 | 36 | 0 | – | – | – | –
4 | 32 | 1 | 43 | 6D | 8F | 09
5 | 0D | 1 | 36 | 72 | F0 | 1D
6 | 31 | 0 | – | – | – | –
7 | 16 | 1 | 11 | C2 | DF | 03
Index | Tag | Valid | B0 | B1 | B2 | B3
8 | 24 | 1 | 3A | 00 | 51 | 89
9 | 2D | 0 | – | – | – | –
A | 2D | 1 | 93 | 15 | DA | 3B
B | 0B | 0 | – | – | – | –
C | 12 | 0 | – | – | – | –
D | 16 | 1 | 04 | 96 | 34 | 15
E | 13 | 1 | 83 | 77 | 1B | D3
F | 14 | 0 | – | – | – | –
Notes: 4 B block, 16 sets

## Slide 17: Current State of Memory System
Cache:
TLB:
Page table (partial):
Index | Tag | V | B0 | B1 | B2 | B3
0 | 19 | 1 | 99 | 11 | 23 | 11
1 | 15 | 0 | – | – | – | –
2 | 1B | 1 | 00 | 02 | 04 | 08
3 | 36 | 0 | – | – | – | –
4 | 32 | 1 | 43 | 6D | 8F | 09
5 | 0D | 1 | 36 | 72 | F0 | 1D
6 | 31 | 0 | – | – | – | –
7 | 16 | 1 | 11 | C2 | DF | 03
Index | Tag | V | B0 | B1 | B2 | B3
8 | 24 | 1 | 3A | 00 | 51 | 89
9 | 2D | 0 | – | – | – | –
A | 2D | 1 | 93 | 15 | DA | 3B
B | 0B | 0 | – | – | – | –
C | 12 | 0 | – | – | – | –
D | 16 | 1 | 04 | 96 | 34 | 15
E | 13 | 1 | 83 | 77 | 1B | D3
F | 14 | 0 | – | – | – | –
Set | Tag | PPN | V | Tag | PPN | V | Tag | PPN | V | Tag | PPN | V
0 | 03 | – | 0 | 09 | 0D | 1 | 00 | – | 0 | 07 | 02 | 1
1 | 03 | 2D | 1 | 02 | – | 0 | 04 | – | 0 | 0A | – | 0
2 | 02 | – | 0 | 08 | – | 0 | 06 | – | 0 | 03 | – | 0
3 | 07 | – | 0 | 03 | 0D | 1 | 0A | 34 | 1 | 02 | – | 0
VPN | PPN | V
0 | 28 | 1
1 | – | 0
2 | 33 | 1
3 | 02 | 1
4 | – | 0
5 | 16 | 1
6 | – | 0
7 | – | 0
VPN | PPN | V
8 | 13 | 1
9 | 17 | 1
A | 09 | 1
B | – | 0
C | – | 0
D | 2D | 1
E | – | 0
F | 0D | 1
Notes: TLB and Cache are separate pieces of hardware; page table stored in memory
Show correlation between TLB & page table (VPN 0x0D and 0x0F in particular)

## Slide 18: Memory Request Example #1
Virtual Address: 0x03D4
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
1
9
1
8
1
7
1
6
0
5
1
4
0
3
1
2
0
1
0
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: VPN: 0xF
TLBT: 0x03
TLBI: 3
TLB Hit: Yes
Page Fault: No
PPN: 0x0D
PA = 001101 0101 00
CT = 0x0D
CI = 5
CO = 0
Hit: yes
Data = 0x36

## Slide 19: Memory Request Example #2
Virtual Address: 0x038F
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
1
9
1
8
1
7
0
6
0
5
0
4
1
3
1
2
1
1
1
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: VPN: 0x0E
TLBT: 0x03
TLBI: 2
TLB Hit: N
Page Fault: Y
PPN: n/a

## Slide 20: Memory Request Example #3
Virtual Address: 0x0020
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
0
9
0
8
0
7
0
6
1
5
0
4
0
3
0
2
0
1
0
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: VPN: 0x00
TLBT: 0x00
TLBI: 0
TLB Hit: No
Page Fault: No
PPN: 0x28
PA = 101000 1000 00
CT: 0x28
CI: 8
CO: 0
Hit: No
Data: n/a

## Slide 21: Memory Request Example #4
Virtual Address: 0x036B
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
1
9
1
8
0
7
1
6
1
5
0
4
1
3
0
2
1
1
1
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: VPN: 0x0D
TLBT: 0x3
TLBI: 1
TLB Hit: Y
Page Fault: N
PPN: 0x2D
PA = 101101 1010 11
CT: 0x2D
CI: A
CO: 3
Hit: Yes
Data: 0x3B

## Slide 22: Memory Overview
Disk
Main memory
(DRAM)
Cache
CPU
Page
Page
Line
Block
requested 32-bits
movl 0x8043ab, %rdi
TLB
MMU
Notes: A lot happens
Cache – mem
Block replacement
Mem – disk
Page in/out

## Slide 23: Practice VM Question
Our system has the following properties
  1 MiB of physical address space
  4 GiB of virtual address space
  32 KiB page size
  4-entry fully associative TLB with LRU replacement
Fill in the following blanks:
________ | Entries in a page table | ________ | Minimum bit-width of PTBR
________ | TLBT bits | ________ | Max # of valid entries in a page table
Notes: Back to testable
1 MiB PA space = 20 bits
4 GiB PA space = 32 bits
32 KiB Page size = 15 offset bits
2^(32 - 15) = 2^17 PTEs
PTBR is a physical address, must be 20 bits
First we need VPN bits, 32 -15 = 17. only one TLB set, so all 17 are tag bits
2^20 physical bytes, a page is 2^15, so 2^5

## Slide 24: Practice VM Question
One process uses a page-aligned square matrix mat[] of 32-bit integers in the code shown below:
#define MAT_SIZE = 2048
for(int i = 0; i < MAT_SIZE; i++)
mat[i*(MAT_SIZE+1)] = i;
What is the largest stride (in bytes) between successive memory accesses (in the VA space)?
Notes: Diagonal entries
2049 ints, so 2049 * 4 bytes
Part 2

## Slide 25: Practice VM Question
One process uses a page-aligned square matrix mat[] of 32-bit integers in the code shown below:
#define MAT_SIZE = 2048
for(int i = 0; i < MAT_SIZE; i++)
mat[i*(MAT_SIZE+1)] = i;
Assuming all of mat[] starts on disk, what are the following hit rates for the execution of the for-loop?
________ | TLB Hit Rate | ________ | Page Table Hit Rate
Notes: Page size 32 KiB = 2^15 B
Mat is 2048 ints = 2^11 ints = 2^13 B
We touch each row once,
A pages holds 2^(13 – 11) = 4 rows
Each page: M HHH = 75%
0 percent. If the TLB misses, we ‘ve never seen that before. Must page fault

## Slide 26: Page Table Reality
Just one issue… the numbers don’t work out for the story so far!
The problem is the page table for each process:
  Suppose 64-bit VAs, 8 KiB pages, 8 GiB physical memory
  How many page table entries is that?
  Moral: Cannot use this naïve implementation of the virtual→physical page mapping – it’s way too big
This is extra (non-testable) material
Notes: 8 kb pages = 13 offset bits
8 GB = 33 total bits
1 PTE for every page -> 2^64/2^13 = 2^51 PTEs
1 PT is (way, 100,000x) bigger than all of physical memory

## Slide 27: A Solution: Multi-level Page Tables
Page table base register
(PTBR)
VPN 1
0
p-1
n-1
VPO
VPN 2
...
VPN k
PPN
0
p-1
m-1
PPO
PPN
Virtual Address
Physical Address
...
...
Level 1
page table
Level 2
page table
Level k
page table
TLB
PTE
VPN
→
PTE
VPN
→
PTE
VPN
→
This is called a page walk
This is extra (non-testable) material

## Slide 28: Multi-level Page Tables
A tree of depth where each node at depth has up to children if part of the VPN has bits
Hardware for multi-level page tables inherently more complicated
  But it’s a necessary complexity – 1-level does not fit
Why it works: Most subtrees are not used at all, so they are never created and definitely aren’t in physical memory
  Parts created can be evicted from cache/memory when not being used
  Each node can have a size of ~1-100KB
But now for a -level page table, a TLB miss requires cache/memory accesses
  Fine so long as TLB misses are rare – motivates larger TLBs
This is extra (non-testable) material
Notes: Some math about how it works out.
Again, memory is super sparse, use trees

## Slide 29
For Fun: DRAMMER Security Attack
Why are we talking about this?
  Recent: Announced in October 2016; Google released Android patch on November 8, 2016
  Relevant: Uses your system’s memory setup to gain elevated privileges
    Ties together some of what we’ve learned about virtual memory and processes
  Interesting: It’s a software attack that uses only hardware vulnerabilities and requires no user permissions
BONUS SLIDES

## Slide 30: Underlying Vulnerability: Row Hammer
Dynamic RAM (DRAM) has gotten denser over time
  DRAM cells physically closer and use smaller charges
  More susceptible to “disturbance errors” (interference)
DRAM capacitors need to be “refreshed” periodically (~64 ms)
  Lose data when loss of power
  Capacitors accessed in rows
Rapid accesses to one row can flip bits in an adjacent row!
  ~ 100K to 1M times
By Dsimic (modified), CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=38868341

## Slide 31: Row Hammer Exploit
Force constant memory access
  Read then flush the cache
  clflush – flush cache line
    Invalidates cache line containing the specified address
    Not available in all machines or environments
  Want addresses X and Y to fall in activation target row(s)
    Good to understand how banks of DRAM cells are laid out
The row hammer effect was discovered in 2014
  Only works on certain types of DRAM (2010 onwards)
  These techniques target x86 machines
hammertime:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
jmp hammertime

## Slide 32: Consequences of Row Hammer
Row hammering process can affect another process via memory
  Circumvents virtual memory protection scheme
  Memory needs to be in an adjacent row of DRAM
Worse: privilege escalation
  Page tables live in memory!
  Hope to change PPN to access other parts of memory, or change permission bits
  Goal: gain read/write access to a page containing a page table, hence granting process read/write access to all of physical memory

## Slide 33: Effectiveness?
Doesn’t seem so bad – random bit flip in a row of physical memory
  Vulnerability affected by system setup and physical condition of memory cells
Improvements:
  Double-sided row hammering increases speed & chance
  Do system identification first (e.g. Lab 4)
    Use timing to infer memory row layout & find “bad” rows
    Allocate a huge chunk of memory and try many addresses, looking for a reliable/repeatable bit flip
  Fill up memory with page tables first
    fork extra processes; hope to elevate privileges in any page table

## Slide 34: What’s DRAMMER?
No one previously made a huge fuss
  Prevention: error-correcting codes, target row refresh, higher DRAM refresh rates
  Often relied on special memory management features
  Often crashed system instead of gaining control
Research group found a deterministic way to induce row hammer exploit in a non-x86 system (ARM)
  Relies on predictable reuse patterns of standard physical memory allocators
  Universiteit Amsterdam, Graz University of Technology, and University of California, Santa Barbara

## Slide 35: DRAMMER Demo Video
It’s a shell, so not that sexy-looking, but still interesting
  Apologies that the text is so small on the video
Notes: https://youtu.be/x6hL-obNhAw

## Slide 36: How did we get here?
Computing industry demands more and faster storage with lower power consumption
Ability of user to circumvent the caching system
  clflush is an unprivileged instruction in x86
  Other commands exist that skip the cache
Availability of virtual to physical address mapping
  Example: /proc/self/pagemap on Linux (not human-readable)
Google patch for Android (Nov. 8, 2016)
  Patched the ION memory allocator

## Slide 37: More reading for those interested
DRAMMER paper: https://vvdveen.com/publications/drammer.pdf
Google Project Zero: https://googleprojectzero.blogspot.com/2015/03/exploiting-dram-rowhammer-bug-to-gain.html
First row hammer paper: https://users.ece.cmu.edu/~yoonguk/papers/kim-isca14.pdf
Wikipedia: https://en.wikipedia.org/wiki/Row_hammer

## Slide 38: Quick Review Answers
What do Page Tables map?
  VPN PPN or disk address
Where are Page Tables located?
  In physical memory
How many Page Tables are there?
  One per process
Can your program tell if a page fault has occurred?
  Nope, but it has to wait a long time
What is thrashing?
  Constantly paging out and paging in
True / False: Virtual Addresses that are contiguous will always be contiguous in physical memory
  Could fall across a page boundary
TLB stands for Translation Lookaside Buffer and stores page table entries