## Slide 1: Floating Point I CSE 351 Winter 2020
Instructor: Teaching Assistants:
Ruth Anderson Jonathan Chen Justin Johnson Porter Jones
Josie Lee Jeffery Tian Callum Walker
Eddy (Tianyi) Zhou
http://xkcd.com/571/

## Slide 2: Administrivia
Lab 1a due tonight Tues 1/21 at 11:59 pm
  Submit pointer.c and lab1Areflect.txt
  Make sure you submit something before the deadline and that the file names are correct
hw5 due Wednesday, hw6 due Friday
Lab 1b due next Monday (1/27)
  Submit bits.c and lab1Breflect.txt

## Slide 3: Unsigned Multiplication in C
Standard Multiplication Function
  Ignores high order bits
Implements Modular Arithmetic
  UMultw(u , v) = u · v mod 2w
• • •
• • •
u
v
*
• • •
u · v
• • •
True Product: bits
Operands: bits
Discard bits: bits
UMultw(u , v)
• • •

## Slide 4: Multiplication with shift and add
Operation u<<k gives u*2k
  Both signed and unsigned
Examples:
  u<<3 == u * 8
  u<<5 - u<<3 == u * 24
  Most machines shift and add faster than multiply
    Compiler generates this code automatically
• • •
u
2k
*
u · 2k
True Product: bits
Operands: bits
Discard bits: bits
UMultw(u , 2k)
0
0
1
0
0
0
•••
•••
k
• • •
0
0
0
•••
TMultw(u , 2k)
0
0
0
•••
•••

## Slide 5: Number Representation Revisited
What can we represent in one word?
  Signed and Unsigned Integers
  Characters (ASCII)
  Addresses
How do we encode the following:
  Real numbers (e.g. 3.14159)
  Very large numbers (e.g. 6.02×1023)
  Very small numbers (e.g. 6.626×10-34)
  Special numbers (e.g. ∞, NaN)
Floating
Point

## Slide 6: Floating Point Topics
Fractional binary numbers
IEEE floating-point standard
Floating-point operations and rounding
Floating-point in C
There are many more details that we won’t cover
  It’s a 58-page standard…
Notes: Start by talking about representing fractional numbers in binary in general
Then about the IEEE Standard for floating point representation, operations,
Will not cover:
  All the details of the 58-page spec
  Or expect you to perform operations
Want to show you how floating point values are represented
  To give you a sense of the kinds of things that can go wrong with them

## Slide 7: Floating Point Summary
Floats also suffer from the fixed number of bits available to represent them
  Can get overflow/underflow, just like ints
  “Gaps” produced in representable numbers means we can lose precision, unlike ints
    Some “simple fractions” have no exact representation (e.g. 0.2)
    “Every operation gets a slightly wrong result”
Floating point arithmetic not associative or distributive
  Mathematically equivalent ways of writing an expression may compute different results
Never test floating point values for equality!
Careful when converting between ints and floats!

## Slide 8: Representation of Fractions
“Binary Point,” like decimal point, signifies boundary between integer and fractional parts:
Example 6-bit representation:
Example: 10.10102 = 1×21 + 1×2-1 + 1×2-3 = 2.62510
xx.yyyy
21
20
2-1
2-2
2-3
2-4

## Slide 9: Representation of Fractions
“Binary Point,” like decimal point, signifies boundary between integer and fractional parts:
Example 6-bit representation:
In this 6-bit representation:
  What is the encoding and value of the smallest (most negative) number?
  What is the encoding and value of the largest (most positive) number?
  What is the smallest number greater than 2 that we can represent?
xx.yyyy
21
20
2-1
2-2
2-3
2-4

## Slide 10: Fractional Binary Numbers
• • •
b–1
.
Representation
  Bits to right of “binary point” represent fractional powers of 2
  Represents rational number:
bi
bi–1
b2
b1
b0
b–2
b–3
b–j
• • •
• • •
1
2
4
2i–1
2i
• • •
1/2
1/4
1/8
2–j

## Slide 11: Fractional Binary Numbers
Value Representation
  5 and 3/4
  2 and 7/8
  47/64
Observations
  Shift left = multiply by power of 2
  Shift right = divide by power of 2
  Numbers of the form 0.111111…2 are just below 1.0
    1/2 + 1/4 + 1/8 + … + 1/2i + … ➙ 1.0
    Use notation 1.0 – ε
101.112
10.1112
0.1011112
Notes:  = lowercase epsilon

## Slide 12: Limits of Representation
Limitations:
  Even given an arbitrary number of bits, can only exactly represent numbers of the form x * 2y (y can be negative)
  Other rational numbers have repeating bit representations
  Value: Binary Representation:
    1/3 = 0.333333…10 = 0.01010101[01]…2
    1/5 = 0.001100110011[0011 ]…2
    1/10 = 0.0001100110011[0011 ]…2

## Slide 13: Fixed Point Representation
Implied binary point. Two example schemes:
  #1: the binary point is between bits 2 and 3 b7 b6 b5 b4 b3 [.] b2 b1 b0
  #2: the binary point is between bits 4 and 5 b7 b6 b5 [.] b4 b3 b2 b1 b0
Wherever we put the binary point, with fixed point representations there is a trade off between the amount of range and precision we have
Fixed point = fixed range and fixed precision
  range: difference between largest and smallest numbers possible
  precision: smallest possible difference between any two numbers
Hard to pick how much you need of each!

## Slide 14: Floating Point Representation
Analogous to scientific notation
  In Decimal:
    Not 12000000, but 1.2 x 107 In C: 1.2e7
    Not 0.0000012, but 1.2 x 10-6 In C: 1.2e-6
  In Binary:
    Not 11000.000, but 1.1 x 24
    Not 0.000101, but 1.01 x 2-4
We have to divvy up the bits we have (e.g., 32) among:
  the sign (1 bit)
  the mantissa (significand)
  the exponent

## Slide 15: Scientific Notation (Decimal)
Normalized form: exactly one digit (non-zero) to left of decimal point
Alternatives to representing 1/1,000,000,000
  Normalized: 1.0×10-9
  Not normalized: 0.1×10-8,10.0×10-10
6.0210 × 1023
radix (base)
decimal point
exponent
mantissa

## Slide 16: Scientific Notation (Binary)
Computer arithmetic that supports this called floating point due to the “floating” of the binary point
  Declare such variable in C as float (or double)
1.012 × 2-1
radix (base)
binary point
exponent
mantissa

## Slide 17: Scientific Notation Translation
Convert from scientific notation to binary point
  Perform the multiplication by shifting the decimal until the exponent disappears
    Example: 1.011224 = 101102 = 2210
    Example: 1.01122-2 = 0.010112 = 0.3437510
Convert from binary point to normalized scientific notation
  Distribute out exponents until binary point is to the right of a single digit
    Example: 1101.0012 = 1.1010012×23
Practice: Convert 11.37510 to normalized binary scientific notation
Notes: Fraction like 1/3 needs an infinite number of digits to be represented, even in base 10!

## Slide 18: Floating Point Topics
Fractional binary numbers
IEEE floating-point standard
Floating-point operations and rounding
Floating-point in C
There are many more details that we won’t cover
  It’s a 58-page standard…
Notes: Start by talking about representing fractional numbers in binary in general
Then about the IEEE Standard for floating point representation, operations,
Will not cover:
  All the details of the 58-page spec
  Or expect you to perform operations
Want to show you how floating point values are represented
  To give you a sense of the kinds of things that can go wrong with them

## Slide 19: IEEE Floating Point
IEEE 754
  Established in 1985 as uniform standard for floating point arithmetic
  Main idea: make numerically sensitive programs portable
  Specifies two things: representation and result of floating operations
  Now supported by all major CPUs
Driven by numerical concerns
  Scientists/numerical analysts want them to be as real as possible
  Engineers want them to be easy to implement and fast
  In the end:
    Scientists mostly won out
    Nice standards for rounding, overflow, underflow, but...
    Hard to make fast in hardware
    Float operations can be an order of magnitude slower than integer ops
Notes: Back in the 80s, it was like the wild west out there
Institute of Electrical and Electronics Engineers
Committee had to balance concerns
  Scientists wanted them to be as real as possible
  Engineers wanted it to be as easy to implement in HW as possible
Floating point can be order of magnitude slower than integer
  When we get super desperate, turn to fixed point
  But computers are pretty fast, right?

## Slide 20: Floating Point Encoding
Use normalized, base 2 scientific notation:
  Value: ±1 × Mantissa × 2Exponent
  Bit Fields: (-1)S × 1.M × 2(E–bias)
Representation Scheme:
  Sign bit (0 is positive, 1 is negative)
  Mantissa (a.k.a. significand) is the fractional part of the number in normalized form and encoded in bit vector M
  Exponent weights the value by a (possibly negative) power of 2 and encoded in the bit vector E
S
E
M
31 30
23 22
0
1 bit
8 bits
23 bits

## Slide 21: The Exponent Field
Use biased notation
  Read exponent as unsigned, but with bias of 2w-1-1 = 127
  Representable exponents roughly ½ positive and ½ negative
  Exponent 0 (Exp = 0) is represented as E = 0b 0111 1111
Why biased?
  Makes floating point arithmetic easier
  Makes somewhat compatible with two’s complement
Practice: To encode in biased notation, add the bias then encode in unsigned:
  Exp = 1 E = 0b
  Exp = 127 E = 0b
  Exp = -63 E = 0b
Notes: E = 1 128 0b 1000 0000
E = 127 254 0b 1111 1110
E = -63 64 0b 0100 0000
E = 1 → 128 → 0b 1000 0000
E = 127 → 254 → 0b 1111 1110
E = -63 → 64 → 0b 0100 0000

## Slide 22: The Mantissa (Fraction) Field
Note the implicit 1 in front of the M bit vector
  Example: 0b 0011 1111 1100 0000 0000 0000 0000 0000 is read as 1.12 = 1.510, not 0.12 = 0.510
  Gives us an extra bit of precision
Mantissa “limits”
  Low values near M = 0b0…0 are close to 2Exp
  High values near M = 0b1…1 are close to 2Exp+1
(-1)S x (1 . M) x 2(E–bias)
S
E
M
31 30
23 22
0
1 bit
8 bits
23 bits

## Slide 23: Polling Question
What is the correct value encoded by the following floating point number?
  0b 0 10000000 11000000000000000000000
  Vote at http://pollev.com/rea
+ 0.75
+ 1.5
+ 2.75
+ 3.5
We’re lost…

## Slide 24: Normalized Floating Point Conversions
FP → Decimal
  Append the bits of M to implicit leading 1 to form the mantissa.
  Multiply the mantissa by 2E – bias.
  Multiply the sign (-1)S.
  Multiply out the exponent by shifting the binary point.
  Convert from binary to decimal.
Decimal → FP
  Convert decimal to binary.
  Convert binary to normalized scientific notation.
  Encode sign as S (0/1).
  Add the bias to exponent and encode E as unsigned.
  The first bits after the leading 1 that fit are encoded into M.

## Slide 25: Precision and Accuracy
Precision is a count of the number of bits in a computer word used to represent a value
  Capacity for accuracy
Accuracy is a measure of the difference between the actual value of a number and its computer representation
  High precision permits high accuracy but doesn’t guarantee it. It is possible to have high precision but low accuracy.
  Example: float pi = 3.14;
    pi will be represented using all 24 bits of the mantissa (highly precise), but is only an approximation (not accurate)

## Slide 26: Need Greater Precision?
Double Precision (vs. Single Precision) in 64 bits
  C variable declared as double
  Exponent bias is now 210–1 = 1023
  Advantages: greater precision (larger mantissa), greater range (larger exponent)
  Disadvantages: more bits used, slower to manipulate
S
E (11)
M (20 of 52)
63 62
52 51
32
M (32 of 52)
31
0

## Slide 27: Representing Very Small Numbers
But wait… what happened to zero?
  Using standard encoding 0x00000000 =
  Special case: E and M all zeros = 0
    Two zeros! But at least 0x00000000 = 0 like integers
New numbers closest to 0:
  a = 1.0…02×2-126 = 2-126
  b = 1.0…012×2-126 = 2-126 + 2-149
  Normalization and implicit 1 are to blame
  Special case: E = 0, M ≠ 0 are denormalized numbers
0
+∞
-∞
Gaps!
a
b

## Slide 28: Denorm Numbers
Denormalized numbers
  No leading 1
  Uses implicit exponent of –126 even though E = 0x00
Denormalized numbers close the gap between zero and the smallest normalized number
  Smallest norm: ± 1.0…0two×2-126 = ± 2-126
  Smallest denorm: ± 0.0…01two×2-126 = ± 2-149
    There is still a gap between zero and the smallest denormalized number
So much closer to 0
This is extra (non-testable) material

## Slide 29: Summary
Floating point approximates real numbers:
  Handles large numbers, small numbers, special numbers
  Exponent in biased notation (bias = 2w-1–1)
    Size of exponent field determines our representable range
    Outside of representable exponents is overflow and underflow
  Mantissa approximates fractional portion of binary point
    Size of mantissa field determines our representable precision
    Implicit leading 1 (normalized) except in special cases
    Exceeding length causes rounding
S
E (8)
M (23)
31 30
23 22
0

## Slide 30
An example that applies the IEEE Floating Point concepts to a smaller (8-bit) representation scheme. These slides expand on material covered today, so while you don’t need to read these, the information is “fair game.”
BONUS SLIDES

## Slide 31: Tiny Floating Point Example
8-bit Floating Point Representation
  The sign bit is in the most significant bit (MSB)
  The next four bits are the exponent, with a bias of 24-1–1 = 7
  The last three bits are the mantissa
Same general form as IEEE Format
  Normalized binary scientific point notation
  Similar special cases for 0, denormalized numbers, NaN, ∞
S
E
M
1
4
3

## Slide 32: Dynamic Range (Positive Only)
S E M Exp Value
0 0000 000 -6 0
0 0000 001 -6 1/8*1/64 = 1/512
0 0000 010 -6 2/8*1/64 = 2/512
…
0 0000 110 -6 6/8*1/64 = 6/512
0 0000 111 -6 7/8*1/64 = 7/512
0 0001 000 -6 8/8*1/64 = 8/512
0 0001 001 -6 9/8*1/64 = 9/512
…
0 0110 110 -1 14/8*1/2 = 14/16
0 0110 111 -1 15/8*1/2 = 15/16
0 0111 000 0 8/8*1 = 1
0 0111 001 0 9/8*1 = 9/8
0 0111 010 0 10/8*1 = 10/8
…
0 1110 110 7 14/8*128 = 224
0 1110 111 7 15/8*128 = 240
0 1111 000 n/a inf
closest to zero
largest denorm
smallest norm
closest to 1 below
closest to 1 above
largest norm
Denormalized
numbers
Normalized
numbers

## Slide 33: Special Properties of Encoding
Floating point zero (0+) exactly the same bits as integer zero
  All bits = 0
Can (Almost) Use Unsigned Integer Comparison
  Must first compare sign bits
  Must consider 0- = 0+ = 0
  NaNs problematic
    Will be greater than any other values
    What should comparison yield?
  Otherwise OK
    Denorm vs. normalized
    Normalized vs. infinity