## Slide 1: x86-64 Programming I CSE 351 Winter 2020
Instructor:
Ruth Anderson
Teaching Assistants:
Jonathan Chen
Justin Johnson
Porter Jones
Josie Lee
Jeffery Tian
Callum Walker
Eddy (Tianyi) Zhou
http://www.smbc-comics.com/?id=2999

## Slide 2: Administrivia
hw7 due Monday, hw8 due Wednesday
Lab 1b due Monday (1/27) at 11:59 pm
  You have lab late days available

## Slide 3: Roadmap
car *c = malloc(sizeof(car));
c->miles = 100;
c->gals = 17;
float mpg = get_mpg(c);
free(c);
Car c = new Car();
c.setMiles(100);
c.setGals(17);
float mpg = c.getMPG();
get_mpg:
pushq %rbp
movq %rsp, %rbp
...
popq %rbp
ret
Java:
C:
Assembly language:
Machine code:
0111010000011000
100011010000010000000010
1000100111000010
110000011111101000011111
Computer system:
OS:
Memory & data
Integers & floats
x86 assembly
Procedures & stacks
Executables
Arrays & structs
Memory & caches
Processes
Virtual memory
Memory allocation
Java vs. C

## Slide 4: Architecture Sits at the Hardware Interface
C Language
x86-64
Intel Pentium 4
Intel Core 2
Intel Core i7
AMD Opteron
AMD Athlon
GCC
ARMv8 (AArch64/A64)
ARM Cortex-A53
Apple A7
Clang
Your program
Program B
Program A
Compiler
Source code
Architecture
Different applications
or algorithms
Perform optimizations,
generate instructions
Different implementations
Hardware
Instruction set
Notes: Different programs written in C, have different algorithms
Compilers figure out what instructions to generate
  do different optimizations
Different architectures expose different interfaces
Hardware implementations have different performance

## Slide 5: Definitions
Architecture (ISA): The parts of a processor design that one needs to understand to write assembly code
  “What is directly visible to software”
Microarchitecture: Implementation of the architecture
  CSE/EE 469

## Slide 6: Instruction Set Architectures
The ISA defines:
  The system’s state (e.g. registers, memory, program counter)
  The instructions the CPU can execute
  The effect that each of these instructions will have on the system state
CPU
Memory
PC
Registers
Notes: Textbook: “the format and behavior of a machine-level program is defined by the ISA, defining the processor state, the format of the instructions, and the effect each of these instructions will have on the state.”

## Slide 7: Instruction Set Philosophies
Complex Instruction Set Computing (CISC): Add more and more elaborate and specialized instructions as needed
  Lots of tools for programmers to use, but hardware must be able to handle all instructions
  x86-64 is CISC, but only a small subset of instructions encountered with Linux programs
Reduced Instruction Set Computing (RISC): Keep instruction set small and regular
  Easier to build fast hardware
  Let software do the complicated operations by composing simpler ones

## Slide 8: General ISA Design Decisions
Instructions
  What instructions are available? What do they do?
  How are they encoded?
Registers
  How many registers are there?
  How wide are they?
Memory
  How do you specify a memory location?
Notes: Registers: word size

## Slide 9: Mainstream ISAs
Macbooks & PCs
(Core i3, i5, i7, M)
x86-64 Instruction Set
Smartphone-like devices
(iPhone, iPad, Raspberry Pi)
ARM Instruction Set
Digital home & networking equipment
(Blu-ray, PlayStation 2)
MIPS Instruction Set
Notes: x86 backwards-compatible all the way to 8086 architecture (introduced in 1978!), has had many, many new features added since.
x86 dominates the server, desktop, and laptop markets.
ARM stands for Advanced RISC Machine.
MIPS was originally an acronym for Microprocessor without Interlocked Pipeline Stages. Developed by MIPS Technologies (formerly MIPS Computer Systems, Inc).

## Slide 10: Writing Assembly Code? In 2019???
Chances are, you’ll never write a program in assembly, but understanding assembly is the key to the machine-level execution model:
  Behavior of programs in the presence of bugs
    When high-level language model breaks down
  Tuning program performance
    Understand optimizations done/not done by the compiler
    Understanding sources of program inefficiency
  Implementing systems software
    What are the “states” of processes that the OS must manage
    Using special units (timers, I/O co-processors, etc.) inside processor!
  Fighting malicious software
    Distributed software is in binary form
Notes: Compilers are much better and more patient than you are
I hope that you are never writing a program in assembly
  Not even to eke the very last bit of performance out
  Because compilers are much better at it
Understanding assembly will help you
  Like how C will help you better appreciate the magic that Java does for you
  Similarly, understanding assembly will help you understand what the machine is doing for you
  Sometimes you actually do have to poke around with GDB in the assembly (this is what gets shipped to you!)

## Slide 11: Assembly Programmer’s View
CPU
Programmer-visible state
  PC: the Program Counter (%rip in x86-64)
    Address of next instruction
  Named registers
    Together in “register file”
    Heavily used program data
  Condition codes
    Store status information about most recent arithmetic operation
    Used for conditional branching
PC
Registers
Memory
Code
Data
Stack
Addresses
Data
Instructions
Condition
Codes
Memory
  Byte-addressable array
  Code and user data
  Includes the Stack (for supporting procedures)
Notes: Preview for the coming lectures

## Slide 12: x86-64 Assembly “Data Types”
Integral data of 1, 2, 4, or 8 bytes
  Data values
  Addresses
Floating point data of 4, 8, 10 or 2x8 or 4x4 or 8x2
  Different registers for those (e.g. %xmm1, %ymm2)
  Come from extensions to x86 (SSE, AVX, …)
No aggregate types such as arrays or structures
  Just contiguously allocated bytes in memory
Two common syntaxes
  “AT&T”: used by our course, slides, textbook, gnu tools, …
  “Intel”: used by Intel documentation, Intel tools, …
  Must know which you’re reading
Not covered
In 351
Notes: Assembly program doesn’t actually have notion of “data types,” but since encoding is so different between integral and floating point data, there are actually different instructions built into assembly because the hardware needs to deal with these numbers differently when performing arithmetic.

## Slide 13: What is a Register?
A location in the CPU that stores a small amount of data, which can be accessed very quickly (once every clock cycle)
Registers have names, not addresses
  In assembly, they start with % (e.g. %rsi)
Registers are at the heart of assembly programming
  They are a precious commodity in all architectures, but especially x86

## Slide 14: x86-64 Integer Registers – 64 bits wide
  Can reference low-order 4 bytes (also low-order 2 & 1 bytes)
%r8d
%r8
%r9d
%r9
%r10d
%r10
%r11d
%r11
%r12d
%r12
%r13d
%r13
%r14d
%r14
%r15d
%r15
%rsp
%esp
%eax
%rax
%ebx
%rbx
%ecx
%rcx
%edx
%rdx
%esi
%rsi
%edi
%rdi
%ebp
%rbp
Notes: Names are largely arbitrary, reasons behind them are not super relevant to us
But there are conventions about how they are used
One is particularly important to not misuse: %rsp
  Stack pointer; we’ll get to this when we talk about procedures
Why is %rbp now general-purpose in x86-64? http://www.codemachine.com/article_x64deepdive.html
r8-r15: still names not indexes
Each is 8-bytes wide
What if we only want 4 bytes?
  We can use these alternate names to use just half of the bytes

## Slide 15: Some History: IA32 Registers – 32 bits wide
%esi
%si
%edi
%di
%esp
%sp
%ebp
%bp
%eax
%ax
%ah
%al
%ecx
%cx
%ch
%cl
%edx
%dx
%dh
%dl
%ebx
%bx
%bh
%bl
16-bit virtual registers
(backwards compatibility)
general purpose
accumulate
counter
data
base
source index
destination index
stack pointer
base pointer
Name Origin
(mostly obsolete)
Notes: Only 6 registers that we can do whatever we want with
Remember how I said we’ve been upgrading x86 since 1978, when it was 16-bit?
Originally just %ax, …
  Could even reference single bytes (high, low)
There used to be more conventions about how they were used
  Just to make it easier when people were writing assembly by hand
  Now irrelevant

## Slide 16: Memory vs. Registers
Addresses vs. Names
  0x7FFFD024C3DC %rdi
Big vs. Small
  ~ 8 GiB (16 x 8 B) = 128 B
Slow vs. Fast
  ~50-100 ns sub-nanosecond timescale
Dynamic vs. Static
  Can “grow” as needed fixed number in hardware while program runs

## Slide 17: Three Basic Kinds of Instructions
Transfer data between memory and register
  Load data from memory into register
    %reg = Mem[address]
  Store register data into memory
    Mem[address] = %reg
Perform arithmetic operation on register or memory data
  c = a + b; z = x << y; i = h & g;
Control flow: what instruction to execute next
  Unconditional jumps to/from procedures
  Conditional branches
    Remember: Memory is indexed just like an array of bytes!

## Slide 18: Operand types
Immediate: Constant integer data
  Examples: $0x400, $-533
  Like C literal, but prefixed with ‘$’
  Encoded with 1, 2, 4, or 8 bytes depending on the instruction
Register: 1 of 16 integer registers
  Examples: %rax, %r13
  But %rsp reserved for special use
  Others have special uses for particular instructions
Memory: Consecutive bytes of memory at a computed address
  Simplest example: (%rax)
  Various other “address modes”
%rax
%rcx
%rdx
%rbx
%rsi
%rdi
%rsp
%rbp
%rN

## Slide 19: x86-64 Introduction
Data transfer instruction (mov)
Arithmetic operations
Memory addressing modes
  swap example
Address computation instruction (lea)

## Slide 20: Moving Data
General form: mov_ source, destination
  Missing letter (_) specifies size of operands
  Note that due to backwards-compatible support for 8086 programs (16-bit machines!), “word” means 16 bits = 2 bytes in x86 instruction names
  Lots of these in typical code
movb src, dst
  Move 1-byte “byte”
movw src, dst
  Move 2-byte “word”
movl src, dst
  Move 4-byte “long word”
movq src, dst
  Move 8-byte “quad word”

## Slide 21: Operand Combinations
 | Source | Dest | Src, Dest | C Analog
movq | Imm | Reg | movq $0x4, %rax | 
 |  | Mem | movq $-147, (%rax) | 
 | Reg | Reg | movq %rax, %rdx | 
 |  | Mem | movq %rax, (%rdx) | 
 | Mem | Reg | movq (%rax), %rdx | 
Cannot do memory-memory transfer with a single instruction
  How would you do it?
var_a = 0x4;
*p_a = -147;
var_d = var_a;
*p_d = var_a;
var_d = *p_a;

## Slide 22: Some Arithmetic Operations
Binary (two-operand) Instructions:
  Beware argument order!
  No distinction between signed and unsigned
    Only arithmetic vs. logical shifts
  How do you implement “r3 = r1 + r2”?
Format | Computation | 
addq src, dst | dst = dst + src | (dst += src)
subq src, dst | dst = dst – src | 
imulq src, dst | dst = dst * src | signed mult
sarq src, dst | dst = dst >> src | Arithmetic
shrq src, dst | dst = dst >> src | Logical
shlq src, dst | dst = dst << src | (same as salq)
xorq src, dst | dst = dst ^ src | 
andq src, dst | dst = dst & src | 
orq src, dst | dst = dst ¦ src | 
Maximum of one memory operand
operand size specifier
Notes: r3 = r1 + r2
  mov r1, r3
  add r2, r3

## Slide 23: Some Arithmetic Operations
Unary (one-operand) Instructions:
See CSPP Section 3.5.5 for more instructions: mulq, cqto, idivq, divq
Format | Computation | 
incq dst | dst = dst + 1 | increment
decq dst | dst = dst – 1 | decrement
negq dst | dst = –dst | negate
notq dst | dst = ~dst | bitwise complement
Notes: Why have a different inc operator?
  Smaller bit representation!
  Maybe faster implementation

## Slide 24: Arithmetic Example
long simple_arith(long x, long y)
{
long t1 = x + y;
long t2 = t1 * 3;
return t2;
}
Register | Use(s)
%rdi | 1st argument (x)
%rsi | 2nd argument (y)
%rax | return value
y += x;
y *= 3;
long r = y;
return r;
simple_arith:
addq %rdi, %rsi
imulq $3, %rsi
movq %rsi, %rax
ret
Notes: Function calling convention (get to it later) says which registers to use for arguments and return value
Compiler knows
  Arithmetic ops are like “+=“
  And it doesn’t need intermediate values anyway
  So it transforms it to...

## Slide 25: Example of Basic Addressing Modes
void swap(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret

## Slide 26: Understanding swap()
%rdi
%rsi
%rax
%rdx
Registers
Memory
Register Variable
%rdi ⇔ xp
%rsi ⇔ yp
%rax ⇔ t0
%rdx ⇔ t1
void swap(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret

## Slide 27: Understanding swap()
0x120
0x118
0x110
0x108
0x100
Word
Address
%rdi
%rsi
%rax
%rdx
0x120
0x100
Registers
Memory
123
456
123
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
Notes: But actually, pointers are just addresses!
Showing here 8-byte words of memory, addresses jump by 8

## Slide 28: Understanding swap()
0x120
0x118
0x110
0x108
0x100
Word
Address
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
Registers
Memory
123
456
123
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret

## Slide 29: Understanding swap()
0x120
0x118
0x110
0x108
0x100
Word
Address
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
123
456
123
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret

## Slide 30: Understanding swap()
0x120
0x118
0x110
0x108
0x100
Word
Address
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
123
456
456
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret

## Slide 31: Understanding swap()
0x120
0x118
0x110
0x108
0x100
Word
Address
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
123
123
456
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret

## Slide 32: Memory Addressing Modes: Basic
Indirect: (R) Mem[Reg[R]]
  Data in register R specifies the memory address
  Like pointer dereference in C
  Example: movq (%rcx), %rax
Displacement: D(R) Mem[Reg[R]+D]
  Data in register R specifies the start of some memory region
  Constant displacement D specifies the offset from that address
  Example: movq 8(%rbp), %rdx

## Slide 33: Complete Memory Addressing Modes
General:
  D(Rb,Ri,S) Mem[Reg[Rb]+Reg[Ri]*S+D]
    Rb: Base register (any register)
    Ri: Index register (any register except %rsp)
    S: Scale factor (1, 2, 4, 8) – why these numbers?
    D: Constant displacement value (a.k.a. immediate)
Special cases (see CSPP Figure 3.3 on p.181)
  D(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]+D] (S=1)
  (Rb,Ri,S) Mem[Reg[Rb]+Reg[Ri]*S] (D=0)
  (Rb,Ri) Mem[Reg[Rb]+Reg[Ri]] (S=1,D=0)
  (,Ri,S) Mem[Reg[Ri]*S] (Rb=0,D=0)
Notes: Syntax for memory operands can be more complex
Designed to do things that are common with pointers
D: displacement, add a constant
Rb: base pointer
Ri: index into array
S: scale the index (pointer arithmetic needs to scale by the size of the pointer target)
  compiler keeps track of what the pointer points to and scales accordingly
  int x[] x[i]
  ith element of an array of ints: Ri=i, S=4 (bytes)
See figure 3.3 in 3e textbook

## Slide 34: Address Computation Examples
%rdx
%rcx
0xf000
0x0100
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
D(Rb,Ri,S)
Mem[Reg[Rb]+Reg[Ri]*S+D]

## Slide 35: Summary
x86-64 is a complex instruction set computing (CISC) architecture
  There are 3 types of operands in x86-64
    Immediate, Register, Memory
  There are 3 types of instructions in x86-64
    Data transfer, Arithmetic, Control Flow
Memory Addressing Modes: The addresses used for accessing memory in mov (and other) instructions can be computed in several different ways
  Base register, index register, scale factor, and displacement map well to pointer arithmetic operations