## Slide 1: x86-64 Programming I
CSE 351 Summer 2024
Instructor:
Ellis Haker
Teaching Assistants:
Naama Amiel
Micah Chang
Shananda Dokka
Nikolas McNamee
Jiawei Huang

## Slide 2: Administrivia
Due today
  HW5 (11:59pm)
  Lab 1a (11:59pm)
Due Friday, 7/5
  RD8 (1pm)
  HW6 (11:59pm)
Quiz 1 released Friday at 11:59pm
Optional reading posted on Ed
  Recent article about designing assembly language design
  Beyond the scope of this course, but very cool!

## Slide 3: Review Questions
Assume that the register %rdx holds the value 0x 01 02 03 04 05 06 07 08
Answer the following questions about the instruction subq $1, %rdx
Operation type:
Operand types:
Operating width:
(extra) Result stored in %rdx:
Notes: 1. Subq is subtraction, so arithmetic
2. 1st type is an immediate bc of dollar sign, 2nd is a register bc of %
3. 8 bytes bc of q
Result = %rdx – 1 = 0x0102030405060707

## Slide 4: Layers of Computing Revisited
So far, we’ve focused on hardware
  How does the CPU store and read data from memory?
Shifting focus to languages & libraries
  How are programs created and executed on the CPU?
  Take CSE 401 to learn more
Still needs hardware support!
  Take CSE 469 to learn more

## Slide 5: Programming Languages & Libraries: 351 View
Topics:
  x86-64 assembly
  Procedures
  Stacks
  Executables
How does your source code become something that your computer understands?
How does the CPU organize and manipulate local data?
Notes: We’ll focus on the first question for the next 3 lectures

## Slide 6: Lecture Topics
Assembly intro
  Instruction set philosophies
X86-64 programming
  Data types
  Instructions
  Registers
  Memory addressing

## Slide 7: Definitions
Instruction Set Architecture (ISA): the parts of a processor design that one needs to understand to write assembly code
  What is directly visible to software
  The “contract” between hardware and software
  351 focus
Microarchitecture: hardware implementation of the ISA
  CSE/EE 469

## Slide 8: Instruction Set Architectures (Review)
ISA defines:
  The system’s state (e.g., registers, memory, program counter)
  The instructions the CPU can execute
  The effect that each of these instructions will have on the system state
Notes: PC stands for program counter

## Slide 9: What is a Register? (Review)
Special locations on the CPU that store a small amount of data
  Accessed very quickly (once per clock cycle)
Have names, not addresses
  In x86, start with % (e.g., %rsi)
Registers are at the heart of assembly programming
  Very useful, but scarce, especially in x86

## Slide 10: Memory vs. Registers (Review)
Memory
Addresses
  Ex: 0x7FFFD024C3DC
Big
  ~16GB
Slow
  ~50-100ns
Dynamic
  Can expand as needed
Registers
Names
  Ex: %rdi
Small
  16 8-byte registers = 128B
Fast
  <1ns
Static
  Fixed number in hardware

## Slide 11: General ISA Design Decisions
Instructions
  What instructions are available? What do they do?
  How are they encoded?
Registers
  How many are there?
  How wide are they?
Memory
  How do you specify a memory location?

## Slide 12: Instruction Set Philosophies (Review)
Complex Instruction Set Computing (CISC): lots of elaborate instructions
  Lots of tools for programmers to use, but hardware must be able to handle all instructions
  x86-64 is CISC, but only a small subset of instructions encountered with Linux programs
Reduced Instruction Set Computing (RISC): keep instruction set small and regular
  Easier to build fast, less power-hungry hardware
  Let software do the complicated operations by composing simpler ones
  ARM, RISC-V

## Slide 13: Instruction Set Philosophies (Review) (pt 2)
Complex Instruction Set Computing (CISC): lots of elaborate instructions
  Lots of tools for programmers to use, but hardware must be able to handle all instructions
  x86-64 is CISC, but only a small subset of instructions encountered with Linux programs
Example: ADDSUBPS
“Adds odd-numbered single-precision floating-point values of the first source operand (second operand) with the corresponding single-precision floating-point values from the second source operand (third operand); stores the result in the odd-numbered values of the destination operand (first operand). Subtracts the even-numbered single-precision floating-point values from the second source operand from the corresponding single-precision floating values in the first source operand; stores the result into the even-numbered values of the destination operand.”

## Slide 14: Mainstream ISAs
PCs, older Macs
x86-64 instruction set
Mobile devices, M1/M2 Macs
ARM instruction set
Mostly research
RISC-V instruction set

## Slide 15: Current Industry Trends - A RISC-y Shift
Historically, there was a lot of debate about RISC vs CISC
  Intel went the CISC route in the 1980s
    Would make programming in assembly easier
    Implementing more things in hardware
Traditional wisdom says the RISC is better for simple systems, not PCs
But things are shifting!
  Apple switched to ARM in 2020
Why?
  Efficiency: RISC uses less power
  Performance: each instruction is faster, easier to parallelize
  Scalability: suitable for devices of all sizes (desktops, laptops, and phones)

## Slide 16: Architecture Sits at the Hardware Interface
Notes: There’s an extra step between architecture and hardware: converting assembly to binary

## Slide 17: Writing Assembly Code? In $CURRENT_YEAR???
Chances are, you’ll never write a program in assembly, but understanding it is the key to the machine-level execution model
  Behavior of programs in the presence of bugs
    When high-level language model breaks down
  Tuning program performance
    Understand optimizations done/not done by the compiler
  Implementing systems software
    What are the “states” of processes that the OS must manage
    Using special units (timers, I/O co-processors, etc.) inside processor!
  Fighting malicious software
    Distributed software is in binary form
Notes: In some industries, it’s relevant (architecture, compilers, systems, security)
Developing an accurate mental model of computation is important! Especially for debugging and improving performance
  VERY rare for compilers to have bugs (modern compilers are really good), but *occasionally* it happens
  Maybe you’re building a new programming language, and you’re the one making the compiler for it!
Detecting hacking attempts - you can read an executable and see if it’s dangerous
  Can “reverse-engineer” a program back into assembly
  NOTE: when you check off the “terms and conditions” that nobody reads, you agree not to do this
    ALSO: doing this in this class (when we don’t tell you to) is academic misconduct

## Slide 18: Lecture Topics
Assembly intro
  Instruction set philosophies
X86-64 programming
  Data types
  Instructions
  Registers
  Memory addressing

## Slide 19: x86-64 Integer Registers – 64 bits wide
Notes: 64 bits = 8 bytes
The big registers shown here (ex: %rax) are 8B, the smaller ones within them (ex: %eax) are 4B
%rsp is a special register. We’ll talk about it later!

## Slide 20: Some History: IA32 Registers – 32 bits wide
Notes: We still have access to these old register names! Now refer to the lower bytes of the 8B register
All of these are on the midterm reference sheet

## Slide 21: x86-64 Assembly “Data Types”
Integral data of 1, 2, 4, or 8 bytes (b, w, l, q)
Floating point data, not covered in 351
  Different registers for those (e.g., %xmm1, %ymm2)
  Come from extensions to x86 (SSE, AVX, …)
No aggregate types such as arrays or structs
  Just contiguously allocate bytes in memory
Two common syntaxes—Must know which you’re reading!
  AT&T: used in our course, gnu tools (including gcc), …
  Intel: used in Intel documentation, Intel tools, …
Notes: Signed and unsigned integers are treated the same. HW doesn’t distinguish!
For arrays and structs, only get single elements at a time.
Why AT&T? It used to be Bell Labs!

## Slide 22: Instruction Sizes and Operands (Review)
Size specifiers
  b = 1-byte (“byte”)
  w = 2-byte (“word”)
  l = 4-byte (“long word”)
  q = 8-byte (“quad word”)
  If using registers, much match width
Operand types
  Immediate: constant value ($)
  Register: 1 of 16 general-purpose registers (%)
  Memory: consecutive bytes of memory at a computed address ( () )
Why is “word” 2 bytes? Because that was the word size when x86 was new, and it has to be maintained for backwards compatibility.
Notes: Register size must match instruction. Ex: if using q, use 8B register. If using l, use 4B. Etc..
See memory addressing slides for more info on memory operands

## Slide 23: Instruction Types (Review)
Transfer data between memory and a register
  Load from memory -> register
    %reg = Memory[address]
  Store from register -> memory
    Memory[address] = %reg
  Note: cannot transfer between two memory locations in one instruction!
Perform arithmetic operation on register or memory data
  Ex: c = a + b; z = x << y; i = h & g;
Control flow: what instruction to execute next
  Unconditional jumps to/from procedures
  Conditional branches
Remember: Memory
is indexed just like an
array of bytes!
Notes: Control flow is the subject of a future lecture

## Slide 24: Moving Data
General form: mov_ <source>, <destination>
  More of a “copy” than a “move”
  Missing letter (_) is for the width specifier
Ex: movq %rax, %rbx
  Copies the 8-byte value from register %rax into register %rbx
Operand Combinations:
  Immediate -> Register or Memory (copies Immediate value to location)
  Register -> Register or Memory (copies data in register to location)
  Memory -> Register (copies data in memory to register)
    Can’t go from memory -> memory in a single instruction!
Notes: _ can be replaced with either b, w, l, or q.
Source can be imm, reg, or mem. Destination can be reg or mem. Can’t have an immediate as the destination.
To move data from mem->mem requires 2 instructions: mem->reg + reg->mem

## Slide 25: Some Arithmetic Operations
Binary (two-argument) operations
  Beware argument order!
    src can be immediate, register, or memory
    dst only register or memory
    Results always stored in dst
  Maximum of one memory operand!
  No distinction between signed and unsigned
    Only arithmetic vs logical shifts
Format | Computation | Notes
addq src, dst | dst = dst + src | 
subq src, dst | dst = dst - src | 
imulq src, dst | dst = dst * src | 
sarq src, dst | dst = dst >> src | Arithmetic
shrq src, dst | dst = dst >> src | Logical
shlq src, dst | dst = dst << src | Same as shlq
xorq src, dst | dst = dst ^ src | 
andq src, dst | dst = dst & src | 
orq src, dst | dst = dst ¦ src | 
Notes: Max of one memory operand, same as mov

## Slide 26: Practice Question
Which of the following are valid implementations of rcx = rax + rbx?
addq %rax, %rcx
addq %rbx, %rcx
movq $0, %rcx
addq %rbx, %rcx
addq %rax, %rcx
movq %rax, %rcx
addq %rbx, %rcx
xorq %rax, %rax
addq %rax, %rcx
addq %rbx, %rcx
Notes: 1. No: addq %rax, %rcx (rcx = rcx + rax)
addq %rbx, %rcx (rcx = rcx + rax + rbx)
2. Yes: movq $0, %rcx (rcx = 0)
addq %rbx, %rcx (rcx = 0 + rbx = rbx)
addq %rax, %rcx (rcx = rax + rbx)
3. Yes: movq %rax, %rcx (rcx = rax)
addq %rbx, %rcx (rcx = rax + rbx)
4. No: xorq %rax, %rax (rax = 0, remember anything xor itself = 0!)
addq %rax, %rcx (rcx = rcx + 0 = rcx)
addq %rbx, %rcx (rcx = rbx + rcx)

## Slide 27: Arithmetic Example
long simple_arith(long x, long y)
{
long t1 = x + y;
long t2 = t1 * 3;
return t2;
}
y += x;
y *= 3;
long r = y;
return r;
Register | Uses
%rdi | 1st arg (x)
%rsi | 2nd arg (y)
%rax | return value
simple_arith:
addq %rdi, %rsi
imulq $3, %rsi
movq %rsi, %rax
ret

## Slide 28: Example of Basic Addressing Modes
Parentheses = memory addressing
  Treat the value in the register as an address
long add_ptr(long* xp, long* yp)
{
long t0 = *xp;
long t1 = *yp;
return t0 + t1;
}
add_ptr:
movq (%rdi), %rdx
movq (%rsi), %rax
addq %rdx, %rax
ret
Compiler Explorer:
https://godbolt.org/z/zc4Pcq

## Slide 29: Understanding add_ptr()
long add_ptr(long* xp, long* yp)
{
long t0 = *xp;
long t1 = *yp;
return t0 + t1;
}
add_ptr:
movq (%rdi), %rdx
movq (%rsi), %rax
addq %rdx, %rax
ret
Register | Variable
%rdi | xp
%rsi | yp
%rdx | t0
%rax | return
Notes: %rdi = xp, so the data location %rdi points to is *xp
%rsi = yp, so the data location %rsi points to is *yp
%rdx gets the value *xp
%rax gets the value *yp + *xp

## Slide 30: Memory Addressing Modes
General format: D(Rb,Ri,S) = Mem[Reg(Rb) + Reg(Ri)*S + D]
  Rb = base register (any register)
  Ri = index register (any register except %rsp)
  S = scale factor (1, 2, 4, 8) - Why these numbers?
  D = displacement value (immediate)
Can leave any of these out:
  D(Rb,Ri) - S=1
  (Rb,Ri,S) - D=0
  (Rb,Ri) - D=0, S=1
  (,Ri,S) - D=0, Rb=0
  etc…
Notes: Why these numbers? Same as data widths. Used for pointer arithmetic / array indexing!
If leaving any out, S defaults to 1, all others default to 0
D(Rb, Ri) = Rb + Ri + D
(Rb, Ri, S) = Rb + Ri*S
(Rb, Ri) = Rb + Ri
(, Ri, S) = Ri*s (note the comma)
In the example (%rdi) on previous slide, %rdi was Rb

## Slide 31: Address Computation Examples
8-bit addresses
Reminder: D(Rb,Ri,S) →Mem[Reg[Rb]+Reg[Ri]*S+D]
  (ignoring memory addressing portion for this exercise)
%rdx | 0xF000
%rcx | 0x0100
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx, %rcx) |  | 
(%rdx, %rcx, 4) |  | 
0x80(, %rcx, 2) |  | 
Notes: Stopped here, we’ll continue on Friday 

## Slide 32: Summary
x86-64 is a complex (CISC) architecture
  There are 3 types instructions
    Data transfer
    Arithmetic
    Control flow
  There are 3 types of operands
    Registers (%)
    Immediates ($)
    Memory ( () )
Registers are small, fast places to store memory
  Limited number, each with their own name