## Slide 1: Caches I
CSE 351 Summer 2024
Instructor:
Ellis Haker
Teaching Assistants:
Naama Amiel
Micah Chang
Shananda Dokka
Nikolas McNamee
Jiawei Huang
Notes: Image not really related to class content, but to recent tech news
Crowdstrike is a major cybersecurity company used by a lot of other businesses
Recent patch for Crowdstrike on windows introduced a bug
Windows servers had an outage, causing bug to occur during reboot
HUGE amounts of stuff shut down - including air traffic control towers, hospitals, etc.

## Slide 2: Administrivia
Today
  HW12 due (11:59pm)
  Lab2 due (11:59pm)
Monday, 7/22
  RD15 due (1pm)
  HW13 due (11:59pm)
  Quiz 2 released (11:59pm)
    Same rules apply as Quiz 1
Wednesday, 7/24
  RD16 due (1pm)
  HW14 due (11:59pm)

## Slide 3: Quiz 1 Grades Released!
Regrade requests will open tonight at 11:59pm
If you received a message about possible academic misconduct, please email me
And even though it’s cheesy…
  Your success in life is not defined by grades
  You are not defined by grades
  We know it seems critically important right now, but we promise, the numbers on a transcript will fade with time.

## Slide 4: Topic Group 3: Scale & Coherence
How do we make memory accesses faster?
How do programs manage large amounts of memory?
How does your computer run multiple programs at once?
Starting with caches, which are implemented in hardware.

## Slide 5: Aside: Units and Prefixes
Traditional prefixes represent powers of 10, we define new ones for base 2
  Ex: 1 Kibibyte = 210 bytes ≈ 103 bytes = 1 Kilobyte
SI prefixes are ambiguous if base 10 or base 2 (does ‘k’ stand for kilo or kibi?)
IEC prefixes are unambiguously base 2
SI Symbol | SI Prefix | SI size | IEC symbol | IEC Prefix | IEC Size
K | Kilo- | 103 | Ki | Kibi- | 210
M | Mega- | 106 | Mi | Mebi- | 220
G | Giga- | 109 | Gi | Gibi- | 230
T | Tera- | 1012 | Ti | Tebi- | 240
P | Peta- | 1015 | Pi | Pebi- | 250
E | Exa- | 1018 | Ei | Exbi- | 260
Z | Zetta- | 1021 | Zi | Zebi- | 270
Y | Yotta- | 1024 | Yi | Yobi- | 280
Notes: Example: kilo = 10^3 = 1000, kibi = 2^10 = 1024
People often say “kilo” when they mean”kibi”!

## Slide 6: How to Remember?
You can always look it up :)
  It’s on the midterm reference sheet
Mnemonics
  Killer Mechanical Giraffe Teaches Pet Extinct Zebra to Yodel
  Kirby Missed Ganondorf Terribly, Potentially Exterminating Zelda and Yoshi
  From xkcd: Karl Marx Gave The Proletariat Eleven Zeppelins, Yo
    https://xkcd.com/992/

## Slide 7: Review Questions
Convert the following to or from IEC:
  512 Mi-students
  233 cats
Compute the average memory access time (AMAT) for a system with the following properties:
  Hit time of 2 ns
  Miss rate of 1%
  Miss penalty of 300 ns
Notes: a. Mi = 2^10, 512 = 2^9, so total is 2^9*2^20 = 2^29 students. B. 2^33 = 2^3 * 2^30 = 2^3 Gi-students = 8 Gi-students
AMAT = HT + MR*MP = 2ns + 0.01*300ns = 2ns + 3ns = 5ns

## Slide 8: How does execution time grow with SIZE?
int array[SIZE];
int sum = 0;
for (int i = 0; i < 200000; i++) {
for (int j = 0; j < SIZE; j++) {
sum += array[j];
}
}
Notes: Expected is a straight line, but actual data is not!

## Slide 9: Actual Data
Notes: Inflection point of the graph si where we exceed cache size

## Slide 10: An Analogy

## Slide 11: Caches
Cache basics
Principle of locality
Memory hierarchies
Cache organization
Program optimizations that consider caches

## Slide 12: Problem: Processor-Memory Bottleneck
“Moore’s Law”
CPU Performance
55%/year
(2X/1.5yr)
DRAM
7%/year
(2X/10yr)
Processor-Memory
Performance Gap (grows 50%/year)
Notes: Moore’s law died around 2002-2005, which is why we started doing multicore

## Slide 13: A Very Silly Analogy
Problem: memory is slow

## Slide 14: A Very Silly Analogy (pt 2)
Solution: caches!

## Slide 15: Cache 💰
Pronounced “cash”
  Often abbreviated to ‘$”
English: hidden storage space for provisions, weapons, or treasures
Computer: Memory with short access time used for the storage of frequently or recently used instructions or data
  I-cache for instructions
  d-cache for data
  More generally: Used to optimize data transfers between any system elements with different characteristics (network interface cache, I/O cache, etc.)

## Slide 16: If caches are so much faster, why do we need memory?
Two common memory technologies
  DRAM: high-capacity, cheap, energy efficient, but slow
  SRAM: much faster, but less energy efficient and expensive
We can’t afford to have all our computer’s memory be SRAM
  Use DRAM to provide large amounts of memory for cheap
  Have a small SRAM cache for speed
SRAM
DRAM
Notes: Other technologies exist too, but these are the most common right now

## Slide 17: General Cache Mechanics
Memory
  Slower, larger, cheaper
  Partition into “blocks”
Cache
  Smaller, faster, more expensive
  Stores a subset of blocks from memory
  Data is copied in block-sized chunks
Notes: A box in this diagram represents a block, not a single byte

## Slide 18: Cache Mechanics: Hit
Data we need is in block b
Block b is in the cache
  Hit!
Data is returned to the CPU

## Slide 19: Cache Mechanics: Miss
Data we need is in block b
Block b is not in the cache already
  Miss!
Block b is fetched from memory
Block b is written into the cache
Notes: Rather than just reading from memory, we want to put it in the cache
Again, don’t just buy the one avocado, buy a bunch and store them

## Slide 20: Cache Mechanics: Miss (pt 2)
Data we need is in block b
Block b is not in the cache already
  Miss!
Block b is fetched from memory
Block b is written into the cache
  Placement policy decides where it goes
  Replacement policy decides what we kick out
Data is returned to the CPU
Notes: Kicked out block 9

## Slide 21: Why Caches Work
Takes advantage of locality
  Common patterns in how programs access data
Temporal locality
  If a program accesses data once, it’s likely to access it again
Spatial locality
  If a program accesses some data, it’s likely to access other data that’s nearby in memory
How do caches take advantage of this?

## Slide 22: Locality Example
sum = 0;
for (i = 0; i < n; i++) {
sum += a[i];
}
return sum;
Data
Temporal: sum, i, and n are accessed every loop iteration
Spacial: consecutive elements of a
Instructions
Temporal: loop body code
Instructions: instructions executed in sequence

## Slide 23: Locality Example 1
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}
Access pattern:
Stride?
Notes: Accesses adjacent elements in memory. Stride = 1
Good cache performance, Use entire block before moving on to the next

## Slide 24: Locality Example 2
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}
Access pattern:
Stride?
Notes: Access the beginning of each row, then the next block of each row, etc. Stride = 4. Bad cache performance 

## Slide 25: Locality Example 3
int sum_array_3D(int a[X][Y][Z])
{
int i, j, k, sum = 0;
for (i = 0; i < Y; i++)
for (j = 0; j < Z; j++)
for (k = 0; k < X; k++)
sum += a[k][i][j];
return sum;
}
Access pattern:
Notes: Access a[0][0][0], a[1][0][0], etc. Really bad cache performance!

## Slide 26: Cache Performance Metrics
Miss Rate (MR)
  Fraction of memory references not found in cache
  (misses / accesses) = 1 - Hit Rate
Hit Time (HT)
  Time to deliver a block in the cache to the processor
  Includes time to determine whether the block is in the cache
Miss Penalty (MP)
  Additional time required because of a miss
  Total miss time = Hit Time + Miss Penalty

## Slide 27: Cache Performance
Average Memory Access Time (AMAT): average time to access data, considering both cache hits and misses
  AMAT = Hit time + Miss Rate × Miss Penalty
(abbreviated AMAT = HT + MR×MP)
Notes: Each access has 100% chance of incurring HT and MR chance of incurring MP

## Slide 28: Practice Questions
Processor specs: 200 ps clock, MP of 50 clock cycles, MR of 0.02 misses/instruction, and HT of 1 clock cycle
  What is the AMAT (in clock cycles)?
Which of these improvements would result in the lowest AMAT?
  190 ps clock
  Miss penalty of 40 clock cycles
  Miss rate of 0.015 misses/instruction
Notes: Clock cycle = amount of time for CPU to do 1 task
HT + MR*MP = 1 + 0.02*50 = 1+1 = 2 cycles. 2 cycles * 200 ps/cycle = 400 ps
A) same number of cycles -> 2 cycles * 190 ps/cycle = 380 ps
B) 1 + 0.02*40 = 1.8 cycles * 200 ps/cycle = 360 ps
C) 1 + 0.015*50 = 1.75 cycles * 200 ps/cycle = 350 ps

## Slide 29: Cache Performance (pt 2)
Misses have a much larger effect on AMAT than hits!
  Going to memory could be 100x slower than accessing the cache (measured in clock cycles)
High miss rate or miss penalty hurt AMAT the most
Ex: Assume HT of 1 clock cycle and MP of 100 clock cycles
If HR = 99%, AMAT = _____
If HR = 97%, AMAT = _____
Increasing hit rate by only 2% cut acces time in half!
Notes: MR = 1-HR
If HR=99%, MR=1%=0.01, 1 + 0.01*100 = 2 cycles
If HR=97%, MR=3%=0.03, 1 + 0.03*100 = 4 cycles

## Slide 30: Can we have more than one cache? Yes!
Why would we want to do that?
  Avoid going to memory at all costs!
Typical performance numbers
  Miss Rate
    L1: 3-10%
    L2: very small (likely <1%)
  Hit Time
    L1: 4 clock cycles
    L2: 10 clock cycles
  Miss Penalty
    50-200 cycles for missing in L2 going to main memory)
    Trend: increasing!
Notes: These numbers are outdated! Trade secrets

## Slide 31: An Example Memory Hierarchy

## Slide 32: Learning About Your Machine
Linux:
  lscpu
  ls /sys/devices/system/cpu/cpu0/cache/index0/
  Example: cat /sys/devices/system/cpu/cpu0/cache/index*/size
Windows:
  wmic memcache get <query> (all values in KB)
  Example: wmic memcache get MaxCacheSize
Modern processor specs: http://www.7-cpu.com/

## Slide 33: Summary
Memory Hierarchy
  Higher levels are faster, smaller, and more expensive
    Contain the most used data from lower levels
  Exploits temporal and spatial locality
  Caches are intermediate levels between memory and the CPU
Cache Performance
  Ideal case: data found in cache (hit)
  Bad case: not found in cache (miss), go to next level in hierarchy
  Average Memory Access Time (AMAT) = HT + MR × MP
    Hurt my high miss rate and miss penalty