## Slide 1: Caches III
CSE 351 Summer 2024
Instructor:
Ellis Haker
Teaching Assistants:
Naama Amiel
Micah Chang
Shananda Dokka
Nikolas McNamee
Jiawei Huang

## Slide 2: Administrivia
Today
  HW14 due (11:59pm)
Friday, 7/26
  RD17 (1pm)
  No HW due!
Sunday, 7/28
  Lab3 due (11:59pm)
Monday, 7/29
  No RD due!
  HW15 + 16 due (11:59pm)
  Quiz 2 due (11:59pm)
Notes: Late due date for Lab3 is Tue 7/30
REMEMBER QUIZ 2

## Slide 3: Caches
Cache basics
Principle of locality
Memory hierarchies
Cache organization
  Direct-mapped (sets; index + tag)
  Associativity (ways)
  Replacement policy
  Handling writes
Program optimizations that consider caches
Notes: Only talking about direct-mapped caches today. This is what you read about for today. We’ll talk about the other kinds later

## Slide 4: Recap: Direct-Mapped Cache
Each block in memory can only go into one set
  Fast and simple
Hash function
  (Block #) mod (# of sets)

## Slide 5: Direct-Mapped: a Problem!
What if we have the following access pattern:
  0, 16, 0, 16, …
  Each access will miss
    Thrashing!
  Rest of the cache unused

## Slide 6: One Solution: Fully Associative
Can store any data block anywhere in the cache
  When loading in a new block, store it in the first unused space
  Only evict old blocks when the entire cache is full!
Problems with this?
Requires complicated hardware to check each set
  More power consumed, slower
No index field needed!
Notes: Tag = entire block#

## Slide 7: Full Solution: Associativity
Rather than just one block per set, we can have multiple
  Cache line = block + relevant metadata (i.e. tag)
  Associativity (E) = number of lines in a set
    Cache is “E-way set associative”
If any block can go in any set, the cache is Fully Associative
1-way (1 block per set, 4 sets)
Direct-Mapped
2-way (2 blocks per set, 2 sets)
4-way (4 blocks per set, 1 set)
Fully-Associative

## Slide 8: Cache Organization: Associativity
K = block size (in bytes), C = cache size (in bytes), E = associativity
S = number of sets = C÷K÷E
Use lowest s = log2(S) bits of block number to find the set
  Direct-Mapped: E = 1, so s = log2(C÷K), same as we saw previously
  Fully Associative: E = C÷K, so log2(1) = 0
Direct-Mapped
n-way Set Associative
Fully Associative
Notes: As E increases, S decreases, so fewer index bits

## Slide 9: Example Placement #1
Where would data from address 0x1833 be placed?
  0b0001 1000 0011 0011
Block size 𝑲: 16 B
Capacity 𝑪/𝑲: 8 blocks
Address 𝒎: 16 bits
s = ____
s = ____
s = ____
Notes: Little k = 4 bits.
First example has 8 sets, so little s = 3, set 0b011 = 3
Second example has 4 sets, to little s = 2, set 0b11 = 3. block can go in either slot in the set
Third example has 2 sets, so little s = 1, set 0b1 = 1. block can go in any of the 4 slots in set 1

## Slide 10: Block Placement and Replacement
If there is an empty line in the set, store data there
  How to tell if the line is empty? Valid bit (0 = empty, 1 = used)
    Stored in cache line
If there are no empty lines, which one do we replace?
  No choice for direct-mapped, easy!
  For other caches, need a replacement policy
    Ideal is least recently used (LRU)
    Most real caches approximate LRU

## Slide 11: Polling Questions
We have a cache of size 2 KiB with block size of 128 B. If our cache has 2 sets, what is its associativity?
  2
  4
  8
  16
If addresses are 16 bits wide, how wide is the Tag field?
Notes: 2 KiB = 2*2^10 = 2^11 B. 128 B = 2^7 B
Associativity (E) = Cache size (C) / block size (K) / number of sets (S) = 2^11 B / 2^7 B / 2 = 2^3 = 8
Little k = log_2(big K) = 7, little s = log_2(big s) = 3. Tag bits = 16-7-3 = 6 bits

## Slide 12: General Cache Layout Review
C = total bytes = K*E*S
(does not include tag or valid bit)

## Slide 13: Notation Review
Parameter | Variable | Formulas
Block size | K (B in book) | C = K*E*S ↔ S=C/K/E k = log2(K) ↔ K = 2k s = log2(S) ↔ S = 2s m = log2(M) ↔ M = 2m m = t + s + k
Cache size | C | 
Associativity | E | 
Number of sets | S | 
Address space | M | 
Address width | m | 
Offset field width | k (b in book) | 
Index field width | s | 
Tag field width | t | 
Notes: Address space = # of bytes/addresses in memory (see Mem & Data slides)

## Slide 14: Example Cache Problem
1KiB address space, 125 cycles to go to memory. Fill in the following table:
Cache size (C) | 64B
Block size (K) | 8B
Associativity (E) | 2-way
Hit Time | 3 cycles
Miss Rate | 20%
Address width (m) | 
Offset bits (k) | 
Index bits (s) | 
Tag bits (t) | 
AMAT | 
Notes: 1KiB = 2^10B = 2^10 addresses = big M, 125 cycles = miss penalty
Address width (little m) = log_2(big M) = 10 bits
Offset bits (little k) = log_2(big K) = 3 bits
Index bits (little s) = log_2(big S). Big S = 2^10 / 2^3 / 2 = 2^6, so little s = 6 bits
Tag bits (t) = 10-3-6 = 1 bit
AMAT = HT + MR*MP = 3 + 0.2*125 = 28 cycles

## Slide 15: Read: General Steps
Break up address into offset, index, and tag
Locate the set using index
Check if any line in the set has our data
  Valid bit = 1 and tag matches
  If yes - hit!
    Otherwise, load in from memory
Read out data from block starting at offset
Notes: New things added this lecture: checking any line in the set (as opposed to only having one line per set), and checking the valid bit

## Slide 16: Read: Direct-Mapped Cache
One line per set (E=1), K=4B
Locate set

## Slide 17: Read: Direct-Mapped Cache (pt 2)
One line per set (E=1), K=4B
Locate set
Check if valid and compare tag
  No match? Old block gets evicted, replaced with new one
Notes: Match if V==1 and Tag==0xabc

## Slide 18: Read: Direct-Mapped Cache (pt 3)
One line per set (E=1), K=4B
Locate set
Check if valid and compare tag
Get data starting at offset
Notes: 2 B because we want a short

## Slide 19: Read: Set Associative Cache
Two lines per set (E=2), K=4B
Locate set

## Slide 20: Read: Set Associative Cache (pt 2)
Two lines per set (E=2), K=4B
Locate set
Check if valid and compare tag for every line in the set
  No match? One line is selected to get evicted and replaced by new one
Notes: The one on the left!

## Slide 21: Read: Set Associative Cache (pt 3)
Two lines per set (E=2), K=4B
Locate set
Check if valid and compare tag for every line in the set
Get data starting at offset

## Slide 22: Types of Cache Misses: 3 C’s
Compulsory (cold-start) miss
  Occurs on the first access to a block
  Smaller block size = more compulsory misses
Conflict miss
  Occurs when cache is large enough to hold multiple data blocks, but they cannot be in the cache at the same time because they conflict
  Lower associativity = more conflict misses
    Does not occur in fully associative caches
Capacity miss
  Occurs when the set of active blocks (the working set) is too big to fit in the cache
  Smaller cache size = more capacity misses

## Slide 23: Code Analysis
Assuming cache starts cold (i.e. all blocks invalid), and sum, i, and j are all stored in registers, calculate the miss rate.
  m = 10 bits, C = 64B, K = 8B, E = 2
#define SIZE 8
short ar[SIZE][SIZE], sum = 0; // &ar=0x200
for (int i = 0; i < SIZE; i++) {
for (int j = 0; j < SIZE; j++)
sum += ar[j][i];
}
Notes: More detailed explanation in next lecture
Big S = 64/8/2 = 4 sets
Little k = 3 bits, little s = 2 bits
Short is 2 B, 4 per block
Access pattern is a[0][0], a[1][0], a[2][0], a[3][0]…
a[0][0], a[2][0], a[4][0], a[6][0] = Set 0
a[1][0], a[3][0], a[5][0], a[7][0] = Set 2
a[4] kicks out a[0], a[5] kicks out a[1], a[6] kicks out a[2], a[7] kicks out a[3]
Each block is evicted before it’s used again. MR = 100%

## Slide 24: Summary
Associativity: number of cache lines in a set
  Direct-Mapped caches have associativity 1
  Fully Associative caches have associativity equal to # of blocks (all in one set)
  Most caches are somewhere in between
3 types of misses
  Compulsory: first time accessing block
  Conflict: block was evicted by another when the cache was not full
  Capacity: block was evicted because the cache was full