## Slide 1: Exam Preparation & Building a Computer
Exam Preparation, Multiplication Implementation Exercise, Building a Computer, Hack CPU Interface

## Slide 2: Week 6 Announcements
Change in office hours times for Sean and Andres
  Sean: Wednesdays 12-1pm  Wednesdays 3-4pm
  Andres: Mondays 12:30-1:30pm  Mondays 3-4pm
GitLab: How to properly tag a commit
  Common scenario: course staff releases starter code and that commit ends up getting tagged instead
  Type “git log” in the command line to see which commit you are on, and use ”git checkout” to move to the commit you want to tag
Late days updated on Canvas through Project 4

## Slide 3: Lecture Outline
Exam Preparation
  Study Strategies, Mock Exam Problem
Multiplication Implementation Exercise
  Multiplying Two Numbers in Hack Assembly
Building a Computer
  Architecture, Fetch and Execute Cycle
Hack CPU Interface
  Implementation and Operations

## Slide 4: Gearing Up For Exams
Make a Study Plan
  What key topics / concepts does your exam cover?
  How might your study guides look different for specific classes?
  What resources, materials, or people might you engage with?
Create a Schedule
  Do not cram
  Office hours, review sessions, study groups
  Reference your weekly time commitments & quarterly calendar
Test Yourself
  What are ways that can help address this?
  Replicate exam-like environments

## Slide 5: Exams Preparation Discussion
How do you usually prepare for your exams?
What is one thing that is effective and ineffective about the way you study? Why?
What are some effective exam preparation strategies that you would find most helpful?
How might you implement some of these effective strategies for change your exam preparation strategy for this quarter?

## Slide 6: Project 6, Part I: Mock Exam Problem
Schedule a 30-minute session based on your group members availability to do one mock exam problem
Determine how you will connect with each other and where your session will be located
Comment your group’s meeting day and time on the Project 6 Mock Exam Groups spreadsheet
  We will make an Ed post with this spreadsheet

## Slide 7: Lecture Outline
Exam Preparation
  Study Strategies, Mock Exam Problem
Multiplication Implementation Exercise
  Multiplying Two Numbers in Hack Assembly
Building a Computer
  Architecture, Fetch and Execute Cycle
Hack CPU Interface
  Implementation and Operations

## Slide 8: Hack: Registers
D Register: For storing Data
A Register: For storing data and Addressing memory
M “Register”: The 16-bit word in Memory currently being referenced by the address in A
REGISTERS
A
108
D
RAM
1100101010010101
...
106
107
108
109
110
...
M

## Slide 9: Hack: A-Instructions
Syntax:
value can either be:
  A decimal constant
  A symbol referring to a constant
Semantics:
  Stores value in the A register
@value

## Slide 10: Hack: A-Instructions
Symbolic Syntax
  Loads a value into the A register
Example:
Binary Syntax
0000000000010101
Family:
A-Instruction
Value:
Binary encoding of 21
@value
A Register
0
D Register
0
A Register
21
D Register
0
...
@21
...

## Slide 11: Hack: Symbols
Symbols are simply an alias for some address
  Only in the symbolic code—don’t turn into a binary instruction
  Assembler converts use of that symbol to its value instead
Example:
@3
D=0
(LOOP)
@21
D=1
@LOOP
...
00
01
02
03
04
0000000000000011
1110101010010000
0000000000010101
1110111111010000
0000000000000010
...
00
01
02
03
04
Assemble
LOOP = 02

## Slide 12: Hack: C-Instructions
Syntax: (dest and jump optional)
  dest is a combination of destination registers:
  comp is a computation:
  jump is an unconditional or conditional jump:
Semantics:
  Computes value of comp
  Stores results in dest (if specified)
  If jump is specified and condition is true (by testing comp result), jump to instruction ROM[A]
dest = comp ; jump
M, D, MD, A, AM, AD, AMD
0, 1, -1, D, A, !D, !A, -D, -A, D+1, A+1, D-1, A-1, D+A, D-A, A-D, D&A, D|A, M, !M, -M, M+1, M-1, D+M, D-M, M-D, D&M, D|M
JGT, JEQ, JGE, JLT, JNE, JLE, JMP

## Slide 13: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Jump:
Condition for jumping
Dest:
Where to store result
Comp:
ALU Operation (a bit chooses between A and M)
Unused
Family:
C-Instruction

## Slide 14: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Chapter 4
Jump:
Condition for jumping

## Slide 15: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Chapter 4
Dest:
Where to store result

## Slide 16: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Comp:
ALU Operation (a bit chooses between A and M)
Chapter 4
Important: just pattern matching text!
Cannot have “1+M”

## Slide 17: Exercise: Implementing Multiplication
Write a program that multiplies R0 and R1 and stores the result in R2
  Remember we don’t have a multiply operation
  We will have to use add and loops to get the job done
Roadmap
  Start with pseudocode using if statements, loops, etc.
  Remove conditionals and loops by using jumps in pseudocode
  Convert pseudocode to assembly

## Slide 18: Exercise: Implementing Multiplication
Goal: Implement R0 × R1 = R2
Pseudocode | Hack Assembly

## Slide 19: Exercise: Implementing Multiplication
Goal: Implement R0 × R1 = R2
Pseudocode | Hack Assembly
Approach: add R0 to the result R1 times

## Slide 20: Exercise: Implementing Multiplication
Goal: Implement R0 × R1 = R2
Pseudocode | Hack Assembly
Approach: add R0 to the result R1 times
R2 = 0
while (R1 > 0) {
R2 = R0 + R2
R1 = R1 - 1
}

## Slide 21: Exercise: Implementing Multiplication
Remove loops from pseudocode
Use labels to notate important sections of the code
Attempt 1: What happens when R1 is 0? What should happen?
R2 = 0
while (R1 > 0) {
R2 = R0 + R2
R1 = R1 - 1
}
START:
R2 = 0
LOOP:
R2 = R0 + R2
R1 = R1 - 1
IF R1 > 0 JMP LOOP
END:
INFINITE LOOP

## Slide 22: Exercise: Implementing Multiplication
Remove loops from pseudocode
Use labels to notate important sections of the code
Attempt 1: What happens when R1 is 0? What should happen?
R2 = 0
while (R1 > 0) {
R2 = R0 + R2
R1 = R1 - 1
}
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP

## Slide 23: Exercise: Implementing Multiplication
Convert to Hack Assembly
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP

## Slide 24: Exercise: Implementing Multiplication
Convert to Hack Assembly
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP
(START)
@R2
M = 0
(LOOP)
(END)

## Slide 25: Exercise: Implementing Multiplication
Convert to Hack Assembly
(START)
@R2
M = 0
(LOOP)
@R1
D = A
@END
D; JLE
(END)
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP

## Slide 26: Exercise: Implementing Multiplication
Convert to Hack Assembly
(START)
@R2
M = 0
(LOOP)
@R1
D = A
@END
D; JLE
(END)
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP

## Slide 27: Exercise: Implementing Multiplication
Convert to Hack Assembly
(START)
@R2
M = 0
(LOOP)
@R1
D = M
@END
D; JLE
(END)
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP

## Slide 28: Exercise: Implementing Multiplication
Convert to Hack Assembly
(START)
@R2
M = 0
(LOOP)
@R1
D = M
@END
D; JLE
@R0
D = M
@R2
M = M + D
(END)
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP

## Slide 29: Exercise: Implementing Multiplication
Convert to Hack Assembly
(START)
@R2
M = 0
(LOOP)
@R1
D = M
@END
D; JLE
@R0
D = M
@R2
M = M + D
@R1
M = M - 1
@LOOP
0; JMP
(END)
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP

## Slide 30: Exercise: Implementing Multiplication
Convert to Hack Assembly
(START)
@R2
M = 0
(LOOP)
@R1
D = M
@END
D; JLE
@R0
D = M
@R2
M = M + D
@R1
M = M – 1
@LOOP
0; JMP
(END)
@END
0; JMP
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP

## Slide 31: Lecture Outline
Exam Preparation
  Study Strategies, Mock Exam Problem
Multiplication Implementation Exercise
  Multiplying Two Numbers in Hack Assembly
Building a Computer
  Architecture, Fetch and Execute Cycle
Hack CPU Interface
  Implementation and Operations

## Slide 32: Building a Computer
All your hardware efforts are about to pay off!
Perspective: BUILDING A COMPUTER
In Project 6, you will build Computer.hdl, the final, top-level chip in this course
  For all intents and purposes, a real computer
  Simplified, but organization very similar to your laptop
Project 7 onward, we will write software to make it useful

## Slide 33: Von Neumann Architecture
COMPUTER
MEMORY
INPUT
CPU
REGISTERS
CONTROL
OUTPUT
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2

## Slide 34: Connecting the Computer: Buses
COMPUTER
MEMORY
INPUT
CPU
OUTPUT
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2
Address Bus
Data Bus
CONTROL
REGISTERS
Control Bus

## Slide 35: Basic CPU Loop
Repeat forever:
  Fetch an instruction from the program memory
  Execute that instruction

## Slide 36: Fetching
Specify which instruction to read as the address input to our memory
Data output: actual bits of the instruction
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2
PC
1
MEMORY
Memory Input: Address
Memory Output: Data
Instruction
D=A;JMP
Instruction Address

## Slide 37: Executing
The instruction bits describe exactly “what to do”
  A-instruction or C-instruction?
  Which operation for the ALU?
  What memory address to read? To write?
  If I should jump after this instruction, and where?
Executing the instruction involves data of some kind
  Accessing registers
  Accessing memory

## Slide 38: Combining Fetch & Execute
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2
PC
1
MEMORY
Memory Input: Address
Memory Output: Data
Instruction
D=A;JMP
Instruction Address
Data Address (From instruction or register)
Data
245

## Slide 39: Combining Fetch & Execute
Could we implement with RAM16K.hdl?
  (Hint: Think about the I/O of RAM)
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2
PC
1
MEMORY
Memory Input: Address
Memory Output: Data
Instruction
D=A;JMP
Instruction Address
Data Address (From instruction or register)
Data
245

## Slide 40: Combining Fetch & Execute
Could we implement with RAM16K.hdl?
  No! Our memory chips only have one input and one output
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2
PC
1
MEMORY
Memory Input: Address
Memory Output: Data
Instruction
D=A;JMP
Instruction Address
Data Address (From instruction or register)
Data
245

## Slide 41: Solution 1: Handling Single Input / Output
Can use multiplexing to share a single input or output
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2
MEMORY
Memory Input: Address
Memory Output: Data
Instruction, when fetching
Data, when executing
Instruction Address
Fetching vs. Executing
Data Address
Mux
DMux

## Slide 42: Solution 1: Fetching / Executing Separately
Need to store fetched instruction so it’s available during execution phase
0101110011100110
1011000101010100
1110001011111100
...
Instructions
1100101010010101
1100100101100111
0011001010101011
...
Data
0
1
2
n
n+1
n+2
MEMORY
Memory Input: Address
Memory Output: Data
Instruction, when fetching
Data, when executing
Instruction Address
Fetching vs. Executing
Fetching vs. Executing
Data Address
Mux
DMux
Register

## Slide 43: Solution 2: Separate Memory Units
Separate instruction memory and data memory into two different chips
  Each can be independently addressed, read from, written to
Pros:
  Simpler to implement
Cons:
  Fixed size of each partition, rather than flexible storage
  Two chips → redundant circuitry

## Slide 44: Lecture Outline
Exam Preparation
  Study Strategies, Mock Exam Problem
Multiplication Implementation Exercise
  Multiplying Two Numbers in Hack Assembly
Building a Computer
  Architecture, Fetch and Execute Cycle
Hack CPU Interface
  Implementation and Operations

## Slide 45: Hack CPU
COMPUTER
ROM
(Instructions)
INPUT
CPU
REGISTERS
CONTROL
OUTPUT
0
1
2
RAM
(Data)
100110010111
100011001111
000000000010
...
Data
0
1
2
addr of next instruction
data out
data in
instr
010111001110
101100010101
111000101111
...
Instructions

## Slide 46: Hack CPU Interface Inputs
inM: Value coming from memory
instruction: 16-bit instruction
reset: if 1, reset the program

## Slide 47: Hack CPU Interface Outputs
outM: value used to update memory if writeM is 1
writeM: if 1, update value in memory at addressM with outM
addressM: address to read from or write to in memory
pc: address of next instruction to be fetched from memory

## Slide 48: Hack CPU Implementation
pc

## Slide 49: Hack CPU Implementation
(each "C" symbol represents a control bit)

## Slide 50: Post-Lecture 10 Reminders
We will do more exam preparation and explore more in-depth the Hack CPU implementation this Thursday
Project 5 due this Thursday (11/3) at 11:59pm
Preston has office hours after class in CSE2 153
  Feel free to post your questions on the Ed board as well
Midterm exam coming up on 11/10 during lecture time