## Slide 1: Test-taking Strategies & Midterm Practice Exam
Hack CPU Logic, Test-taking Strategies, Midterm Practice Exam, Practice Exam Walkthrough and Rubric

## Slide 2: Week 7 Announcements
CSE 390B final is Tuesday of finals (12/13), 4:30-6:20pm
  Please let the course staff know if you have a conflicting final
Project reminders
  First check specification and textbook when you have a question
  Please avoid submitting a link on the project documents
  Please assign problems to the pages when submitting the project document on Gradescope
  Please find a time for the Project 6 mock exam problem and update the spreadsheet (if your group has not already)
Andres’ office hours now on Mondays from 3:30-4:30pm
  Location: CSE2 153

## Slide 3: Lecture Outline
Hack CPU Logic
  Implementation and Operations
Test-taking Strategies
  Maximizing Success on Exam Day
Midterm Practice Exam
  Mock Exam, Debrief, and Reflection
Practice Exam Solutions and Rubric
  Walkthrough of Solutions and Exploring Sample Rubrics

## Slide 4: Hack CPU
COMPUTER
ROM
(Instructions)
INPUT
CPU
REGISTERS
CONTROL
OUTPUT
0
1
2
RAM
(Data)
100110010111
100011001111
000000000010
...
Data
0
1
2
addr of next instruction
data out
data in
instr
010111001110
101100010101
111000101111
...
Instructions

## Slide 5: Hack CPU Interface Inputs
inM: Value coming from memory
instruction: 16-bit instruction
reset: if 1, reset the program

## Slide 6: Hack CPU Interface Outputs
outM: value used to update memory if writeM is 1
writeM: if 1, update value in memory at addressM with outM
addressM: address to read from or write to in memory
pc: address of next instruction to be fetched from memory

## Slide 7: Hack CPU Implementation
pc

## Slide 8: Hack CPU Implementation
(each "C" symbol represents a control bit)

## Slide 9: CPU Operation: Instruction Handling
(each "C" symbol represents a control bit)

## Slide 10: CPU Operation: Instruction Handling
0000000000000101
A-instruction
@5

## Slide 11: CPU Operation: Instruction Handling
0000000000000101
A-instruction
@5
CPU handling of an A-instruction:
Decodes the instruction into:
  op-code
  15-bit value
Stores the value in the A-register
Outputs the value (not shown in this diagram)

## Slide 12: CPU Operation: Instruction Handling
C-instruction
D=D+1;JMP
1110011111010111

## Slide 13: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Jump:
Condition for jumping
Dest:
Where to store result
Comp:
ALU Operation (a bit chooses between A and M)
Unused
Family:
C-Instruction

## Slide 14: CPU Operation: Instruction Handling
C-instruction
D=D+1;JMP
1110011111010111
CPU handling of a C-instruction:
Decodes the instruction bits into:
  Op-code
  ALU control bits
  Destination load bits
  Jump bits
Routes these bits to their chip-part destinations
The chip-parts (most notably, the ALU) execute the instruction

## Slide 15: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Comp:
ALU Operation (a bit chooses between A and M)
Chapter 4
Important: just pattern matching text!
Cannot have “1+M”

## Slide 16: CPU Operation: Handling C-Instructions
1110011111010111
011111
writeM
1…01
1…10
ALU data inputs:
Input 1: from the D-register
Input 2: from either:
      A-register, or
      data memory
ALU control inputs:
Control bits (from the instruction)

## Slide 17: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Chapter 4
Dest:
Where to store result

## Slide 18: CPU Operation: Handling C-Instructions
1110011111010111
writeM
1…01
1…10
0…11
0
1
0
ALU data output:
Result of ALU calculation
Fed simultaneously to: D-register, A-register, data memory
Which destination actually commits to the ALU output is determined by the instruction’s destination bits
011111

## Slide 19: CPU Operation: Handling C-Instructions
ALU control outputs:
Is the output negative?
Is the output zero?
1110011111010111
writeM
1…01
0…11
1…10
011111

## Slide 20: CPU Operation: Control
pc

## Slide 21: CPU Operation: Control

## Slide 22: CPU Operation: Control
PC operation (abstraction)
Outputs the address of the next instruction:
Restart: PC = 0
No jump: PC++
Go to: PC = A
Conditional go to: if (condition) PC = A
    else PC ++
load
16
1
16
pc
Address of next instruction

## Slide 23: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Chapter 4
Jump:
Condition for jumping

## Slide 24: CPU Operation: Control
load
16
1
16
Address of next instruction
pc
PC operation (implementation)
if (reset==1) PC = 0
else
// In the course of handling the current instruction:
load = f (jump bits, ALU control outputs)
if (load == 1) PC = A // jump
else PC++ // next instruction
111 a c c c c c c d d d j j j

## Slide 25: Hack CPU Implementation: That’s It!

## Slide 26: Lecture Outline
Hack CPU Logic
  Implementation and Operations
Test-taking Strategies
  Maximizing Success on Exam Day
Midterm Practice Exam
  Mock Exam, Debrief, and Reflection
Practice Exam Solutions and Rubric
  Walkthrough of Solutions and Exploring Sample Rubrics

## Slide 27: Test-taking Strategies Discussion
What are some test-taking strategies you have previously utilized in taking your exams?
Were those strategies you tried effective or not? Why?
How might you try a new test-taking strategy on the CSE 390B midterm or any other upcoming exam?

## Slide 28: Test-taking Strategies
Survey the entire exam before beginning
  Helps plan how much time to allocate for each problem
Read exam directions and question statements carefully
  Use highlights, underlines, circles on important details
Answer the questions you feel the most confident in first
If stuck on a problem, make a mark on the problem and revisit the question later

## Slide 29: Test-taking Strategies
Prioritize how you will answer questions
  Do this based on confidence level for each type of question or how long you think each will take
Rely on a methodological approach for each question
  Helps make taking the test feel more systematic
If stuck on a question, demonstrate what you know
  Many exams reward partial credit
If time allows, double check your answers
  Catches any small mistakes that may have been made earlier

## Slide 30: Lecture Outline
Hack CPU Logic
  Implementation and Operations
Test-taking Strategies
  Maximizing Success on Exam Day
Midterm Practice Exam
  Mock Exam, Debrief, and Reflection
Practice Exam Solutions and Rubric
  Walkthrough of Solutions and Exploring Sample Rubrics

## Slide 31: Midterm Practice Exam
The exam is closed-note, closed-book
  You may only use the midterm reference sheet
Questions are not necessarily in order of difficulty
You will have 25 minutes to complete the mock exam
  We will give you a 5-minute warning
Remember to relax and take deep breaths

## Slide 32: Mock Exam Debrief & Reflection
What did you learn about yourself through this process? About your test-taking practices?
What are two test-taking strategies that you would like to engage with in your next exam? Why?
What is one thing that can help you relax and calm down before or during your exam?

## Slide 33: Lecture Outline
Hack CPU Logic
  Implementation and Operations
Test-taking Strategies
  Maximizing Success on Exam Day
Midterm Practice Exam
  Mock Exam, Debrief, and Reflection
Practice Exam Solutions and Rubric
  Walkthrough of Solutions and Exploring Sample Rubrics

## Slide 34: Question 1: Circuit Design
Part a: Truth Table
11  10  01  00  11
At | Bt | At+1 | Bt+1
1 | 1 | 1 | 0
1 | 0 | 0 | 1
0 | 1 | 0 | 0
0 | 0 | 1 | 1

## Slide 35: Question 1: Circuit Design
Part a: Truth Table
11  10  01  00  11
At | Bt | At+1 | Bt+1
1 | 1 | 1 | 0
1 | 0 | 0 | 1
0 | 1 | 0 | 0
0 | 0 | 1 | 1

## Slide 36: Question 1: Circuit Design
At | Bt | At+1 | Bt+1
1 | 1 | 1 | 0
1 | 0 | 0 | 1
0 | 1 | 0 | 0
0 | 0 | 1 | 1
Part a: Truth Table
Part b: Boolean Expressions
At+1 = (At & Bt)
At+1 = (~At & ~Bt)

## Slide 37: Question 1: Circuit Design
At | Bt | At+1 | Bt+1
1 | 1 | 1 | 0
1 | 0 | 0 | 1
0 | 1 | 0 | 0
0 | 0 | 1 | 1
Part a: Truth Table
Part b: Boolean Expressions
At+1 = (At & Bt) | (~At & ~Bt)
At+1 = (At & Bt)
At+1 = (~At & ~Bt)

## Slide 38: Question 1: Circuit Design
At | Bt | At+1 | Bt+1
1 | 1 | 1 | 0
1 | 0 | 0 | 1
0 | 1 | 0 | 0
0 | 0 | 1 | 1
Part a: Truth Table
Part b: Boolean Expressions
At+1 = (At & Bt) | (~At & ~Bt)
Bt+1 = (At & ~Bt) | (~At & ~Bt)
= ~Bt & (At | ~ At) [Factor out ~Bt]
= ~Bt [At | ~ At = 1]
At+1 = (At & Bt)
At+1 = (~At & ~Bt)
Bt+1 = (At & ~Bt)
Bt+1 = (~At & ~Bt)

## Slide 39: Question 1: Circuit Design
At | Bt | At+1 | Bt+1
1 | 1 | 1 | 0
1 | 0 | 0 | 1
0 | 1 | 0 | 0
0 | 0 | 1 | 1
Part a: Truth Table
Part b: Boolean Expressions
At+1 = (At & Bt) | (~At & ~Bt)
Bt+1 = (At & ~Bt) | (~At & ~Bt)
= ~Bt & (At | ~ At) [Factor out ~Bt]
= ~Bt [At | ~ At = 1]
Part c: Drawing the Circuit

## Slide 40: Question 1: Circuit Design Sample Rubric
Category | Points | Criteria
Truth Table | 4 points | 1 point for each row in the truth table that is correct
Boolean Expressions | 6 points | 4 points for correct expression for At+1 2 points if truth table is wrong but expression matches truth table 2 points for correct expression for Bt+1 1 point if truth table is wrong but expression matches truth table
Circuit Diagram | 5 points | 3 points for having circuits that match the Boolean expressions in part b 2 points for fully correct diagram
Total | 15 points | 

## Slide 41: Question 2: Math Puzzle
Dana needs 300 pickets for her colorful picket fence. She wants equal amounts of each of her 4 selected colors. She already has 32 red, 26 green, 9 yellow, and no blue. If the pickets cost 25 cents and you get 20% off if you purchase 50 or more of the same color, and 30% off if you purchase 60 or more of one color, how much does Dana need to spend? List your answer to two decimal places. You may use a calculator application on your computer to solve this problem.

## Slide 42: Question 2: Math Puzzle
Dana needs 300 pickets for her colorful picket fence. She wants equal amounts of each of her 4 selected colors. She already has 32 red, 26 green, 9 yellow, and no blue. If the pickets cost 25 cents and you get 20% off if you purchase 50 or more of the same color, and 30% off if you purchase 60 or more of one color, how much does Dana need to spend? List your answer to two decimal places. You may use a calculator application on your computer to solve this problem.
Solution
(Rounding down is also acceptable)

## Slide 43: Question 3: Hack Assembly Programming
Write a Hack assembly program that stores -1, 0, or 1 in R1 based on the sign of R0. To be more specific, your program should store a -1 in R1 if R0 is negative, a 0 in R1 if R0 is 0, and a 1 in R1 if R0 is positive.

## Slide 44: Question 3: Hack Assembly Programming
Write a Hack assembly program that stores -1, 0, or 1 in R1 based on the sign of R0. To be more specific, your program should store a -1 in R1 if R0 is negative, a 0 in R1 if R0 is 0, and a 1 in R1 if R0 is positive.
Equivalent pseudocode:
if (R0 < 0){
R1 = -1;
} else if (R0 > 0){
R1 = 1;
} else { //R0 == 0
R1 = 0;
}

## Slide 45: Question 3: Hack Assembly Programming
Write a Hack assembly program that stores -1, 0, or 1 in R1 based on the sign of R0. To be more specific, your program should store a -1 in R1 if R0 is negative, a 0 in R1 if R0 is 0, and a 1 in R1 if R0 is positive.
One solution:
@R0
D = M
@NEGATIVE
D; JLT
@POSITIVE
D; JGT
// R0 == 0 case
@R1
M = 0
@END
0; JMP
(NEGATIVE)
// R0 < 0 case
@R1
M = -1
@END
0; JMP
(POSITIVE)
// R0 > 0 case
@R1
M = 1
(END)
@END
0; JMP
Equivalent pseudocode:
if (R0 < 0){
R1 = -1;
} else if (R0 > 0){
R1 = 1;
} else { //R0 == 0
R1 = 0;
}

## Slide 46: Question 3: Hack Assembly Sample Rubric
Category | Points | Criteria
Has Infinite End Loop | 1 point | 1 point if program has an Infinite End Loop
Conditional Checks | 4 points | 2 points for having at least two checks for cases. Almost all solutions will need a check for 2 of the three cases (negative, zero, positive). 2 points for correctly matching jump condition to cases (e.g. jump to negative case when negative, etc.)
Assigns Correct R1 Value | 3 points | One point for each case: negative: R1 = -1 zero: R1 = 0 positive: R = 1
Fully Correct Implementation | 2 points | Covers any little mistakes that may result in an incorrect implementation (e.g., forgetting to jump to the end when a case is done)
Total | 10 points | 

## Slide 47: Question 4: Metacognitive Skills
Name two metacognitive skills that we have covered in CSE 390B thus far.

## Slide 48: Post-Lecture 12 Reminders
CSE 390B midterm this Thursday (11/10) during lecture at 2:30pm
Project 6: Mock Exam Problem & Building a Computer due next Thursday (11/17) at 11:59pm
Preston has office hours after class in CSE2 153
  Feel free to post your questions on the Ed board as well