## Slide 1: Finals Preparation & Computer Networks
Gearing up for Finals Week, E-Portfolio Workshop,
Overview of Computer Networks
Notes: Record. You messed up the number of bugs for If.java

## Slide 2: Lecture Outline
Gearing up for Finals Week
  Study Plan Outline and Tips for Success
E-Portfolio Workshop
  Reflection Work Session and Feedback
Overview of Computer Networks
  How Computers Connect to The Internet

## Slide 3: Gearing up for Finals Week
Revisit and reassess your goals each day
  Break-up into different levels—minimal, solid, reach
Have an accountability buddy
  Study groups or working sessions—having someone who can help you stay motivated, accountable, and avoid procrastination
Recall Bloom’s Taxonomy
  How is your preparation involving higher level thinking skills?
Stick to a routine
  Provides normalcy & structure for maintaining sleep and wellness

## Slide 4: Planning for Success on Finals Week
In groups, discuss the following for 4-6 minutes:
What are some metacognitive strategies that you plan on using to succeed in finals week?
  How can you stay disciplined or keep yourself accountable in applying these metacognitive skills?
In terms of academic and metacognitive subjects, what are your strengths and weaknesses going into finals?
  How can you cultivate your strengths and improve the areas you are weaker in?

## Slide 5: Developing a Plan for Finals Week
First, list the commitments that you have for finals week (final exams, final projects, presentations, etc.)
Then, outline the steps that you’ll need to follow to complete those tasks
  Be specific with these steps — instead of “review derivatives,” add detail about the how: “Review lecture slides and examples on derivatives and redo five derivative problems on WebAssign”
Lastly, add dates to when you will work on and complete each of the steps (be realistic here!)
  Add these to your calendar

## Slide 6: Lecture Outline
Gearing up for Finals Week
  Study Plan Outline and Tips for Success
E-Portfolio Workshop
  Reflection Work Session and Feedback
Overview of Computer Networks
  How Computers Connect to The Internet

## Slide 7: E-Portfolio Workshop
Individually, spend 15-20 minutes completing the following steps:
  Aim to finalize the two metacognitive skills, two examples of you applying them, and one technical skill you plan on reflecting on
  Begin drafting your reflection on a document (should be in paragraph form in final e-portfolio, but bullet points ok for now)
Then, get into groups of 3-4 and complete the following:
  One group member presents on their reflection so far
  Each group member listening should provide one question, comment, constructive feedback, or complement to the presenter
  Repeat until everyone has had a chance to present

## Slide 8: Five-minute Break!
Feel free to stand up, stretch, use the restroom, drink some water, review your notes, or ask questions
We’ll be back at:

## Slide 9: Lecture Outline
Gearing up for Finals Week
  Study Plan Outline and Tips for Success
E-Portfolio Workshop
  Reflection Work Session and Feedback
Overview of Computer Networks
  How Computers Connect to The Internet

## Slide 10: Overview of Computer Networks
We will go over an overview of networks
  Take CSE 333 (Systems Programming), CSE 461 (Computer Networks), and CSE 452 (Distributed Systems) to learn more
Our focus:
  Brief intro to what connecting to the internet looks like under the hood
  What that connection might look like implemented in our computer

## Slide 11: How Do Computer Networks Work?
How do you think we connect computers in different physical locations?
What modes of communication do you think computers use to network with one another?

## Slide 12: Networks = Really, Really Long Wires
At a fundamental level, there’s nothing magic about the Internet—it’s the same concepts we used to build our CPU, just with longer wires
  Still 1s and 0s, still just combinational + sequential logic
12
Combinational & Sequential Logic
Computer.hdl
Combinational & Sequential Logic
Computer.hdl
≈

## Slide 13: Thinking about the Network: Layers
To manage the complexity, we think about the network in layers
It’s all 0s and 1s, but each layer is a different way of “framing” or thinking about those 0s and 1s
  Each layer zooms out a little more
Application Layer
Physical Layer
0
0
1
0
1
1
0
0
1
1
0
0
webpage (.html)
meme (.png)
dest address
source address
data
Data Link Layer
Other layers exist between here; out of 390B scope

## Slide 14: Application Layer
Conceptually the “top” layer: looking at internet traffic as direct communication between applications
Common use: HTTP (HyperText Transfer Protocol)
  Your browser sends an HTTP request to a server
  The server sends back an HTTP response with data attached
I found it:
14
I would like to load: http://instagram.com/dog/latest_story.png
Browser
Server

## Slide 15: Application Layer
I would like to load: http://instagram.com/dog/latest_story.png
Conceptually the “top” layer: looking at internet traffic as direct communication between applications
Common use: HTTP (HyperText Transfer Protocol)
  Your browser sends an HTTP request to a server
  The server sends back an HTTP response with data attached
I found it:
15
Browser
Server
dest address
source address
data
dest address
source address
data
dest address
source address
data
dest address
source address
data
Data Link Layer

## Slide 16: Data Link Layer
A computer network is simply multiple computers connected by a single wire
Why is it better to send smaller chunks of data?
16
computer
00:1d:4f:47
computer
4c:44:1e:8f
computer
de:ad:be:ef
dest address
4c:44:1e:8f
source address
24:48:96:12
data
router
(also a computer)
24:48:96:12
Gets data from Internet (beyond scope of 390B)

## Slide 17: Data Link Layer
Every computer will “hear” the message
How do the other computers know to ignore an incoming packet of data?
17
computer
00:1d:4f:47
computer
4c:44:1e:8f
computer
de:ad:be:ef
dest address
4c:44:1e:8f
source address
24:48:96:12
data
router
(also a computer)
24:48:96:12
Gets data from Internet (beyond scope of 390B)

## Slide 18: NIC (Network Interface Card)
We don’t want the CPU to waste time always listening to the network wire, especially when it’s not even the destination computer
Solution: the NIC—a new piece of the computer dedicated to dealing with the network wire
  Listens to the network wire until it hears a destination address, checks if it matches this computer, and only sends to CPU if so
computer
00:1d:4f:47
dest address
4c:44:1e:8f
source address
24:48:96:12
data
NIC

## Slide 19: NIC Implementation in Your Computer
Before, we would have to accept NIC as “magic”
Now, we can imagine exactly how to build this chip, and for a simple implementation, turns out it’s doable!
1
1
0
0
0
1
1
Next Index:
3
=
=
=
=
=
=
=
=
AND
0
1
1
1
0
1
0
0
(controls whether to pass on to CPU)

## Slide 20: NIC Implementation in Your Computer
Before, we would have to accept NIC as “magic”
Now, we can imagine exactly how to build this chip, and for a simple implementation, turns out it’s doable!
1
1
0
0
0
1
1
Next Index:
3
=
=
=
=
=
=
=
=
AND
0
1
1
1
0
1
0
0
(controls whether to pass on to CPU)
Making a choice? Our good friend Mux.hdl!

## Slide 21: NIC Implementation in Your Computer
Before, we would have to accept NIC as “magic”
Now, we can imagine exactly how to build this chip, and for a simple implementation, turns out it’s doable!
1
1
0
0
0
1
1
Next Index:
3
=
=
=
=
=
=
=
=
AND
0
1
1
1
0
1
0
0
(controls whether to pass on to CPU)
Making a choice? Our good friend DMux.hdl!

## Slide 22: NIC Implementation in Your Computer
Before, we would have to accept NIC as “magic”
Now, we can imagine exactly how to build this chip, and for a simple implementation, turns out it’s doable!
1
1
0
0
0
1
1
Next Index:
3
=
=
=
=
=
=
=
=
AND
0
1
1
1
0
1
0
0
(controls whether to pass on to CPU)
Making a choice? Our good friend DMux.hdl!
Constantly incrementing an address? Sounds like PC.hdl

## Slide 23: NIC Implementation in Your Computer
Before, we would have to accept NIC as “magic”
Now, we can imagine exactly how to build this chip, and for a simple implementation, turns out it’s doable!
1
1
0
0
0
1
1
Next Index:
3
=
=
=
=
=
=
=
=
AND
0
1
1
1
0
1
0
0
(controls whether to pass on to CPU)
Making a choice? Our good friend DMux.hdl!
Constantly incrementing an address? Sounds like PC.hdl!

## Slide 24: NIC Implementation in Your Computer
Before, we would have to accept NIC as “magic”
Now, we can imagine exactly how to build this chip, and for a simple implementation, turns out it’s doable!
1
1
0
0
0
1
1
Next Index:
3
=
=
=
=
=
=
=
=
AND
0
1
1
1
0
1
0
0
(controls whether to pass on to CPU)
Making a choice? Our good friend DMux.hdl!
Constantly incrementing an address? Sounds like PC.hdl!
Selectable read/write? Sounds like RAM.hdl!

## Slide 25: NIC Implementation in Your Computer
Before, we would have to accept NIC as “magic”
Now, we can imagine exactly how to build this chip, and for a simple implementation, turns out it’s doable!
1
1
0
0
0
1
1
Next Index:
3
=
=
=
=
=
=
=
=
AND
0
1
1
1
0
1
0
0
(controls whether to pass on to CPU)
Making a choice? Our good friend DMux.hdl!
Constantly incrementing an address? Sounds like PC.hdl!
Selectable read/write? Sounds like RAM.hdl!

## Slide 26: NIC Implementation in Your Computer
Before, we would have to accept NIC as “magic”
Now, we can imagine exactly how to build this chip, and for a simple implementation, turns out it’s doable!
1
1
0
0
0
1
1
Next Index:
3
=
=
=
=
=
=
=
=
AND
0
1
1
1
0
1
0
0
(controls whether to pass on to CPU)
Making a choice? Our good friend DMux.hdl!
Constantly incrementing an address? Sounds like PC.hdl!
Bitwise/multi-bit operations? Sounds like And16.hdl!
Selectable read/write? Sounds like RAM.hdl!
Bitwise/multi-bit operations? Sounds like And16.hdl!

## Slide 27: NIC Implementation in Your Computer
Before, we would have to accept NIC as “magic”
Now, we can imagine exactly how to build this chip, and for a simple implementation, turns out it’s doable!
1
1
0
0
0
1
1
Next Index:
3
=
=
=
=
=
=
=
=
AND
0
1
1
1
0
1
0
0
(controls whether to pass on to CPU)
Making a choice? Our good friend DMux.hdl!
Bitwise/multi-bit operations? Sounds like And16.hdl!
Constantly incrementing an address? Sounds like PC.hdl!
Selectable read/write? Sounds like RAM.hdl!
Bitwise/multi-bit operations? Sounds like And16.hdl!

## Slide 28: Connecting NIC to Memory
The keyboard and screen communicated with the CPU via memory maps—agreed-upon regions of RAM that can be read/written by the hardware of the devices themselves
The NIC could be implemented in the same way
  Every time the right address is detected, copy the following data into part of RAM where the CPU can retrieve it once it gets a chance
CPU
NIC
Screen
Keyboard

## Slide 29: Takeaways: Computer Networks
The network is fundamentally the same hardware we’ve been looking at
Its incredible power comes from scale: how much data and how many computers it connects
  To manage this complexity, we think of it in layers
Interfacing with the network can be done with specialized hardware
  This frees the CPU from monitoring constantly
  Access data only when needed

## Slide 30: Lecture 18 Reminders
Next week: CSE 390B Victory Lap, TA-led Activities
Project Reminders
  Project 7, Part II (Professor Meeting Report) due tonight (12/1) at 11:59pm
  Project 8 (Debugging & Implementing a Compiler) due next Tuesday (12/6) at 11:59pm
  Final Project, Part I (E-Portfolio Outline) due next Thursday (12/8) at 11:59pm
Course Staff Support
  Eric has office hours in CSE2 153 today after lecture
  Feel free to post your questions on the Ed board as well