## Slide 1: Bloom’s Taxonomy & Sequential Logic
Bloom’s Taxonomy, Introduction to Sequential Logic, Representing Time in Hardware, The Data Flip-Flop (DFF)

## Slide 2: Lecture Outline
Bloom’s Taxonomy
  Applying Higher Levels of Cognition to Learning
Introduction to Sequential Logic
  The Problem with Combinational Logic
Representing Time in Hardware
  Clock Signals and Units of Time in Hardware
The Data Flip-Flop (DFF)
  Implementation and Examples

## Slide 3: Bloom’s Taxonomy
Remembering
Understanding
Applying
Analyzing
Creating
Evaluating
Recalling facts and basic concepts
Explaining ideas or concepts
Using information in a new (or similar) situation
Drawing connections among ideas
Justifying your decisions or position
Producing something new

## Slide 4: Bloom’s Taxonomy in Action
Remembering
Understanding
Applying
Analyzing
Creating
Evaluating
Remembering what Java objects are
Understanding the use Java objects
Using Java objects defined in the standard class libraries
How do Java objects relate to other real-word tools?
Justifying why one would use a particular Java object (ArrayList)?
Creating your own Java objects in your CSE 143 assignments

## Slide 5: Bloom’s Taxonomy Discussion
In groups of 3-4, discuss the following points:
Identify various aspects of your academic responsibilities as a UW student (e.g., attending lecture) and categorize them in one of the levels on Bloom’s Taxonomy
Discuss how you can practically engage in higher-order levels of thinking in Bloom’s Taxonomy

## Slide 6: Lecture Outline
Bloom’s Taxonomy
  Applying Higher Levels of Cognition to Learning
Introduction to Sequential Logic
  The Problem with Combinational Logic
Representing Time in Hardware
  Clock Signals and Units of Time in Hardware
The Data Flip-Flop (DFF)
  Implementation and Examples

## Slide 7: Why Consider Time Now?
Needed for our abstraction
  We need to talk about hardware maintaining state for memory
  We need vocabulary to talk about time
Needed for our implementation
  Physical implementations of chips cannot be instantaneous
  We need to account for physical delays in signal propagation

## Slide 8: The Problem with Combinational Logic
Consider the following circuit:
Let’s assume that a=0, b=1, and c=0
  The output should be 1
What’s the result if we change b=0 and c=1?
  The result should still be 1
  However, out is briefly 0 if we change c first

## Slide 9: Autopilot Control Circuit Example
Consider this autopilot control circuit:
  Either the pilot or copilot is flying at any time
  The pilot and copilot can separately request autopilot
  Only the person flying can request autopilot
Copilot Autopilot Request
Pilot Autopilot Request
Pilot flying?
Autopilot Engaged

## Slide 10: Autopilot Control Circuit Example
Consider this autopilot control circuit:
  Either the pilot or copilot is flying at any time
  The pilot and copilot can separately request autopilot
  Only the person flying can request autopilot
Let’s assume every logic gate takes 1ms to compute
  For example, if an input changes at t=4ms, the gate will only output the new result at t=5ms
Copilot Autopilot Request
Pilot Autopilot Request
Pilot flying?
Autopilot Engaged

## Slide 11: Autopilot Control Circuit Example
CAR | 1 | 1 | 1 | 1 | 1 | 1
PF | 1 | 0 | 0 | 0 | 0 | 0
PAR | 1 | 1 | 1 | 1 | 1 | 1
A | 0 |  |  |  |  | 
B | 0 |  |  |  |  | 
C | 1 |  |  |  |  | 
AE | 1 |  |  |  |  | 
0ms
1ms
2ms
3ms
4ms
5ms
6ms
Copilot Autopilot Request
Pilot Autopilot Request
Pilot Flying?
Autopilot Engaged

## Slide 12: Autopilot Control Circuit Example
CAR | 1 | 1 | 1 | 1 | 1 | 1
PF | 1 | 0 | 0 | 0 | 0 | 0
PAR | 1 | 1 | 1 | 1 | 1 | 1
A | 0 |  |  |  |  | 
B | 0 |  |  |  |  | 
C | 1 |  |  |  |  | 
AE | 1 |  |  |  |  | 
0ms
1ms
2ms
3ms
4ms
5ms
6ms
Copilot Autopilot Request
Pilot Autopilot Request
Pilot Flying?
Autopilot Engaged
??

## Slide 13: Autopilot Control Circuit Example
CAR | 1 | 1 | 1 | 1 | 1 | 1
PF | 1 | 0 | 0 | 0 | 0 | 0
PAR | 1 | 1 | 1 | 1 | 1 | 1
A | 0 | 0 |  |  |  | 
B | 0 |  |  |  |  | 
C | 1 |  |  |  |  | 
AE | 1 |  |  |  |  | 
0ms
1ms
2ms
3ms
4ms
5ms
6ms
Copilot Autopilot Request
Pilot Autopilot Request
Pilot Flying?
Autopilot Engaged

## Slide 14: Autopilot Control Circuit Example
CAR | 1 | 1 | 1 | 1 | 1 | 1
PF | 1 | 0 | 0 | 0 | 0 | 0
PAR | 1 | 1 | 1 | 1 | 1 | 1
A | 0 | 0 | ? |  |  | 
B | 0 |  |  |  |  | 
C | 1 |  |  |  |  | 
AE | 1 |  |  |  |  | 
0ms
1ms
2ms
3ms
4ms
5ms
6ms
Copilot Autopilot Request
Pilot Autopilot Request
Pilot Flying?
Autopilot Engaged

## Slide 15: Autopilot Control Circuit Example
CAR | 1 | 1 | 1 | 1 | 1 | 1
PF | 1 | 0 | 0 | 0 | 0 | 0
PAR | 1 | 1 | 1 | 1 | 1 | 1
A | 0 | 0 | 1 |  |  | 
B | 0 |  |  |  |  | 
C | 1 |  |  |  |  | 
AE | 1 |  |  |  |  | 
0ms
1ms
2ms
3ms
4ms
5ms
6ms
Copilot Autopilot Request
Pilot Autopilot Request
Pilot Flying?
Autopilot Engaged

## Slide 16
Describe the behavior of the Autopilot Engaged (AE) output between 1ms to 6ms.
Copilot Autopilot Request
Pilot Autopilot Request
Pilot Flying?
Autopilot Engaged
CAR | 1 | 1 | 1 | 1 | 1 | 1
PF | 1 | 0 | 0 | 0 | 0 | 0
PAR | 1 | 1 | 1 | 1 | 1 | 1
A | 0 | 0 | 1 |  |  | 
B | 0 |  |  |  |  | 
C | 1 |  |  |  |  | 
AE | 1 |  |  |  |  | 
0ms
1ms
2ms
3ms
4ms
5ms
6ms

## Slide 17
Describe the behavior of the Autopilot Engaged (AE) output between 1ms to 6ms.
CAR | 1 | 1 | 1 | 1 | 1 | 1
PF | 1 | 0 | 0 | 0 | 0 | 0
PAR | 1 | 1 | 1 | 1 | 1 | 1
A | 0 | 0 | 1 | 1 | 1 | 1
B | 0 | 0 | 0 | 1 | 1 | 1
C | 1 | 1 | 0 | 0 | 0 | 0
AE | 1 | 1 | 1 | 0 | 1 | 1
0ms
1ms
2ms
3ms
4ms
5ms
6ms
Copilot Autopilot Request
Pilot Autopilot Request
Pilot Flying?
Autopilot Engaged

## Slide 18: Autopilot Control Circuit Example
Copilot Autopilot Request
Pilot Autopilot Request
Pilot Flying?
Autopilot Engaged
Critical Path
CAR | 1 | 1 | 1 | 1 | 1 | 1
PF | 1 | 0 | 0 | 0 | 0 | 0
PAR | 1 | 1 | 1 | 1 | 1 | 1
A | 0 | 0 | 1 | 1 | 1 | 1
B | 0 | 0 | 0 | 1 | 1 | 1
C | 1 | 1 | 0 | 0 | 0 | 0
AE | 1 | 1 | 1 | 0 | 1 | 1
0ms
1ms
2ms
3ms
4ms
5ms
6ms

## Slide 19: Combinational vs. Sequential Logic
So far, we have ignored “time” in our circuits
Our chips used combinational logic
  When given inputs, the chip computes its output instantaneously
  The output is a function of the current inputs, with no memory of previous events
Today, we’ll start exploring what happens when we consider time, ultimately building to sequential logic

## Slide 20: What is Sequential Logic?
Sequential logic incorporates time in hardware
Output depends on present value of its input signals and a sequence of past inputs
Sequential logic resolves the problem introduced with combinational logic
  Does so by adding a delay for the entire circuit before evaluating the result
  All the circuits will be evaluated between one clock cycle and the output will be evaluated at the end of the clock cycle

## Slide 21: Combinational vs. Sequential Abstraction
Clock Signal
0
1
in
out
t=1
t=2
t=3
t=4
t=0
in
out
Combinational: a function of the current inputs
Sequential: a function of previous inputs (has “memory”)
a
b
c
d
e
f(a)
f(b)
f(c)
f(d)
f(e)
a
b
c
d
e
f(a)
f(b)
f(c)
f(d)

## Slide 22: Lecture Outline
Bloom’s Taxonomy
  Applying Higher Levels of Cognition to Learning
Introduction to Sequential Logic
  The Problem with Combinational Logic
Representing Time in Hardware
  Clock Signals and Units of Time in Hardware
The Data Flip-Flop (DFF)
  Implementation and Examples

## Slide 23: Representing Time: Clock Signals
We physically represent time in hardware with a clock signal
  A clock signal changes its frequency at a set time rate
  Alternates between a low signal and a high signal of equal length
A cycle is a period of time between a low and high signal
  Represents one unit of time in hardware
  We can change how long a unit of time is by alternating the length of the low and high signals

## Slide 24: Physical Timekeeping
Hardware keeps track of time using an alternating signal
  Creates the idea of discrete time: state changes only occur in discrete intervals, right when signal alternates
Physical Time
Clock Signal
0
1

## Slide 25: Physical Timekeeping
Hardware keeps track of time using an alternating signal
  Creates the idea of discrete time: state changes only occur in discrete intervals, right when signal alternates
Physical Time
Clock Signal
0
1
Discrete Time Intervals
t=1
t=2
t=3
t=4
t=0

## Slide 26: Adding a Clock: Ideal
We want this behavior from a simple, combinational Not gate:
Clock Signal
0
1
in
0
1
out
0
1
t=1
t=2
t=3
t=4
t=0

## Slide 27: Adding a Clock: Reality
Combinational logic may be incorrect for a period immediately after inputs change
  Computation delays (logic gates) and propagation delays (wires)
Clock Signal
0
1
in
0
1
out
0
1
t=1
t=2
t=3
t=4
t=0
In the autopilot example, this arrow would represent the 3ms of uncertainty after inputs change

## Slide 28: Adding a Clock: Clock Cycles
Choose a clock cycle length slightly longer than the delays
Clock Signal
0
1
in
0
1
out
0
1
t=1
t=2
t=3
t=4
t=0
> 3ms

## Slide 29: Adding a Clock: Abstraction
If we use a long enough clock cycle, we can pretend that combinational chips (like Not) work instantly
Clock Signal
0
1
in
0
1
out
0
1
t=1
t=2
t=3
t=4
t=0

## Slide 30: Five-minute Break!
Feel free to stand up, stretch, use the restroom, drink some water, review your notes, or ask questions
We’ll be back at:

## Slide 31
Which of the following statements about sequential logic is FALSE?
We represent time with a clock signal that alternates between high and low signals
The DFF allows us to reuse outputs as inputs in a circuit
The outputs for a DFF at time t=2 is determined by the inputs at time t=3
Sequential logic is important because it addresses slight delays caused in circuit gates
We’re lost…

## Slide 32: Lecture Outline
Bloom’s Taxonomy
  Applying Higher Levels of Cognition to Learning
Introduction to Sequential Logic
  The Problem with Combinational Logic
Representing Time in Hardware
  Clock Signals and Units of Time in Hardware
The Data Flip-Flop (DFF)
  Implementation and Examples

## Slide 33: The Data Flip-Flop Gate
Simplest state-keeping component
  1-bit input, 1-bit output
  Wired to the clock signal
  Always outputs its previous input: out(t) = in(t-1)
Implementation: a gate that can flip between two stable states (remembering 0 vs. remembering 1)
  Gates with this behavior are “Data Flip Flops” (DFFs)

## Slide 34: Aside: Treating the DFF as a Primitive
Disclaimer: DFFs can be made from Nand gates exclusively
  But requires wiring them together in a “messy” loop that the hardware simulator can’t simulate and isn’t very educational
For simplicity, we will treat the DFF as a primitive in the projects
  Just like Nand, you can use the built-in implementation

## Slide 35: Data Flip-Flop (DFF) Behavior
Clock Signal
0
1
in
0
1
out
0
1
t=1
t=2
t=3
t=4
t=0

## Slide 36: Sequential Chips
A category of chips that utilize the clock signal, in addition to any combinational logic
Capable of:
  Maintaining state
  Optionally, acting on that state and the current inputs
    Can incorporate combinational logic as well
Constructed from:
  DFFs
  Combinational logic (which is entirely constructed from Nand)

## Slide 37: Sequential Chips
Combinational Logic
f
DFF
output
output(t) = f(state(t-1), input(t))
DFF
DFF
input

## Slide 38: D Flip-Flop: Time Series
DFF Specification:
out(t) = in(t-1)
in | 0 | 0 | 1 | 1 | 0 | 1 | 0 | ...
out | 0 | 0 | 0 | 1 | 1 | 0 | 1 | ...
time | t=0 | t=1 | t=2 | t=3 | t=4 | t=5 | t=6 | ...
Example: out(t=3) = in(t=2)

## Slide 39: DFF Example 1: Specification
Example specification: out(t) = Xor(a(t-1), b(t-1))
Takes two inputs, a and b, and outputs the Xor of them
  Note that out at time t is determined by a and b at time t-1
  We will need to use a DFF
Exercise: Draw out the corresponding circuit diagram and HDL implementation

## Slide 40: DFF Example 1: Time Series
Example specification: out(t) = Xor(a(t-1), b(t-1))
Example: out(t=3) = Xor(a(t=2), b(t=2))
a | 0 | 0 | 1 | 1 | 1 | 0 | 0 | ...
b | 0 | 1 | 0 | 1 | 1 | 1 | 0 | ...
out | 0 | 0 | 1 | 1 | 0 | 0 | 1 | ...
time | t=0 | t=1 | t=2 | t=3 | t=4 | t=5 | t=6 | ...

## Slide 41: DFF Example 1: Circuit Diagram & HDL
Example specification: out(t) = Xor(a(t-1), b(t-1))
Circuit diagram:
HDL:

## Slide 42: DFF Example 1: Circuit Diagram & HDL
Example specification: out(t) = Xor(a(t-1), b(t-1))
Circuit diagram:
HDL:
CHIP Example1 {
IN a, b;
OUT out;
PARTS:
Xor(a=a, b=b, out=xorout);
DFF(in=xorout, out=out);
}

## Slide 43: DFF Example 2: Specification
Example specification: out(t) = Xor(out(t-1), in(t-1))
Notice how the specification uses out(t-1) as an input for out(t)
  Implies the necessity of circular wiring, separated by a DFF
Exercise: Draw out the corresponding circuit diagram and HDL implementation

## Slide 44: DFF Example 2: Time Series
Example specification: out(t) = Xor(out(t-1), in(t-1))
Example: out(t=1) = Xor(in(t=0), out(t=0))
in | 0 | 0 | 1 | 1 | 1 | 0 | 0 | ...
out | 0 | 0 | 0 | 1 | 0 | 1 | 1 | ...
time | t=0 | t=1 | t=2 | t=3 | t=4 | t=5 | t=6 | ...

## Slide 45: DFF Example 2: Circuit Diagram & HDL
Example specification: out(t) = Xor(out(t-1), in(t-1))
Circuit diagram:
HDL:

## Slide 46: DFF Example 2: Circuit Diagram & HDL
Example specification: out(t) = Xor(out(t-1), in(t-1))
Circuit diagram:
HDL:
CHIP Example2 {
IN in;
OUT out;
PARTS:
Xor(a=in, b=prevout, out=xorout);
DFF(in=xorout, out=prevout, out=out);
}

## Slide 47: DFF Example 3: Specification
Example specification: out(t) = And(Not(out(t-1)), in(t-1))
Exercise: Draw out the corresponding circuit diagram and HDL implementation

## Slide 48: DFF Example 3: Time Series
Example specification: out(t) = And(Not(out(t-1)), in(t-1))
Example: out(t=1) = And(Not(out(t=0)), in(t=0))
in | 1 | 1 | 0 | 1 | 1 | 0 | 0 | ...
out | 0 | 1 | 0 | 0 | 1 | 0 | 0 | ...
time | t=0 | t=1 | t=2 | t=3 | t=4 | t=5 | t=6 | ...

## Slide 49: DFF Example 3: Circuit Diagram & HDL
Example specification: out(t) = And(Not(out(t-1)), in(t-1))
Circuit diagram:
HDL:

## Slide 50: DFF Example 3: Circuit Diagram & HDL
Example specification: out(t) = And(Not(out(t-1)), in(t-1))
Circuit diagram:
HDL:
CHIP Example3 {
IN in;
OUT out;
PARTS:
Not(in=prevout, out=notprevout);
And(a=in, b=notprevout, out=andout);
DFF(in=andout, out=prevout, out=out);
}

## Slide 51: Post-Lecture 6 Reminders
Exciting lecture topics this Thursday!
  Metacognitive Subject: Cornell Note-taking Method
  Technical Subject: Computer Memory
Project 3 due this Thursday (10/20) at 11:59pm
Preston has office hours after class in CSE2 153
  Feel free to post your questions on the Ed board as well