## Slide 1: Memory Representation & Hack Assembly
Memory Representation, Hack Assembly Review, Implementing Multiplication in Hack, Project 5 Overview

## Slide 2: Lecture Outline
Hack Assembly Memory Representation
  I/O, Memory Mapping, External vs. Internal Memory
Hack Assembly Language Review
  Registers, A-Instructions, Symbols, & C-Instructions
Multiplication Implementation Exercise
  Multiplying Two Numbers in Hack Assembly
Project 5 Overview
  Specification Annotation, Machine Language, & Building Computer Memory

## Slide 3: Review: What is Binary?
A base-n number system is a system of number representation with n symbols
Decimal system is a base-10 number system
  Base-10 symbols: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9
  Increase a number by moving to the next greatest symbol
  Add another digit when we run out of symbols
Binary is a base-2 number system
  Often prefixed with 0b (e.g., 0b1101, 0b10)
  Base-2 symbols: 0, 1

## Slide 4: Hexadecimal
Base-16 number system
  Symbols: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
Commonly used for referring to memory addresses
  Simple to convert between binary and hexadecimal
  Hexadecimal uses fewer digits to represent a value than binary
Uses the prefix 0x to indicate a number is written in hexadecimal
  32 is decimal, 0x32 is hexadecimal

## Slide 5: Number Representation Comparison
Decimal | Hexadecimal | Binary
0 | 0x0 | 0b0000
1 | 0x1 | 0b0001
2 | 0x2 | 0b0010
3 | 0x3 | 0b0011
4 | 0x4 | 0b0100
5 | 0x5 | 0b0101
6 | 0x6 | 0b0110
7 | 0x7 | 0b0111
8 | 0x8 | 0b1000
9 | 0x9 | 0b1001
10 | 0xA | 0b1010
11 | 0xB | 0b1011
12 | 0xC | 0b1100
13 | 0xD | 0b1101
14 | 0xE | 0b1110
15 | 0xF | 0b1111

## Slide 6: Binary and Hexadecimal Conversion
One-to-one correspondence between binary and hexadecimal
To convert from binary to hexadecimal, swap out binary bits digits for the corresponding hexadecimal digit (or vice versa)
Example: 0x3A is 0b0011_1010
  0x3 == 0b0011
  0xA == 0b1010

## Slide 7: Hack Assembly: Input / Output
Two memory maps are created for you by underlying hardware
  SCREEN is a huge map where each pixel is one bit
  KEYBOARD is a single 16-bit word map with code of current key
Example:
@KBD
D=M
@SCREEN
M=D
D contains code of current key (e.g., 67 for “C”)
First 16 bits of screen (top left) show binary for 67

## Slide 8: Hack: Input / Output
I/O is memory mapped
  Corresponds to some region of RAM
  Low-level drivers are constantly refreshing
COMPUTER
MEMORY
KEYBOARD
CPU
REGISTERS
CONTROL
SCREEN
ROM
1110001011111100
RAM
1100101010010101
0110010101100000
1101010010111001
0010110101001000
1010001001001000
1101101111101001
PC
A/M
D

## Slide 9: Hack: Memory Mapped Output
Each bit of the screen memory map corresponds to one pixel (1 = black, 0 = white)
The start of the memory map is accessible via the SCREEN symbol in Hack.asm
RAM
1100101010010101
0110010101100000
1101010010111001
0010110101001000
1010001001001000
1101101111101001
SCREEN

## Slide 10: Hack: External Memory Abstraction
Programmer sees one RAM32K memory region
  Only 16K + 8K + 1 words are being used
Split into three parts: SCREEN, KEYBOARD, and the rest
  Screen: 8K words
  Keyboard: 1 words
  The rest: 16K words (used for data and instructions)
Programmer can use the same interface to interact with the SCREEN, KEYBOARD, or normal RAM
  Just specify address, value, and other inputs
  Address determines what part we are interacting with

## Slide 11: Hack: Internal Memory Implementation
In reality, separate memory chips for memory devices is unnecessary
  “Drivers” are code relaying changes in memory values to the device
In Hack, it’s not as simple as one RAM32K chip
  Use internal SCREEN and KEYBOARD chips so our virtual computer can detect and show changes in the screen and keyboard
Our memory chip has three subchips: SCREEN, KEYBOARD, and RAM16K
  Process the address given by the programmer and relay the request to the appropriate subchip

## Slide 12: Hack: Memory Abstraction User View
RAM
1100101010010101
0110010101100000
1101010010111001
0010110101001000
1010001001001000
1101101111101001
0010110101001000
1010001001001000
0010110101001000
1101101111101001
0010110101001000
1010001001001000
0010110101001000
1010001001001000
1101101111101001
0010110101001000
1010001001001000
1101101111101001
USER
Screen address
Keyboard address

## Slide 13: Hack: Memory Abstraction Internal View
USER
IMPLEMENTATION
RAM16K
1100101010010101
0110010101100000
1101010010111001
0010110101001000
1010001001001000
1101101111101001
SCREEN
1100101010010101
0110010101100000
1101010010111001
KEYBOARD
1100101010010101
RAM

## Slide 14
Hexadecimal is useful because it’s easier for humans to read while still being interpretable by a computer
0x390B in binary is 0b0011_1001_0000_1011
390 in hexadecimal is 0x186
A programmer can only read from and write to the SCREEN and KEYBOARD parts of the Hack computer
We’re lost…
Which of the following statements is FALSE?

## Slide 15: Lecture Outline
Hack Assembly Memory Representation
  I/O, Memory Mapping, External vs. Internal Memory
Hack Assembly Language Review
  Registers, A-Instructions, Symbols, & C-Instructions
Multiplication Implementation Exercise
  Multiplying Two Numbers in Hack Assembly
Project 5 Overview
  Specification Annotation, Machine Language, & Building Computer Memory

## Slide 16: The Hack Computer
The hardware you will build
  16-bit word size
  ROM: sequence of instructions
    ROM[0], RAM[1]…
  RAM: data sequence
    RAM[0], RAM[1]…
16
COMPUTER
MEMORY
KEYBOARD
CPU
REGISTERS
CONTROL
SCREEN
ROM
(16-bit Instructions, Read-Only)
1110001011111100
RAM
(16-bit Data, Read/Write)
1100101010010101
PC
A/M
D

## Slide 17: The Hack Machine Language
Two types of instructions (16-bit)
  A-instructions load data
  C-instructions perform computations
Program: sequence of instructions
17
COMPUTER
MEMORY
KEYBOARD
CPU
REGISTERS
CONTROL
SCREEN
ROM
(16-bit Instructions, Read-Only)
1110001011111100
RAM
(16-bit Data, Read/Write)
1100101010010101
PC
A/M
D

## Slide 18: Hack: Control Flow
Startup
  Hack instructions loaded into ROM
  Reset signal initializes computer state (instruction 0)
Execution
  Usually, advance to next instruction each cycle
  On jump instruction, write a different address into the PC
0101110011100110
1011000101010100
1110001011111100
0101110101101110
0001011000111010
0010111011011001
0110111110101001
0001110010110110
ROM (Instructions)
0
1
2
3
4
5
6
7
...

## Slide 19: Hack: Registers
D Register: For storing Data
A Register: For storing data and Addressing memory
M “Register”: The 16-bit word in Memory currently being referenced by the address in A
REGISTERS
A
108
D
RAM
1100101010010101
...
106
107
108
109
110
...
M

## Slide 20: Hack: A-Instructions
Syntax:
value can either be:
  A decimal constant
  A symbol referring to a constant
Semantics:
  Stores value in the A register
@value

## Slide 21: Hack: A-Instructions
Symbolic Syntax
  Loads a value into the A register
Example:
Binary Syntax
0000000000010101
Family:
A-Instruction
Value:
Binary encoding of 21
@value
A Register
0
D Register
0
A Register
21
D Register
0
...
@21
...

## Slide 22: Hack: Symbols
Symbols are simply an alias for some address
  Only in the symbolic code—don’t turn into a binary instruction
  Assembler converts use of that symbol to its value instead
Example:
@3
D=0
(LOOP)
@21
D=1
@LOOP
...
00
01
02
03
04
0000000000000011
1110101010010000
0000000000010101
1110111111010000
0000000000000010
...
00
01
02
03
04
Assemble
LOOP = 02

## Slide 23: Hack: Built-In Symbols
Using ( ) defines a symbol in ROM / Instructions
Assembler knows a few built-in symbols in RAM / Data
R0, R1, ..., R15: Correspond to addresses at the very beginning of RAM (0, 1, …, 15)
  “Virtual registers,” Useful to store variables
SCREEN, KBD: Base of I/O Memory Maps
Example:
A Register
0
D Register
0
A Register
3
D Register
0
...
@R3
...

## Slide 24: Hack: C-Instructions
Syntax: (dest and jump optional)
  dest is a combination of destination registers:
  comp is a computation:
  jump is an unconditional or conditional jump:
Semantics:
  Computes value of comp
  Stores results in dest (if specified)
  If jump is specified and condition is true (by testing comp result), jump to instruction ROM[A]
dest = comp ; jump
M, D, MD, A, AM, AD, AMD
0, 1, -1, D, A, !D, !A, -D, -A, D+1, A+1, D-1, A-1, D+A, D-A, A-D, D&A, D|A, M, !M, -M, M+1, M-1, D+M, D-M, M-D, D&M, D|M
JGT, JEQ, JGE, JLT, JNE, JLE, JMP

## Slide 25: Hack: C-Instructions Example
(EXAMPLE)
@55
D=A+1
00
01
A Register
55
D Register
56

## Slide 26: Hack: C-Instructions Example
(EXAMPLE)
@55
D=A+1
@R2
M=D
00
01
02
03
RAM
0
1
2
?
?
56
...
A Register
55
D Register
56
A Register
2
D Register
56

## Slide 27: Hack: C-Instructions Example
(EXAMPLE)
@55
D=A+1
@R2
M=D
@EXAMPLE
D;JGT
00
01
02
03
04
05
RAM
0
1
2
?
?
56
...
A Register
0
D Register
56
(Will jump to instruction 0, since D > 0)
A Register
2
D Register
56
A Register
55
D Register
56

## Slide 28: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Jump:
Condition for jumping
Dest:
Where to store result
Comp:
ALU Operation (a bit chooses between A and M)
Unused
Family:
C-Instruction

## Slide 29: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Chapter 4
Jump:
Condition for jumping

## Slide 30: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Chapter 4
Dest:
Where to store result

## Slide 31: Hack: C-Instructions
Symbolic:
Binary:
dest = comp ; jump
1 1 1 a c1 c2 c3 c4 c5 c6 d1 d2 d3 j1 j2 j3
Comp:
ALU Operation (a bit chooses between A and M)
Chapter 4
Important: just pattern matching text!
Cannot have “1+M”

## Slide 32
1 1 1 1 1 0 0 1 1 1 0 0 1 0 0 1
1 1 1 0 0 0 1 1 0 0 0 0 0 0 1 1
1 1 1 0 1 0 0 1 1 1 0 1 0 0 1 0
1 1 1 1 0 0 1 1 0 0 0 0 0 0 1 1
We’re lost…
What is the C-instruction encoding for D;JGE?

## Slide 33
What is the C-instruction encoding for D;JGE?

## Slide 34: Five-minute Break!
Feel free to stand up, stretch, use the restroom, drink some water, review your notes, or ask questions
We’ll be back at:

## Slide 35: Lecture Outline
Hack Assembly Memory Representation
  I/O, Memory Mapping, External vs. Internal Memory
Hack Assembly Language Review
  Registers, A-Instructions, Symbols, & C-Instructions
Multiplication Implementation Exercise
  Multiplying Two Numbers in Hack Assembly
Project 5 Overview
  Specification Annotation, Machine Language, & Building Computer Memory

## Slide 36: Exercise: Implementing Multiplication
Write a program that multiplies R0 and R1 and stores the result in R2
  Remember we don’t have a multiply operation
  We will have to use add and loops to get the job done
Roadmap
  Start with pseudocode using if statements, loops, etc.
  Remove conditionals and loops by using jumps in pseudocode
  Convert pseudocode to assembly

## Slide 37: Exercise: Implementing Multiplication
Goal: Implement R0 × R1 = R2
Pseudocode | Hack Assembly

## Slide 38: Exercise: Implementing Multiplication
Goal: Implement R0 × R1 = R2
Pseudocode | Hack Assembly
Approach: add R0 to the result R1 times

## Slide 39: Exercise: Implementing Multiplication
Goal: Implement R0 × R1 = R2
Pseudocode | Hack Assembly
Approach: add R0 to the result R1 times
R2 = 0
while (R1 > 0) {
R2 = R0 + R2
R1 = R1 - 1
}

## Slide 40: Exercise: Implementing Multiplication
Remove loops from pseudocode
Use labels to notate important sections of the code
Attempt 1: What happens when R1 is 0? What should happen?
R2 = 0
while (R1 > 0) {
R2 = R0 + R2
R1 = R1 - 1
}
START:
R2 = 0
LOOP:
R2 = R0 + R2
R1 = R1 - 1
IF R1 > 0 JMP LOOP
END:
INFINITE LOOP

## Slide 41: Exercise: Implementing Multiplication
Remove loops from pseudocode
Use labels to notate important sections of the code
Attempt 1: What happens when R1 is 0? What should happen?
R2 = 0
while (R1 > 0) {
R2 = R0 + R2
R1 = R1 - 1
}
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP

## Slide 42: Exercise: Implementing Multiplication
Convert to Hack Assembly
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP
(START)
@R2
M = 0
(LOOP)
(END)

## Slide 43: Exercise: Implementing Multiplication
Convert to Hack Assembly
(START)
@R2
M = 0
(LOOP)
@R1
D = A
@END
D; JLE
(END)
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP

## Slide 44: Exercise: Implementing Multiplication
Convert to Hack Assembly
(START)
@R2
M = 0
(LOOP)
@R1
D = M
@END
D; JLE
(END)
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP

## Slide 45: Exercise: Implementing Multiplication
Convert to Hack Assembly
(START)
@R2
M = 0
(LOOP)
@R1
D = M
@END
D; JLE
@R0
D = M
@R2
M = M + D
(END)
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP

## Slide 46: Exercise: Implementing Multiplication
Convert to Hack Assembly
(START)
@R2
M = 0
(LOOP)
@R1
D = M
@END
D; JLE
@R0
D = M
@R2
M = M + D
@R1
M = M - 1
@LOOP
0; JMP
(END)
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP

## Slide 47: Exercise: Implementing Multiplication
Convert to Hack Assembly
(START)
@R2
M = 0
(LOOP)
@R1
D = M
@END
D; JLE
@R0
D = M
@R2
M = M + D
@R1
M = M – 1
@LOOP
0; JMP
(END)
@END
0; JMP
START:
R2 = 0
LOOP:
IF R1 <= 0
JMP to END
R2 = R0 + R2
R1 = R1 - 1
JMP LOOP
END:
INFINITE LOOP

## Slide 48: Lecture Outline
Hack Assembly Memory Representation
  I/O, Memory Mapping, External vs. Internal Memory
Hack Assembly Language Review
  Registers, A-Instructions, Symbols, & C-Instructions
Multiplication Implementation Exercise
  Multiplying Two Numbers in Hack Assembly
Project 5 Overview
  Specification Annotation, Machine Language, & Building Computer Memory

## Slide 49: Project 5 Overview
Part I: Annotation
  Come prepared to your upcoming Student-TA 1:1 meeting to work on Project 5 (e.g., specification reading and identifying annotation strategies you would want to use)
Part II: Machine Language
  Implement Max.asm in Hack Assembly
Part III: Building Computer Memory
  Implement Memory.hdl in HDL
Part IV: Project 5 Reflection

## Slide 50: Project 5, Part I: Annotation
Fill out the Assignment Timeline
  Divide up Project 5 into doable chunks for the days you plan to work on the assignment
  Describe each day’s task in as much detail as possible
Annotate the Project 5 Specification
  Identify five annotation strategies that you want to try
  Practice these strategies on the Project 5 specification
Complete Annotation Reflection Questions
  Reflect on the strategies you used and why or why not they were effective

## Slide 51: Annotate the Project 5 Specification
We’ll provide you with an opportunity to start annotating the Project 5 specification in class now
Recall these annotation strategies:
  Highlighting, underlining or using [brackets] to note key points or ideas
  Circling unfamiliar words or confusing parts of the text
  Paraphrasing or summarizing passages/chapters/sections
  Commenting or reacting to the text 🤯

## Slide 52: Project 5: Tools
Running a Test Script (recommended flow):
Quickly Iterating or Experimenting:
Max.asm
Max.hack
Assembler
CPUEmulator
The test scripts use the .hack files directly! Don’t let your .asm and .hack get out of sync!
Max.asm
CPUEmulator
Can still “run” the program, even without a script

## Slide 53: Post-Lecture 9 Reminders
Project 4 due tonight (10/27) at 11:59pm
Project 5 (Annotation, Machine Language, & Building Computer Memory) released today, due next Thursday (11/3) at 11:59pm
Course Staff Support
  Eric has office hours in CSE2 153 today after lecture
  Post your questions on the Ed discussion board