## Slide 1: Growth Mindset & Arithmetic Logic Unit
Growth vs. Fixed Mindset, Negative Numbers in Binary, Arithmetic Logic Unit (ALU), Project 3 Overview

## Slide 2: Project 2 Check-in
How has Project 2 been going?
  👍 If you’re feeling great about completing Project 2 by tonight
  If you’re feeling decent about where you are right now
  👎 If you’re feeling behind or unlikely to submit on time
A few common questions about Project 2:
  Can’t see message at bottom of Hardware Simulator? Try reducing window size (Settings  Displays  Change size to < 150%)
  Can’t use typical Boolean Function Synthesis on Or.hdl
  DMux.hdl: Follow same implementation strategy as other gates
Double-check your submission on GitLab
  Navigate to GitLab, open tags, and verify that the associated commit includes your expected changes
👍

## Slide 3: Lecture Outline
Growth vs. Fixed Mindset
  Setting SMART Goals
Negative Numbers in Binary
  Unsigned, Signed, and Two’s Complement Representations
Arithmetic Logic Unit (ALU)
  Overview and Examples of ALU Functions
Project 3 Overview
  ALU Implementation Strategy
  HDL Tips and Tricks

## Slide 4: Growth vs. Fixed Mindset

## Slide 5: Setting SMART Goals
S – Be specific, simple and significant.
M – Make sure your goals are measurable. How many times within a week, month, the quarter do you want to do x goal?
A – Make sure your goals are achievable. Is your goal within your scope of control?
R – Be realistic and reasonable.
T – Be time-bound. When will you accomplish your goal?

## Slide 6: SMART Goals Group Discussion
SMART GOAL FRAMEWORK
S — Specific
M — Measurable
A — Achievable
R — Realistic
T — Timebound
Attending CSE 390B
office hours at least 5x this quarter (or once every other week)
SPRING QUARTER GOALS
What are skills, practices or habits that are not strengths YET?
SPHERE OF CONTROL
Getting a 4.0 in a course VS. Attending course office hours

## Slide 7: Lecture Outline
Growth vs. Fixed Mindset
  Setting SMART Goals
Negative Numbers in Binary
  Unsigned, Signed, and Two’s Complement Representations
Arithmetic Logic Unit (ALU)
  Overview and Examples of ALU Functions
Project 3 Overview
  ALU Implementation Strategy
  HDL Tips and Tricks

## Slide 8
What are the Sign and Magnitude (signed) and Two’s Complement binary representations of the number -7?
Signed: 0b1001, Two’s Complement: 0b1111
Signed: 0b0111, Two’s Complement: 0b1001
Signed: 0b1111, Two’s Complement: 0b0111
Signed: 0b1111, Two’s Complement: 0b1001
We’re lost…

## Slide 9: Two’s Complement
One binary interpretation to represent negative values
Most significant bit (MSB) has a negative weight
  Add the remaining bits as usual (with positive weights)
Example: 0b1101 in Two’s Complement
  –(1 × 23) + (1 × 22) + (0 × 21) + (1 × 20) = –8 + 4 + 0 + 1
  = –3
Negation procedure: Take bitwise complement and add one
  –x = ~x + 1
  Example: Negate x = 4

## Slide 10: Two’s Complement
One binary interpretation to represent negative values
Most significant bit (MSB) has a negative weight
  Add the remaining bits as usual (with positive weights)
Example: 0b1101 in Two’s Complement
  –(1 × 23) + (1 × 22) + (0 × 21) + (1 × 20) = –8 + 4 + 0 + 1
  = –3
Negation procedure: Take bitwise complement and add one
  –x = ~x + 1
  Example: Negate x = 4
  –4 = ~0b0100 + 1 = 0b1011 + 0b1= 0b1100 = –8 + 4 = –4

## Slide 11: Four-bit Values in Various Representations
Binary Value | Unsigned Binary | Signed Binary | Two’s Complement
0b0000 | 0 | 0 | 0
0b0001 | 1 | 1 | 1
0b0010 | 2 | 2 | 2
0b0011 | 3 | 3 | 3
0b0100 | 4 | 4 | 4
0b0101 | 5 | 5 | 5
0b0110 | 6 | 6 | 6
0b0111 | 7 | 7 | 7
0b1000 | 8 | -0 | -8
0b1001 | 9 | -1 | -7
0b1010 | 10 | -2 | -6
0b1011 | 11 | -3 | -5
0b1100 | 12 | -4 | -4
0b1101 | 13 | -5 | -3
0b1110 | 14 | -6 | -2
0b1111 | 15 | -7 | -1

## Slide 12: Two’s Complement Addition
The process for adding binary in Two’s Complement is the same as that of unsigned binary
Hardware performs the exact same calculations
  It doesn’t need to know the sign of the values, it performs the same calculation
  The only difference is representation of sum
Example: 0b1001 + 0b0010
  Unsigned interpretation:
  Signed interpretation:
  Two’s Complement interpretation:
carry |  |  |  | 
a | 1 | 0 | 0 | 1
b | 0 | 0 | 1 | 0
sum |  |  |  | 

## Slide 13: Two’s Complement Addition
The process for adding binary in Two’s Complement is the same as that of unsigned binary
Hardware performs the exact same calculations
  It doesn’t need to know the sign of the values, it performs the same calculation
  The only difference is representation of sum
Example: 0b1001 + 0b0010 = 0b1011
  Unsigned interpretation: 9 + 2 = 11
  Signed interpretation: –1 + 2 = –3 (?)
  Two’s Complement interpretation: –7 + 2 = –5
carry |  |  |  | 
a | 1 | 0 | 0 | 1
b | 0 | 0 | 1 | 0
sum | 1 | 0 | 1 | 1

## Slide 14: Lecture Outline
Growth vs. Fixed Mindset
  Setting SMART Goals
Negative Numbers in Binary
  Unsigned, Signed, and Two’s Complement Representations
Arithmetic Logic Unit (ALU)
  Overview and Examples of ALU Functions
Project 3 Overview
  ALU Implementation Strategy
  HDL Tips and Tricks

## Slide 15: The Von Neumann Architecture
COMPUTER
MEMORY
(This picture will get more detailed as we go!)
INPUT
CPU
REGISTERS
CONTROL
OUTPUT

## Slide 16: The Arithmetic Logic Unit
Computes a function on two inputs to produce an output
Input Control Bits specific which function should be computed
  Supports a combination of logical (And, Or) and arithmetic operations (+, –)
Indicate properties of the result with Output Control Bits (commonly called Flags)
Input Control Bits
Output Control Bits
(Flags)
Output
Input A
Input B

## Slide 17: Our ALU Implementation
Inputs & Outputs
  16-bit inputs x and y and output out
  Interpret in Two’s Complement
Input Control Bits
  Six control bits (zx, nx, zy, ny, f, no) specify which function to compute
  26 = 64 different possible functions to choose from (only 18 of interest)
Output Control Bits (Flags)
  2 bits (zr and ng) describing the properties of the output
x
y
out
16
16
16
zx
nx
zy
ny
f
no
zr
ng

## Slide 18: ALU Functions: Client’s View
We support 18 different functions of interest
  3 that simply give constant values (ignoring operands)
  10 that change a single input, possibly with a constant
  5 that perform an operation using both inputs
 |  |  |  |  |  | out
 |  |  |  |  |  | 0
 |  |  |  |  |  | 1
 |  |  |  |  |  | -1
 |  |  |  |  |  | x
 |  |  |  |  |  | y
 |  |  |  |  |  | !x
 |  |  |  |  |  | !y
 |  |  |  |  |  | -x
 |  |  |  |  |  | -y
 |  |  |  |  |  | x+1
 |  |  |  |  |  | y+1
 |  |  |  |  |  | x-1
 |  |  |  |  |  | y-1
 |  |  |  |  |  | x+y
 |  |  |  |  |  | x-y
 |  |  |  |  |  | y-x
 |  |  |  |  |  | x&y
 |  |  |  |  |  | x¦y

## Slide 19: ALU Functions: Client’s View
We support 18 different functions of interest
  3 that simply give constant values (ignoring operands)
  10 that change a single input, possibly with a constant
  5 that perform an operation using both inputs
To select a function, set the control bits to the corresponding combination
zx | nx | zy | ny | f | no | out
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y

## Slide 20: ALU Functions: Implementer’s View
These 18 functions are really a clever combination of 6 core operations:
zx | nx | zy | ny | f | no | out
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y
if zx==1,
set x to 0
if zy==1,
set y to 0
if nx==1,
negate x
if f==1, result is x + y
else, result is x & y
if no==1,
negate result
1
PREPROCESS INPUTS
2
COMPUTE
3
POSTPROCESS OUTPUT
if ny==1,
negate y

## Slide 21: ALU Functions: Implementer’s View
Example: Compute x - 1
  Given inputs x=0b0101 (5), y=0b0010 (2)
zx | nx | zy | ny | f | no | out
... |  |  |  |  |  | ...
0 | 0 | 1 | 1 | 1 | 0 | x-1
... |  |  |  |  |  | ...

## Slide 22: ALU Functions: Implementer’s View
Example: Compute x - 1
  Given inputs x=0b0101 (5), y=0b0010 (2)
if zx==1,
set x to 0
if zy==1,
set y to 0
if nx==1,
negate x
1
PREPROCESS INPUTS
if ny==1,
negate y
x=0b0101 (5)
Unchanged
y=0b0000 (0)
Zeroed
x=0b0101 (5)
Unchanged
y=0b1111 (-1)
Negated
zx | nx | zy | ny | f | no | out
... |  |  |  |  |  | ...
0 | 0 | 1 | 1 | 1 | 0 | x-1
... |  |  |  |  |  | ...

## Slide 23: ALU Functions: Implementer’s View
Example: Compute x - 1
  Given inputs x=0b0101 (5), y=0b0010 (2)
if zx==1,
set x to 0
if zy==1,
set y to 0
if nx==1,
negate x
if f==1, result is x + y
else, result is x & y
1
PREPROCESS INPUTS
2
COMPUTE
if ny==1,
negate y
x=0b0101 (5)
Unchanged
y=0b0000 (0)
Zeroed
x=0b0101 (5)
Unchanged
y=0b1111 (-1)
Negated
out=0b0100 (4)
x (5) + y (-1)
zx | nx | zy | ny | f | no | out
... |  |  |  |  |  | ...
0 | 0 | 1 | 1 | 1 | 0 | x-1
... |  |  |  |  |  | ...

## Slide 24: ALU Functions: Implementer’s View
Example: Compute x - 1
  Given inputs x=0b0101 (5), y=0b0010 (2)
if zx==1,
set x to 0
if zy==1,
set y to 0
if nx==1,
negate x
if f==1, result is x + y
else, result is x & y
if no==1,
negate result
1
PREPROCESS INPUTS
2
COMPUTE
3
POSTPROCESS OUTPUT
if ny==1,
negate y
x=0b0101 (5)
Unchanged
y=0b0000 (0)
Zeroed
x=0b0101 (5)
Unchanged
y=0b1111 (-1)
Negated
out=0b0100 (4)
x (5) + y (-1)
out=0b0100 (4)
Unchanged
zx | nx | zy | ny | f | no | out
... |  |  |  |  |  | ...
0 | 0 | 1 | 1 | 1 | 0 | x-1
... |  |  |  |  |  | ...

## Slide 25: ALU Output Control Bits
zr is 1 if out == 0
ng is 1 if out < 0
We’ll use these in a later project
  The basis of comparison
  Example: To evaluate if x == 4, compute x - 4 and check zr flag
These can be deceptively difficult to implement
  Start early on Project 3
x
y
out
16
16
16
zx
nx
zy
ny
f
no
zr
ng

## Slide 26: Five-minute Break!
Feel free to stand up, stretch, use the restroom, drink some water, review your notes, or ask questions
We’ll be back at:
Any song recommendations? Respond on Poll Everywhere at https://pollev.com/cse390b
Research shows mid-lecture breaks reduce the decline of attention in the middle of lecture (Olmsted, 1999)
Olmsted III, John. “The Mid-Lecture Break: When Less Is More.” Journal of Chemical Education (1999). https://pubs.acs.org/doi/abs/10.1021/ed076p525.

## Slide 27
out=0b1110, zr=0, ng=0
out=0b1011, zr=0, ng=1
out=0b1101, zr=1, ng=0
out=0b1001, zr=1, ng=1
We’re lost…
Given inputs x=0b1010 and y=0b0110 and the following input control bits, what is the resulting output and output control bits?
IN
x[16], y[16], // 16-bit inputs
zx, // zero the x input?
nx, // negate the x input?
zy, // zero the y input?
ny, // negate the y input?
f, // compute out = x + y
if 1 or x & y (if 0)
no; // negate the out output?
OUT
out[16], // 16-bit output
zr, // 1 if (out == 0),
0 otherwise
ng; // 1 if (out < 0),
0 otherwise
zx | nx | zy | ny | f | no | out
... |  |  |  |  |  | ...
0 | 1 | 1 | 1 | 1 | 1 | x+1
... |  |  |  |  |  | ...

## Slide 28: Lecture Outline
Growth vs. Fixed Mindset
  Setting SMART goals
Negative Numbers in Binary
  Unsigned, Signed, and Two’s Complement Representations
Arithmetic Logic Unit (ALU)
  Overview and Examples of ALU Functions
Project 3 Overview
  ALU Implementation Strategy
  HDL Tips and Tricks

## Slide 29: Project 3 Overview
Part I: 24-Hour Time Audit
Part II: Boolean Arithmetic
  Goal: Implement the ALU, which performs the core computations we need (+ and &)
  First, implement HalfAdder.hdl, FullAdder.hdl, and Add16.hdl
  Then, implement the ALU in the order suggested by the specification
  Chapter 2 of the textbook has more details on the adders and ALU
Part III: Project 3 Reflection

## Slide 30: ALU Implementation Strategy
First, handle zeroing out and negating inputs x and y and negating the output
  Ignore the f bit (only compute And) and ignore flag outputs
  Test your implementation using ALU-nostat-noadd.tst
Next, implement the And and Add operations using f
  How do we make decisions in hardware?
  Test your implementation using ALU-nostat.tst
Lastly, implement the logic for the status flags (zr and ng)
  Test your full ALU using ALU.tst

## Slide 31: HDL Tips: Slicing
Sometimes want to connect only part of a multi-bit bus
HDL lets us with slicing notation
Example: ChipA has eight output pins, and we want to connect the first four to ChipB’s four inputs:
Note: We can only slice chip connections, not internal wires (e.g., w1[0..3] is not allowed)
  If we need to use half an 8-bit wire, make two 4-bit wires and slice the output they’re connected to
ChipA
ChipB
ChipA (out[0..3]=w1);
ChipB (in=w1);
w1 (4)
out (8)
in (4)

## Slide 32: HDL Tips: Connections
Can connect a chip output multiple times, or not at all!
  Hint: In Add16.hdl, do we need to use the last carry bit?
ChipA
ChipB
ChipA (out[0..3]=w1,
out[2..5]=w2,
out[5]=w3);
ChipB (in=w1);
ChipB (in=w2);
ChipC (in=w3);
w1 (4)
out (8)
in (4)
ChipB
ChipC
in (4)
in (1)
w2 (4)
w3 (1)

## Slide 33: HDL Tips: Constants
A bus of true or false contain all 1s or all 0s, respectively, and implicitly act as whatever width is needed
Example: ChipB has four inputs and ChipC has one input
  ChipB (in=true) assigns four input bits a value of 1 (true)
  ChipC (in=true) assigns one input bit a value of 1 (true)
  ChipC (in=false) assigns one input bit a value of 0 (false)
ChipB (in=true);
ChipC (in=true);
ChipC (in=false);
ChipB
true (4)
in (4)
ChipC
in (1)
ChipC
in (1)
true (1)
false (1)
Fountain of endless 1s
Bottomless serving of 0s

## Slide 34: Lecture 4 Wrap-up
Exciting topics for Week 3!
  Metacognitive Subject: Note-taking Practices 📝
  Technical Subject: Sequential Logic & Building Memory
Project Reminders
  Project 2 due tonight (Thursday, 4/7) at 11:59pm PDT
  Project 3 (24-Hour Time Audit & Boolean Arithmetic) released, due next Thursday (4/14) at 11:59pm PDT
Join the students-only CSE 390B Discord channel!
  https://discord.gg/Q6KBuBj8