## Slide 1: Cornell Notes & Memory
Cornell Note Taking Discussion, Storing Data: Bit, Representing and Building Memory, Program Counter Overview

## Slide 2: Project 3 Check-in
How has Project 3 been going?
  👍 If you’re feeling great about completing Project 2 by tonight
  If you’re feeling decent about where you are right now
  👎 If you’re feeling behind or unlikely to submit on time
Double-check your submission on GitLab
  Navigate to GitLab, open tags, and verify that the associated commit includes your expected changes
  Guide for untagging on GitLab on the Ed discussion board
👍

## Slide 3: Lecture Outline
Cornell Note Taking Discussion
  Compare and Contrast Cornell Notes
Storing Data: Bit
  Bit Overview and Implementation
Representing and Building Memory
  Array Abstraction, Reading and Writing
  Building From the Bit
Program Counter (PC) Overview
  Control Flow of Computer Programs

## Slide 4: Cornell Note Taking Discussion
In small groups, compare and contrast your Cornell Notes from Tuesday’s lecture
  What are some of the key points you wrote in your summary?
  What were some of the questions you came up with?
  What are you still left feeling confused/uncertain about after Tuesday’s lecture?

## Slide 5: Lecture Outline
Cornell Note Taking Discussion
  Compare and Contrast Cornell Notes
Storing Data: Bit
  Bit Overview and Implementation
Representing and Building Memory
  Array Abstraction, Reading and Writing
  Building From the Bit
Program Counter (PC) Overview
  Control Flow of Computer Programs

## Slide 6
Memory can be though of as which data structure? How is memory similar to this data structure? Different?
Map
Array
Queue
Tree
We’re lost…

## Slide 7: Computer Overview
CPU is the “brain” of our computer
  Does necessary computations (add, subtract, multiply, etc.)
Memory is used to store values for later use
  Requires persistence across multiple computations
  Needs to change values at our discretion

## Slide 8: Storing Data: Bit
A Flip-Flop changes state every clock cycle
We will build the abstraction of a “Bit” that only changes when we instruct it to
Bit
load
in
out
if load(t-1) out(t) = in(t-1)
else out(t) = out(t-1)

## Slide 9: Bit Behavior
0
1
in
0
1
out
0
1
t=1
t=2
t=3
t=4
t=0
load
Bit
load
in
out
if load(t-1) out(t) = in(t-1)
else out(t) = out(t-1)

## Slide 10: Bit Behavior
0
1
in
0
1
out
0
1
t=1
t=2
t=3
t=4
t=0
load
Bit
load
in
out
if load(t-1) out(t) = in(t-1)
else out(t) = out(t-1)

## Slide 11: Bit Time Series
Bit Specification:
Example 1: load(t=0) == 1 so out(t=1) = in(t=0)
load | 1 | 0 | 0 | 1 | 1 | 1 | 0 | ...
in | 1 | 0 | 0 | 0 | 1 | 0 | 1 | ...
out | 0 | 1 | 1 | 1 | 0 | 1 | 0 | ...
time | t=0 | t=1 | t=2 | t=3 | t=4 | t=5 | t=6 | ...
if (load(t-1)): out(t) = in(t-1)
else: out(t) = out(t-1)

## Slide 12: Bit Time Series
Bit Specification:
Example 1: load(t=0) == 1 so out(t=1) = in(t=0)
Example 2: load(t=2) == 0 so out(t=3) = out(t=2)
load | 1 | 0 | 0 | 1 | 1 | 1 | 0 | ...
in | 1 | 0 | 0 | 0 | 1 | 0 | 1 | ...
out | 0 | 1 | 1 | 1 | 0 | 1 | 0 | ...
time | t=0 | t=1 | t=2 | t=3 | t=4 | t=5 | t=6 | ...
if (load(t-1)): out(t) = in(t-1)
else: out(t) = out(t-1)

## Slide 13
Which gates will we need to implement a Bit? Select all that apply.
Mux
Xor
And
DFF
We’re lost…
if load(t-1) out(t) = in(t-1)
else out(t) = out(t-1)
Bit
load
in
out

## Slide 14: Implementing a Bit
Bit Specification:
Exercise: fill in the connections to the gates to create a circuit diagram of Bit
if load(t-1) out(t) = in(t-1)
else out(t) = out(t-1)

## Slide 15: Implementing a Bit
Bit Specification:
Exercise: fill in the connections to the gates to create a circuit diagram of Bit
if load(t-1) out(t) = in(t-1)
else out(t) = out(t-1)

## Slide 16: Lecture Outline
Cornell Note Taking Discussion
  Compare and Contrast Cornell Notes
Storing Data: Bit
  Bit Overview and Implementation
Representing and Building Memory
  Array Abstraction, Reading and Writing
  Building From the Bit
Program Counter (PC) Overview
  Control Flow of Computer Programs

## Slide 17: Memory Representation
Memory can be abstracted as one huge array
Addresses are indices into different memory slots
  The width of an address is fixed for the system
  The nand2tetris project will use 16-bit addresses
Each value in memory takes up a fixed width
  Not the same as address width
  The nand2tetris project uses 16-bit slots (values) in memory

## Slide 18: Memory Representation
Read and write to memory by specifying an address
  More details next week
Example: x = memory[01...00]
  Reads the value in memory at address 01...00 and stores it in x
Example: memory[01...00] = 7
  Writes the value 7 in the memory slot at address 01...00

## Slide 19: Five-minute Break!
Feel free to stand up, stretch, use the restroom, drink some water, review your notes, or ask questions
We’ll be back at:
Any song recommendations? Respond on Poll Everywhere at https://pollev.com/cse390b
Research shows mid-lecture breaks reduce the decline of attention in the middle of lecture (Olmsted, 1999)
Olmsted III, John. “The Mid-Lecture Break: When Less Is More.” Journal of Chemical Education (1999). https://pubs.acs.org/doi/abs/10.1021/ed076p525.

## Slide 20: Lecture Outline
Cornell Note Taking Discussion
  Compare and Contrast Cornell Notes
Storing Data: Bit
  Bit Overview and Implementation
Representing and Building Memory
  Array Abstraction, Reading and Writing
  Building From the Bit
Program Counter (PC) Overview
  Control Flow of Computer Programs

## Slide 21: Building Memory: Register
Bits store a single value (0 or 1)
  In memory, we need to store 16-bit values
Registers are conceptually the same as a Bit
  Allows us to store and change 16-bit values
  Groups together 16 individual bits that share a load signal
// if (load(t-1)): out(t) = in(t-1)
// else: out(t) = out(t-1)
CHIP Register {
IN in[16], load;
OUT out[16];
...
}

## Slide 22: RAM: Random Access Memory
Abstraction of Computer Memory: just a giant array
Goal: create hardware that can provide that abstraction
Key attribute of arrays: “random access” lets us index into them at any point
0 0000000 | 0 0000000 | -1 1111111 | 25 0011001 | 124 1111100 | 0 0000000 | 9 0001001 | -15 1110001
24 11000 | 25 11001 | 26 11010 | 27 11011 | 28 11100 | 29 11101 | 30 11110 | 31 11111
...
...
memory[26] = -1;

## Slide 23: Building Memory: RAM8 From Registers
RAM interface:
  load: if 1, then in should be written to specified memory slot
  in: 16-bit input used to update specified memory slot if load is 1
  address: address used to specify memory slot
  out: 16-bit output from the slot specified by address
RAM8 can be built from 8 registers
  address width is log2(8) = 3 bits
RAM8
...
0
1
n-1
load
in
16
address
k
out
16
Register
Register
Register

## Slide 24: Building Memory: RAM8 From Registers
Step 1: Route in to every register
  We don’t want to update every register, however
  Solution: choose which register to enable with address
Step 2: Choose which register to use for the output
When we think about making choices in hardware, we want to think about Mux and DMux
RAM8
...
0
1
n-1
load
in
address
16
k
out
16
Register
Register
Register

## Slide 25: Building Memory: The Rest of RAM
After RAM8, can build larger RAM chips from a combination of smaller RAM chips
  For example, RAM64 can be built using eight RAM8 chips
Technique is similar to RAM8 but will have to use different portions of the address
The blocks section of the reading will be helpful
  For example, can think of each RAM8 as a block of RAM64

## Slide 26: Lecture Outline
Cornell Note Taking Discussion
  Compare and Contrast Cornell Notes
Storing Data: Bit
  Bit Overview and Implementation
Representing and Building Memory
  Array Abstraction, Reading and Writing
  Building From the Bit
Program Counter (PC) Overview
  Control Flow of Computer Programs

## Slide 27: Program Counter (PC)
Memory is used to store data as well as code
Instructions and operations are stored at different addresses in memory
Program Counter in the CPU keeps track of which address contains the instruction that should be executed next

## Slide 28: Program Counter (PC)
Keeps track of what instruction we are executing
  If the PC outputs 24, on the next clock cycle the computer runs the instruction at address 24 in the code segment
Program counter specification:
if (reset[t] == 1) out[t+1] = 0
else if (load[t] == 1) out[t+1] = in[t]
else if (inc[t] == 1) out[t+1] = out[t] + 1
else out[t+1] = out[t]
PC
load
in
16
out
16
inc
reset

## Slide 29: Project 4 Overview
Part I: Cornell Note Taking
  Practice taking detailed notes in another class
  Think critically about the technique
Part II: Building Memory
  Memory & Sequential Logic: Build our first sequential chips, from a 1-bit register to a 16K RAM module
  Program Counter: Build counter that tracks where we are in a program, with support for several operations we’ll need later
  Note: Folder split for performance reasons only
Part III: Project 4 Reflection

## Slide 30: Lecture 6 Wrap-up
Stoked for these subjects lined up for Week 4!
  Metacognitive Subject: Annotation Strategies
  Technical Subject: Machine Languages and Hack Assembly
Project Reminders:
  Project 3 due tonight (Thursday, 4/14) at 11:59pm PDT
  Project 4 (Cornell Note Taking & Building Memory) released, due next Thursday (4/21) at 11:59pm PDT
  Late days from Project 2 and before are updated on Canvas